## Slide 1: Isotopic Composition of the Light Cosmic Rays with HELIX
Keith McBride
11/12/2022
PIKIMO 2022 - Cincinnati
High Energy Light Isotope eXperiment

## Slide 2
Introduction
[1] Fermi -rays
The Galaxy in gamma rays
>1 GeV
Cosmic rays produce gamma rays and other cosmic rays when colliding with gas, the Interstellar Medium
Disk
Mostly protons, but many kinds of nuclei
Diffusion-halo model, with some parameters not so well understood
[2] Ptuskin slides 2013 Cargese
How far do cosmic rays extend into the halo?
Background on Galactic Cosmic Ray Propagation

## Slide 3: Beryllium Isotopes in GCRs
Beryllium nuclei are secondary
  products of interactions during propagation
9Be is stable, 10Be is long-lived but unstable
Ratio is sensitive to time of GCR propagation
  Larger cosmic ray halo, H, longer timescale for diffusion into that halo
Until recently, very few intermediately high energy measurements…
HELIX Science
HELIX is optimized for this kind of light nuclei measurement!
10Be has half-life of 1.4 Myrs [3]
GALPROP sims with varying halo size [4]
Data retrieved with [5]

## Slide 4: Magnet Spectrometers
1. Measure rigidity in magnetic field
  B
2. Measure velocity, , and charge, , separately
3. Calculate the mass of particle
* Requires high precision tracking and strong magnetic field for high precision mass measurements
HELIX Science
ρ
Detector
Tracking hit positions
Cosmic ray
HELIX is this capable experiment

## Slide 5: Measuring Mass with HELIX
HELIX Instrument
[6] Park, N. ICRC 2021
Time-of-flight system to measure and
Drift Chamber Tracker for measurement
Higher measurements with Ring Imaging Cherenkov (RICH)
Staged approach – HELIX stage 1 shown

## Slide 6: Superconducting magnet
HELIX Instrument
Good for levitating steel-toe boots and deflecting relativistic particles
  Binary measurement of magnet ON/OFF
Cryogen Operation, 4K
  1 Tesla field
Flown previously on successful HEAT balloon experiments [7]
  Proven flight heritage
Up to 7 days of hold time
Thermal Vacuum Test, Jan 2022 at NASA Armstrong Test Facility

## Slide 7: Drift Chamber Tracker
Gas-filled (CO2 + Ar) tracker
  Charged nuclei leaves ionization trail
Detect ionization with wires
  Strong electric drift field, 1.3 kV/cm
  Induced current pulses map to distances
Staggering of sense wires to resolve Left/Right ambiguity
HELIX Instrument
  Measures the Rigidity,

## Slide 8: Drift Chamber Tracker
Detect ionization with sense wires
  3 separate sense wire planes
  216 sense wires total
Additional non-bending plane measurement along sense wire
  Readout per end of sense wires
Density and electric field contribute to resolution
  High voltage control system
  On track for better than 70μm resolution
HELIX Instrument
  Measures the Rigidity,
Inside the DCT
DCT Bending Plane Display
Example muon straight-through
58cm

## Slide 9: Ring-Imaging Cherenkov System
Charged particle
(cosmic ray)
Light/wavefront
Cherenkov light with opening angle
High GCRs radiate in aerogel medium
Transparent aerogel with high index of refraction, [8]
Extensive testing of aerogel:
  vacuum, thermal, beam line scanned, and shaken [9]
HELIX Instrument
  Measures the velocity,
SiPM array
aerogel array
[10]
Silicon PhotoMultiplier (SiPM)

## Slide 10: Time-Of-Flight
Made up of three planes of scintillator:
  Top and bottom planes
  Aperture defining scintillator paddle just under the DCT
  SiPMs per end of paddle to measure light
2.3 m separation of top + bottom
  High-precision (timing) up to 1 GeV/n, turn-on of the RICH
Light amplitude → measurement
Total acceptance ~ 0.1 m2 sr
HELIX Instrument
  Measures the velocity, , and charge,
Bottom TOF installed on payload
1.6m

## Slide 11: Expected HELIX performance
Targeting 2.5% mass resolution
HELIX will resolve Be isotopes:
  Stage 1: Up to E ~ 4 GeV/n [blue]
  Stage 2: Extends to 10 GeV/n [green]
Chemical and isotopic composition of several light nuclei
Conclusions
HELIX will significantly improve our understanding of GCR propagation
AMS data preliminary

## Slide 12: Conclusions
HELIX will resolve Beryllium isotopes in the first stage up to 4 GeV/n with mass resolution 3%
Production of flight components complete
Thermal vacuum test of payload successful
Working for Long Duration Balloon flight opportunity
NASA Grant 80NSSC18K0232
Isotope measurements significantly improve our understanding of GCR propagation

## Slide 13: HELIX Collaboration
Introduction

## Slide 14: Citations
[1] https://svs.gsfc.nasa.gov/11342
[2] http://www.issibern.ch/cargese2013/images/d/d6/PTUSKIN_Cargese2013.pdf
[3] Korschinek et. Al. (2010) NIM B Vol 268, 2: https://doi.org/10.1016/j.nimb.2009.09.020
[4] R. Trotta et al 2011 ApJ 729 106 https://doi.org/10.1088/0004-637x/729/2/106
[5] Maurin, D., Melot, F., and Taillet, R., \A database of charged cosmic rays,“ A&A, vol. 569, p. A32, 2014. [Online]. Available: https://doi.org/10.1051/0004-6361/201321344
[6] Park ICRC 2021 Berlin https://pos.sissa.it/395/091
[7] Nutter, S, et al. Detection of Cosmic-Ray Antiprotons with the HEAT-Pbar Instrument. Aug. 2001.
[8] Tabata et al. NIM A, 952 2020
[9] O’Brien ICRC 2021 Berlin https://pos.sissa.it/395/090
[10] Wisher ICRC 2019 Madison https://pos.sissa.it/395/090

## Slide 15: Extra Stuff

## Slide 16: Isotopes Offer Insights
Secondary-primary ratios are sensitive to the material pathlength
HELIX Science
Fig from [3]
Fig from [4]
    Need to measure unstable (clock) isotopes like 10Be at higher energies
Degeneracy of diffusion coeff and halo size in models like GALPROP
    B and Be are secondary GCRs - byproducts of primaries (accelerated at sources)
    Galactic Cosmic Rays (GCRs)

## Slide 17: Other systematic Uncertainties
Backup
New cross-section measurements at higher energies are needed
Isotopes produced above the HELIX payload in atmosphere during flight, relevant for interpreting the data as GCR fluxes
Isotope production during propagation in diffusion-halo models (or others) that include nuclear interaction networks, relevant for interpreting data in the context of the models
  See the proceeding by Neeraj Amin for NA61/SHINE from ICRC 2021
  And see the relevant paper by Maurin et. al. (2022) on the arxiv: arxiv:2203.00522

## Slide 18: Mass Resolution with Magnet Spectrometers
Challenge in confidently separating the close peaks of 9Be & 10Be
For beryllium isotopes, a good benchmark is 2.5% mass resolution
Resolve 10Be, shown in histogram
HELIX Science
HELIX is designed to meet this resolution goal
Z=4

## Slide 19: Tracker images
Backup

## Slide 20: RICH Focal Plane
Focal plane of SiPMs
1 m2 area – half-filled in Stage 1
  200 SiPM arrays – 12,800 SiPMs
  Fully populated, 400 SiPM arrays in Stage 2
HELIX Instrument
  Measures the velocity,
SiPM array
Stage 1 populated Focal Plane
resolution 0.1% ( >= 4)

## Slide 21: Aerogel measurements
Beam line scanned
  TRIUMF – electrons
  Using CCD to image Cherenkov ring
36 aerogel tiles
See O’Brien ICRC 2021 proceeding for more details
Backup
Aerogel
[5]

## Slide 22: Time-Of-Flight Readout
Measuring at both ends yields hit position along paddle
  Complements the DCT bending plane
Fast channel - timing between sections for
  TDC timing resolution is better than 25 ps
On track for timing resolution better than 50ps for > 3
Slow channel – amplitude for measurement
Aiming for resolution of 0.1% and resolution of 0.1e (<11)
HELIX Instrument
  Measures the velocity, , and charge,
[3] Park, N. ICRC 2021

## Slide 23: GCR Abundances
Sources accelerate He, C, O, Si and Fe (primary cosmic rays)
Overabundant in some elements
  Li, Be, B and F
  Sc, Mn, sub-iron
Spallation (high energy collisions) of primaries produces lighter elements
Wealth of precise data from AMS-02 on the GCR nuclei
Nuclei => Charge
Isotope => Mass
Li,Be,B
[4]