## Slide 1: MightyPix
Ivan Peric and MightyPix team

## Slide 2: Mighty Tracker
Mighty Tracker
SciFi Tracker
  Scintillating fibres with SiPM readout
Inner Tracker and Middle Tracker
  Silicon sensors meet requirements of radiation hardness and granularity
  Baseline technology: HV-CMOS pixel chip MightyPix
  In total over 46000 silicon sensors to cover area of 18 m2 (minus beam-pipe hole)
Schematic of one layer of the Mighty Tracker. [1]
SciFi
MT
IT
~ 4 m
1 m
Notes: The upgrade of the downstream tracking system is called the Mighty Tracker
The Mighty Tracker is a hybrid approach making use of both scintillating fibres (SciFi) and HV-MAPS technology. This solution balances cost and physics performances
We have high granularity, timing resolution, and radiation hardness.

## Slide 3: MightyPix
HV-CMOS sensor
Sensing element and readout circuit on same chip
n-well/p-substrate diode acts as sensor
Readout electronics isolated from high voltage by deep n-well
High reverse bias creates thick depletion region between deep n-well and p-substrate
Ionising particles create electron/hole pairs, collected via drift
-HV
-HV
p-substrate
1.8 V
Depletion region
Working principle of HV-CMOS sensors.

## Slide 4: MightyPix
MightyPix is based on knowledge from ATLASPix1 and MuPix2
Final design parameters and requirements:
First prototype: MightyPix1
Parameter | Required Value | Notes
Chip size |  | 
Pixel size |  | 
Time resolution |  | Hit assigned to right BX
Power consumption |  | 
NIEL3 |  | Includes safety factor of 2
Cooling |  | Test beam studies
Parameter | Required Value | Notes
Chip size |  | 
Pixel size |  | 
Time resolution |  | Hit assigned to right BX
Power consumption |  | 
NIEL3 |  | Includes safety factor of 2
Cooling |  | Test beam studies
1 HV-CMOS pixel chip for the ATLAS experiment at CERN
2 HV-CMOS pixel chip for the Mu3e experiment at PSI
3Non Ionising Energy Loss
Notes: The sensors have to sustain the expected 1-MeV neutron equivalent fluence of 6x1014neq cm2
A baseline pixel size of 50µm x 150µm is assumed.

## Slide 5: MightyPix1: Overview
Implemented in TSI 180 nm process
Submitted in May 2022
Chip size: ~ 2 cm × 0.5 cm  full column length, ¼ width
Pixel matrix: 29 columns, 320 rows
Pixel:
  165 μm × 55 μm
  CMOS amplifier and CMOS comparator
Data format: 2 × 32 bit words per hit trasmitted
Data output rate: 1.28 Gbit/s going to lpGBT
The first prototype: MightyPix1

## Slide 6: MightyPix1: Overview
Digital interfaces:
  Timing and Fast Control (TFC)
  Slow Control (I2C)
  Configuration shift register (SR) interface
Clock generation:
  External: 40 MHz and 640 MHz coming from lpGBT
  Internal: CML and CMOS PLL with 40 MHz reference clock
Bias voltages:
  Integrated 10 bit voltage DACs
  Can be supplied externally
The first prototype: MightyPix1

## Slide 7: MightyPix1: Analogue Part
Pixel contains:
  Sensor diode
  Charge Sensitive Amplifier (CSA)
  Comparator
  Threshold tune DAC
  RAM for tune bits
Source: Ivan Perić
Amplifier
Sensor
Comparator
Th
BL
TDAC
Injection
EnInjection_row_i
RAM
Q(0:2)
3
RAM in
WrRAM(0:2)_row_i
Cinj
Bias resistance
Tout
Data transfer line
column control(in pixel control reg)
-HV
1.8V
Hit buffer
Pixel
Offset
AnalogOut
row control (in pixel control reg)
VMinus
Injection
AmpOut

## Slide 8: MightyPix1: Analogue Part
Working principle:
1. Charge collected by pixel n-well
2. Converted to voltage signal by Charge Sensitive Amplifier
3. Analog voltage pulse shaped and converted to digital signal by comparator
4. Hit information stored in hit buffer
Source: Ivan Perić
Amplifier
Sensor
Comparator
Th
BL
TDAC
Injection
EnInjection_row_i
RAM
Q(0:2)
3
RAM in
WrRAM(0:2)_row_i
Cinj
Bias resistance
Tout
Data transfer line
column control(in pixel control reg)
-HV
1.8V
Hit buffer
Pixel
Offset
AnalogOut
row control (in pixel control reg)
VMinus
Injection
AmpOut

## Slide 9: MightyPix1: Analogue Part
Working principle:
1. Charge collected by pixel n-well
2. Converted to voltage signal by Charge Sensitive Amplifier
3. Analog voltage pulse shaped and converted to digital signal by comparator
4. Hit information stored in hit buffer
Source: Ivan Perić
Amplifier
Sensor
Comparator
Th
BL
TDAC
Injection
EnInjection_row_i
RAM
Q(0:2)
3
RAM in
WrRAM(0:2)_row_i
Cinj
Bias resistance
Tout
Data transfer line
column control(in pixel control reg)
-HV
1.8V
Hit buffer
Pixel
Offset
AnalogOut
row control (in pixel control reg)
VMinus
Injection
AmpOut

## Slide 10: MightyPix1: Analogue Part
Working principle:
1. Charge collected by pixel n-well
2. Converted to voltage signal by Charge Sensitive Amplifier
3. Analog voltage pulse shaped and converted to digital signal by comparator
4. Hit information stored in hit buffer
Source: Ivan Perić
Amplifier
Sensor
Comparator
Th
BL
TDAC
Injection
EnInjection_row_i
RAM
Q(0:2)
3
RAM in
WrRAM(0:2)_row_i
Cinj
Bias resistance
Tout
Data transfer line
column control(in pixel control reg)
-HV
1.8V
Hit buffer
Pixel
Offset
AnalogOut
row control (in pixel control reg)
VMinus
Injection
AmpOut

## Slide 11: MightyPix1: Analogue Part
Working principle:
1. Charge collected by pixel n-well
2. Converted to voltage signal by Charge Sensitive Amplifier
3. Analog voltage pulse shaped and converted to digital signal by comparator
4. Hit information stored in hit buffer
Source: Ivan Perić
Amplifier
Sensor
Comparator
Th
BL
TDAC
Injection
EnInjection_row_i
RAM
Q(0:2)
3
RAM in
WrRAM(0:2)_row_i
Cinj
Bias resistance
Tout
Data transfer line
column control(in pixel control reg)
-HV
1.8V
Hit buffer
Pixel
Offset
AnalogOut
row control (in pixel control reg)
VMinus
Injection
AmpOut

## Slide 12: MightyPix1
MightyPix1 has been produced – first results soon