## Slide 2: Data analysis activities and needs of XEI section – Experimental Areas
I. Ortega, on behalf of the Experimental Areas team (J. Tan and S. Dechamps)

## Slide 3: Outlook
Current use cases
  UC#1: XBPF event processing
  UC#2: XBPF time-of-flight
  UC#3: Cherenkov Threshold (XCET)
  UC#4: EA instruments in CESAR
  UC#5: Calibration of EA instruments
Future use cases
  UC#6: Real-time monitoring of critical parameters
Solutions developed in the section
Difficulties found
Wishlist

## Slide 4: UC#1: XBPF event processing
Data sources
  Live data from the instrument
Algorithms
  Event reconstruction from data decoding
Performance required
  4.8 seconds (North Area spill)
Where it runs
  FESA server
Results storage
  NXSCALS
Results presentation/notification
  DIP server
Tools used
  C++ (FESA)
Status / criticality
  Operational. Currently investigating larger data buffer (limited to 10^5 particles due to CPU performance)

## Slide 5: UC#2: XBPF Time-of-flight
Data sources
  Live data from the instrument
Algorithms
  Time alignment, histograms, gaussian fit, statistics
Performance required
  4.8 seconds (North Area spill)
Where it runs
  FESA server
Results storage
  NXCALS
Results presentation/notification
  DIP server
Tools used
  C++ (FESA)
Status / criticality
  Operational, but needs urgent maintenance for 2023

## Slide 6: UC#3: Cherenkov Threshold XCET
Data sources
  Live data from the instrument
Algorithms
  Rolling average, peak detection
Performance required
  400ms (East Area spill)
Where it runs
  FESA server
Results storage
  NXCALS
Results presentation/notification
  DIP server
Tools used
  C++ (FESA)
Status / criticality
  Operational.

## Slide 7: UC#4: EA instruments in CESAR
Data sources
  Live data from the instrument
Algorithms
  Histograms, gaussian fit, statistics (max/min, average, std. dev.)
Performance required
  4.8 s (North Area spill)
Where it runs
  CESAR server (CCR server)
Results storage
  NXCALS
Results presentation/notification
  CESAR GUI
Tools used
  Java
Status / criticality
  BE-CSM responsibility. Operational. Being upgraded as part of the North Area consolidation.

## Slide 8: UC#5: Calibration of instruments
Data sources
  Live data from the instrument
Algorithms
  Histograms, gaussian fit, statistics (max/min, average, std. dev…), differentiation, integration
Performance required
  4.8 s (North Area spill)
Where it runs
  Linux virtual machine
Results storage
  Local files
Results presentation/notification
  Python application
Tools used
  Python (PyQt, Tkinter, numpy, mathplotlib…), C++
Status / criticality
  Operational

## Slide 9: UC#6: Real-time monitoring
Data sources
  Live data from the instrument
Algorithms
  Min/max detection, gaussian fit, statistics
Performance required
  400ms (East Area spill)
Results presentation/notification
  Email , web
Status / criticality
  Future use case

## Slide 10: Solutions Developed in the Section
Python apps with Comrad for instrument calibration (one app per instrument)
ROOT apps for XBPF calibration

## Slide 11: Difficulties found
Maintenance: we use acc-py -> problems of compatibility with new version releases. We need to revise the code of our apps (time-consuming)
Performance of XBPF data decoding

## Slide 12: Wishlist
A stable python distribution. If new versions are released, ensure retro-compatibility
An online monitoring tool