## Slide 1: MDI Summary – Detectors integration in the interaction region
Fabrizio Palla - INFN Pisa
On behalf of
M. Boscolo, A. Ciarma, F. Fransesini, S. Lauciani, and L. Pellegrino – INFN Frascati
F. Bosi – INFN Pisa
M. Dams – NBI Copenhagen
Detector Concept Meeting
CERN – 7 November 2022

## Slide 2: The IDEA Concept

## Slide 3: Requirements
Interaction region detectors must be integrated with the beam pipe
  The vertex detector innermost radius should profit of the reduced beam pipe diameter (2 cm) and should cover
  Must not interefere with the Luminosity Calorimeter (clearance of ~120 mrad)
  The mounting of the vertex and the outer tracker must be done inside the support tube
  Minimize the radiation lengths

## Slide 4: LumiCals
Challenge:
- MDI region is very busy, LumiCals pushed far inside detector volume
CLD Si Tracker

## Slide 7: Vertex and Outer Trackers
Inside the same volume of the support tube that holds also the LumiCal
  Vertex detector supported by the beam pipe
  Outer Tracker (1 barrel and 6 disks) fixed to the support tube
Minimal number of detector module variants
  One module type only for the Vertex
  One module type only for the Outer barrel and disks

## Slide 8: Vertex detector modules
Chip 1
Chip 2
32 mm
8.4 mm
Readout
Module concept inspired by ARCADIA INFN R&D
  Pixel size 25x25 µm2
  Active area 640 pixel (16 mm) in z and 256 pixels (6.4 mm) in
  Chip periphery plus an inactive zone: total 2 mm in
  Chips are side-abuttable in z
  Assume total thickness of 50 µm
Composed of 2 pixelated parts: total of 8.4 mm 32 mm (z)
  Power budget not established yet: assume (conservatively)
z 640 pixel
R-phi 256 pixel

## Slide 9: Half-ladder layout – layer 1
z=0
Chip 1
Chip 2
Chip 1
Chip 2
96.5 mm
0.2 mm
Chip 1
Chip 2
8.4 mm
0.1 mm
Layer 1 ladders are placed at 12 mm radius

## Slide 10: Half-ladder layout – layer 2
z=0
Chip 1
Chip 2
Chip 1
Chip 2
160.9 mm
0.2 mm
Chip 1
Chip 2
8.4 mm
Chip 1
Chip 2
Chip 1
Chip 2
8.4 mm
0.1 mm
Layer 2 ladders are placed at 20 mm radius

## Slide 11: Half ladder layout – layer 3
16.3 mm
Layer 3 ladders are placed at 32 mm radius
Overlapping in 2 parallel ladders separated by 500 µm
- see engineering drawings later
Passive parts on the sides
z=0
Chip 1
Chip 2
Chip 1
Chip 2
Chip 1
Chip 2
Chip 1
Chip 2
Chip 1
Chip 2
Chip 1
Chip 2
Chip 1
Chip 2
Chip 1
Chip 2
0.2 mm
0.2 mm
0.2 mm
0.2 mm
z=0
257.5 mm
z=0
Chip 1
Chip 2
Chip 1
Chip 2
Chip 1
Chip 2
Chip 1
Chip 2
Chip 1
Chip 2
Chip 1
Chip 2
Chip 1
Chip 2
Chip 1
Chip 2
0.2 mm
0.2 mm
0.2 mm
0.2 mm

## Slide 12
Layer 1
14 overlapping staves of 6 modules each
Power budget of the modules (only)
~23 W
Hybrids at higher radius (+2 mm wrt sensors), not to interfere with LumiCal clearence
Disclaimer
In this and the following we have made a study of a realistic mechanical geometrical layout, including hybrids and readout bus, but still missing the final module frame mechanical support

## Slide 13: Vertex layer supports
Conical carbon fibre shaped structure, held by the beam pipe (see later)

## Slide 14: Vertex overall assembly
Total weight to be estimated, but far less than 100 grams
Air cooled

## Slide 15
Mounting 2 halves (in ) on the beam pipe cooling manifolds

## Slide 16: Outer layers modules
Based on ATLASPIX3 R&D
  50 x 150 µm
  Up to 1.28 Gb/s downlink
  TSI 180 nm process
  132 columns of 372 pixels
  Active (total) length (r-phi x z)
    18.6 (21) mm x 19.8 (20.2) mm
  Module is made of 2x2 chips – total length:
    size 42.2 mm x 40.6 mm
  Power budget not established yet:
    assume
Power
Data IN/OUT
HV

## Slide 17
Outer Tracker Barrel
48 staves of 32 modules each (at different radii)
Power budget
~2.63 kW
Cooling using water 4 pipes (2 mm diameter) per stave

## Slide 18
Outer Tracker Disk 1
2 sides (front and back) each with 4 petals.
One petal is made of different staves of overlapping modules in z.
Total modules per disk: 196
Power budget ~340 W
Cooling using 1 water pipe (2 mm diameter)

## Slide 19: Typical module stave
Cooling pipes
Lower modules
Upper modules
Front
Carbon fibre spacer
Carbon fibre pacers
Back
Electrical bus

## Slide 20: Support cylinder
All elements in the interaction region (vertex, Tracker and LumiCal) are mounted rigidly on a support cylinder that guarantees mechanical stability and alignment
  Once the structure is assembled it is slided inside the rest of the detector

## Slide 23: Outer barrel and disks
Barrel:
  a truss structure with 2 layers of modules (at radii of 31.5 cm and 28.5 cm)
  Fixed to the support tube
3 disks per side
  Fixed by the support tube

## Slide 24: Overall layout

## Slide 25: Is it feasible?
Mechanical stability of the support cylinder is not an issue

## Slide 28: Is it feasible?
Mechanical stability of the support cylinder is not an issue
Vertex detector weight (<< 100 grams) on the beam pipe is well supported

## Slide 30: Is it feasible?
Mechanical stability of the support cylinder is not an issue
Vertex detector weight (<< 100 grams) on the beam pipe is well supported
Integration of the detectors is doable

## Slide 33: Is it feasible?
Mechanical stability of the support cylinder is not an issue
Vertex detector weight (<< 100 grams) on the beam pipe is well supported
Integration of the detectors is doable
  Open remaining issue to be investigated is whether or not LumiCal can be inserted as unique assembled structure or must be splitted due to 4 mm difference between the bellow and the inner LumiCal radius
    Ongoing design effort to reduce the bellow size

## Slide 34
54 mm
58 mm
Needs tuning of the bellow size.
Study ongoing

## Slide 35: Conclusions
A preliminary layout of the interaction region with LumiCal, vertex and outer tracker of the IDEA detector is being engineered
  Feasibility studies of vertex and track integration successfully made
  LumiCal conceptual integration done
Next steps:
  Vertex detector
    Ladders mechanical support design
    Study the feasibility of air cooling
    Study the routing of the services (readout and power cables)
  Outer Tracker
    Study the routing of the services (readout and power cables, cooling manifolds)
  Lumical
    Engineering and assembly
  Finalize detector assembly and its maintenance
  Insert the layout in the GEANT simulation

## Slide 36
Thank you for the attention
Fabrizio.Palla@cern.ch

## Slide 37: Backup

## Slide 38
Layer 2
22 overlapping staves of 10 modules each
Power budget of the modules (only)
~59 W
Hybrids at higher radius (+2.5 mm wrt sensors), not to interfere with LumiCal clearence

## Slide 39
Layer 3
15 overlapping double staves of 32 modules each
Power budget of the modules (only)
~130 W
Staves staggered by 500 µm wrt to the previous to profit of overlap

## Slide 40
Double stave
2 parallel strings of detectors overlapped by 500 µm

## Slide 41: Stave Layer 1

## Slide 42: Stave Layer 2

## Slide 43: Layer 1

## Slide 44: Layer 2

## Slide 45: Layer 3

## Slide 46: Support Carbon Fiber
Superseeded by the conical shape

## Slide 48: Cold stave

## Slide 49: Stave Outer Tracker
Upper Cold Plate with pixel sensor
Double Pixel Stave
Terminal part to fix to the flange

## Slide 50: Stave Outer Tracker
Lower Cold Plate with pixel sensors
Double Pixel Stave
Terminal part to fix to the flange

## Slide 51: Truss Structure
Plate Truss upper-lower truss structure th=0.5 mm side 1mm
Plate Truss lateral truss structure th=0.5 mm side 1mm
Plate Truss Structure glued together
All Material Carbon Fiber MJ46
C carbon Fiber profile supporting cold plate

## Slide 52: Truss Structure

## Slide 53: Cold Stave
Kapton Tube
Bus Circuit
Pixel Detector
Terminal Part to fix to the Truss structure

## Slide 54: Outer Tracker
N.48 Double Stave

## Slide 55: Inner disk with conceptual mechanical support structure