Muon collider international cooperation

WP7 Muon Collider Magnetic Systems

Task 3 Fast Ramped Accelerator

Mom KickOff 23 November 2022

Participants: Davide Aguglia (CERN), Jerome Beard (LNCMI), Fulvio Boattini (CERN), Luca Bottura (CERN), Marco Breschi (UNIBO), Herbert De Gersem (TUD), Anna Kario (UTWENTE), Herman ten Kate (UTWENTE), Rebecca Miceli (UNIBO), Pier Luigi Ribani (UNIBO)

F.Boattini presented a proposal of the list of subjects that the task3 shall investigate. The subjects can be resumed as below:

1. Power Converters
  1. Design of the two harmonics circuit according to the specifications coming from the optics design and the magnets characteristics; (CERN
    Identification of alternative powering schemes; CERN; LNCMI
  2. Definition of the control problem, i.e. what accuracy level is requested from sector to sector; CERN
2. Resistive magnets (Dipoles and Quadrupoles)
  1. Analyze different types with different combination of electric steel types with the goal to minimize global energy content and losses and maximize the magnetic induction in the gap; UNIBO
  2. Consider the problem of FECO utilization wrs2 activation of Cobalt (preliminary calculations with Fluka are probably required); CERN
  3. Build mathematical model of the magnets, to be used for the calculation of the powering system; TUD
  4. Magnets losses computation / measurement in conditions of high fronts and magnetic saturation (CERN, UNIBO, TUD);
3. Superconducting magnets
  1. Definition of vertical and horizontal apertures. Data must come from optics; CERN
  2. Preliminary 2D magnetic design based on either LHC or FCC dipole design modified according to field/aperture requirements, provided these are not too far from “existing” designs; (CERN, UNIBO)
4. HTS based magnets
  1. Scoping studies for dBdt application in the range of 300T/s and with DB of ±2T; (UTWENTE)

Action points and comments emerged during the discussion

Iron losses computation in fast ramping dipoles (and quadrupoles).
- Decide the best model to use for losses computation and perform a preliminary calculation on the MAP design (TUD).
- Perform qualification measurements on a suited steel setup model, with and without saturation in order to validate / tune the losses model. Which materials, where to test them, under which conditions? (CERN, TUD, UNIBO).

Resistive magnets design
- Identify the space of analysis for the design of the resistive magnet cross section. Set up a DOE (Design of Experiments) table that allows identifying trends. (CERN, UNIBO)
- Example of vars to consider:
  - X section type (H, Windowframe exc..)
  - Steel material and combination of the same
  - Configuration of coils (litz wires, vertical bars of given thickness…)
  - Coil window dimensions?
- Example of KPIs to evaluate:
  - power, stored energy, losses, mass, cost

Optimization for the design of the powering system (magnets + power converters)
- The optimization principle was not explicitly reported in the presentation. Nevertheless this is the approach we would like to follow as soon as the mathematical models of the magnets will be ready. This is not an action but a comment from D.Aguglia.
- With respect to this, we shall define the KPIs to qualify the global designs (power, stored energy, losses, mass, cost). This is an ongoing action from CERN and is getting more specific as the optics and magnet design advances.

Rise awareness among the muon collider community, around a good design value for both NbTi and Nb3Sn superconducting magnets
SC magnets experts highlighted that a design value for both technologies should be considered in the range of 8T for NbTi and 14T for the Nb3Sn. Aiming at the maximum theoretical values (10T and 16T respectively) is considered not reliable.

Continuous discussion with beam physics to define more reliable values for magnets aperture, field quality etc… (CERN)