## Slide 1
Presenter Name
Date
The 7th International Conference on
Micro Pattern Gaseous Detectors 2022
Studying signals in particle detectors with resistive elements such as the 2D resistive-strip bulk Micromegas
Djunes Janssens
djunes.janssens@cern.ch
Supervisors: J. D’Hondt , E. Oliveri, W. Riegler, H. Schindler and R. Veenhof.
December 14th, 2022

## Slide 2: Introduction
  Novel detector structures are proposed regularly, mixing old and new ideas, with detectors containing resistive elements widening the landscape of possible configurations.
  The use of these technologies in experiments makes it necessary to understand and characterize its response for the design and optimization of the next generation of particle detectors and their application.
T. Alexopoulos et al., Nucl. Instrum. Meth. A 640 (2011) 110.
M. Tornago, R. Arcidiacono, N. Cartiglia et al., Nucl. Instrum. Meth. A 1003 (2021).
AC-Coupled LGAD
Resistive-strips micromegas

## Slide 3: Introduction
  We want to use Garfield++ and COMSOL to model the signal formation in detectors with resistive elements by applying an extended form of the Ramo-Shockley theorem.
  Outline:
  Ramo-Shockley theorem extension for conductive media
  Overlook of the numerical approach
  Obstacles to modeling a full size MPGD
  Ongoing benchmarking of the modeling of a resistive-strip bulk Micromegas
  Cross-coupling
  Summary
Garfield++: https://garfieldpp.web.cern.ch/garfieldpp/
COMSOL Multiphysics: https://www.comsol.ch

## Slide 4: Ramo-Shockley theorem
  The Ramo-Shockley theorem allows the current induced by an externally impressed charge density on any electrode to be calculated by the usage of a so-called weighting potential .
Readout strip
Gas gap
Insulator
Weighting potential for only perfect insulators and electrodes with infinite conductivity.
Cathode/Mesh
S. Ramo, PROC. IRE 27, 584 (1939).
W. Shockley, Journal of Applied Physics. 9 (10): 635 (1938).
Vw
This static can be calculated for a grounded electrode by:
Remove the drifting charges
Put the electrode at potential Vw
Grounding all other electrodes

## Slide 5: Ramo-Shockley theorem
  Using this framework, the induced current sourced by a point charge q can be calculated in a single using the calculated the weighting potential of the electrode.
GEM
XY strip readout
e- endpoints
This can be repeated for every charge in the avalanche created in the detector:

## Slide 6: Ramo-Shockley theorem
  This theorem has been used to scan the parameter space to study the changes in charge sharing between the three sets of strips of an XYU read-out.
x
y
u
XYU read-out image
42 %
38 %
20 %
Simulated charge sharing
Measured PH spectrum
Submitted paper to NIM-A is available on the RD51 notes: RD51-NOTE-2022-09
K. Floethner’s conference poster: The novel XYU-GEM for ambiguity reduced tracking

## Slide 7: Ramo-Shockley theorem extension for conducting media
  For detectors with resistive elements, the time dependence of the signals is not solely given by the movement of the charges in the drift medium but also by the time-dependent reaction of the resistive materials.
Readout strip
Gas gap
R layer
Insulator
Weighting potential for a resistive layer separating the gas gap and insulating layer.
Vwϴ(t)
W. Riegler, Nucl. Instrum. Meth. A 535 (2004), 287-293.
W. Riegler, Signals in Particle Detectors, CERN’s Academic Training Lecture Regular Programme (2019): https://indico.cern.ch/event/843083/
Cathode/Mesh
This dynamic can be calculated for a grounded electrode by:
Remove the drifting charges
Put the electrode at potential Vw at time t = 0
Grounding all other electrodes
V

## Slide 8: Overview of the numerical methodology
  These weighting potentials can only be obtained analytically for a small subset of the larger group of existing detectors; thus, a numerical method is used.
  COMSOL® :
  Numerically obtain the dynamic weighting potential.
  Garfield++:
  Detailed microscopic simulation of particle detectors based on ionization measurements in gases or semiconductors.
Garfield++: https://garfieldpp.web.cern.ch/garfieldpp/
COMSOL Multiphysics: https://www.comsol.ch
D. Janssens et al., Nucl. Instrum. Meth. A 1040 (2022)
Resistive planes
Mesh
Pillar
e-
e-
+
+
μ
Cathode
Insulating layer
Via
1-3 mm
6 mm
Pads

## Slide 9: Signal formation in a MicroCAT detector
  The MicroCAT’s two-dimensional interpolating readout structure allows for a reduced number of electronic readout channels without loss of spatial resolution.
  This resistive readout concept has recently enjoyed renewed interest with the development of a DC-Coupled LGAD device: arXiv:2204.07226 [physics.ins-det].
F. Bartol et al. J. Phys. III France, 6 (1996), p. 337
A. Sarvestani et al., Nucl. Instrum. Meth. A 410 (1998) 238–258
H. Wagner et al. Nucl. Instrum. Meth. A 482 (2002) 334–346
Weighting potential map for one readout node

## Slide 10: Some of the detectors containing resistive elements
Spatial resolution study:
MicroCAT’s two-dimensional interpolating readout
μ-Resistive-WELL
Small-pad resistive Micromegas
Resistive-strip bulk Micromegas
AC-Coupled LGAD
Timing resolution study:
Multigap Resistive Plate Chambers (MRPC)
Resistive PICOSEC Micromegas Detector
Diamond3D sensor
AC-Coupled LGAD
We are working on extending the list of resistive detectors geometries that can be modelled. Some of the detector types will be used to benchmark the model.
Preliminary
Electron
Hole
Pion
Bias Column
Readout Column
A comprehensive overview of the PICOSEC effort was given yesterday by A. Utrobicic and M. Lisowska.

## Slide 11: Signal formation in resistive-strip Micromegas
  The resistive-strips present in the geometry of this Micromegas geometry is known for its spreading of the signal over the strips orthogonal to them.
Resistive-strips
Mesh
Pillar
5 mm
128 µm
250 µm
e-
e-
+
+
μ
Cathode
Insulating layer
Ar/CO2
93/7
Read-out strips
T. Alexopoulos, et al., Nucl. Instrum. Meth. A 640 (2011) 110.
M. Byszewski1 and J. Wotschack, JINST 7 C02060 (2011).

## Slide 12: Size of the resistive layer
  Given a parallel-plate type geometry with a grounded resistive layer separated from the pad electrodes by an insulating layer.
d3
Top electrode
ε1
Pads
Resistive layer
wx
d1
ε2
Q
a
b
Q
wx
wy
(x0, y0)
  The induced charge on each pad can be analytically calculated to study the effect of the size of the resistive layer:
  with the infinite number of time constants are given by
Time-dependent part
  This sum is slowly converging for thin large-area detectors, where the number sums that need to be performed scales as
As found in the notes of W. Riegler

## Slide 13: Size of the resistive layer
  The size of the resistive layer does play a role in the evolution of the signal. For the initial part of the induced current for a large-area resistive detector can be approximated by a smaller counterpart.
Q
0.5 mm
a
a

## Slide 14: Size of the resistive layer
  Coordinate mapping in COMSOL allows to represent large area detectors, such as a Resistive-strips micromegas, by pushing back the boundaries.
  This can be validated by comparing the numerical solution (markers) with the analytical result solution (full lines).
COMSOL coordinate mapping: link.
Qe
0.5 mm
5 mm
10 cm
Scaled area

## Slide 15: Signal formation in resistive-strip bulk Micromegas
With this scaling method we can accurately fix the boundary conditions of our numerical model to calculate the weighting potential.
Voltage [V]
Scaled area
Scaled area
y-strip
x-strip
Resistive-strip
Ground of R-strip

## Slide 16: Signal formation in resistive-strip bulk Micromegas
+
Using this we calculate the induced signal caused by an 80 GeV/c muon for four neighboring strips.
The APV-25 ASIC is represented by a unipolar shaper using
with a time constant of 𝜏 = 50 ns and shaping order of n = 1.
APV25 parameters taken from this link
Mesh
5 mm
128 µm
250 µm
e-
+
μ
Insulating layer
Ar/CO2
93/7
1
2
3
4
e-
Resistive-strip
Cathode

## Slide 17: SPS test beam measurements
  During the latest RD51 test beam campaign at the CERN SPS we tested two different kind of resistive-strip bulk Micromegas tracking detectors are used to study the signals read out by the APV25’s.
μ
100 kΩ/❑
1 MΩ/❑
Here the trigger comes from the coincidence of 3 scintillators.

## Slide 18: SPS test beam measurements
100 kΩ/❑ resistive-strips
1 MΩ/❑ resistive-strips
The lower resistivity spreads the signal over more strips resulting in a lower amplitude in each.
Preliminary
Preliminary
Preliminary
Preliminary

## Slide 19: Benchmark of the modelling effort
Preliminary
Measurement
100 kΩ/❑ resistive-strips
1 MΩ/❑ resistive-strips
Preliminary
Measurement
The model still needs some work. There are discrepancies in the signal shapes compared to experiment.
Preliminary Simulation
Preliminary Simulation

## Slide 20: Outlook: coupling between the electrodes
To take external impedances and capacitive coupling into account, one calculates the currents and puts them into an equivalent circuit of the detector as ideal currents, adding the external circuit (LTSpice).
Electrode 1
Resistive layer
e-
R1
R2
Vwϴ(t)
Electrode 2
Alternatively, we can view the external impedance elements as a part of the detector medium and absorb them into the weighting potential (COMSOL).
Gatti E., Padovini G., Radeka V., Nucl. Instrum. Methods, 193 (1982), pp. 651-653
COMSOL’s electrical circuit interface: link

## Slide 21: Summary
  We want to use Garfield++ and COMSOL to model the signal formation in detectors with resistive elements by applying an extended form of the Ramo-Shockley theorem.
  We discussed the use of the extended form of the Ramo-Shockley theorem for the calculation of induced signals in resistive particle detectors.
  Techniques such as coordinate scaling are used to accurately represent the total size of the geometry and its boundary conditions
  This was applied to the resistive-strip bulk Micromegas to compare the simulated signal shapes with the measured ones during the latest RD51 test beam campaign at the CERN SPS. This comparison still needs to be better understood and worked out
  Outlook:
  Improving model such as the implementation of the external impedances to include coupling between electrodes
  Looking how to improve the spatial resolution of lower resistive detectors using the signal shape
  Thank you for your attention!

## Slide 22: Backup slides

## Slide 23: Outlook: coupling between the electrodes
To take external impedances and capacitive coupling into account, one calculates the currents and puts them into an equivalent circuit as ideal currents.
For this, the impedance between each electrode ought to be determined, which in general, can not be reduced to a circuit built of a series of resistors and capacitors.
Impedance matrix
W. Riegler, Signals in Particle Detectors, CERN’s Academic Training Lecture Regular Programme (2019): https://indico.cern.ch/event/843083/
Weighting potential

## Slide 24: Outlook: coupling between the electrodes
An RPC type geometry is one of the few resistive geometries that can be represented by a discrete electrical circuit. We can calculate the cross-coupling when attaching external impedances.
R2
Electrode 1
Resistive layer
Electrode 2
e-
R1
d2
d1
εr , σ

## Slide 25: Outlook: coupling between the electrodes
Alternatively, we can view the external impedance elements as a part of the detector medium and absorb them into the weighting potential.
Electrode 1
Resistive layer
e-
R1
R2
Vwϴ(t)
Electrode 2
This will show up as a time-dependent contribution on top of the one already provided from the resistive layer.
Gatti E., Padovini G., Radeka V., Nucl. Instrum. Methods, 193 (1982), pp. 651-653
COMSOL’s electrical circuit interface: link

## Slide 26: Ramo-Shockley theorem extension for conducting media
where .
  The time-dependent weighting potential is comprised of a static prompt and a dynamic delayed component:
Examples of systems of which the weighting potential is analytically obtainable see W. Riegler, JINST 11 (2016) no.11, P11002.
Further reading: W. Riegler, P. Windischhofer, Nucl. Instrum. Meth. A 980 (2020)
=
R = 1 kΩ/❑
R = 10 kΩ/❑
R = 100 Ω/❑
Charge has reached the cathode at t = T
250 μm
10 μm
400 μm
Direct induction
Reaction from resistive material
The current induced by a point particle q is given by:
R = 1 kΩ/❑
R = 10 kΩ/❑
R = 100 Ω/❑

## Slide 27: Overview of the numerical methodology
  COMSOL is a finite element solver capable of solving the electrodynamics field equations using the Electric Currents module and time solver.
  The ramping time of the step function for the Vw pulse is taken is taken smaller than the reaction time of the resistive material.
Time [s]
Vw pulse [V]
Resistive Stips
Mesh
Insulator
y-Strips
x-Strips
Resistive-strips micromegas

## Slide 28: Size of the resistive layer
  The size of the resistive layer does play a role in the evolution of the signal. For the initial part of the induced current for a large-area resistive detector can be approximated by a smaller counterpart.
Q
0.5 mm
a
a

## Slide 29: Diamond 3D Pixel Detector
A 3D geometry with thin columnar resistive electrodes orthogonal to the diamond surface, is expected to provide significantly better time resolution with respect to the extensively studied planar diamond sensors.
With the team of the INFN TimeSpot project, we are exploring the modelling of signal induction on the readout columns.
Weighting potential of a readout column at z = 250 μm.
Preliminary
Electron
Hole
Pion
Bias Column
Readout Column
Drift lines as modelled by Garfield++
Anderlini L. et al., Frontiers in Physics 8 (2020)
For timing measurements and first modelling results see talk by M. Veltri:
“A 4D diamond detector for HL-LHC and beyond”.
x
y
v

## Slide 30: Signal formation in AC-Coupled LGAD
In collaboration with INFN Torino group of N. Cartiglia, we are currently looking at simulating the currents induced in the AC-Coupled Low Gain Avalanche Diode (LGAD) geometry.
When successfully benchmarked, it can be used to understand and explore novel readout designs.
M. Tornago, R. Arcidiacono, N. Cartiglia et al., Nucl. Instrum. Meth. A 1003 (2021).
See N. Cartiglia’s Friday VCI talk: “4d-tracking, LGADs, and fast timing detectors”.

## Slide 31: Signal formation in AC-Coupled LGAD
y-axis [mm]
x-axis [mm]
100 μm
100 μm
200 μm
The role that the prompt component plays can be understood by looking at the central pad on the bottom row.
Prompt weighting potential:
Full weighting potential:
Delayed component
Total signal
AC Pad
Resistive n+
Coupling dielectric
p-Si

## Slide 32: Simulation partition overview
Cathode
APV-25

## Slide 33: Non-uniform resistivity
Non-uniformity map of the readout cell

## Slide 35: MRPC simulation using grid based avalanche method