## Slide 1
Neutron and beta imaging with Micromegas detectors with optical readout
MPGD 2022 – 15/12/2022
A. Cools, E. Ferrer-Ribas, T. Papaevangelou, E. C. Pollacco, T. Benoit, D. Desforge
(Université Paris-Saclay, CEA, IRFU)
F.M. Brunbauer, L. Ropelewski, E. Oliveri (CERN)
F. Beau, L. Devel, C. Malgorn (Université Paris-Saclay, CEA, Institut Joliot)
F.J. Iguaz-Gutierrez (Soleil Synchrotron)
A. Sari (Université Paris-Saclay, CEA, List)
1

## Slide 2
CONTEXT
Light production mechanisms
Light detection devices
DETECTOR CHARACTERIZATION WITH X-RAY SOURCES
APPLICATIONS
B-imaging
Preliminary results with tritium samples
Neutron radiography
Preliminary results with a neutron source
CONCLUSION and PERSPECTIVES
2

## Slide 3
CONTEXT
Advantages:
2D pixelized readout of high granularity
Megapixel resolution from commercial cameras
Integrated imaging approach
Applications:
Real-time neutron imager
β imager for sub-becquerel activity measurements
3

## Slide 4
Scintillation
f Fluorescence
Prompt emission of photon after absorption of incident radiation.
(1 ns to 1 µs)
Primary scintillation
Coming from the excitation of the gas due to incident particles.
Secondary scintillation
Coming from avalanche amplification.
LIGHT PRODUCTION MECHANISMS
Gas mixture : Ar/CF4
4

## Slide 5
LIGHT DETECTION DEVICES
Hamamatsu CMOS camera
Readout noise
Photon number resolving
Dark current
Cooling Sensor temperature Dark current
Air - 20 °C 0.016 e- /pixels/s
Pixels
Number Size
4096 x 2304 4.6 µm x 4.6 µm
Minimum exposure time
Mode Rate
Standard 1 µs/frame
Ultra quiet 100 ms/frame
5

## Slide 6
LIGHT DETECTION
6

## Slide 7
DETECTOR CHARACTERIZATION WITH X-RAY SOURCES
7

## Slide 8
DETECTOR CHARACTERIZATION WITH X-RAYS
ORCA - Quest qCMOS
Lens 25 mm
Cover PLA
Glass Micromegas
55Fe
Experimental set-up for x-rays
Bulk on glass from CERN and IRFU
Charge readout test in Argon+5%Iso:
  gain above 104 and FWHM reaches 16%
Glass Micromegas
S. Aune, T. Benoit, M. Kebbiri
Coated glass with 150 nm of ITO (Indium Thin Oxide)
Pillars with hexagonal pattern and large pitch (6 mm)
Charge readout spectrum in Ar/Iso 5%
8

## Slide 9
DETECTOR CHARACTERIZATION WITH X-RAYS (CERN GDD)
X-ray radiography (20 kV) – Ar/CF4(20%)
High gain: 1 min exposure time gives images with good contrast
60 sec full detector image with simple background suppression.
60 sec exposure time bat radiography with simple background suppression and beam profile correction.
9

## Slide 10
SOLEIL BEAM TEST (16/11-18/11)
Goals
Determination of Point Spread Function
Spatial resolution dependence on drift gap, drift field
and beam energy
Detector homogeneity
1x1mm beam, Primary Scintillation
(Va=0 V, Vd=0 V)
1x1mm beam, Amplification
(Va=400 V, Vd=210 V)
0.035x0.035mm beam, Amplification
(Va=400 V, Vd=210 V)
PRELIMINARY
10
Synchrotron Soleil (4 keV – 15 keV)

## Slide 11
Va=450 V, Vd=100 V
35 x 35 µm2 beam, 6keV, Drift gap = 3 mm
PRELIMINARY
11

## Slide 12
B-imaging
Preliminary results with tritium samples
Neutron radiography
Preliminary results with a neutron source
12

## Slide 13
Β-IMAGING
Tumor heterogeneity: different cell types inside a tumor
  Heterogeneity effect on drug targeting?
  Will help the developing of more efficient drugs
  Requires better detection sensibilities
Pharmaceutical needs at the cell level for drug development:
  Assess the drug distribution among cells
  Evaluate the impact of the cell heterogeneity on drug biodistribution
  At the cell level: Quantification of 3H concentration in single cell samples
13
Molecule labelling and tracking with tritium

## Slide 14
PRELIMINARY RESULTS WITH TRITIUM SAMPLES
First deposit : tritiated glucose
Activity measurement limits and dynamic range → Activities: 0.3 Bq and 60 Bq
Spatial resolution → gap between drops: 2 cm – 1 cm – 5 mm
Tritium deposits schema and picture
β
Cathode
Mesh
ITO
Glass
Light cover
Camera
VIS light
e-
OPTIMED-BETA set-up scheme
14

## Slide 15
PRELIMINARY RESULTS WITH TRITIUM SAMPLES
60 Bq drops positions are well assessed
0.3 Bq drops hardly visible
180 frames of 10 sec (30 min) added with simple background suppression 20% of CF4
Integration method :
Light intensity profile
Ar/CF4(20%)
15

## Slide 16
PRELIMINARY RESULTS WITH TRITIUM SAMPLES
Both 60 Bq and 0.3 Bq drops positions are well assessed
Better signal-to-noise ratio and counting events capability
20000 frames of 100 msec (33 min), individual pixel background thresholding, 20% of CF4
Clustering method :
16

## Slide 17
PRELIMINARY RESULTS WITH TRITIUM SAMPLES
Both 60 Bq and 0.3 Bq drops positions are well assessed
Better signal-to-noise ratio and counting events capability
20000 frames of 100 msec (33 min), individual pixel background thresholding, 20% of CF4
Clustering method :
Clusters barycenter histogram
17

## Slide 18
NEUTRON RADIOGRAPHY
Acquisition modes:
  Event-by-event: track reconstruction:
  potentially higher resolution (100 µm), better ɣ-to-n suppression
  Integrated: real-time radiography:
  ɣ-to-n suppression less efficient
Micromegas-based neutron imager
10B4C neutron-to-charge converter
  Thermal neutrons absorbed by 2 µm thin 10B4C layer
  Conversion efficiency: 5%
  (α or Li) fragments causes strong ionisation compared to electrons
  Drawback: fragments long range in the gas (5 mm)
Boron converter principle
18

## Slide 19
PRELIMINARY RESULTS WITH A NEUTRON SOURCE
Cathode
Mesh
ITO
Glass
Light cover
Camera
VIS light
e-
Experimental set-up
OMNIS set-up schema
B4C
Neutron source
Slow neutron
α & 7Li
10 mm
19

## Slide 20
PRELIMINARY RESULTS WITH A NEUTRON SOURCE (CERN GDD)
Drift field affects the diffusion in the gas
Transverse diffusion in 80% Argon + 20% CF4 gas mixture.
Diffusion spreads the light
50 V/cm drift field
800 V/cm drift field
2000 V/cm drift field
50 V/cm
800 V/cm
2000 V/cm
PRELIMINARY
20

## Slide 21
CONCLUSION
What we have done
Several types of Micromegas on glass were built and tested
Setups of optical readout detectors for neutron and beta detection
Detector characterization at X-ray facilities, with beta samples and neutron sources
Image processing in progress
Outlook
Beam test at Soleil accelerator: spatial resolution measurement and determination of point spread function
Investigate image treatment methods
β-imaging: tests on isolated single tumor cells
Neutron radiography: Irradiation at neutron facilities
21

## Slide 22
THANK YOU
22

## Slide 23
BACK UP
23

## Slide 24
PRELIMINARY RESULTS WITH TRITIUM SAMPLES
 | Mean activity (Bq) | Mean STD (Bq)
High activity | 8,4 | 0,74
Low activity | 0,087 | 0,022
Clustering method :
Charge readout coupling
Optical readout
24

## Slide 25: Light production mechanisms
Light yield : amount of light determines the signal to noise ratio. It depends on electric field, pressure and gas mixture.
Scintillation : excited atoms or molecules emit photons during de-excitation.
Scintillation
f Fluorescence
Prompt emission of photon after absorption of incident radiation.
(1 ns to 1 µs)
Phosphorescence
: Delayed emission of photons after absorption.
(1 ms to 100 s)
Primary scintillation
From the creation of primary electron coming from the excitation of gaz due to incident particles.
Secondary scintillation
From the creation of secondary electrons taking place during avalanche amplification.
Electroluminescence
Electrons with energy lower than ionization threshold just excite atoms or molecules.
25
Notes: 25

## Slide 26
PRELIMINARY RESULTS WITH TRITIUM SAMPLES
β particle range in Ar-Isobutane gas mixture
26

## Slide 27
DETECTOR CHARACTERIZATION WITH X-RAYS
X-ray radiography
MTF measurement
60 sec exposure time lead target radiography with simple background suppression.
27

## Slide 28
SOLEIL BEAM TEST (16/11-18/11)
Va=550 V, Vd=210 V
28

## Slide 29
SOLEIL BEAM TEST (16/11-18/11)
Va=550 V, Vd=210 V
29

## Slide 30
30

## Slide 31
31

## Slide 32
32