## Slide 1
What we do in the SHADOWS
ECAL Edition
Sebastian Ritter EURIZON Detector School – 27.7.2023
sebastian.ritter@uni-mainz.de

## Slide 2: WHAT is SHADOWS?
Proposed off-axis experiment on the NA62/HIKE beam line at CERN ECN3
Search for feebly interacting particles (FIPs)
Time scale:
  Decision on approval expected in December
  Ready for construction in LS3
ECAL:
  Measure ALP -> decays
  Reconstruct mass
400 GeV proton beam
SHADOWS
NA62/HIKE
beam
dump

## Slide 3: ECAL CONCEPT AND SIMULATION
General:
  Sandwich ECAL with iron absorbers and plastic scintillator layers
  35 layers, 20 total, 2.5 x 2.5 m² cross section
Tile ECAL study:
  Different tile sizes tested for a tile-on-SiPM
  For required pointing resolution 1 x 1 cm² tiles needed, 2.2M channels
Strip ECAL study
  Tiles joined into 250 x 1 x 1 cm³ scintillator strips
  Double sided WLS-on-SiPM readout, 18k channels
  Energy and angular resolution basically the same
ECAL layers
shower

## Slide 4: ECAL CONCEPT AND SIMULATION
General:
  Sandwich ECAL with iron absorbers and plastic scintillator layers
  35 layers, 20 total, 2.5 x 2.5 m² cross section
Tile ECAL study:
  Different tile sizes tested for a tile-on-SiPM
  For required pointing resolution 1 x 1 cm² tiles needed, 2.2M channels
Strip ECAL study
  Tiles joined into 250 x 1 x 1 cm³ scintillator strips
  Double sided WLS-on-SiPM readout, 18k channels
  Energy and angular resolution basically the same
reco vertex error in z
  mean: -272 mm
  sigma: 1786 mm

## Slide 5: So what?
Baseline design for scintillator strip based ECAL
  Energy and pointing resolution requirements fulfilled
  ALP mass reconstruction capabilities achieved
  Estimated cost below 1M €
Proposal for CERN ECN3 upgrade in cooperation with HIKE will be handed in in 3 weeks
Best case I will spend the rest of my PhD designing and building the proposed ECAL
relative error on reco mass

## Slide 6
Highly recommended!