## Slide 1: "A Multi-ion Clock with In+/Yb+ Coulomb Crystals"
T. E. Mehlstäubler
16.10.2023 – Kingscliff 2023
Physikalisch-Technische Bundesanstalt, Bundesallee 100, 38116 Braunschweig
Leibniz Universität Hannover, Welfengarten 1, 30167 Hannover

## Slide 2
International Joint Laboratory for
Trapped-Ion Integrated Atomic-Photonic Circuits
Int. Collaborations:
NICT Toyko (J)
University of Osaka (J)
CMI (Prag, Cz)
NPL (London, UK)
W. Zurek (Los Alamos NL) R. Nigmatullin (Uni Sydney, Au)
Haggai Landa (IBM, IL)
…
Visiting scientists:
S. Ignatovich (ILP, Novosibirsk)
N. Ohtsubo (NICT, Tokyo)
M. Kitao (Osaka University)
M. Doležal (CMI, Prag)
L. Ye (JPL/CALTECH)
…
Industry Partners:
Grintech (Jena)
Naneo (Lindau)
D&G (Stuttgart)
Toptica (München)
Vacom (Jena)
Infineon (Munich)
…
The Team “Quantum Clocks and Complex Systems”
exchange with
Osaka and Tokyo

## Slide 3
“Quantum Clocks and Complex Systems”
115In+ Multi-Ion Clock
Dynamics of Coulomb-Crystals
Integrated Ion Traps
1.
2.
3.
QTZ User Facility
„Ion Traps“
4.
Precision Spectroscopy in 172Yb+ Ions
5.
Topological Defects & Transport
Integrated & Scalable Traps
Nanophotonics
Quantum Information
In+ /Yb+ crystals – optical clock
Test of Local Lorentz Invariance &
Isotope Shifts/search for new bosons

## Slide 4
Why Multi-Ion Clocks?

## Slide 5
Test of Fundamental Physics
Relativistic Geodesy
https://space-geodesy.nasa.gov/techniques/VLBI.html
Timing & Navigation, autonomous driving…
GNSS
Applications of Clocks

## Slide 6
Mehlstäubler et al., „Atomic Clocks for Geodesy“, Rep. Prog. Phys. 81, 6 (2018)
Short-range 1/r²
local variations
Long-range 1/r :
height changes
Review article:
Example: impact of groundwater body on gravity acceleration dg and gravitational potential dN
Resolution of FG5 gravimeter: 10 nm/s² ≈ 10-9 g
Clocks as Quantum Sensors for Geodesy

## Slide 7
Gruber et al 2011
(GOCEplus study)
Differences European leveling network (EUVN-DA) vs. Heights from GPS + GOCE geoid
Clocks can serve
as height references !
 10-18 resolution needed !
Height inconsistencies (satellite to leveling data)
Gravity satellite data  ca. > 100 km spatial resolution
Tide gauge in Amsterdam
Tide gauge in Marseilles
Bjerhammar, Boll. di Geodesia e Scienze Affini 185 (1975) Vermeer, Rep. Finnish Geodetic Inst., 83 (1983)

## Slide 8
2021 Bloomberg TV "Atomic Clocks are Reinventing Time“ > 820 000 views
Featuring Don Lincoln (Fermi Lab),
David Hume (NIST) and
Tanja Mehlstäubler (PTB/LUH).
On Bloomberg TV and YouTube:
https://www.youtube.com/watch? v=hzLTgtFaPLY
Time Dilation

## Slide 9
3D-Paul trap
single Yb+-ion
nsec
s0 ~10 nm
Trap Depth ~ 104 K
r
E(r) = 0
deep traps → long trapping times for single ion (up to months)
ions are trapped at E = 0 → no systematic shifts to 1st order
strong trapping potentials → strong localization (≈ nm): 1st oder Doppler free, if
high level control of internal & external degrees of freedom
physics package can be very compact and robust
Accuracy of Single Ion Clocks  for 10-19 clocks
ponderomotive potential
Dn/n = - Ekin/mc2 = - v²/2c²
2nd oder Doppler
Notes: 9

## Slide 10
Mathieu equation
(writing t = W t/2)
Ion motion in trap
Quadrupole Potential
(Micro)motion in RF ion traps
micromotion
(rf driven motion)
secular frequency (laser cool)
Wuerker and Langmuir, 1959
 Aluminum powder
Notes: 10

## Slide 11
Trap Depth ~ 104 K
Nobel Prize 2012: “for groundbreaking experimental methods, that allow to manipulate and measure single quantum systems.”
3D-Paul trap
single Yb+-ion
nsec
s ~10 nm
r
E(r) = 0
Trapped Ions
Notes: 11

## Slide 12
Current stability of optical
ion clocks
1 day
10s - 100 days !
3x10-15 @1s
Ion clocks: stability limited by quantum projection noise; high duty cycle
?
Number of atoms
Frequency
Resolved linewidth (laser, atom)
mit
How well can we resolve the atomic frequency?
Instability: statistical error
Allan Deviation

## Slide 13
1 day
3x10-15 @1s
Instability: statistical error
Allan Deviation
Clock laser requirements relaxed
with multiple atomic absorbers
Keller et al., Appl. Phys. B (2014) „Simple vibration insensitive cavity for laser stabilization at the 10-16 level”
10s - 100 days !
For compact devices:

## Slide 14
Multi-Ion Approach

## Slide 15
Multi-Ion Clocks ?
needed: „experimental methods, that allow to manipulate and measure many-body quantum systems.”
single Yb+ ion
Coulomb crystal of 37 Yb+ ions
Quantum Metrology ↔ Quantum Simulation & Information
37 days averaging
1 day averaging
Herschbach et al., Appl. Phys. B 107, 891 (2012)
Averaging time
Lower instability with Nions
Less stringent requirements for clock laser
Basis for entangled clocks  1/N scaling
Basis for multi-ensemble clocks 1/t scaling
Notes: 15

## Slide 16
single Yb+-ion
Linear array of Coulomb crystals
our approach: bottom up, scalable ion traps
Scaling up the number of ions for metrology
Laser 1
Laser 2
t1
t2
Rosenband and Leibrandt, arXiv:1303.6357 (2013), Borregaard and Sorensen, PRL 111, 090802 (2013), Kessler et al., PRL 112 (2014), Lebedev et al., PRA 89 (2014)
Basis for multi-ensemble clocks and new interrogation protocols in one system
 Cascaded clock operation
Notes: 16
Already classically it would be a major breakthrough +
also Platform for novel protocols

## Slide 17
In+: Herschbach et al., Appl. Phys. B 107, 891 (2012)
Lu+: Arnold et al., PRA 92, 032108 (2015)
Ca+: Aharon et al., NJP 21, 083040 (2019)
Al+: Cui et al., PRL 129, 193603 (2022)
Sn2+: Leibrandt et al., arXiv:2205.15484 (2022)
Sr+: Steinel et al., arXiv:2212.08687 (2022)
Multi-Ion Clocks
Notes: 17

## Slide 18
on-axis micromotion (distorted ERF-fields)  FEM based design & tolerances
heating of ion motion  low noise on-board filters
warming of trap (URF ≈1 kV, IRF ≈1 A)  heat management
magnetic fields & gradients  non-magnetic materials
quadrupole shifts  averaging, zeroing, J ≤ ½ states
control of a complex many-body system  automated particle detection, computer controlled problem recognition, sorting & reloading
 high motional control (phonons)
+
+
+
+
+
+
+
+
+
+
Challenges
Solution:
Challenges:
Notes: Not only filter boards but also PT100s on board 

## Slide 19
on-axis micromotion (distorted ERF-fields)  FEM based design & tolerances
heating of ion motion  low noise on-board filters
warming of trap (URF ≈1 kV, IRF ≈1 A)  heat management
magnetic fields & gradients  non-magnetic materials
quadrupole shifts  averaging, zeroing, J ≤ ½ states
control of a complex many-body system  automated particle detection, computer controlled problem recognition, sorting & reloading
 high motional control (phonons)
+
+
+
+
+
+
+
+
+
+
Challenges
Solution:
Challenges:
axial micromotion
trap related
Notes: Not only filter boards but also PT100s on board 

## Slide 20
on-axis micromotion (distorted ERF-fields)  FEM based design & tolerances
heating of ion motion  low noise on-board filters
warming of trap (URF ≈1 kV, IRF ≈1 A)  heat management
magnetic fields & gradients  non-magnetic materials
quadrupole shifts  averaging, zeroing, J ≤ ½ states
control of a complex many-body system  automated particle detection, computer controlled problem recognition, sorting & reloading
 high motional control (phonons)
+
+
+
+
+
+
+
+
+
+
Challenges
Solution:
Challenges:
Notes: Not only filter boards but also PT100s on board 

## Slide 21
Ion Coulomb Crystals, Epot > Ekin
3D
T < 20 mK
2D
1D
Tcrystal ≈ 1 mK
Non-linear, self-organized system with back-action!

## Slide 22
Kiethe et al., Probing Nanofriction and Aubry-type Signatures in a Finite Self-Organized System, Nat. Communs. (2017)
Kiethe et al., Nanofriction and Motion of Topological Defects in Coulomb Crystals, NJP (2018)
Pyka et al., Topological defect formation and spontaneous symmetry breaking in ion Coulomb crystals, Nat. Commun. 4, 2291 (2013)
Partner et al., NJP (2013), Physica A (2015)
Puebla et al., Fokker-Planck formalism approach to Kibble-Zurek scaling laws and nonequilibrium dynamics, PRB (2017)
Kiethe et al., Finite-temperature spectrum at the symmetry-breaking linear to zigzag transition, PRB (2021)
Timm et al., Energy localization in an atomic chain with a topological soliton, Phys. Rev. Research (2020)
Timm et al., Quantum nanofriction in trapped ion chains with a topological defect, Phys. Rev. Research (2021)
Timm et al., Heat transport in a Coulomb ion crystal with a topological defect, arXiv:2306.05845 (2023)
Localized Defect
Extended Defect
Dynamics of a Complex, Self-Organized System with Back-Action
Creation of Topological Defects – 2nd order Phase Transitions
Build your own solid-state system…
Energy transport and Quantum Friction

## Slide 23
Example: photos of first 3 collective modes of linear crystal
Coupled Many-Body System:
Notes: Dissipation auf starkem Übergang
Kohärente Manipulation auf schmalen Übergang

## Slide 24
Motional heating of spatially extended ion crystals
Kalincev et al., „Motional heating of spatially extended ion crystals“, Quantum Sci. Technol. 6, 034003 (2021)
Heating of ion out of
quantum mechanical
ground state
..causes time dilation
Higher-order phonon heating is suppressed!
Notes: Not only filter boards but also PT100s on board 

## Slide 25
BUT: Micromotion gradients couple noise into secular motion
Kalincev et al., „Motional heating of spatially extended ion crystals“, Quantum Sci. Technol. 6, 034003 (2021)
Notes: Not only filter boards but also PT100s on board 

## Slide 26
In spatially extended crystals field gradients determine heating of individual phonon modes!
Kalincev et al., „Motional heating of spatially extended ion crystals“, Quantum Sci. Technol. 6, 034003 (2021)
Notes: Not only filter boards but also PT100s on board 

## Slide 27
Motional heating of spatially extended ion crystals
individual time dilation per ion.
e.g. 22-ion crystal (3D):
Dn TD /n0 = -7.2 x 10-19 /s
for worse case ion
 Cannot be compensated by magic rf drive
1D
3D
Notes: Not only filter boards but also PT100s on board 

## Slide 28
+
+
Problem: asymmetry in electron shell !
Quadrupole moment q
let‘s ions interact with
electric field gradients.
Find candidates with low q
Atomic Candidates: Electric Quadrupole Moment
Beloy et al., Phys. Rev. A 95, 043405 (2017), Huntemann et al., PRL 108, 090801 (2012)
 | Al+ | In+ | Yb+ (F-state)
Q(eaB2) | -0.17 x 10-5 | -1.59 x 10-5 | -4.1 x 10-2
Dn/n0 max shift for 10 ions with naxial=82 kHz | -0.0005 x 10-18 | -0.02 x 10-18 | -77 x 10-18

## Slide 29
Electric quadrupole moment of the 2F7/2 state
[1] R. Shaniv, et al., Phys. Rev. Lett. 116, 140801 (2016)
[2] L. S. Dreissen, et al., Nature Commu. 13, 1-6 (2022)
[3] R. Lange, et al., Phys. Rev. Lett. 125, 143201 (2020)
Axial secular frequency
Quadrupole moment
Angle between B-field and trap axis
[1]
Our measurements:
kHz
mrad/s [2]
Can be comparable to Ref. [3] with clock measurements:
( Hz)
Quadrupole shift + potential LV

## Slide 30
Our atomic candidates: In+ (clock) sympathetically cooled with Yb+
1S0, F = 9/2
3P0
3P1
236.5 nm
230.5 nm
159 nm
g = 360 kHz
g = 0.8 Hz
g = 194 MHz
1P1
N. Herschbach et al., Appl. Phys. B 107, 891 (2012)
115In+ …a first „simple“ approach:
[1] Safronova et al., Phys. Rev. Lett. 107, 143006 (2011)
172Yb+
+
115In+
+
Large mass, m = 115 u:
Time dilation: /n = - Ekin/mc2 = - v²/2c² = -10-18 @TDoppler = 0.5 mK
Low blackbody shift[1]: Da0 = 5 x 10-8 Hz/(V/m)²
Dn/n = (1.36 ± 0.1)×10-17 @ T = 300 K
Directly detectable transition to 3P1!
direct cooling: T < 100 µK
Low 2nd order Zeeman shift: 4.1 Hz/mT²
(27Al+: 72 Hz/mT² , 171Yb+: 52 kHz/mT²)

## Slide 31
Our atomic candidates: In+ (clock) sympathetically cooled with Yb+
1S0, F = 9/2
3P0
3P1
236.5 nm
230.5 nm
159 nm
g = 360 kHz
g = 0.8 Hz
g = 194 MHz
1P1
115In+ …heavy ion, potential for 10-19
172Yb+ … heavy ion + 2 clock transitions
t ~ 1.6 years
E3 transition, g ≈ nHz:
467 nm
411 nm
Spatially resolved detection with ROIs on CCD
172Yb+
+
115In+
+

## Slide 32
on-axis micromotion (distorted ERF-fields)  FEM based design & tolerances
heating of ion motion  low noise on-board filters
warming of trap (URF ≈1 kV, IRF ≈1 A)  heat management
magnetic fields & gradients  non-magnetic materials
quadrupole shifts  averaging, zeroing, J ≤ ½ states
control of a complex many-body system  automated particle detection, computer controlled problem recognition, sorting & reloading
 high motional control (phonons)
+
+
+
+
+
+
+
+
+
+
Challenges
Solution:
Challenges:
axial micromotion
trap related
Notes: Not only filter boards but also PT100s on board 

## Slide 33
Ti and Au sputtering
Precision measurement microscope
Industrial grade fs-laser µm precision machining
Fineplacer®, precision < 1 µm
Flip-Chip-Bonding
Thermo-Compression
Ribbon Bonding
Wire Bonding
3D Ion Trap Production at PTB Clean Room
Notes: Not only filter boards but also PT100s on board 

## Slide 34
Herschbach et al., Appl. Phys. B 107, 891 (2012)
Laser structured chips
 High precision
Precision Scalable Chip Ion Traps
Low axial micromotion (optimized by FEM simulations)
3D micromotion compensation + laser access
Separated (protected) loading and spectroscopy segment
Notes: 34
Already classically it would be a major breakthrough +
also Platform for novel protocols

## Slide 35
Tolerance on notches
N. Herschbach et al., Appl. Phys. B (2012)
FEM calculations of RF-potential
Finite length effect on rf field
10-18
10-18
GND
URF
Minimized on-axis rf trap fields

## Slide 36
PT100 temperature sensor
(sT = 30 – 60 mK)
Laser cut and structured, ultra-precise, 3D laser access, UHV proof, non-magnetic, integrated electronic filters, ...
Pyka et al., APB (2014) Dolezal et al., Metrologia (2015), Keller et al., PRA 99 (2019), Nordmann et al., RSI 91 (2020)
Scalable Chip Ion Traps for Metrology
Notes: Not only filter boards but also PT100s on board 

## Slide 37
Ion traps for other groups

## Slide 38
Technology Transfer
1 Patent
2 Patents submitted (in 2023)
„Opticlock“ trap licensed an LaserNanoFab GmbH

## Slide 39
Photonic Integrated Systems for Chip Scale Clocks
©S. Sauer
1000 ions in 2D array

## Slide 40
Characterization of Ion Trap Systematics
2) Low axial excess micromotion across all trapping regions
1) Very low trap warming
 time dilation shifts <10-18
 trap-related BBR shift uncertainty <10-18
3) Low heating rate of <0.5 phonons/s at 1MHz
Nordmann et al., Rev. Sci. Instrum. 99, 11301 (2020)
Dolezal et al., Metrologia, 52, 842-856 (2014);
Brownnutt et al., Rev. Mod. Phys. 87, 1419 (2015)
Kalincev et al., Quantum Sci. Technol. 6, 034003 (2021)
“Probing Time Dilation in Coulomb Crystals in a high-precision Ion Trap”, Keller et al., Phys. Rev. Appl. 11, 011002 (2019)
Notes: In general, the dominant uncertainties in an ion clock are trap related. Especially when going to multipe ions the shifts due to ion motion increase. That‘s why a lot of work went into the trap development.
Here you can see our trap. It is a segmented, linear Paul trap made out of Aluminum nitride. It consists of multiple layers, contains several segments where we can trap several ion crystal at the same time and has built in temperature sensors for BBR shift evaluation. Here you can see a cross-cut through the trap. We have compensation electrodes in the radial direction to have the ions in the rf node. However, the EMM in axial direction is given by the design and precision of the alignment. We have shown that the time dilation shift is below 10^-18 across several 100µm of our trap. Also the trap heating is low leading to trap-
And we also have low heating rates of <0.5 phonon per second which means that we have no significant temperature increases during our clock sequence. This trap is used in the following experimental setup

## Slide 41
Linear crystals of Yb+ ions
Does micromotion really vanish along the crystal? (at nodal line)

## Slide 42
Measuring micromotion in rf traps precisely
Sensitivity: s(Dn/n)D2 < 10-20
Photon-correlation technique
J. Keller et al., J. Appl. Phys. 118, 104501 (2015)
New model for WRF ~ G
Berkeland et al., J. Appl. Phys., 83 (1998)
Relative Amplitude DS/S
Phase of µ-Motion Signal
old
new

## Slide 43
atomic resolution: nm micromotion amplitudes & temporal resolution: ns
Atomically resolved micromotion of individual ions
Time dilation of individual ions due to rf motion:
|Dn/n|D2 < 1 × 10-19 over 300 µm
Keller et al., “Probing Time Dilation in Coulomb Crystals in a high-precision Ion Trap”, Phys. Rev. Appl. (2019)

## Slide 44
Time dilation shift of individual ions due to rf motion:
|Dn/n|D2 < 1 × 10-19 over 300 µm
Crosstalk between ions: |E21/Erf,2|< 10-3
Atomically resolved micromotion of individual ions
“Probing Time Dilation in Coulomb Crystals in a high-precision Ion Trap”, Keller et al., Phys. Rev. Appl. 11, 011002 (2019)

## Slide 45
Effect | Max shift | ) | Max shift | )
Time dilation (thermal) | -2 | 0.4 | -19 | 4
Heating (per second) | -3.1 | 0.2 | -0.6 | 0.02
Time dilation (EMM) | -1.8 | 0.8 | -1.3 | 0.6
AC Stark (thermal MM) | -0.003 |  | -0.03 | 
AC Stark (EMM) | -0.2 | 0.1 | -0.2 | 0.1
El. quadrupole shift | -0.02 | <0.01 | -1.1 | 0.02
BBR at 300 K | -137 | 0.15 | -137 | 0.54
Total | -141.3 | 0.9 | -158.7 | 4.1
Effect |  |  |  | 
Time dilation (thermal) | -2 | 0.4 | -19 | 4
Heating (per second) | -3.1 | 0.2 | -0.6 | 0.02
Time dilation (EMM) | -1.8 | 0.8 | -1.3 | 0.6
AC Stark (thermal MM) | -0.003 |  | -0.03 | 
AC Stark (EMM) | -0.2 | 0.1 | -0.2 | 0.1
El. quadrupole shift | -0.02 | <0.01 | -1.1 | 0.02
BBR at 300 K | -137 | 0.15 | -137 | 0.54
Total | -141.3 | 0.9 | -158.7 | 4.1
Confinement A
Confinement B
Units: 10-19
Keller et al., “Controlling systematic frequency uncertainties at the 10−19 level in linear Coulomb crystals“, PRA 99, 1 (2019)
2019: Measurement based multi-ion uncertainty budget (trap based)
A) Direct cooling
B) Sympathetic cooling
temperature uncertainty
Notes: With our measurements we can derive a projected uncertainty budget for both confinements A and B
All shifts are detailed in this publication
I will just point out that we can see the advantage of the direct cooling on Indium where we expect frequency uncertainties at the level of 1e-19
This budget shows how well our ion traps are performing and that we could use them for multi-ion spectroscopy at the 10-19 level.

## Slide 46
Clock Operation

## Slide 47
Long term reference
Atomic Reference
Laser
f ~ 1000 THz
Local Oscillator
Short term reference
feedback
feedback
Ultrastable Cavity
1 Hz
Oscillator
Frequency Comb
flaser= fatom?
Ingredients for an optical clock
our lab:
sDn/n = 1.1 x 10-16 @ 1 s

## Slide 48
Ultra-stable clock lasers in our lab
Systematic noise contributions: Keller et al., Appl. Phys. B, 116 (2014)
10-16 laser stability demonstrated: Didier et al., Opt. Lett., 44 (2019)
12 cm
30 cm
sf/f = 4 x 10-16 @ 1 s
sf/f = 1.0 x 10-16 @ 1 s

## Slide 49
4 Yb+ and 10 In+
4 Yb+ and 10 In+ sorted
6 Yb+ and 15 In+
6 Yb+ and 16 In+
Multi-ion spectroscopy  spatially resolved bi-chromatic ion detection on same EMCCD camera (230 nm and 370 nm)
Collaboration with Asphericon (Jena)
T. Nordmann et al., Bichromatic UV detection system for atomically-resolved imaging of ions, Rev. Sci. Inst. (2023)

## Slide 50
DC increase, RF lowering and radial field:
172Yb+
115In+
1)
2)
3)
or
Target:
Success per swap: 90 %
To be published: Nordmann et al. (2023)
For optimal sympathetic cooling: Automatized sorting of In+/Yb+ crystals

## Slide 51
Example: photos of first 3 collective modes of linear crystal
Coupled Many-Body System:
Notes: Dissipation auf starkem Übergang
Kohärente Manipulation auf schmalen Übergang

## Slide 52
Clock Evaluation and Measurement Campaigns
Dörscher et al., Metrologia 58 015005 (2021)  ratio Sr - 171Yb+ at level 2.5 x 10-17
July-September 2021: Frequency ratio measurement 115In+ - Sr - 171Yb+ at < 10-16 level
March 2022: international clock comparison campaign: optical clock measurements against Yb and Sr lattice clocks at PTB, INRIM and SYRTE at < 10-17 level
 EMPIR project „ROCIT“
115In+
Sr
171Yb+
Optical clock comparison versus Paris (F) and Torino (IT)
via European Fiber Network

## Slide 53
Summer 2021: First frequency ratio 115In+ - 87Sr - 171Yb+
115In+/172Yb+ clock versus 171Yb+ (E3) single ion clock[3]
Frequency ratio measurement of 115In+ versus 87Sr at NICT in Japan 2020[1]
[1] Ohtsubo et al., Opt. Lett. 45, 5950 (2020)
[2] Dörscher et al., Metrologia 58 015005 (2021)
[3] Huntemann et al., Phys. Rev. Lett. 116, 063001
Yb+
In+
 2 orders of magnitude improvement
115In+/172Yb+ clock versus 87Sr lattice clock[2]
Notes: For comparison, the best so-far published ion clock was measured against a Sr lattice clock achieved an instability of … and averaged down to the low 10^-15. For comparison, I put in a bar at 10^-15.
We also performed a measurement against the PTB Sr lattice clock with 150ms pulse time and because of cooling reasons with 3Yb+ ions and one in+
We reached a two orders of magnitude lower instability compared to the best published clock and averaged down to the low 10^-17/high 10^-18 level. This was confirmed when we were also measuring against the Yb+ single ion clock at PTB

## Slide 54
2022: EMPIR Projekt ROCIT – Evaluation of In+/Yb+ clock
Yb+
Yb+
Yb+
In+
74 % uptime
In+ versus Sr-lattice
3 x 10-18
 2 orders of magnitude improvement
120 ms
pulses
Signal of In+ clock transition at 236 nm

## Slide 55
2022 – Evaluation of In+/Yb+ crystal clock
Systematic Uncertainty
Preliminary, to be published
5.5
8.6

## Slide 56
Fist frequency ratio measurements with multiple ions
2In4Yb
4In8Yb
2In4Yb
1In3Yb
1In3Yb
1In3Yb
Stable and accurate at the level of 10-17
Feb
March
115In+/171Yb+
115In+/87Sr
clock transition of all 8 In+ ions @ 120ms pulse time  no loss of contrast observed

## Slide 57
Multi-ion spectroscopy
• • • • • • • • • • • •
Spatially resolved individual In+ ion signals
• In+ • Yb+ 4In+ 8Yb+
All ions contribute with the same contrast:
Notes: So far I‘ve only talked about the single-ion clock but we‘ve also performed multi-ion spectroscopy. We see that we can keep a good contrast even with up to 8In+ ions which is a great result. Nevertheless, there are many challenges when concerning multi-ion spectroscopy. These will be discussed in my poster tomorrow

## Slide 58
Multi-ion spectroscopy
8In+ & 4Yb+
Averaged clock transition of all 8 In+ ions @ 120ms pulse time
 no loss of contrast observed
Notes: We can also keep the Fourier-limited linewidth for multiple ions. Due to our camera-based readout, we can resolve all individual ions and see that they all contribute with the same contrast

## Slide 59
Test: radial E3 excitation of 8 172Yb+ ions with a flat-top beam
Outlook: prospects for a multi-ion Yb+ clock  173Yb+
Clock spectroscopy with 173Yb+ ions would reduce the Stark shift by factor 100 [1]
[1] V. A. Dzuba, V. V. Flambaum, Phys. Rev. A (2016)

## Slide 60
E2 transition  10-17 possible
Θ = 2.08 ea02 , B || z
E3 transition  10-19 possible
Θ = -0.041ea02 , B || z
Huntemann et. al, PRL 108, 090801 (2012)
Outlook: prospects for a multi-ion Yb+ clock
Example: quadrupole shifts with 10 ions
„possible means“ = control quadrupole shift to 1 %
typical axial frequency in our trap
typical axial frequency in our trap

## Slide 61
Testing local Lorentz invariance with a single 172Yb+ ion
Laura S. Dreissen, Chih-Han Yeh, Henning A. Fürst, Kai C. Grensemann and Tanja E. Mehlstäubler
New limit in electron-photon sector at 10-21 level
Nat. Commun. 13 (Nov. 2022)

## Slide 62
Testing General Relativity – Einstein’s Equivalence Principle
Universality of Free Fall (UFF)
„The trajectory of a point mass
in a gravitational field only
depends on its initial position and
velocity.“
Local Position Invariance (LPI)
„The result of your experiment is independent of its location in space and time.“
Local Lorentz Invariance (LLI)
„The result of your experiment is independent of the orientation and velocity of the laboratory frame.“
Local Position
Invariance
Einstein’s
Equivalence Principle
Universality of
Free Fall
Local Lorentz
Invariance
UFF
LPI
LLI

## Slide 63
Analog of the Michelson-Morley experiment  Electron Orbitals
A. A. Michelson and E.W. Morley, Philos. Mag. S.5, 24(151), 449-463 (1887)
Measure modulation in energy difference with sidereal day frequency 93 h

## Slide 64
SME theory background - Spectroscopy
LLI is quantified in the SME by adding a symmetry-breaking cµn tensor to kinetic term of SM Langragian
Non-common mode energy shift at time-modulation period related to sidereal day:
T0(2) is quadrupole moment operator of electronic momentum distribution
Can‘t separate electron and photon sector!  use combined tensor components:
with
D. Colladay and V. A. Kostelecký, PRL 58, 116002 (1998) Dzuba et al., Nat. Phys. 12, 465 (2016)
sidereal day frequency 93 h
siderial day = 23 h 56 min 4.1 s
Notes: Yb+: enhancement factor 14 to Ca+ ! : \Delta E  no boost, no annual modulation included !! C0 contains spatial elements of frame dependent cµn tensor!

## Slide 65
SME theory background - Spectroscopy
LLI is quantified in the SME by adding a symmetry-breaking cµn tensor to kinetic term of SM Langragian
Non-common mode energy shift at time-modulation period related to sidereal day:
T0(2) is quadrupole moment operator of electronic momentum distribution
Can‘t separate electron and photon sector!  use combined tensor components:
with
D. Colladay and V. A. Kostelecký, PRL 58, 116002 (1998) Dzuba et al., Nat. Phys. 12, 465 (2016)
Notes: Yb+: enhancement factor 14 to Ca+ ! : \Delta E  no boost, no annual modulation included !! C0 contains spatial elements of frame dependent cµn tensor!

## Slide 66
SME theory background - Spectroscopy
LLI is quantified in the SME by adding a symmetry-breaking cµn tensor to kinetic term of SM Langragian
Non-common mode energy shift at time-modulation period related to sidereal day:
Elements of the tensor
LV energy shift
T0(2) is quadrupole moment operator of electronic momentum distribution:
D. Colladay and V. A. Kostelecký, PRL 58, 116002 (1998) Dzuba et al., Nat. Phys. 12, 465 (2016)
Notes: Also others, HCIs + Thorium have been identified. Here: currently accessible ones.

## Slide 67
SME theory background - Spectroscopy
M. A. Hohensee et al., Phys. Rev. Lett., 111: 050401 (2013)
For a state:
Challenge:
suppress influence from the 1st-order Zeeman shift due to magnetic field noise!
Measure energy differences between states with large
Notes: Also others, HCIs + Thorium have been identified. Here: currently accessible ones.

## Slide 68
The full experimental sequence
P=85%
-1/2
non-linear energy splitting

## Slide 69
Probe laser for the electric octupole (E3) transition
b) Active magnetic field stabilization
Feedback stabilization: noises at up to 550 Hz: reduced to nT ( µG)
a) Ultra-stable laser system

## Slide 70
Coherent excitation of the E3 transition
Coherent atomic state manipulation via E3 in 1st-order Zeeman sensitive transition
Up to 90 % excitation probability!
H. A. Fürst et al., PRL 125, 163001 (2020)
ms
years
[2]
[3]

## Slide 71
Ramsey spectroscopy
RF composite pulses
Composite pulse sequence to suppress B-field noise
(1st oder Zeeman sensitivity)
Factor 10,000 in coherence time
s
Ramsey

## Slide 72
Simulated stability diagram UR10
G. T. Genov et al., Phys. Rev. Lett. 118, 133202 (2017)
UR 10 sequence:
Simple spin-echo scheme
Ch.-H. Yeh et al., NJP (2023)
104 more robust against errors!
F > 0.85 is reached for |ηω| < 0.03 for a fixed pulse duration error |ηt | = 0.004

## Slide 73
Ramsey dark-time scan of the rf pulse sequence
maximized
proportional to
rad/s
Retrieved population as a function of the acquired phase
Contains the quadrupole shift and a potential LLI violation
Contrast of 75%
Improved the coherence time by x 104
LV: modulation of the phase
Sensitivity at T = 1.15s
s achieved

## Slide 74
Theoretical description
, proportional to
Quadrupole shift + potential LV
, proportional to
Interaction picture and RWA:
Drifts in the ambient magnetic field
R. Shaniv, et al., Phys. Rev. Lett. 120, 103202 (2018)
Purpose: measure dependent terms, suppress dependent terms

## Slide 75
Single ion test of LLI - 5 week measurement campaign (2022)
Fit function:
1-p
2 = 0:92.
Chi 2 = 0.92
/s]

## Slide 76
Single ion test of LLI
new scheme matches previous result obtained by optical clocks 9 times faster !
sets new improved bounds in the electron-photon sector, all in 10-21 range
Correlated LV parameters | Measurement time: s
Correlated LV parameters | 
Components of the symmetry-breaking tensor
L. S. Dreissen et al., Nat. Comm. 13, 7314 (Nov. 2022)
Notes: consists of two Ramsey pi/2 pulses for spreading the population into the Zeeman substates and then bringing them back into the F,1/2 state
even isotope  first order sensitive to the magnetic field noise  multiple pi-pulses for suppressing the magnetic field noise in the environment
the sensitivity to LV is delta…… where N is the number of ions, tau is the interrogation time (Ramsey dark time), and T is the total measurement time

## Slide 77
Isotope shift measurement in search for new boson

## Slide 78
King plot analysis
Normalize to the IS of a second transitions:
Less sensitive to nuclear charge moment
Common mode effects drop out
J. C. Berengut, et al., Phys. Rev. Lett. 120, 091801 (2018)
King plot analysis:
Normalize to a second transition to eliminate the dominant terms
Observe nonlinearities in King plot of two different transitions in at least 3 isotopes
Linear in
Possible nonlinear contributions
Possible bounds on a new boson

## Slide 79
King Plot Analysis - Yb+-Isotope shifts (Yb-168, 170, 172, 174, 176)
[18] I. Counts, et al., Phy. Rev. Lett. 125, 123002 (2020). [19] J. Hur, et al., Phy. Rev. Lett. 128, 163201 (2022).
[20] N. L. Figueroa, et al., Phy. Rev. Lett. 128, 073001 (2022). [21] Koki Ono, et al., Phy. Rev. X 12, 021033 (2022).
[22] O. Saleh, et al., Phy. Rev. A 103, L030801 (2021)
MIT: 168,170,172,174,176Yb+ E2 and E3 transition measured with 300 Hz and 500 Hz precision [19]
PTB: 3 Hz and 16 Hz achieved (2023)
Generalized King Plot[19] normalized with 578nm[21]
For visibility data points are shown with enlarged uncertainty interval by a factor of 100
yellow line is a single source fit
87.6 σ for a second nonlinearity source
 Compare to nuclear structure calculations
 New bounds to be published 2023

## Slide 80
Yb+-Isotope shift measurements (Yb-168, 170, 172, 174, 176)
[18] I. Counts, et al., Phy. Rev. Lett. 125, 123002 (2020). [19] J. Hur, et al., Phy. Rev. Lett. 128, 163201 (2022).
[20] N. L. Figueroa, et al., Phy. Rev. Lett. 128, 073001 (2022). [21] Koki Ono, et al., Phy. Rev. X 12, 021033 (2022).
[22] O. Saleh, et al., Phy. Rev. A 103, L030801 (2021)
Isotope shift measurement in
search for new boson
MIT: 168,170,172,174,176Yb+ E2 and E3 transition measured with 300 Hz and 500 Hz precision
PTB: 3 Hz (E2) and 16 Hz (E3) achieved
 86 sigma signal for second source of non-linearity
 Manuscript in preparation

## Slide 81
Frequency-normalized King plot – Yb+ lines versus Yb neutral 578 nm
578 nm data from Koki Ono, et al., Phy. Rev. X 12, 021033 (2022)
(error bars smaller than data points)

## Slide 82
King plot analysis
Normalize to the IS of a second transitions:
Less sensitive to nuclear charge moment
Common mode effects drop out
J. C. Berengut, et al., Phys. Rev. Lett. 120, 091801 (2018)
King plot analysis:
Normalize to a second transition to eliminate the dominant terms
Observe nonlinearities in King plot of two different transitions in at least 3 isotopes
Linear in
Possible nonlinear contributions
Possible bounds on a new boson
 Manuscript in preparation

## Slide 83
Acknowledged support and cooperation regarding clock campaignes:
Stefan Weyers, Johannes Rahm, Erik Benkler, Burghard Lippardt, Thomas Legero (PTB)
Miroslav Dolezal and Petr Balling (CMI)
Sr-lattice clock and 171Yb+-single ion team at PTB
Thank you for your attention!
6 Yb+ + 15 In+
6 Yb+ + 16 In+

## Slide 85
First locking to multiple ions
→ dead time increase due to clock cycle
→ improved code will solve the issue
Instabilty at 1s
No fit  model curve

## Slide 86
In+ (PTB) / Sr (PTB)
In+ (PTB) / Yb+ (PTB)
Yb+ (PTB) / Sr (PTB)
In+ (PTB) / Yb (INRIM)
In+ (PTB) / Sr (SYRTE)
Yb (INRIM) / Sr (PTB)
Yb (INRIM) / Sr (SYRTE)
Sr (PTB) / Sr (SYRTE)
Yb+ (PTB) / Yb (INRIM)
Yb+ (PTB) / Sr (SYRTE)
Februar / March 2022 – International Campaign

## Slide 87
Quantum-Technology Competence Center of PTB
Standardization of Ion Traps for QT Applications
Characterization under Reproducible and Standardized Conditions
Service for Industry and Academia
User Platform “Ion Traps” (2019)
Automized Measurement Protocols via
Infineon Trap
EVAQS: Test and Development of XHV Technologies for QT with German Industry (Allectra, engionic Fiber Optics)

## Slide 89
Integration of Nano-Optics

## Slide 90
Integrated Nano-Photonics for high Scalability
Fabrication @ LioniX (NL)
VIS
IR
IR
UV
UV
VIS
IR
SiN and Al2O3 waveguides and Bragg outcouplers integrated into ion trap
Collaboration: K. Mehta (Cornell University, US)

## Slide 91
2020
Trap chip with integrated with Si3N4 and Al2O3 waveguides for an Yb+ ion clock
Collaboration: Karan Mehta (Cornell), production at LioniX (NL): first chip Aug. 2023
2020: Clock on a Chip  PIC ion trap
Design
Fabricated optics chip without gold layer

## Slide 92
2020
Clock on a Chip  PIC ion trap
Includes mode converter to HG10 mode
Peshkov et al., Annalen der Physik 2300204 (2023)
 Use higher-oder light modes to suppress Stark shifts
Excitation probability
in 1.5 ms (1 mW)

## Slide 93: Ion trap technology levels
First PICs arrived in August!
Carl Grimpe, G. Du and Anastasiia Sorokina
end of SiO2 cladding
IR PICs from AMO
First light coupled through chip. Test at 760 nm

## Slide 94: Nanofabrikation von PICs
December 2021: „ATIQ“
Development of traps with
Si3N4, AlN and Al2O3 waveguides and grating couplers with German partners
E-Beam written optical grating (AMO, Aachen)
2µm
Photonic integrated ion traps for quantum computing (QC)
Notes: Im ATIQ Projekt ist die AMO GmbH in Aachen, die eng mit der RWTH Aachen zusammenarbeitet, für die Nanofabrikation der Photonic Integrated Chips kurz PICs zuständig. Die Fabrikation ist eine Herausforderung, da eine sehr höhe Auflösung im Nanomenter Bereich erforderlich ist, was jetzt Dank der Fortschritte in den Fabrikationstechniken möglich ist. Sie verwenden für die Fabrikation lithographische Methoden, die feinen Strukturen werden Elektronenstrahl geschrieben. Für die Optik müssen unterschiedlichen Schichten auf dem Chip deponiert werden und um die Oberfläche für Ionenfallen brauchbar zu machen, entwickelt das Fraunhoferinstitut in Jena passende transparente leitfähige Schichten.

## Slide 95: TEST measurements
In
Out
FA
Simplified and automised measurements flow
Sample preparation:
  Polishing/contacting fiber array (FA) with PM fibers to the chip
Getting the alignment with U-WG loop
Select GC, focus, and measure!

## Slide 96: Ion trap technology levels
First PICs arrived in August!
Integrated ion trap PIC from LioniX

## Slide 97: The ALP-QuSense Platform
Future Dream: all optical integrated QT sensor platforms
Compact PIC-based Clocks

## Slide 98
©S. Sauer
Laser
beams
Optically integrated ion traps
©J.E.Jordan
Array of ions
Array of detectors
Future Traps - Clock on a Chip
Optical waveguides with Bragg-coupler

## Slide 99
Direct fluorescence of In+ (g = 360 kHz)
 detection + cooling
In+ detection at 230 nm interleaved with Yb+ cooling
State-of-the-art with 115In+ set-up
1S0, F = 9/2
3P0
3P1
236.5 nm
230.5 nm
g = 360 kHz
g = 0.8 Hz
Single ion fluorescence s=10
red detuned
blue detuned
2021: First scans of clock transition
120 ms
pulses
Signal of In+ clock transition at 236 nm

## Slide 100
Multi-ion spectroscopy
5 In+ & 5 Yb+
8 In+ & 4 Yb+
100ms sympathetic cooling
frad = 820kHz (for single Yb+ ion)
fax = 120kHz (for single Yb+ ion)
200ms sympathetic cooling
frad = 725kHz (for single Yb+ ion)
fax = 105kHz (for single Yb+ ion)
Notes: So far I‘ve only talked about the single-ion clock but we‘ve also performed multi-ion spectroscopy. We see that we can keep a good contrast even with up to 8In+ ions which is a great result. Nevertheless, there are many challenges when concerning multi-ion spectroscopy. These will be discussed in my poster tomorrow

## Slide 101
2nd order Doppler shift (thermal)
TD,Yb = 0.47mK = Yb+ Doppler temperature
Set upper bound for the radial mode temperatures from Rabi flops:
Trad,1+Trad,2 <6TD,Yb
 Trad,1+Trad,2=3.5±2.5TD,Yb
Upper bound for axial temperature from influence on indium fluorescence:
Tax<10TD,Yb
 Tax=5.5±4.5TD,Yb

## Slide 102
Ponderomotive Potential
Charged ions interact strongly with environment
→ trap with electric fields ?
BUT: Non-Trapping Theorem
How to trap ions ? The Paul trap
Notes: 102

## Slide 103
Time Dilation due to Heating of Secular Motion
Brownnutt et al., Rev. Mod. Phys. 87, 1419 (2015)
3D Chip Trap
Comparison to international ensemble of ion traps:
Power Spectral Density
Heating of ion out of
quantum mechanical
ground state
..causes time dilation
Single ion heating rate =
ndc = 0.7 ± 0.2 phonon/s @ 626 kHz
 Dn TD /n0 = -1.7 x 10-20 /s for 115In+
Electrode – Ion Distance (µm)
.
Notes: Not only filter boards but also PT100s on board 

## Slide 104
Linear ion traps
URF !
UDC
UDC
URF !
Radial direction: RF potential
Axial direction: DC potential
ERF = 0
radial
axial

## Slide 105
Riehle, Frequency Standards, Wiley VCH 2004
Stability versus Accuracy
stable +
accurate
accurate
reproducible
accuracy = the frequency deviation from its true value
i.e. the unperturbed center of the atomic transition (atom at rest, T = 0 K)
Notes: marksman’s sequence of bullet holes on a target