## Slide 1
AWAKE ChDR BPM summary
E. Senes
… with many thanks to the BI colleagues, AWAKE OP and SY/ABT for the support

## Slide 2: Project summary
Hopefully, this time in less than 115 slides
However, it’s hard to summarize almost 4 years of work in 20’

## Slide 3
2019 – PTFE demonstrator

## Slide 4
2019 – PTFE demonstrator
2020/21 – In-air alumina prototype

## Slide 5
2019 – PTFE demonstrator
2020/21 – In-air alumina prototype
2022 – Vacuum version
Filters and diodes

## Slide 6
2019 – PTFE demonstrator
2020/21 – In-air alumina prototype
2022 – Vacuum version
TRIUMF
electronics
Filters and diodes

## Slide 7
PTFE demonstrator
2019
2019 – PTFE demonstrator

## Slide 8
PTFE results
Lessons learned
It was shown the possibility to test with good beam stability, but some diagnostics logging at 1 Hz logging
Just check out the thesis …
1
It was developed the filter, variable attenuator and RF diode technique
2
Started collecting 30 GHz parts from BE/RF and old lab. A lot of coding for automation of the measurements.
3
List of results
Input used to design the alumina radiators
4
2 detectors 26.5 – 40 GHz
2 detectors 75 GHz
Single plane diode + attenuator + filter

## Slide 9
Simulation results
1
Angle tolerance (Alumina)
3
90° radiator BPRW-style and reflections (Alumina)
4
Probe-based simulation (PTFE)
Some more in the thesis, relevant shown
Additional results
2
Cutoff frequency (PTFE, Alumina)

## Slide 10
In-air Alumina prototype
Diodes, BPFs and attenuators 2021 data, revisited in 2022
2020/21 – In-air alumina prototype

## Slide 11
In-air alumina results
Lessons learned
We can test with excellent beam stability, but 1 Hz logging for charge
1
Full development of variable attenuator technique
2
I collected, refurbished and wrote code for lots of 30 GHz parts from BE/RF
3
Validation test for the vacuum tight radiators
4
Developed a standardized measurement protocol
Alumina ø6 and ø15 mm in-air
Kacper’s test
AWAKE May test

## Slide 12
Typical measurement
An example: a horn antenna measurement
430 pC
Pointing stability within 100 um (usually)
Size stability less than 100 um

## Slide 13: Lesson learnt
An example: a horn antenna measurement
FULL DATASET REPROCESSED IN SUMMER 2022 UPON REQUEST
Constant input voltage in the diode
Remote attenuator compensated in the data post-processing

## Slide 14: Lesson learnt
FULL DATASET REPROCESSED IN SUMMER 2022 UPON REQUEST
An example: a horn antenna measurement

## Slide 15: Results summary
 | Coupler | Charge (pC) | Slope (1/mm)
#1 | Horn | 430 | 2.5 %
#2 | Transition | 180 | 2.4 %
#3 | Transition | 125 | 2.3 %
#4 | Transition | 121 | 2.3 %
All the measurements are consistent within the experimental errors to a sensitivity of 2.3-2.5 % mm-1
When coupling with the horns, a large charge increase is required to match the same signal levels. The horn is far from an ideal coupler …
Even if a prepulse might be present, the main peak scales with charge and position

## Slide 16: Results summary (2)
It was developed a strong measurement protocol based on Schottky diodes, BPFs, and variable attenuators.
1
Experience with the limited RF detection available (not even our VNA …)
A lot of work procuring, refurbishing, adapting instrumentation
Code development for scopes, attenuators, analysis …

## Slide 17: Results summary (2)
It was developed a strong measurement protocol based on Schottky diodes, BPFs, and variable attenuators.
1
This method removes uncertainties from the Schottky diodes transient response, that we can’t easily qualify.
2
Experience with the limited RF detection available (not even our VNA …)
A lot of work procuring, refurbishing, adapting instrumentation
Code development for scopes, attenuators, analysis …

## Slide 18: Results summary (2)
It was developed a strong measurement protocol based on Schottky diodes, BPFs, and variable attenuators.
1
This method removes uncertainties from the Schottky diodes transient response, that we can’t easily qualify.
2
Experience with the limited RF detection available (not even our VNA …)
A lot of work procuring, refurbishing, adapting instrumentation
Code development for scopes, attenuators, analysis …
The insight was deemed sufficient to design vacuum-tight buttons
3

## Slide 19
AWAKE Tests
Diodes, BPFs and attenuators May 2022
Filters and diodes

## Slide 20: Typical tests
Parasitic measurements only
Same setup developed at CLEAR
1e11 ppb
Protons: No signal from 1e11 ppb with this system sensitivity (no amplifier)
Typical signal with electrons shown

## Slide 21: Electrons-only tests - summary
Charge scan:
 | Charge (pC) | Slope (1/mm)
#1 | 200 | 4.8 ± 0.2 %
#2 | 550 | 4.5 ± 0.11 %
Signal increases from both radiators when the charge is increased
Position scan:
Two measurements at low and high charge
Measured 3 dB signal difference between the arms with beam in centre
Similar position sensitivity in both measurements

## Slide 22: Proton tests – intense protons
Parasitic measurements only
No signal from 1e11 ppb with this system sensitivity
Some signal from 3e11 ppb, however with large variation
3e11 ppb
Quick statistic measurements with the available diagnostic & time constraints

## Slide 23: Proton signal statistics
Statistical study with electrons and protons
Systematic study limited by test equipment, time, available logging …

## Slide 24
AWAKE Tests
TRIUMF electronics August-December 2022
TRIUMF
electronics

## Slide 25: TRIUMF electronics
Work performed and data collected:
Full CW calibration, both lab and tunnel
RF generator
30.5 GHz
50Ω Load
BPF
SPLITTER
MIXER
Channel Under Test
Charge scan
Rough position scan
IF direct measurements
LO phase scan
Position scan (December run, with Collette)
FURTHER DEVELOPMENT AWAITING FOR INPUT AND PLANS

## Slide 26
RED = eBPM
BLACK = ChDR BPM
Current status
Full infrastructure for 2x BPMs ready and in place
Tw0 intense years of work to achieve:
Partial commissioning of 1x BPM done, paused for the moment
THE WORK IS WELL ADVANCED, BUT REQUIRES FURTHER UNDERSTANDING OF THE ChDR BPM DEVICE

## Slide 27
My proposal

## Slide 28
There is at least material for 2 Papers:
Paper #1:
A letter on the use of ChDR for future BPMs, showing some of the latest results with position scans in AWAKE.
Based on the Thibaut’s template that has been sitting in overleaf for long
Paper #2:
PRAB paper specific on AWAKE:
“Development of beam position monitors for co-propagating charged particle beams”
Content:
To be discussed …

## Slide 29
There is at least material for 2 Papers:
Paper #1:
A letter on the use of ChDR for future BPMs, showing some of the latest results with position scans in AWAKE.
Based on the Thibaut’s template that has been sitting in overleaf for long
Paper #2:
PRAB paper specific on AWAKE:
“Development of beam position monitors for co-propagating charged particle beams”

## Slide 30
There is at least material for 2 Papers:
Paper #1:
A letter on the use of ChDR for future BPMs, showing some of the latest results with position scans in AWAKE.
Based on the Thibaut’s template that has been sitting in overleaf for long
Paper #2:
PRAB paper specific on AWAKE:
“Development of beam position monitors for co-propagating charged particle beams”
Content:
The AWAKE problem, different spectral power of e- and p+
ChDR BPMs test at AWAKE with BPF and diodes. Discussion of reflections and the asymmetric emission problem.
HF BPMs with BPF filters measurements of protons and electrons and both, using data of the May and December scans in AWAKE.
To be discussed which data to be used. In principle this could leave room for a later paper (Collette ?) on the button characterization at CLEAR in different frequency bands (>40 GHz is NOT AWAKE relevant )
This most likely concludes that the proton shape is shot-by-shot dependent, so further studies will be required to assess the resolution degradation due to the protons (Beth ?)
There are still data to be looked into:
Proton data
Electron December data

## Slide 31
Eugenio Senes | AWAKE ChDR BPMs summary
eugenio.senes@cern.ch