## Slide 1: Coherent Cherenkov diffraction radiation studies at CLEAR
Preliminary results from the KAPTEOS
measurement campaign 3.-7. October
Andreas Schlögelhofer

## Slide 2
20 m
Polarized light
Mirror
Polarizer
Crystal
DC Laser @ 1550 nm
Fast photodiode
High BW
Oscilloscope
FCC BI 2022 – November 2022
Laboratory
Andreas Schlögelhofer
5 x 2.5 mm
  electric field modulus and polarization up to 10 GHz
EO probe from Kapteos

## Slide 3
ChDR
beam
ChDR
X
Y
Z
FCC BI 2022 – November 2022
Andreas Schlögelhofer
ChDR vacuum test stand
Θ

## Slide 4: Direct beam field
Z
Z
Y

## Slide 5: Direct beam field
Averaged traces
Traces are leveled for bias offset using first 1 ns of data
Average trace of 600 shots (equals 1 minute)
σ = 54.6 +- 3.4 ps
FWHM = 128.5 +- 7.9 ps

## Slide 6: Direct beam field
Averaged traces
Charge @ dump
Insertion loss laser
Final traces are corrected for average of charge during 1 minute
Final traces are corrected for average of insertion loss during 1 minute

## Slide 7: Direct beam field - impact scan
1/r fitting function
The peak e-field
with parameters
300 pC, σ = 5 ps (FWHM = 11.8 ps), 200 MeV
yields:
Emax = 1435.2 / r
Measurement is roughly a factor 7.3 off
 Check jitter effects and bandwidth limitations

## Slide 8: Jitter for direct beam field
Jitter measurement best for direct beam field measurements when close to the beam to obtain a good single shot signal
Each measurement is an aquisition of 600 traces @ 10 Hz, equals 1 minute for each acquisition
1 count = maximum value in trace
17:47, 17:50, 17:53, 17:55, 17:58

## Slide 9: Bandwidth considerations
Low frequency = -
High frequency = 10.00 GHz
Low frequency = 1.63 GHz
High frequency = 10.00 GHz
 FWHM underestimated as pulse shifts due to lack of DC components
10 GHz
10 GHz

## Slide 10: Bandwidth considerations
Bandwidth
with FWHM = 11.8 ps
factor 4.0
Jitter
with FWHM = 58 ps
factor 2.26
In total
 roughly factor 9
 overestimate by 20 %

## Slide 11: «Single pulse response»
ChDR pulse
Direct beam field (expected 58 ps)
10 GHz
10 GHz

## Slide 12: «Single pulse response»
ChDR pulse
Direct beam field
1.63 GHz

## Slide 13: ChDR Vacuum TS – long trace
 | Time [ns] |  | Wavelength [cm] | 
Frequency [GHz] | Vacuum | Alumina (ε=9) | Vacuum | Alumina (ε=9)
1.72 | 0.583 | 1.749 | 17.48 | 5.83
2.12 | 0.472 | 1.415 | 14.14 | 4.71
2.70 | 0.370 | 1.111 | 11.10 | 3.70
2.88 | 0.347 | 1.042 | 10.41 | 3.47
3.14 | 0.319 | 0.957 | 9.56 | 3.19
3.40 | 0.294 | 0.882 | 8.82 | 2.94
3.49 | 0.287 | 0.860 | 8.59 | 2.86
3.72 | 0.269 | 0.806 | 8.06 | 2.69

## Slide 14: ChDR in-air test stand
beam
Z
X
Y
Θ

## Slide 15: ChDR in-air teststand – polarization
probe  radiator: 9 mm distance
beam  radiator: 10 mm distance
average over 2400 traces (4 minutes @ 10 Hz)

## Slide 16: ChDR in-air teststand
probe  radiator: 9 mm distance
beam  radiator: 10 mm distance
average over 2400 traces (4 minutes @ 10 Hz)

## Slide 17: ChDR in-air teststand – shielded

## Slide 18: ChDR in-air teststand
to compare with vertical polarization

## Slide 19
ChDR
beam
ChDR
X
Y
Z
FCC BI 2022 – November 2022
Andreas Schlögelhofer
ChDR vacuum test stand
Θ

## Slide 20: ChDR Vacuum-TS – charge scan

## Slide 21: ChDR Vacuum-TS – charge scan

## Slide 22: ChDR THz-TS – impact scan

## Slide 23: ChDR THz-TS – impact scan

## Slide 24: ChDR THz-TS – impact scan

## Slide 25: ChDR Vacuum-TS – impact scan

## Slide 26: ChDR Vacuum-TS – impact scan

## Slide 27: ChDR Vacuum-TS – impact scan

## Slide 28: Conclusion
First look on results is very consistent
Compares well to analytical models (and CST)
Analysis still to be optimized (error bars,…)
Key results so far:
  Absolute e-field measurement
  Horizontal polarization maintained
  Cut-off frequency
  1/h for impact scan at very low frequencies

## Slide 29: Outlook
CST, CST, CST,…
Conduct EO spectral decoding tests at CLEAR
  1 week of parasitic beam time so far
  Analysis not started yet, but proof of principle shown
North Area
  In discussion with Inaki on feasibility
ATF2
  Applied for collaboration with Renjun
  EAJADE recently approved

## Slide 30: Attachment

## Slide 31: ChDR In-Air TS – surface (center)

## Slide 32: ChDR In-Air TS – direct (closest)