## Slide 1: Introduction to Non-linear Longitudinal Beam Dynamics
H. Damerau
CERN
4 October 2023
Introduction to Accelerator Physics

## Slide 2
Copyright statement and speaker’s release for video publishing
The author consents to the photographic, audio and video recording of this lecture at the CERN Accelerator School. The term “lecture” includes any material incorporated therein including but not limited to text, images and references.
The author hereby grants CERN a royalty-free license to use his image and name as well as the recordings mentioned above, in order to post them on the CAS website.
The material is used for the sole purpose of illustration for teaching or scientific research. The author hereby confirms that to his best knowledge the content of the lecture does not infringe the copyright, intellectual property or privacy rights of any third party. The author has cited and credited any third-party contribution in accordance with applicable professional standards and legislation in matters of attribution.

## Slide 3
Introduction
Linear and non-linear longitudinal dynamics
  Equations of motion, Hamiltonian, RF potential
Longitudinal manipulations
  Bunch length and distance control by multiple RF systems
  Bunch rotation
Synchrotron frequency distribution
  Effect on longitudinal beam stability
Summary
Outline

## Slide 4
Introduction

## Slide 5
Signals generated by radio-frequency systems in particle accelerators are of the form
  Resonance effect: large voltage with little effort
  Inherently non-linear
  Linear longitudinal beam dynamics only an approximation
Introduction
Effect of non-linearity on beam?
Tools to describe and analyse non-linearity
Use non-linearity to improve beam conditions

## Slide 6
Non-linear longitudinal dynamics

## Slide 7
Triple splitting at Ekin = 2.5 GeV
Split in four at flat top energy
26 GeV/c
Ekin = 2.5 GeV
2nd injection
Non-linear RF allows to control all longitudinal parameters
Number of bunches, bunch length and emittance, longitudinal stability
h = 7
Eject 72 bunches
Inject 4+2 bunches
gtr
Controlled blow-ups
h = 84
h = 21
Example: LHC-type beam in the CERN PS

## Slide 8
Compression, merging and spitting
Split in four at flat top energy
26 GeV/c
Ekin = 2.5 GeV
2nd injection
Non-linear RF allows to control all longitudinal parameters
Number of bunches, bunch length and emittance, longitudinal stability
h = 9
Eject 48 bunches
Inject 4+4 bunches
gtr
Controlled blow-ups
h = 84
h = 21
Example: LHC-type beam in the CERN PS

## Slide 9
Inject 4+4 bunches
gtr
Controlled blow-ups
Where profit from non-linear RF?
Transition crossing
RF voltage reduction during acceleration
RF manipulation from 8 bunches in h = 9 to 12 in h = 21
Splitting at the flat-top
Bunch shortening (rotation) before extraction
h = 9
Eject 48 bunches
h = 84
h = 21

## Slide 10
Inject 4+4 bunches
gtr
Controlled blow-ups
Where profit from non-linear RF?
Transition crossing
RF voltage reduction during acceleration
RF manipulation from 8 bunches in h = 9 to 12 in h = 21
Splitting at the flat-top
Bunch shortening (rotation) before extraction
h = 9
Eject 48 bunches
h = 84
h = 21

## Slide 11
Applications
Introduce extra non-linearity
  Bunch lengthening in double-harmonic RF system to reduce peak current (space charge)
  Short and long bunches with multi-harmonic RF systems
  Adapt bunch-to-bunch distance
Profit from non-linearity for beam stabilization
  Stabilize beam using higher-harmonic RF
  Controlled longitudinal emittance blow-up

## Slide 12
Linear longitudinal beam dynamics

## Slide 13
Interaction between particles and RF
Energy dependent phase advance, f:
Phase dependent energy gain, DE:
Simple accelerator model:
Works for arbitrary shape of acceleration amplitude g(f)

## Slide 14
Usual longitudinal beam dynamics already non-linear, since RF system usually provides sinusoidal amplitude
Linear longitudinal beam dynamics?
Linear longitudinal beam dynamics
same structure

## Slide 15
Construct Hamiltonian from equations of motion
Hamiltonian constant on trajectory
‘Energy conservation’
Linear longitudinal beam dynamics
same structure

## Slide 16
The Hamiltonian from the equations can be written as
Linear longitudinal beam dynamics

## Slide 17
Particles move on circular trajectories in f-/wS phase space
RF potential is parabolic, W(f) ~ f
Hamiltonian is constant on these trajectories
Linear longitudinal beam dynamics
/wS
f
H = const.
f
U

## Slide 18
Linear longitudinal phase space
Simple model
Circular trajectories
All particles have same synchrotron frequency
Normalized bucket area: Ab = pr2 = p3
Harmonic oscillator

## Slide 19
Non-linear longitudinal beam dynamics

## Slide 20
with this becomes
Introduce most simple non-linearity
RF amplitude function
Standard longitudinal beam dynamics  Lectures F. Tecker

## Slide 21
Introduce most simple non-linearity
using
this Hamiltonian simplifies to

## Slide 22
In the centre of the bucket, particles move on elliptical trajectories in Df-DE phase space
Hamiltonian is constant on these trajectories
In the bucket centre, particles oscillate with the synchrotron frequency, wS = 2pfS
Linear part of non-linear bucket
DE
Df
H = const.

## Slide 23
Compare two particles on the same trajectory
  No phase deviation 2. No energy deviation
Longitudinal emittance
1.
2.

## Slide 24
Longitudinal emittance, el
Surface occupied by particles in longitudinal phase space
Preserved in physical [pDt DE] = eVs
Compare two particles on the same trajectory
  No phase deviation 2. No energy deviation
Longitudinal emittance
1.
2.

## Slide 25
More non-linearity: multi-harmonic RF
RF amplitude
Example case n = 2 and r = 0.5
Both RF systems in counter-phase
Both RF systems in phase at bunch
Local voltage gradient decreased
Bunch is stretched
Lower peak current
Local voltage gradient increased
Bunch is compressed
Higher peak current

## Slide 26
Example application: space charge in PSB
RF amplitude
Space charge instantaneous current
Inverted gradient at bucket centre
Flattened bunch with reduced peak current  Space charge reduction at low energy
t [ns]
0
-400
400
0.6
0.4
0
0.2
-0.2
-0.4
-0.6
0.8
0
0.4
DE [MeV]
I [A]
Time projection
Energy projection
Vh=1 = 8 kV, Vh=2 = 6 kV, counter-phase

## Slide 27
Do long and short bunches simultaneously!
Example BESSY VSR
Depending on user of synchrotron radiation: need long or short bunches
4  0.5 GHz NC (existing)
4  1.5 GHz supercond.
4  1.75 GHz supercond.
Long and short bunches simultaneously
Markus Ries et al.

## Slide 28
Bunch length modulation
Future 3-harmonic RF system for BESSY VSR
Markus Ries et al.
RF voltage sum
RF Potential
Longitudinal phase space
Short deep or bathtub potential well
RF voltages sum up or cancel
Short or stretched bucket

## Slide 29
300 mA average current
High-current single bunches
         short (0.8 mA) & long (10 mA)
Special high-current density bunches
Filling pattern
Markus Ries et al.
Two electron storage ring in one
Thanks to longitudinal beam dynamics trick

## Slide 30
2.
1.
2.
1.
1. Add h1 component such that bunches approach to 245 ns (small spacing) → big spacing becomes 327 ns
2. Synchronize on h1 to the PS
3. Trigger extraction kicker in-between the small spacing
4. Eject two bunches per ring at a distance of 327 ns
Example: adjust bunch spacing
Was used at CERN PSB-to-PS to transfer 2 bunches at once
Circumference ratio CPS/CPSB = 4
Ratio virtually moved to 2/7: use hRF = 2 + 1
Next bunch ejected
Short gap for ejection kicker
Christian Carli
Spacing larger than CPSB/2  hPS = 7, CPS/7

## Slide 31
The Hamiltonian describing the system becomes
Introduce general non-linearity
Equations of motion
same structure
Replace  arbitrary amplitude

## Slide 32
Using
The Hamiltonian can be rewritten, with RF potential W(f)
Arbitrary RF waveform

## Slide 33
Longitudinal beam manipulations using non-linearity

## Slide 34
Calculate aspect ratio of bucket trajectories
Equating both sides gives
with emittance as
Not efficient at all
16 times more RF voltage needed to cut bunch length in half
Change RF voltage to change bunch length?

1.
2.

## Slide 35
Individual particles in matched bunch oscillate but no macroscopic motion
Abruptly changing the RF voltage flips particles to new trajectories
The bunch distribution seems to rotate
Exchange of bunch length and momentum spread
Abrupt change of RF voltage
Matched
Mismatched

## Slide 36
Introduce sudden change: bunch rotation
Quickly exchange longitudinal phase space behind bunch
Increase RF voltage much faster than period of fS

## Slide 37
Quickly exchange longitudinal phase space behind bunch
Increase RF voltage much faster than period of fS
Introduce sudden change: bunch rotation

## Slide 38
Switch RF voltage much faster than period of fS
Introduce sudden change: bunch rotation

## Slide 39
Fit 14 ns long bunches into 5 ns long buckets in the SPS
Double-step bunch rotation
Example: PS to SPS transfer at CERN
80 MHz (h = 168)
40 MHz (h = 84)
4s = 14 ns
11 ns
4 ns
Adiabatic shortening
Bunch rotation
Bunch splittings
Extraction

## Slide 40
Bunch length now proportional to and not
Can save enormous RF voltage
Bunch shortening from 14 ns to 4 ns (ratio ~3.5)
Starting from 100 kV at 40 MHz
Slow shortening would require
Installed RF voltage is only about 1.2 MV
Example: rotation at PS-SPS transfer
Simulation
Extraction
-30
30
0
4 ns
t [ns]
RF voltage
Measurement

## Slide 41
Need large momentum spread for slow extraction
Jump RF phase such that bunch at unstable fixed point
Jump back
Let bunch rotate, switch RF off at large momentum spread
Non-linearly of bunch rotation helps
Profiting from the non-linear rotation
Bunch profile evolution
Longitudinal phase space
Measurement
Simulation

## Slide 42
Need large momentum spread for slow extraction
Jump RF phase such that bunch at unstable fixed point
Jump back
Let bunch rotate, switch RF off at large momentum spread
Almost constant momentum distribution after rotation
Example: using the non-linearity
Time projection
Energy projection
60
40
0
20
-20
-40
-60
2
0
1
I [A]
3
DE [MeV]
t [ns]
0
-20
20
Bunch profile evolution
Measurement
Measurement

## Slide 43
Synchrotron frequency distribution

## Slide 44
General synchrotron frequency
Synchrotron frequency depends on trajectory
Calculate average velocity for given trajectories in longitudinal phase space  Action angle, J
General expression for wS
The angular frequency becomes
(for bucket boundaries fl  fu)

## Slide 45
Distribution for stationary bucket
Single-harmonic RF in stationary bucket
K(x): 1st kind elliptical integral function
wS versus trajectory duration
wS vs. surface encircled by trajectory
Exact Approx.
Exact Approx.

## Slide 46
Distribution for stationary bucket
Single-harmonic RF in stationary bucket
Different synchrotron frequencies of particles in bunch
Total spread Dw/wS depends on filling factor of bucket
K(x): 1st kind elliptical integral function
wS versus trajectory duration
Exact Approx.
Exact Approx.
Dw/wS
Dw/wS
wS vs. surface encircled by trajectory

## Slide 47
Example: Emittance control with noise
Current emittance
Target emittance
Noise excitation of bunch by band-width limited noise
Controlled longitudinal blow-up in the PSB
Choose upper frequency to cover synchrotron frequency at bunch centre
Choose lower frequency to match target emittance
Excite
D. Quartullo

## Slide 48
Analogy: pendulums mounted on a bar
All particles have the same resonance frequency
Easy to excite macroscopic oscillation
Resonance frequencies of individual particles varies
Difficult to excite macroscopic oscillation
Large synchrotron frequency spread increases stability
Excitation
Excitation

## Slide 49
Bucket filling ratio
?
Easy to excite
Prone to instability
Smaller or larger bunch or bucket? What is more stable?
Large fS spread
More stable

## Slide 50
Acceleration of protons in the CERN PS (Etotal = 3.4  26 GeV)
Plateau
Arrival at flat-top
gtr
Example: stabilization with lower voltage
Constant RF voltage
Bucket area grows
Risk of Instability
Energy
Voltage
Area

## Slide 51
Acceleration of protons in the CERN PS (3.4  26 GeV total)
Plateau
Arrival at flat-top
Example: stabilization with lower voltage
Constant RF voltage
Bucket area constant  Instability
Energy
Voltage
Area
gtr
Same principle also applied in SPS and LHC
Prevent bucket filling to decrease

## Slide 52
Additional non-linearity by double RF
V2/V1 = 1/2, h2/h1 = 2
Synchrotron frequency
RF system at twice the main frequency and at half amplitude
Both RF systems in phase
Important increase in synchrotron frequency spread
Improves stability

## Slide 53
Additional non-linearity by double RF
V2/V1 = 1/3, h2/h1 = 3
Synchrotron frequency
RF system at twice the main frequency and at half amplitude
Both RF systems in phase
Important increase in synchrotron frequency spread
Improves stability

## Slide 54
Additional non-linearity by double RF
V2/V1 = 1/4, h2/h1 = 4
RF system at twice the main frequency and at half amplitude
Local regions of bunch with no fS gradient
Again prone to instability
Reduce voltage of 2nd harmonic RF system
Improving stability depends on appropriate voltage ratio
Synchrotron frequency

## Slide 55
Two RF systems in counter-phase?
Dferr = 5°
V2/V1 = 1/2, h2/h1 = 2
Synchrotron frequency
Large frequency spread at bunch centre with perfectly adjusted phases
Minor phase offset causes locally unstable regions
Works only for very short bunches
Electron accelerators
2nd RF twice frequency, half amplitude in counter-phase

## Slide 56
Quadrupolar coupled-bunch oscillations at flat-top
Main RF system: h1 = 21, 10 MHz, 4 out of 18 bunches
Higher-harmonic RF system: h2 = 84, 40 MHz
Both RF systems in phase:
Highest peak current, but most stable
Double RF, in phase
(Imperfect) counter-phase
Example: damping observations in the PS
Single-harmonic RF

## Slide 57
Summary
Longitudinal beam dynamics
  Everything non-linear
Longitudinal manipulations
  Tricks to adjust length and distance of bunches
  Do more with less RF
Synchrotron frequency spread
  More RF voltage may result in less stability
  Higher peak density may be more stable
  Improve stability and control emittance

## Slide 58
A big Thank You
to all colleagues providing support, material and feedback
Wolfgang Höfle, Andreas Jankowiak, Erk Jensen, Danilo Quartullo, Markus Ries, Elena Shaposhnikova, Frank Tecker

## Slide 59
Thank you very much for your attention!

## Slide 60
References
A. Hofmann, Landau damping, CERN-2006-002, 2006, pp. 271-304, http://cds.cern.ch/record/941315/files/p271.pdf
C. Bovet et al., A selection of formulae and data useful for the design of A.G. synchrontrons, CERN-MPS-SI-INT-DL-70-4, 1970, http://cds.cern.ch/record/104153/files/cm-p00047617.pdf
G. Dome, Theory of RF Acceleration and RF noise, CERN-1984-015, 1984, pp. 215-253, http://cds.cern.ch/record/863008/files/p215.pdf
D. Quartullo, E. Shaposhnikova, H. Timko, Controlled longitudinal emittance blow-up using band-limited phase noise in CERN PSB, J. Phys. : Conf. Ser. 874 012066, http://iopscience.iop.org/article/10.1088/1742-6596/874/1/012066
F. Tecker, Longitudinal beam dynamics, CERN-2014-009, 2006, pp. 1-21, http://cds.cern.ch/record/1982417/files/1-21%20Tecker.pdf

## Slide 61
Spare slides

## Slide 62
Stationary bucket in normalized coordinates
RF bucket properties become independent from accelerator parameters
Significant simplification of equations, easy to use
Exception: conservation of longitudinal phase space
Example of stationary bucket
Bucket height
Bucket area