## Slide 1
Introduction to ALBA Synchrotron
Caterina Biscari
1 October 2023

## Slide 3
ALS
SSRL
CAMD
SOLEIL
DAFNE
ELETTRA
SLS
ANKA
PETRA III
ASTRIDII
SESAME
SAGA
Synchrotron light sources in the world
IN OPERATION
IN CONSTRUCTION
SIRIUS
CLS
APS
NSLS II
CHESS
SURF
ALBA
ESRF
DIAMOND
BESSYII
MAXIV
SOLARIS
ELSA
DELTA
DELSY
KSRS
SSRC
AS
INDUS
SRLI
HELIOS2
BSRF
SSRF
TPS
NSRRC
NSRL
PLS
HISOR
SUBARU
UVSOR
NSSR
RITSSR
SPRING8
PFKEK
TSRF
HEPS
SKIF

## Slide 4
ALBA is near Barcelona,
70 km from here

## Slide 5: ALBA Synchrotron Radiation Facility
National public institution with 50% national + 50% regional funding (Ministerio de Ciencia e Innovación) and GenCat (Department de Recerca i Universitats)
National and international (28%) staff
National and international (40%) users
National and international collaborations
CELLS, the public consortium in charge of building and running the facility, was founded in 2003

## Slide 6: Synchrotron Light Source: ALBA
XAIRA
NCD-SWEET
MISTRAL
3SBAR
NOTOS
LOREA
CLAESS
CIRCE
MINERVA
BOREAS
FAXTOR
MIRAS
MSPD
XALOC

## Slide 7
The ALBA complex of accelerators
LINAC: 100 MeV
BOOSTER: 100 MeV-3 GeV, 260 m circumference, emittance = 10 nm·rad, sharing the same tunnel with the storage ring
STORAGE RING: 3 GeV, 268.8 m circumference, emittance = 4.5 nm·rad
G. Benedetti – 109 Congresso Società Italiana di Fisica – Salerno – 14 September 2023
ALBA operates at 250 mA in top-up mode

## Slide 8: ALBA storage ring – 3rd generation light source 3 GeV electrons - 270 m circumference
ALBA accelerator

## Slide 9
In operation since 2012
G. Benedetti – 109 Congresso Società Italiana di Fisica – Salerno – 14 September 2023
ALBA is delivering 5800 hour/year with a beam for users availability of ~98%

## Slide 10
The ALBA storage ring lattice
G. Benedetti – 109 Congresso Società Italiana di Fisica – Salerno – 14 September 2023
unit cell
matching cell
0
ALBA storage ring parameters | 
Energy | 3 GeV
Circumference | 269 m
Emittance | 4.5 nm·rad
Number of cells | 8 unit + 8 match
N. of straights | 4 long / 12 medium / 8 short
Straigh lengths | 7.8 / 4.2 / 2.3 m
Straight ratio | 36%

## Slide 11
ALBA photon spectra

## Slide 12: What synchrotron light sources provide to society?
XAIRA
NCD-SWEET
MISTRAL
3SBAR
NOTOS
LOREA
CLAESS
CIRCE
MINERVA
BOREAS
FAXTOR
MIRAS
MSPD
XALOC

## Slide 13: Sustainable Development Index
The Sustainable Development Index (SDI) measures the ecological efficiency of human development, recognizing that development must be achieved within planetary boundaries. It was created to update the Human Development Index (HDI) for the ecological realities of the Anthropocene.
https://www.sustainabledevelopmentindex.org/
(gapminder.org)
SDI gets higher if
Increase: life expectancy, education and income
Decrease: consumption-based CO2 emissions and material footprint

## Slide 14: ALBA acting on SDi
Health: development of drugs and vaccines,
Understanding disease mechanisms, developing bio materials, bio preparedness, food
Studying environment, contamination
Knowledge, training
cultural and historical heritage preservation
Contributing to carbon neutrality and to lowering energy consumption
Energy materials (production, storage, transport)
Non contaminant materials
Batteries
Catalisis
Green H production
Complex materials
Quantum materials
Microelectronics based in spintronics
…
Increase: life expectancy, education and income
Decrease: consumption-based CO2 emissions and material footprint
Nature Nanotechnology (2016) O. Bulle ….L. Aballe, M. Foester, …G. Gaudin , ALBA

## Slide 15: ALBA Synchrotron Research Infrastructure
Life Science
From the protein, to cell, to tissues
Chemistry and Material Science
Energy material, catalysts, environment
Electronic and Magnetic Structure of Matter
Advanced materials
Interdisciplinary and Multimodal Section
Includes contribution to JEMCA and Data science
Cell infected by covid-19
Battery developments
Nanomaterials for data storage
Four Scientific Sections
doi.org/10.1016/j.mtadv.2023.100403
DOI: 10.1002/adfm.20230035

## Slide 16: BEAMLINES at ALBA: Available today
Instruments for material science
XAIRA
NCD-SWEET
MISTRAL
3SBAR
NOTOS
LOREA
CLAESS
CIRCE
MINERVA
BOREAS
FAXTOR
MIRAS
MSPD
XALOC
TEM
Cryo-EM
Instruments for life science
Instruments for metrology

## Slide 17
Joint Electron Microscope Center at ALBA (JEMCA)
50% Funded through Catalan ERDF and 50% co-funded by different partners
Material Science - 60-300 keV Spectra (S)TEM
TEM just finished commissioning
First users now
Life science - 200 kV Glacios cryo-TEM
Cryo-EM receiving users
Overbooking Factor >2
Atomic resolution aberration corrected HAADF STEM images of one of the catalyst nanoparticles and a zoom out of the Co2FeO4 cubic spinel structure
IS21 family transposase
Journal of the American Chemical Society, 2023. DOI: 10.1021/jacs.3c06288
Nature Commun
. DOI: 0.1038/s41467-023-38071-x

## Slide 18
We participate in exploring the universe:
ALBA - European Space Agency collaboration
ATHENA Mission (2036)
Advanced Telescope for High-ENergy Astrophysics
Will study the high energy universe, including black holes
MINERVA: BL to test hundreds of mirrors to be mounted in ATHENA satellite
In commissioning. Starting operation now

## Slide 19: USERS
Joint academic and industrial
Private
Academic
Competitive and free access
Public results
Direct access covering operational costs
Results can be confidential
2 calls per year
Average overbooking factor ~2
2/3 from Spain
Publications and User visits

## Slide 20
Spanish proposals
(1598 granted over 2876)
International proposals (871 granted over 1972)
European proposals
Academic Users

## Slide 21: Industrial users – advancing in the innovation More than 75 companies, 55% from Spain, 1/3 SME, More than 500 experiments
Examples:
Improved optics for nanoelectronics manufacturing, Battery with higher energy capacity, Battery recycling, Greener concrete, Robust adhesives, Efficient products for agriculture Nanotechnology for food packaging, Drug discovery, development and validation, New polymers for biomedical applications, Biochemical Efficacy of cosmetic

## Slide 22: Industrial services and examples
  One-time services
  Long contract services (including or not personnel)
  Partnerships with other facilities/platforms to provide a complete service
BASF IMPROVING THE PRODUCTION OF BATTERIES FOR ELECTRIC VEHICLES
New methodology to produce nickel-rich cathode materials used in Li batteries optimizing the production process. Increasing throughput by a factor of 3, and the efficiency of future cathode active materials production for battery electric vehicles
HELIX BioStructrures performs first post-lockdown COVID-19 measurements at ALBA

## Slide 23
ALBA
key numbers
+450 yearly experiments
+2850 publications
+240 staff
+ 2400 yearly user visits
+ 3700 national and + 3500 international users
+2500 public experiments
+500 industrial experiments
+900
Proteins in PDB
<IF>2022 = 10

## Slide 24
Networking at International level
> 35.000 users from all EU & beyond
researchers from all research area
> 300 operating End Stations
> 5.000 publications/year
> 15 spin off companies
1.000.000 h beamtime /year
Excellence-driven access free of charge
19 facilities - 16 institutions - 10 countries
LEAPS is the largest consortium of analytical facilities world-wide and further expanding its service to an interdisciplinary European user community

## Slide 25
Evolution of Synchrotron Radiation Sources
Increase in Brilliance
Increase in Resolution Power
Increase in Coherence
Increase in Data management capacity
Representation of photon beam on sample

## Slide 26
Birth of a new generation of synchrotron light sources
The implementation of the Diffraction Limited Storage Ring concept with MBA lattices (4th generation light sources) has been spearheaded by a couple of brand-new facilities: MAX IV in Sweden (2016) and Sirius in Brazil (2020).
Afterwards, many existing 3rd generation light sources followed suit or are planning to do so.
And in particular, EBS (ESRF) has introduced the Hybrid-MBA lattice (P. Raimondi) and SLS-II (PSI) has contributed with the anti-bend cell (A. Streun), that further enhance the emittance reduction.
ESRF-EBS is in operation since 2021, SLS has just shutdown to start the installation of the new storage ring
Representation of photon beam on sample
‘60s ‘70s ‘90s ‘20s

## Slide 27
Motivation for light sources upgrades
Why electron beam emittance is so important for a synchrotron light source?
What is the limit to minimise the beam emittance?
The smaller the electron beam emittance, the higher the photon source brilliance and coherence:
Faster experiments
Higher resolution (either spatial, in time or in energy)
And more performances...
Emittance εe,x = σxσx’ is related with the brilliance and coherent fraction of the generated photon beam:
Σ’s are the convolution of electron beam and intrinsic photon size and divergence:
Brilliance and coherent fraction are maximised for small electron emittances until the diffraction limit is reached:
~100 pm·rad for diffraction limit at 1 nm (1.24 keV) ~10 pm·rad for difraction limit at 1 Å (12.4 keV)

## Slide 28
The MBA cell concept
How the emittance of a storage ring can be reduced to the diffraction limit?
Basically one has to split the bending action among as many dipoles as possible→ Multi-Bend Achromat concept (MBA) introduced in the 1990’s
Proceedings PAC 1995
Equilibrium emittance scaling law:
θ
“3rd generation”
“4th generation”
Liu Lin “Towards Diffraction Limited Storage Ring Based Light Sources”, IPAC17, Copenhagen (2017)
And eventually, high quadrupole and sextupole gradients are also needed...

## Slide 29
Low emittance implies high field gradients for quadrupoles and sextupoles
High sensitivity to errors
Small aperture magnets
Strong non-linear dynamics
Tight requirements on stability and feedback
Small dynamic aperture
Small aperture vacuum chambers
Difficult injection
Limited possibility of local pumping
High coupling impedance
Why the MBA concept took so long to be implemented?
It was not until mid 2000s that, thanks to the experience gained with 3rd generation facilities and to the availability of NEG-coated vacuum chambers for distributed pumping, the first designs of facilities taking profit of the MBA cell were developed (MAX IV design report issued on 2008)
The MBA idea to design diffraction limited light sources is from th ‘90s, but many technological challenges had to be solved to bring it to reality...

## Slide 30: ALBA II Project
Renovation of storage ring providing a brighter photon beam
New beamlines
Upgrade of existing beamlines
Upgrade of data infrastructure and services
https://www.cells.es/en/science-at-alba/alba-ii-upgrade/alba-ii-whitepaper.pdf
ALBA ALBA II

## Slide 31
Re-use existing tunnel: storage ring with same circumference 268.8 m
Keep beam energy at 3 GeV
Re-use existing injector with εxbooster = 10 nm∙rad
Re-use infrastructures as much as possible
Existing insertion device beamlines: preserve 16 cells and beamlines positions
Bending beamlines can and must be relocated
Straight sections at least 4 m long
Straight sections βx*≈ βy*≈ 1-2 m
Reduce the emittance by at least a factor 1/10
ALBA-II design

## Slide 32
The emittance from ALBA to ALBA-II
ALBA-II will reduce the emittance by a factor 1/20: from 4.5 nm·rad to 220 pm·rad
Reproduced from: R. Bartolini “Overview of ongoing 4th generation light source projects worldwide”, 7th DLSR Workshop (2021)
3rd generation
4th generation
4th generation with anti-bends

## Slide 33
Brilliance Horizontal Coherent fraction
vs. Photon Energy
100 eV 1 keV 10 keV
100 eV 1 keV 10 keV
IDs performances from ALBA to ALBA-II
Brilliance and coherent fraction will increase by more than a factor 10, especially for hard X-rays beamlines

## Slide 34
A lightweight tracking code running in GPUs
M. Carlà “UFO, a GPU code tailored toward MBA lattice optimiszation”, IPAC22
A particle accelerator code running on GPUs was fully developed at ALBA to speed up the evaluation of lots of lattices (millions...) for the optimisation of linear and non-linear optics of ALBA-II:
Run on GPUs
Use 32 bits variables instead of 64 (whenever possible)
Simplify pass-methods (whenever possible)

## Slide 35
The 6BA baseline lattice for ALBA-II
The search for the best MBA for the ALBA upgrade started in 2019 and after many studies and tests the ALBA-II baseline lattice based on a Six Bend Achromat (6BA) cell with anti-bends and distributed sextupoles has an emittance εx= 220 pm·rad
6 gradient bends 1.2 T and 15 T/m (w/o longitudinal gradient)
10 gradient anti-bends 70 T/m
6 matching quads < 100 T/m
14 sextupoles < 5000 T/m2

## Slide 36
 | ALBA
Energy | 3 GeV
Circumference | 268.8 m
Symmetry | 4-fold
Lattice | 8+8 DBA cells
Emittance | 4.5 nm·rad
Nº of cells | 8+8
# of straights | 4 / 12 /8
Straight length | 7.8 / 4.0 / 2.3m
Straight ratio | 36%
ALBA II
3 GeV
268.8 m
16-fold
16 6BA cells
220 pm·rad
16
16
4.0 m
25%
20
Main parameters of the ALBA-II lattice
Benedetti et al. “A distributed sextupoles lattice for the ALBA low emittance upgrade”, IPAC21

## Slide 37
Non-linear dynamics and injection cell
14 families of sextupoles for the unit cell (5 SH + 9 SV)
plus up to 14 + 14 individual sextupoles in the two cells modified for the injection
Dynamic aperture and energy acceptance are optimised using recipes that include genetic algorithms (NSGA2...)
Dynamic aperture optimised to ±7 mm, allowing off-axis injection
Lifetime is 5.5 hours with 100% coupling and w/o 3rd harmonic cavity.
To further increase lifetime, a 3rd harmonic RF cavity will be installed.

## Slide 38
Injection into the ALBA-II storage ring
The beam from the booster is injected off-axis through a thick and a thick septum and a multipole pulsed kicker conceived and designed at ALBA (DDK) reduces its large oscillations within the dynamic aperture.
The requirement for the ALBA-II off-axis injection scheme is at least ±6 mm of horizontal dynamic aperture
SE-THICK
SE-THIN
KI-DDK
For ALBA-II we decided from the beginning to adopt only well known and tested injection schemes.
The ALBA-II lattice is very tight, all the injection elements have to fit in a 4 metres long straight section.

## Slide 39
The ALBA-II Double Dipole Kicker
Powering all 4+4 rods, a multipole field is produced for off-axis injection.
Switching off either the inner or outer rods, a dipole field is produced.
A dipole is needed for on-axis injection during the ALBA-II commissioning.
The ALBA-II straight sections have very little room and combining two kickers in one is very useful.
powering 4 inner + 4 outer rods
switching 4 inner rods off
stored beam
injected beam
Pulsed multipole kickers were introduced at KEK in Japan in the 2000’s and furher developed at BESSY-II.
After 2020, the MAX-IV, Sirius and Soleil synchrotrons designed their own design and installed it for off-axis injection.
ALBA is now developing a novel design with a special geometry of the coils:
ceramic vacuum chamber
with grooves for 4+4 rods

## Slide 40
Magnets from ALBA to ALBA-II
arc architecture
ALBA-II
Total magnet equivalent length: 10.13 m
Compactness: 10.13/12.7 = 80%
ALBA
Total magnet equivalent length: 6.18 m
Compactness: 6.18/12.7 = 49%

## Slide 41
Prototyping the ALBAII arc
Accelerators systems being designed and built
A 7.5 M€ program funded to design, construct and test prototypes for ALBA-II

## Slide 42
Main RF high power components re-used from ALBA
Upgrade from IOT transmitters to Solid State Power Amplifiers
ALBA-II RF system
Short bunches lead to high Touschek effect and short beam lifetime, a system of 3rd harmonic cavities has been already designed and tested and will be installed in ALBA-II.
ALBA EU-HOM NC cavity
Parameter | Value | Unit
Frequency | 500 | MHz
Number of cavities | 6 | -
Voltage | 2.4 | MV
RF acceptance | 7 | %
Energy loss/ turn | 1.028 | MeV
Transmitter power (at 300 mA) | 90 | kW
Synchrotron frequency* | 2.25 | kHz
Bunch length (σ)* | 7 | ps
*w/o harmonic cavity

## Slide 43
RF 3rd harmonic active cavity
Bunch lengthening with the ALBA 3rd harmonic active prototype system was successfully tested with beam in BESSY-II storage ring in 2023.
In ALBA-II, three 3rd hamonic cavities will render more than 20 hours of lifetime
SSPA
DLLRF

## Slide 44: What ALBA II will provide
Full infrastructure to tackle the grand challenges of our time for the Spanish and European users
ALBA II combines the excellence and availability of the user program of ALBA with the development of full characterization suites for characterizing multi-lengthscale problems
TRL 4-7
Enhanced microscopy capabilities
Multimodal methodologies to address complex development tasks
High throughput capabilities and big-data connectivity for fast innovation
And optimized operando environments to optimize functional materials and devices

## Slide 45: Evolution from 3rd to 4th generation synchrotrons increase in Brilliance, flux, coherence of synchrotron light by orders of magnitude – boosted by long photon paths
FLUX

## Slide 46
New plots have been assigned to ALBA for building long BLs
ALBA II – enlarging the infrastructure

## Slide 47
Long Beamlines
Decision just taken on the first two to be built
After a process open to the whole user community for proposals and a thoughtful evaluation
CODI
BL03 Superbend
CORUS
BL08 ID source
Main building
Coherence Diffraction Imaging
will be dedicated to life science
will be dedicated to material science

## Slide 48: BEAMLINES at ALBA II (2031)
Instruments for material science
XAIRA
NCD-SWEET
MISTRAL
3SBAR
NOTOS
LOREA
CLAESS
CIRCE
MINERVA
BOREAS
FAXTOR
MIRAS
MSPD
XALOC
TEM
Cryo-EM
Instruments for life science
CORUS
CALIMA
CODI
Instruments for metrology

## Slide 49
Space for Long BL endstations and other institutions
Strategic interactions on-going with other institutions to build one institute for life science and one for material science

## Slide 50
Thanks to all ALBA team, and in particular to Gabriele Benedetti for providing most ALBA II Accelerator slides
Questions welcome
Looking forward to your visit on 5 October
We are hiring:
https://public.cells.es/jobs/#!/jobs