## Slide 1: SPS-BGI Mechanical Design Discussion ML-MME 3
INDEX
Cooling Sealing O-ring
Cooling Coupling
Feedthrough Design
RF Contacts
Parallelism Tolerances
HV Requirements
Vacuum x ML Discussion
Requests

## Slide 2: Cooling Sealing O-ring
Radiation dose:
Based on the SPS radiation report 2015-2018, comparing the measures of the BLMs along the years on LSS5 between the quadrupoles 516 and 517, the highest radiation dose is found in 2015 near QD51710 (see picture) and approximately is 1 kGy
If we consider a life expectancy of 10 years, we can assume that accumulated dose around the instrument will be 10 kGy
Requirements:
Material: Non-magnetic, radiation resistant (10 kGy)
Temperature: under 100 C
Dimension:
  Inner diameter: 24 mm
  Cordon diameter: 2 mm
Source: SPS radiation report 2015-2018

## Slide 3: Cooling Sealing O-ring
Contact:
Angst+Pfister, Switzerland: https://www.apsoparts.com/en-CH/11400601-hitecr-o-ring-epdm-70-10-02.html
Source: COMPILATION OF RADIATION DAMAGE TEST DATA – Part III: Materials used around high-energy accelerators

## Slide 4: Cooling Coupling MCB Staubli
ST number: ST1639839 / ST1639836
Bore diameter: 3 mm / 5 mm
Maximum pressure: 100 bar / 70 bar
Temperature range: - 20 ºC to + 150 ºC
Materials: SS + EPDM (seal)
Parts:
  BSP male thread socket: MCB03.1150/IC / MCB05.1151/IC
  BSP female thread plug: MCB03.7100/IC / MCB05.7101/IC
MCB05:
MCB03:

## Slide 5: Feedthrough Design
ST number: ST1641972
Considerations:
The top electrode has been modified and a elliptical pocket has been created
The spring probe was incorporated in the model as a stp file directly provided by the manufacturer (https://www.harwin.com/products/P25-4023/). Three head variants have been ordered (spherical radius, serrated and star) and will be electrically tested. A vacuum acceptance test is ongoing
The connector spring probe - feedthrough pin has been designed by ML and will be produced at CERN. Therefore, a drawing needs to be produced
Top electrode
Spring probe
Connector
Feedthrough pin

## Slide 6: Feedthrough Design
Is the pocket in the top electrode necessary? Wouldn’t it be enough if the spring probe touches the top electrode from the outside? The pocket is created to guide the spring probe and ensure a good electrical contact in a defined volume
At the moment there is only a point contact between the spring probe and the top electrode, is that good for the electrical contact and the high voltage? Yes, because even if we have a big voltage, the current is on the order of microamps.
The distance between the connector and the feedthrough is 1.3mm at the moment, is it ok? On one side, the triple junction where the sparks are created appears when we have in contact a conductor surface, an insulator surface and vacuum. In this case, Alumel (feedthrough’s pin material) and SS/ Cu are conductors, so no risk is foreseen. On the other side, the potential difference is zero in the assembly, so no gap is needed
Top electrode
Spring probe
Connector
Feedthrough pin

## Slide 7: RF Contact Fingerstock – Requirements / Contact
Fingerstock
Requirements:
Material: Non-magnetic and radiation resistant (10 kGy)
2 mm < Height < 4 mm
Contact:
EURO Technologies, Italy: https://www.euro-technologies.eu/en/product/fingerstock-contact-strips/
Cu-Be

## Slide 8: RF Contact Fingerstock – Positioning
Positioning 1 | Positioning 2
Easier to install (only hole drilling and screwing is needed) | Easier to assemble (smoothly sliding)
Slot: 1.194 mm | Slot: 11.656 mm

## Slide 9: RF Contact Fingerstock – Fixation Low Head Cap Screws
Option 1 - P0207.A4 | Option 2 – P0208.A4
h = 0.8 mm | h = 1.5 mm

## Slide 10: RF Contact Spira Shield
Requirements:
Material: Non-magnetic and radiation resistant (10 kGy)
Groove Dimension: L <= 2 mm and G <= 4 mm
Contacts:
SPIRA, California (USA): https://www.spira-emi.com/product/spira-shield/
E-SONG EMC, Seoul (Korea): https://esongemc.com/eng/page/product/m04/Spiral_Spring_Gasket.php
Is it possible to re-use the holes for the disassembly?
Spira shield Groove: support arms
M3
Spira shield Groove: bottom electrode
M5
Spira shield Groove: bottom electrode

## Slide 11: Parallelism Tolerances
250 mm
0.1 mm

## Slide 12: HV Requirements ”Rules of Thumb” from the NASA HV workshop
HV (-30 kV)
Conductor surface
Insulator surface
p.d.
General
GND
Conductor surface
Minimise surface irregularities  polished 316L SS
Radius corners and edges generously
Min. vacuum gap = 3 kV/mm  10 mm
Min. distance within insulator material = 4 kV/mm  7.5 mm
Radius corners and edges that are close to the conductor surfaces at HV
Material with high dielectric strength, low (relative) permittivity and good thermal conductivity: Al2O3, MACOR, AlN
Middle shape would give a better Standoff Voltage
Min. distance along insulator surface = 1 kV/mm  30 mm

## Slide 13: HV Requirements Triple Junctions
Definition: where a conductor, insulator and vacuum come together
Ignition points for discharges are essential to control!
Mitigations shown in the attached picture, which all work by reducing the electric field at the triple point junction

## Slide 14: Vacuum x ML Discussion
Friday 25th of November Conclusions:
  A sector valve to do fast interventions is not needed, since the sector is destined to beam instrumentation
  UHV CF are preferred
  For the gas injection, the instrument should be moved upstream
  A meeting is foreseen to discuss about the injection constraints and equipment

## Slide 15: Requests
Special roughness for the pocket created to install the 90º adaptor
Support arms thickness of 19 mm
Rounded radii of the ion trap
Rounded cap screws near HV parts
Change the aperture from 82 mm to 84 mm
Update the 3D model