## Slide 1: VUII
What is better than a telescope? .. an onion?

## Slide 2: Disclaimer
Nikhef currently has no budget for VUII
  I work 1 day a week on LHCb.
    This includes current velo support(U1)
    Student support
    Design on VUII
    So development is slow, but here are my incoherent thoughs
NEWS FLASH – NOTHING HAPPEND
So here is the same story

## Slide 3: Future of the velo?

## Slide 4
Or maybe this?

## Slide 5: Barrel with expanding size
Maybe not the best use of silicon.

## Slide 6
The nion
So good it makes you cry!
Increases the acceptance.
Curved shape should gives better Z resolution.
Optimezed used of silicon

## Slide 7
Increases the acceptance
In yellow is the old acceptance

## Slide 8
Each track has minimal 4 hits

## Slide 10
IP strecht of +/-35 mm, gives even bigger acceptance, but some tracks have only 3 hits.

## Slide 14: Some numbers
Onion
23 modules, 46 ASICs
332,1 shown length.
Upgrade I
52 modules , 624 ASICs
1026,4, 624

## Slide 15
A single set of modules:
- Design can change depending on location inside dectector
Modules can be replaced
1 set of LV/cooling connection
Multi functional support:
- 3d printed aluminium
- Hollow tubes, for cooling supply
- Low voltage supply.
- If more stiffness is required glassfiber-epoxy can be added
3d printed support gives option to create extreme layouts, like the onion shape

## Slide 17: Some materials
boron carbide - tank armor, bulletproof vests
Boron nitride - 2.1 g/cm3
Atomically thin boron nitride is one of the strongest electrically insulating materials. Monolayer boron nitride has an average Young's modulus of 0.865TPa and fracture strength of 70.5GPa, and in contrast to graphene, whose strength decreases dramatically with increased thickness, few-layer boron nitride sheets have a strength similar to that of monolayer boron nitride
And a lot more

## Slide 18
Inlet
Outlet
Cooling substrate:
0,2mm wall thickness
Light weight ceramic
Total thickness 1mm
Some selected values:
Sensor size 20x40mm
Smal section for connectors and components
Soldered sensor to cooling
Research is ongoing on fluid connection
Micro connectors
Soldering
etc

## Slide 19: Plans
Micro fluid connector developments (Jan 23)
LV as mechanical support (cooling) (feb 23)
Soldering ASIC to cooling (mar 23)
Use all to build a Timepix4 prototyp module.

## Slide 20: Micro connectors.
Some commercial ideas that can be adopted to be used for us

## Slide 21: Cooling support
3d printed aluminium
3d printed SiC
Contact ongoing with companies.
BeO (internal review on possibly using this)
Notes: https://bist.lc/shop/fittings/ultra-high-pressure-14000-psi/ultra-high-pressure-hplc-advanced-fitting-1-pack/