## Slide 1: Challenges with fast timing on large pixel matrices
  Xavier Llopart
  8th February 2023

## Slide 2: Velopix (2016)
Technology |  | TSMC 130nm – 8 metal
Pixel Size |  | 55 x 55 µm
Pixel arrangement |  | 256 x 256 (2x4 superpixels)
Sensitive area |  | 1.98 cm2
Data driven (Tracking) | Mode | Binnary (hitmap) + TOA
 | Event Packet | 30-bit
 | Max rate | 5x106 hits/mm2/s
 | Max Pix rate | ~50 KHz/pixel
TOT energy resolution |  | < 1Kev
Time resolution |  | 25ns
Readout bandwidth |  | 4x @5.12 Gbps
Minimum threshold |  | <500 e-
Cluster occupancy of whole velo when fully closed (22/10/2022)
March 2022

## Slide 3: Mapping the material in the LHCb vertex locator using secondary hadronic interactions
https://doi.org/10.1088/1748-0221/13/06/P06008

## Slide 4: Timepix4 (2019)
Technology |  |  | 65nm – 10 metal
Pixel Size |  |  | 55 x 55 µm
Pixel arrangement |  |  | 4-side buttable 512 x 448
Sensitive area |  |  | 6.94 cm2
Readout Modes | Data driven (Tracking) | Mode | TOT and TOA
 |  | Event Packet | 64-bit
 |  | Max rate | 3.58x106 hits/mm2/s
 |  | Max Pix rate | 10.8 KHz/pixel
 | Frame based (Imaging) | Mode | CRW: PC (8 or 16-bit)
 |  | Frame | Not-zero-suppressed
 |  | Max count rate | ~5 x 109 hits/mm2/s
TOT energy resolution |  |  | < 1Kev
Time resolution |  |  | 195ps bin  ~60psrms
Readout bandwidth |  |  | 16x @10.24 Gbps
Minimum threshold |  |  | <500 e-
Timepix4v0 with 4x300 µm (256x256) edgeless Si sensor (August 2020)
Analog Power @400mW/cm2
K. Heijhoff (Nikhef)
https://indico.cern.ch/event/1121147
X. Llopart et al 2022 JINST 17 C01044

## Slide 5: Towards HL-LHC in LHCb
https://indico.cern.ch/event/1140707/contributions/5067786/attachments/2536255/4365084/Gkougkousis_VERTEX22.pdf
If track time information <20psrms Primary Vertices can be reconstructed !!

## Slide 6: Initial LHCb requirements for Velopix2
Priority
Challenging!
doable

## Slide 7: Velopix2 demo chip  PicoPix
TSMC HPC+ 28nm  Provides great level of integration at the Pixel level
  Large choice of standard cell libraries included characterized at 0.8V, 0.9V and 1V
  Radiation tolerance is better than in 65nm and 130nm
  Make use of different Macro blocks being developed in the section (Serializer, DACs, ADC, IO Pads, DC-DC,…)
  TSMC 28nm is a 90% linear shrinkage process from 32nm technology
Designed as a “real” small scale prototype of the large Velopix2 to avoid to get false expectations on final design:
  Analog FE
  Local VCO
  Pixel data clustering
  Pixel readout
  SEE robust architecture
  Clock distribution using dDLL approach (as in Timepix4)
  High-speed links
  On-chip Bandgap and biasing DACs
  UVM Functional verification
Chip should be ready to be bump bonded to different sensor types:
  ACF Anisotropic Conductive Film
Slow Control protocol can be simplified  reused from Medipix4/Timepix4?
Required ASIC for future sensor developments

## Slide 8: Project manpower/Status
Direct manpower:
  CERN:
    V.Sriskaran: Analog FE + analog periphery (100%)
    X.Llopart: Project management & digital designer (50%)
    S. Esposito: Functional verification and architecture debugging (50%)
  NIKHEF:
    V.Gromov: On-pixel PLL
    C.Akgun: Sigma-delta
    A.Vitkovskiy (from summer 2023)  PCS (Physical Coding Sublayer)
  IGFAE:
    A. Fernandez: DAQ studies
  More CERN manpower (another full time digital designer) will be available by the end of the year:
    Delayed due to CHIPS support to other projects
Indirect manpower:
  Many IP blocks in TSMC 28nm being designed in the CERN R&D (Serializer, SLVS drivers/receivers, PADs…)
Current submission plans Q2/2024

## Slide 9: Radiation hardness of TSMC HPC+ 28nm
Increase of parasitic leakage in NMOS  NO ELTs
Decrease of ION in PMOS
G.Borghello
W

## Slide 10: Radiation vs corner models
Corner model simulations contain measured radiation shifts:
  NMOS: not true for VGS<~100mV
  PMOS: fits rather well
G.Borghello

## Slide 11: Summary of 28nm Radiation effects
Caused by charge trapped in the oxides
In 28nm, the source of TID-induced degradation are the STI oxides
  leakage current increase only in nMOS
  larger degradation in narrow channel devices (RINCE)
  larger degradation in long channel devices
In general  wider (W) transistors behave better under radiation
Available corner models covers expected shifts  We can ~simulate rad effects
Other important effect: temperature, bias, dose-rate, variability…
  Temperature: lower is better
  Dose-rate: being evaulated
larger in pMOS
G.Borghello

## Slide 12: PicoPix ASIC
Price for 100 chips and all options
Design time comparable to a full-scale design if targeting a “real” Velopix2 prototype
  Might be spaced limited in the periphery…
Bump-bonding with diced ASICs
Pixel Matrix
64x64 54µm
Periphery
3.456 mm
1 mm
3.456 mm
Pixel Matrix
64x64 45µm
Periphery
2.88 mm
1 mm
2.88 mm
Scenario A
Scenario B
~120 K$
~75 K$
Pixel Size | 
Drawn | Si
50 | 45
51 | 45.9
52 | 46.8
53 | 47.7
54 | 48.6
55 | 49.5
56 | 50.4
57 | 51.3
58 | 52.2
59 | 53.1
60 | 54
61.111… | 55

## Slide 13: Time resolution in tracking detectors: VELO2 case
Target resolution of <20psrms track time is required to distinguish PV
Single plane resolution of <50psrms  σ2sensor (40psrms) + σ2ASIC
σ2ASIC (30psrms) σ2analogFE + σ2conversion + σ2clock
σ2conversion   TDCbin = 40ps  11.5 psrms
σ2clock  Reference clock at pixel level < 10 psrms
σ2analogFE  <25psrms

## Slide 14: Analog FE
What are the achievable limits?
Proposed scheme

## Slide 15: Beyond Timepix4  sub-25ps time resolution?
Sensor technologies: thin planar, LGAD, 3D, CMOS …
  Radiation hardness, input capacitance, …
  Not further discussed here…
Front-end: There is a limit on time resolution that are achievable for small pixels with limited power
TDC: Distribution of reference clock with <20ps skew for large pixel arrays:
  N. Egidos et al., "20-ps Resolution Clock Distribution Network for a Fast-Timing Single-Photon Detector," in IEEE Transactions on Nuclear Science, vol. 68, no. 4, pp. 434-446, April 2021, doi: 10.1109/TNS.2021.3057581.
R.Ballabriga, The Timepix4 analog front-end design: Lessons learnt on fundamental limits to noise and time resolution in highly segmented hybrid pixel detectors https://doi.org/10.1016/j.nima.2022.167489
Timepix4
60 psrms @ Qin=10 ke- and 0.5W/cm2
20 psrms @ Qin=10 ke- and 1.5W/cm2
Slide from CERN Detector Seminar 11th February 2022

## Slide 16: Analog front-end pixel for PicoPix
Study of four different topologies by S. Emiliani:
Current comparator provides the best performances in jitter and matching.
Conventional tuning DACs use binary structure:
  Consumes large silicon area → sub-binary radix DAC
V. Sriskaran

## Slide 17: Status Analog FE island
Schematic well defined:
  4 analog channels group
  7-bit sub-binary radix Threshold DAC per pixel (28-bit/island)
  4-bit Testbit + 4-bit Maskbit:
Initial full custom layout steps indicate that the analog island should fit in a drawn 50x50 µm  45x45 µm (Si)
Analog
50 µm (drawn)
V. Sriskaran

## Slide 18: Simulated jitter at front-end output versus input capacitance
NB: 110 fF is the total pixel capacitance obtained with 3D-trench sensor.
DOI: 10.1088/1748-0221/15/09/P09029
Why not using more power per pixel to enhance the timing performances ?
Simulation using schematic view!!
37.8 µm (Si)
49.5 µm (Si)
V. Sriskaran

## Slide 19: Power drop in a 336 x 336 array of 42 µm pixels (33 µA per analog pixel)
 | Pixel A | Pixel B
VGND [mV] | 45 | 90
VGND_KRUM [mV] | 45 | 61
Peaking time [ns] | 1.71 | 2.27
IDS(MINPUT) [µA] | 17.3 | 11.9
σTOA (ps r.m.s) | 12 | 24
IKRUM [nA] | 98 | 69
ToT [ns] | 42 | 68
→ The power drop along the pixel must be minimized to avoid top-down effect!
→ Systematic IKRUM mismatch: ToT mismatch and gain mismatch!
37.8 µm (Si)
V. Sriskaran

## Slide 20: Power drop in a 336 x 336 array of 42 µm pixels (33 µA per analog pixel)
 | Pixel A | Pixel B
VGND [mV] | 8 | 14
VGND_KRUM [mV] | 8 | 14
Peaking time [ns] | 2.06 | 2.1
IDS(MINPUT) [µA] | 17.3 | 16.5
σTOA (ps r.m.s) | 9 | 11.5
IKRUM [nA] | 98 | 82.6
ToT [ns] | 42 | 49
Advantages of using TSVs:
  Improved Analog & digital power distribution → Better uniformity in pixel performances
  Improved readout bandwidth
  Minimized top-down radiation mismatch
Disadvantages:
  Post-processing required  Cost, risk,…
  Added material in the substrate
  Complex assembly due to different thermal requirements (Bump-bonding, BGA,…)
37.8 µm (Si)

## Slide 21: On-time measurements <30psrms
Distribution of the Clock Reference
On-Pixel TDC

## Slide 22: Time and Energy Measurement
Time of arrival (TOA):
  Fine TOA  measure from the rising edge of Hit to first Clock edge
  Coarse TOA  Sample a BxID transmitted across the matrix
Time over threshold (TOT):
  Measure the discriminator ON duration  Equivalent energy measurement
Reference clock distribution is critical:
Pixel to pixel skew (static) can be corrected (calibrated)
Clock jitter (dynamic) cannot be corrected
On-Pixel Time-to-Digital Converter (TDC):
40ps bin  25GHz clock bin
Low area, low power TDC
Energy measurement:
Required to correct the FE timewalk
High energy measurement resolution is required

## Slide 23: Full digital double column DLL [448 dDLL: 224 Top Matrix and 224 Bottom Matrix]
Chart: Delay code
BCspectre | 0.27757 | 0.33289 | 0.3165 | 0.37181 | 0.73063 | 0.78595 | 0.77124 | 0.82655
TCspectre | 0.40701 | 0.47999 | 0.46629 | 0.53927 | 1.102 | 1.175 | 1.1647 | 1.2376
WCspectre | 0.68415 | 0.79703 | 0.78717 | 0.90004 | 1.9021 | 2.0149 | 2.0124 | 2.1253
iWoRID 2018
X. Llopart et al 2019 JINST 14 C01024
Timepix4 ~23 mW/cm2 @40MHz clock with <100ps skew
Timepix3 ~100mW/cm2 @40MHz clock with ~1.2ns skew
Dynamic digital power consumption is distributed across the clock period
Measured in Timepix4v2
ADB
coarse
delay
section
fine
delay
section
15
15
ctrl_fine
buffer
ByPass
1
ctrl_coarse
bypass
out
in

## Slide 24: Full digital double column DLL for PicoPix
Main idea: Instead of a distributing the same control code (8-bits) for all DLL stages  tune each stage individually:
  In Timepix4 32 stations @ LSB=4-5ps  ± 128-160 ps resolution
  In Picopix @ LSB=4-5ps  ± 4-5 ps resolution
Serial protocol to communicate with the dDLL column stations:
  Broadcast command to speed-up DLL lock (as in Timepix4)
  Non-Broadcast command for fine tuning
  Bypass dDLL stations
  Delay equalization for top-down delay mismatch
Chart: Δ(measured-ideal)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
25.5 | -0.00211 | -0.004708 | -0.002441 | -0.00504 | -0.002773 | -0.005371 | -0.003104 | -0.005703 | -0.003436 | -0.006034 | -0.003767 | -0.006366 | -0.004099 | -0.006697 | -0.00443 | -0.007029
25.4 | 0.001413 | 0.001861 | 0.00231 | 0.002758 | 0.003207 | -0.0012 | -0.000752 | -0.000303 | 0.000145 | 0.000594 | 0.001042 | 0.001491 | 0.001939 | -0.002468 | -0.002019 | -0.001571
25.3 | -0.002098 | -0.003459 | 3.9e-05 | -0.001322 | -0.002683 | -0.004044 | -0.005405 | -0.006766 | -0.003268 | -0.004629 | -0.001132 | -0.002493 | -0.003854 | -0.005215 | -0.006576 | -0.007937
25.2 | -0.003005 | -0.006176 | -0.004488 | -0.0028 | -0.001112 | -0.004283 | -0.002595 | -0.005766 | -0.004078 | -0.007249 | -0.005561 | -0.003873 | -0.002185 | -0.005356 | -0.003668 | -0.006839
25.1 | -0.001005 | -0.001127 | -0.001249 | -0.001371 | -0.001493 | -0.001615 | -0.001737 | -0.001859 | -0.00198 | -0.002102 | -0.002224 | -0.002346 | -0.002468 | -0.00259 | -0.002712 | -0.002834
25 | -0.003863 | -0.005795 | -0.002868 | -0.0048 | -0.001873 | -0.003805 | -0.005737 | -0.007668 | -0.004741 | -0.006673 | -0.003746 | -0.005678 | -0.002751 | -0.004683 | -0.006615 | -0.008546
24.9 | -0.000249 | -0.00398 | -0.002863 | -0.001746 | -0.000629 | -0.004361 | -0.003244 | -0.002127 | -0.00101 | -0.004741 | -0.003624 | -0.002507 | -0.00139 | -0.005122 | -0.004005 | -0.002888
24.8 | 0.000899 | 0.000216 | 0.004382 | 0.003699 | 0.003016 | 0.002333 | 0.00165 | 0.000967 | 0.000284 | -0.000399 | 0.003767 | 0.003084 | 0.002401 | 0.001719 | 0.001036 | 0.000353
24.7 | -0.001049 | -0.003532 | -0.001166 | -0.003649 | -0.001283 | -0.003766 | -0.0014 | -0.003883 | -0.001517 | -0.004 | -0.001634 | -0.004117 | -0.001751 | -0.004234 | -0.001868 | -0.004351
24.6 | 0.001826 | 0.002392 | 0.002959 | 0.003525 | 0.004091 | -0.000146 | 0.00042 | 0.000987 | 0.001553 | 0.002119 | 0.002685 | 0.003251 | 0.003818 | -0.000419 | 0.000147 | 0.000713

## Slide 25: Column clock DLL Calibration
Column clock DLL used to distribute clock across pixel matrix with a known phase
Principal working mechanism of a DLL is that all the cells in the delay line are identical, but:
  Our columns are long (might be few cm) and we will suffer from PVT + radiation non-uniformities  Need to measure and calibrate
How to measure delay line mismatches:
  In Timepix4 we could bypass 1 delay cell at a time an relock  measure bad behavior in DLL
  @lock we store the digital locking value
  Stations with more delay when bypassed show a higher locking value
In PicoPix… we do the same:
  But since the locking precision is higher we can compensate the on-pixel clock phase errors better

## Slide 26: PicoPix example in RTL
20ns clock period
Top – down mismatch of ~90ps total added
Input clock 10ps rms jitter + 0.5ps jitter in each delay line station
Chart: Delay line station
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
Measured | 576.79 | 587.96 | 593.03 | 599.63 | 600.85 | 612.35 | 616.34 | 624.1 | 624.66 | 635.01 | 640.77 | 648.36 | 648.18 | 659.18 | 665.31 | 671.31 | 671.64 | 660.64 | 659.62 | 648.62 | 647.57 | 641.24 | 634.5 | 623.81 | 622.15 | 617.54 | 611.69 | 600.26 | 599.8 | 592.2 | 587.55 | 591.61
No mismatch | 625 | 625 | 625 | 625 | 625 | 625 | 625 | 625 | 625 | 625 | 625 | 625 | 625 | 625 | 625 | 625 | 625 | 625 | 625 | 625 | 625 | 625 | 625 | 625 | 625 | 625 | 625 | 625 | 625 | 625 | 625 | 625
Calculated | 576.945 | 586.8024 | 591.7312 | 596.6599 | 596.6599 | 606.5173 | 611.446 | 626.2322 | 621.3035 | 636.0896 | 641.0183 | 650.8758 | 645.947 | 660.7332 | 665.6619 | 670.5906 | 670.5906 | 665.6619 | 665.6619 | 650.8758 | 645.947 | 641.0183 | 641.0183 | 626.2322 | 621.3035 | 611.446 | 611.446 | 601.5886 | 601.5886 | 591.7312 | 586.8024 | 581.8737
Chart: Delay line station
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
Uncorrected | 48.21 | 85.25 | 117.22 | 142.59 | 166.74 | 179.39 | 188.05 | 188.95 | 189.29 | 179.28 | 163.51 | 140.15 | 116.97 | 82.79 | 42.48 | -3.83 | -50.47 | -86.11 | -120.73 | -144.35 | -166.92 | -183.16 | -192.66 | -191.47 | -188.62 | -181.16 | -167.85 | -143.11 | -117.91 | -85.11 | -47.66 | -14.27
Corrected | 0.15501 | -1.0025 | -2.3014 | -5.2715 | -9.4616 | -15.2943 | -20.1883 | -18.0561 | -21.4126 | -20.333 | -20.0847 | -17.5689 | -19.8019 | -18.2487 | -17.8968 | -18.6162 | -19.6655 | -14.6436 | -8.6017 | -6.3459 | -7.9689 | -8.1905 | -1.6722 | 0.74996 | -0.096578 | -6.1905 | -6.4345 | -5.1059 | -3.3173 | -3.7862 | -4.5337 | -14.27
Uncorrected:
Max-Min=381.95ps
Stdev=142.8ps
Corrected:
Max-Min=22.16ps
Stdev=7.5ps

## Slide 27: How can we extend the Timepix4 TDC to meet PicoPix requirements?
Timepix4 uses a VCO with 1 peripheral PLL that generates a Vcontrol distributed to all pixels:
  In Timepix4 1 LSB is 195ps
  1 TDC every 2x4 pixels  power/area reduction
PicoPix VCO @1.28GHz with 10 phases 78.125ps bins  22.5 psrms (!?)
How to deal with systematic effects (Column supply drops, TID, mismatch…)?
stage | Phase[0] | Phase[1] | Phase[2] | Phase[3]
0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 0
2 | 1 | 1 | 0 | 0
3 | 1 | 0 | 0 | 0
4 | 0 | 0 | 0 | 0
5 | 0 | 0 | 0 | 0
6 | 0 | 0 | 0 | 1
7 | 0 | 0 | 1 | 1
VCO Oscillation pattern

## Slide 28: Free running On-pixel DCO
Explored the idea of the on-pixel free-running DCO with event-by-event calibration:
  With 3 bits oscillation control
  Using 7T cells with extracted parasitic
Advantages:
  No control voltage distributed along the column
  Systematic effects can be suppressed
  Faster oscillation times and lower dynamic power  better time resolution
Disadvantages:
  Requires DCO calibration measurement  data bandwitdth!
Timepix4 VCO (65nm)
PicoPix DCO (28nm)
 | freq | Phases | Phase mismatch [max-min] | LSB | Area | power
Timepix4 VCO | 640 MHz | 8 | ~25% | 195ps | ~350µm2 | ~500µW
PicoPix DCO | 2-3 GHz | 10 | < 5% | 50-33ps | ~38µm2 | ~150µW
0
1
2
3
4
5
6
7
8
9

## Slide 29: Region Digital PLL
Design of a low power, low area digital PLL:
  Reference clock cleaning
  Clock multiplication 40  320 MHz
  < 10ps p-p jitter
Challenge to cope with dynamic supply (VDD/GND)
  Digital power analysis is essential to understand the limits of the circuit
V.Gromov

## Slide 30: Pixel to output data readout
On-pixel data reduction
Large readout bandwidth

## Slide 31: On pixel event processing  Data reduction
Most events are clusters of 1-4 pixels
  Readout only the largest event in a cluster  Best time (TOA) and energy (TOT) resolution
Cluster events in X and Y in a single data output packets:
  1 data packet per cluster
  Master (M) pixel found using arbitration circuitry as in Medipix4
  TOA and TOT only on Master (M) pixel
  Hitmap of pixels around Master (M)
Advanced on-pixel data filtering possible:
  Accept events only in certain TOT range
  Accept events only in certain TOA range
  Accept events only for certain hitmap range
M
M
Fundamental to filter undesired data at pixel level !!!

## Slide 32: Pixel Matrix organization: PicoPix SuperPixel
1 Analog island:
  4 FE + 4 Disc
  Threshold (5-bit) and TOT (3-bit) calibration
1 TDC:
  Discriminator inputs are OR-ed  Only 1 TDC measurement per SuperPixel
  In Timepix4 each pixel has an independent measurement  “Simpler” block for PicoPix
Arbitration:
  Finds the pixel with larger charge  Winner
  From Medipix4
  Works across SuperPixels in all directions
Hitmap:
  Finds pixel with a HIT around the Winner
  Works across SuperPixels in all directions
Packet Formatter:
  Might add local filtering: TOT, size of hitmap,…
FIFO:
  Stores data temporarily
Analog
TDC
SuperPixel
Arbitration
Hitmap
Packet Formatter
FIFO

## Slide 33: PixeMatrix organization: SuperPixelRegion and Full Columns
Contains 2xN SuperPixels:
  N is a parameter in the RTL code
  N=4  32 pixels
  N=8  64 pixels
1 dDLL station node
Pixel readout architecture
Pixel and SuperPixel configuration
Should be the macro block for array formation
M SuperPixelRegions form a full pixel column:
  M is a parameter in the RTL code
  M=16, N=4  512 pixels
SuperPixel
SuperPixel
SuperPixel
SuperPixel
SuperPixel
SuperPixel
SuperPixel
SuperPixel
dDLL + dPLL
SuperPixelGroup

## Slide 34: Event-by-event VCO calibration
Ref clock @40MHz:
  FTOA 6-bits  Max VCO freq before overflow 2.52 GHz
  Calibration could be done after event (ON-CAL):
    To measure the VCO frequency: FTOA_CAL(6) + UFTOA_STOP(5) + UFTOA_CAL(5) = 16-bits
  Pixel (cluster) busy for 3-4 clock cycles  100ns @40MHz (50ns @80MHz)

## Slide 35: Types of pixel packets
Event packet:
1 packet/event
Address+hitmap+TOA+TOT
DCO Calibration packet:
Cumulative calibration data  improved DCO measured frequency
To be sent every N events or by DAQ request
Event counter packet:
Used for threshold equalization, counting…
512 pixels/DC

## Slide 36: High Speed Links in 28nm
WP6 ASIC Roadmap
Planned submission in Q1/2023
Demonstrate:
  Electrical: correct operation of high-speed transmitter
  Optical: SiPh integration, end-to-end optical link
  Dual Channel WDM*:2 NRZ links on one fiber
S.Bieregel (CERN-ESE-ME)
https://indico.cern.ch/event/1138500/
*Wavelength Division Multiplexing

## Slide 37: Architectural Exploration
Architectural Choices will be evaluated through simulations
  Arbitration scheme
  Datapath architecture
  Hit filtering
Simulation parameters
  Hit Location PDF
    Or Montecarlo data
  Hit Energy PDF
    Or Montecarlo data
  Fifo sizes and connections
  Matrix size
  On-pixel hit arbitration scheme
  On-pixel hit filtering functions
Configurations
Random Packet Generator
Arbitration
Matrix datapath model
Periphery datapath model
Results
Address and ToT distribution
Filtered data size
Buffers saturation
Buffers saturation
Data Throughput
Parameters
Hit Probability Density Function

## Slide 38: Simulations

## Slide 39: Digital simulation environment
Full Column  M=16 SuperPixelRegions and N=4 SuperPixels
  128 TDCs
  Full dDLL + EOC controller
Noise sources modelled:
  ClkDLL jitter as random gaussian
  VCO jitter as random gaussian
  FE ENC as random Gaussian
Modified FE pixel model represent more realistically the rise-time slope  critical to extract correct timing
  Model includes analog pile-up
  Fall time is a constant slope

## Slide 40: Event simulation
Simulation:
  Events: 1000
  Qin: uniform distributed [1Ke- to 10Ke-]
  Basic charge sharing sensor model
  Clk jitter =10psrms
  DCO jitter =1psrms
  Winner takes it all enabled  Master
  DCO calibration by running average
Chart: Qin[Ke-]
Measure in cluster events with larger Qin (TOT)
TW correction using TOT
Filtering events with lower Qin (TOT)
Chart: Qin[Ke-]

## Slide 41: Timewalk correction
From the measured TOT (ns)  Qin
  Typical fit for the front-end (Krumenacher ) we need 4 parameters (Atot, Btot, Ctot and Ttot):
From Qin  TOA (ns):
  Fit need 3 parameters (Ctoa, Ttoa and Dtoa):
For the level of TOA precision required we will need a pixel-by-pixel calibration:
  On-pixel correction for Atot could be added but will increase pixel area…
c
c
Chart: Qin[ke-]

## Slide 42: How to get the <30psrms timing ?
Chart: Qin[Ke-]
Chart: Qin[Ke-]
<30psrms

## Slide 43: Other building pieces…

## Slide 44: On chip DC-DC Converter?
WP 5.2
A proposal for a 5V, 250mA fully-integrated DC-DC converter in 28nm CMOS: 5V to 0.9V converter
Great simplification of the module
Target TID 1Grad
Expected output ripple <3mV
Output current limits the power consumption but can be done if internal power is split by blocks of columns
G. Ripamonti (CERN-ESE-ME)
https://indico.cern.ch/event/1138502/

## Slide 45: Other macro blocks ….
 | Designer | Institute
Periphery |  | 
R2R Buffer | Markus (WP 5.1) | CERN
DAC (8-bit) | Markus (WP 5.1) | CERN
DAC(12-bit) Sig-Delta | Can | NIKHEF
DAC(12-bit) Pseudo | Viros/Markus | CERN
BandGap | Bergamo origin to be modified by Viros | CERN
AEOC | Viros | CERN
Monitoring ADC | Tobias (WP 5.1) | CERN
On-Pixel CC-PLL | Vladimir | NIKHEF
Periphery PLL | dPLL or from Serializer | NIKHEF/CERN
PADs |  | 
SLVS Tx/Rx | WP 5.1 | CERN
Serializer | WP 6 | CERN
DC/DC | WP 5.2 | CERN

## Slide 46: Feasibility of a <30psrms large hybrid pixel (~50 µm) ASIC
Sensor with no/very low charge sharing is required (3D) otherwise many events will not be “on-time”  Massive TOT filtering on-pixel required
Analog FE requires power  What is the minimum acceptable pixel column height? Can TSVs be used?
If events 1-4 pixel clusters  no external re-clustering required
  Try to order all packets by TOA at the periphery  to be studied…
On-pixel calibration and post-processing is required:
  On pixel: Threshold equalization (5-7 bits), event filtering,…
  On pixel region: dDLL clock reference
  External: dDLL clock reference, TOT timewalk correction
Studying many novel ideas: On-region dPLL + LDO, DACs, DC-DC on chip, serializers,…
Massive use of modern ASIC design techniques are essential Aim towards a first time good Si:
  Digital-on-top methodology
  Functional verification
  Dynamic power analysis (Voltus)

## Slide 47: Summary and Project Status
PicoPix is intended to be a “realistic” demonstrator chip for a possible future upgrade of the LHCb Velo project (LS4)
  Main requirement is to target a time resolution < 30psrms
  Other very challenging requirements (pixel size, radiation hardness, power, bandwidth,…)
Status  “exploration phase” of the specs limitations for a large 30psrms target ASIC:
  Front-end limits and optimization
  On-pixel TDC
  dDLL reference clock distribution
  On-pixel clock-cleaning PLL (Nikhef) + local LDO
  1st full column RTL exists
  Architecture readout simulations to start soon
Project organization:
  Bi-weekly design meetings have been organized
  Design team: CERN, Nikhef and IGFAE
Expected submission Q2/2024

## Slide 48: SPARE

## Slide 49: TOA resolution for a 10Ke- input [THR@1Ke-]
Chart: Event#
Chart: Event#
Running Average 16
Event-by-Event

## Slide 50: TOA resolution for a 10Ke- input [THR@1Ke-] with charge sharing
Chart: Events
Chart: TOT
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50
No Charge Sharing Qin (10Ke-) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 78 | 329 | 90 | 1 | 0 | 0 | 0 | 0 | 0 | 0
Charge Sharing no Filtering | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 5 | 6 | 22 | 32 | 26 | 31 | 36 | 27 | 17 | 24 | 13 | 16 | 18 | 16 | 14 | 18 | 13 | 10 | 12 | 11 | 11 | 8 | 8 | 10 | 6 | 7 | 10 | 8 | 13 | 13 | 31 | 8 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Charge Sharing Filtering >5Ke- | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 16 | 16 | 14 | 18 | 13 | 10 | 12 | 11 | 11 | 8 | 8 | 10 | 6 | 7 | 10 | 8 | 13 | 13 | 31 | 8 | 0 | 0 | 0 | 0 | 0 | 0 | 0
257 filtered events  TOA improved 5 psrms