## Slide 1: HTS Coating for the FCC-hh Beamscreen Status report
Sergio Calatroni on behalf of the Collaborators
19.1.2023

## Slide 2: Need for a beam screen in a p-p collider
Synchrotron radiation load:
~30 W/m/beam (@16 T) (LHC < 0.2 W/m)
~5 MW total in arcs + Image currents, + electron cloud, + …
The synchrotron radiation cannot be dumped on the cold bore at 1.9 K: considering cryo efficiency, this would require almost 5 GW of electrical power
In the LHC, the beam screen is held in the 4÷20 K interval

## Slide 3: Power consumption, vacuum and impedance
100 MW
200 MW
300 MW
From:
Ph. Lebrun
L. Tavian
V. Baglin
0
500
1000
1500
2000
2500
3000
0
50
100
150
200
Total power to refrigerator [W/m per beam]
Beam-screen temperature Tbs [K]
Tcold mass = 1.9 K (Nb3Sn magnets)
Tcold mass = 4.5 K (HTS magnets)
Multi-bunch instability growth time: 25 turns 9 turns (DQ=0.5)

## Slide 4: Impedance breakdown
Injection energy
Collision energy
P. Krkotic et al., EPL, 140 (2022) 64001
doi: 10.1209/0295-5075/acaac3

## Slide 5: Surface impedance: the key
RS Surface resistance (property of the surface)
The lower the resistivity , the higher the time  it takes for developing beam instabilities
: instabilities rise-time
: betatron tune-shift
Ib: bunch current
M: number of bunches
E: beam energy
L: bunch length
R: accelerator radius
c: speed of light
b: vacuum chamber radius
f: wakefields frequency
: electrical resistivity
 Risetime of beam instabilities
ZT Transverse impedance (property of the beam)

## Slide 6: Surface impedance: the key
: instabilities rise-time
: betatron tune-shift
Ib: bunch current
M: number of bunches
E: beam energy
L: bunch length
R: accelerator radius
c: speed of light
b: vacuum chamber radius
f: wakefields frequency
: electrical resistivity
What could be better than copper at 50 K?
High-Temperature Superconductors (HTS)
RS Surface resistance (property of the surface)
 Risetime of beam instabilities
ZT Transverse impedance (property of the beam)

## Slide 7: Choice of HTS for the FCC-hh beam screen
Nature 414, 368-377 (15 November 2001)
High-Tc superconducting materials for electric power applications
David Larbalestier, Alex Gurevich, D. Matthew Feldmann & Anatoly Polyanskii
Requirements:
HTS must operate at 50 K and 16 T
Critical field (FCC-hh dipoles):
Hc2 , Hirr >> 16T
Critical current (1m thickness):
Jc > 25 kA/cm2 (2.5x108 A/m2)
Surface resistance:
Rs better than for copper
Superconductor Science and Technology, Volume 11, Number 8
Synthesis and properties of fluorine-doped Tl(1223): bulk materials and Ag-sheathed tapes
E Bellingeri, R E Gladyshevskii, F Marti, M Dhallé and R Flükiger

## Slide 8: How to make it in practice ?
Coat the inside of the screen
with Tl-1223 films
Manufacture the screen using REBCO tapes soldered to the screen

## Slide 9: Challenges
Use HTS inside the FCC-hh beam screen with:
  Up to 16 T of magnetic field
  Surface currents up to 1 A (Jc > 2.5x108 A/m2)
  Operating temperature 40-60 K
  Surface resistance ( at frequency < 1 GHz) better than copper
Guaranteeing compatibility with the accelerator environment:
  Low outgassing
  Low Secondary Electron Yield
  Robustness to synchrotron radiation
  Negligible impact on magnetic field profile
  Reduced lifecycle impact

## Slide 10: (Oversimplified) Timeline
2015
  First ideas of using HTS for beam-impedance mitigation (first ideas from Lucio Rossi) and first evaluation of potential performance
  First public discussions of these ideas (EUCAS Lyon)
2016
  Start of the formal collaborations within the FCC-hh study
  CNR-SPIN & TU-Wien: Tl-based HTS
  ALBA – ICMAB – IFAE and UPC (Barcelona): Coated Conductors
2020
  Many results beyond expectation!
  Agreement to start the next phase of the collaboration

## Slide 11
Cu ~ 20 mm
Ag ~ 2 mm
REBCO HTS ~ 1 – 3 mm
Buffers ~ 0.2 – 1 mm
Metallic Substrate ~ 30 – 100 mm
REBCO Coated Conductors are commercially available
with different widths in Km length
Tc ≈ 91 K
Hc2 (4.2K) > 100 T
Hirr (4.2K) > 60 T
Joffre Gutierrez

## Slide 12
REBCO
T = 50 K, n = 8 GHz
T. Puig et al, Supercond. Sci. Technol. 32 (2019)
REBCO CCs have lower Rs than Cu in a broad H,T region
A. Romanov, et al. Scientific reports 10 (2020)

## Slide 13
REBCO Rs
Cu Rs
REBCO Xs
The G-R model predicts a much larger benefit from REBCO at lower operating frequencies
Gittleman-Rosenblum model prediction of Zs
A. Romanov, et al. Scientific reports 10 (2020)
Estimation of depinning frequency wp
wp
REBCO CCs have high depinning frequencies
Enables operation up to high frequencies
T = 50 K, n = 1 GHz
Gittleman-Rosenblum model predictions based on our Zs experimental data

## Slide 14
Initial study shows that CCs have a weak dependence with the RF power
P. Krkotic, et al. Supercond. Sci. Technol. 35 (2022)
T = 50 K, n = 8 GHz
FCC-hh
Opens the possibility for high-power applications:
Future high-energy or high-power linacs (SLAC collaboration), Muon collider

## Slide 15: Tl-1223, critical temperature and surface resistance
bulk sample (mixing and reacting the precursors)
“Good” phase 1223 is often mixed with 1212 phase
Alessandro Leveratto

## Slide 16: Goals for the new collaboration round (2021-2023)
Move from small-size samples to a proof-of-concept device (for Coated Conductors)
Demonstrate a scaled-up coating implementation (for Tl-HTS)
Continue and further develop the work on material characterization (transport, microstructure, RF, synchrotron radiation) fostering exchanges between the consortia.
Invest into lower frequency RF characterization and do not rely only on extrapolations
Ensuring full compatibility with the FCC-hh:
  Guarantee magnetic field quality while keeping good impedance, through striations of HTS. Simulations and experimental validation
  Assessment of correct operational temperature for a-C coating. A possible increase may result in extra power savings
  Do not forget intrinsic non-linearities of HTS, and their potential effect on the beam

## Slide 17: Annual Collaboration meeting, Rome 11.11.2022 https://indico.cern.ch/event/1170520/
Few highlights
Effect on magnetic field quality
Lowe(er) frequency measurements
Synchrotron radiation studies
Multifrequency measurements

## Slide 21
Joan O’Callaghan

## Slide 22
Montse Pont

## Slide 23
Montse Pont

## Slide 26: Follow-up from Rome plenary meeting 11.11.2022
Characterization at ~1 GHz is a fundamental need, still to be fully demonstrated
  Parallel-plate resonator being commissioned at UPC, for samples
  We need impedance testing of proof-of-concept device
  Demonstrate the appropriate frequency scaling laws, and assess creep
  Keep an eye on imaginary part
Increasing operating temperature would be very relevant for the FCC-hh
  From 50 K to 70 K (also motivated by carbon coating) allows large energy savings
  Challenging for REBCO (flux creep…)
  Tl-HTS is extremely challenging, temperature increase could be also an opportunity.
Experimental validation of magnetic field profile in striated beam screen
  Critical issue for accelerator, and may open up new beam screen designs (and active compensation of multipoles)
PSD to be assessed in collaboration with KEK
Thanks to Massimo and Roberto for helping pushing this forward

## Slide 27: Drawing of proof-of-concept beam screen
Christian Duclos

## Slide 28: Measurement of surface resistance of beam screen “Two-rods” system
Resonator with 2 fundamental modes (at same frequency)
Measurement of Q-factor of both modes makes it possible to “subtract the contribution” of the inner rods from the resistive losses
Even mode
Odd mode
Developed, ready and tested for HL-LHC beam screens (carbon coating, LESS)
Kristof Brunner

## Slide 29: Possible configurations for FCC-hh beam screen
Nikki Tagdulang

## Slide 30: HTS tape hexagonal “beam screen”

## Slide 31: Measurement of magnetic field quality
• Test in the 11 T model @ SM18
• Feather in Fresca2 rotating coil magnetic measurement
• Integration study needed
• Possibility to move up (or down) the beam screen to be investigated
The measurement precision for the multipoles is ~0.1 unit
Carlo Petrone

## Slide 32: Collaborators
CCs Consortium (12/2020-11/2023) (Kickoff meeting 1/2021)
  IFAE KE4944
  ALBA KE4945
  UPC KE4946
  CSIC-ICMAB KE4947
Tl-HTS Consortium (3/2021-2/2024) (Kickoff meeting 4/2021)
  SPIN KE5072
  TU-Vienna KE5073
  Roma Tre KE5084

## Slide 33: Budget situation
 | 2021 | 2022 | 2023 | 2024 | Totals (kEUR) | Paid (kEUR) | Open (kEUR)
CERN (this activity only, bc 11346 FCC 3.4.6 vacuum sys.) | 40 kCHF | 40 kCHF | 40 kCHF | 20 kCHF | 140 kCHF |  | 
KE4944 - HTS CC tapes (IFAE) | 60 | 50 | 50 |  | 160 | 110 | 50
KE4945 - HTS CC tapes (ALBA) | 50 | 100 | 30 |  | 180 | 150 | 30
KE4946 - HTS CC tapes (UPC) | 25 | 35 | 20 |  | 80 | 60 | 20
KE4947 - HTS CC tapes (CSIC-ICMAB) | 60 | 80 | 40 |  | 180 | 140 | 40
KE5072 - Thallium cuprate performances (CNR-SPIN) | 100 |  |  | 74 | 174 | 100 | 74
KE5073 - Thallium Based HTS coating (TUWIEN) | 60 | 60 |  | 60 | 180 | 60 | 120
KE5084 - Thallium and REBCO coated cond (UNIROMA3) | 50 | 30 |  | 11 | 91 | 50 | 41

## Slide 34
Multi-shape low impedance coatings for high energy physics applications
RF haloscope cavity for axion detection
Mushroom cavity for high accelerating gradients
Two rod system for impedance measurements