## Slide 1: ATLAS-GTU TAI Workshop
Geometry development for the visualization applications-
29.11.2022
Giorgi Mirziashvili
Georgian Technical University (GE)

## Slide 2
Simplification

## Slide 3: Simplification
A polygon is a collection of vertices, edges, and faces that define the shape of a polyhedral object in 3D computer graphics and volumetric modeling. The faces are usually triangles, quadrilaterals, or other simple convex polygons.
To visualize any geometry you need to use polygons
More polygons load the system more

## Slide 4: simplification
In order to visualize the components of the atlas detector , we use the geometry simplification

## Slide 5: simplification
In order to reduce the load on the system, we first reduce the approximation.
as shown in the figure, we reduce the accuracy of the geometry from 0.1 to 10

## Slide 6: simplification
Face: 1268
Face: 368
lowering the accuracy of the geometry gives a difference polygons of about 70.98%
polygon cannot be round. round objects are replaced by polygonal cuboid, but with a large number of these triangles, which resembles a circle

## Slide 7: simplification
but reducing the accuracy of the geometry does not always help reduce the load on the system
On the bodies we remove small holes on the geometry
Face: 860
Face: 24
this gives a difference in the number of polygons in some cases up to 98%

## Slide 8: simplification
Face: 2964
Face: 132
we also change small circles to polygons and fill empty objects
visually the difference is almost imperceptible. But the difference of polygons is about 95.5%
we simplify this way mainly such geometries as: handrails, stairs, and other small round geometries

## Slide 9: simplification
1100
36
we also combine several similar objects into one, which also gives difference about 97%

## Slide 10: simplification
we also remove small roundings that are barely visible, which also reduces the polygons
Face: 20
Face: 116

## Slide 11: simplification
Face: 479187
Face: 16464
Detailed
Simplified
Use the above methods to facilitate the geometry, we get a difference in polygons of about 97%, which significantly affects the system load
But the visual part is almost indistinguishable

## Slide 12: simplification
For today, we have simplified 83 atlas detector geometries that can be seen in Tracer