## Slide 1: WP4 Mechanics Introduction, status and plan
Corrado Gargiulo for WP4

## Slide 2: Activities
WP4.
Activity n.1 Low mass mechanics
Task-a for future Tracking Detectors
  Task-b for future Cryostats of Calorimeters and Detector Magnets
Activity n.2 Robotics
            for automated detector inspection, installation and maintainability in future HEP Experiments
Activity n.3 New Coolants
            for high-performance cooling for future detectors

## Slide 3: Low mass mechanics for tracker
4.1a | Develop ultra lightweight mechanics and cooling substrates for tracking detectors. Substrate design options: Si Chip integrated microchannel/ 3D printed microchannel/ microvascular carbon/ air cool
Year | Milestones Deliverables | 
2020 | Investigation of suitable designs supported by FE & CFD analysis and test samples - for sensor cooling substrates (Si microchannel, 3D print microchannel, Carbon vascular, Carbon foam) - for ultralight mechanical integrated support (carbon structure)  Report on identified technologies and materials for mechanics-cooling substrate | ✔
2021 | Identification of the most promising design options | ✔
2022 | Integrated mechanics-cooling substrate bases on identified design option Breadboard model (BM) prototype  microchannel (3D print, Si) Carbon vascular, Carbon foam | ✔
2023 | Engineering model (EM) non-final grade  microchannel (3D print), Carbon vascular, Carbon foam | ✔
2024 | Qualiﬁcation model (QM) final grade  AIR COOLING Carbon foam (ITS3) DEMONSTRATOR | ✔
2025 | Qualiﬁcation model (QM) final grade  Microchannel and INTERCONNECTIVITY DEMONSTRATOR | ✔
2026 | Qualiﬁcation model (QM) final grade  Ultrathin Mech & Cool for Vertex in primary Vacuum DEMONSTRATOR | ✔
2027 | Components level characterisation test campaign | ✔
2028 | System level characterisation test campaign | 
WP4.1.a
IRIS
interconnection
Ceramic Microchannels
Carbon vascular
Carbon foam radiator

## Slide 4: Low mass composite cryostats for Calorimeters and Detector Magnets
WP4.1.b
4
4.1b | Cryostats in HEP are still the purview of metals. New detectors design aims to Ultra LightWeight (ULW) cryostats for both magnets and calorimeters. Carbon Fibre Reinforced Plastic (CFRP) will be explored and compared to metal
Year | Milestones Deliverables | 
2020 | Investigate status CFRP cryo tank for aerospace LH2 and LOX.  Report | ✔
2021 | Preliminary Design of HEP CFRP cryostats and technology choices based on FEA and test  BM design EM design | ✔
2022 | Cryostat’s scaled sections prototypes (BM-EM) of specific features and interfaces (flanges, sealing, wall,..) Report on CFRP Cryostat design assessment and comparison to Al solution | ✔
2023 |  | ✔
2024 | Qualiﬁcation model (QM) final grade  1m3 CFRP DEMONSTRATOR for SC Magnet; experimental test setup | ✔
2025 | Qualiﬁcation model (QM) final grade  1m3 CFRP DEMONSTRTAOR for LAr Cal; experimental test setup | 
2026 | Qualiﬁcation model (QM) final grade  transparent Carbon bempipe ( primary-secondary vacuum) | 
2027 | Qualification Tests cryo-temp, helium leak tightness, LAr permeability, vacuum, long term | 
2028 | Design of full scale CFRP Cryostats for LAr, for SC Magnet and of beampipe | 
Wall
Carbon sandwich
ATLAS Cryostat
Low mass beampipe
Sealed flanges
Leak tight winding

## Slide 5: Robots for HEP Experiments
4.2 | New HEP detectors must be designed to be easily maintained and possibly robot friendly to maximize detector accessibility and decrease personnel exposures to hazards. Development of Interfaces (for Hands-on, Move, Match)
Year | Milestones Deliverables | 
2020 | Detector requirements for Remote handling/access ( LS3, HL, and beyond). "Best Practice Design for HEP Detector Interfaces to Robotic Systems“ Report, Best practice design | ✔
2021 | Identification of industrial solutions robotic system for detector’s remote handling and maintenance Report Identification of Cavern specific requirements (magnetic field) Principle Design Hands-on, Move, Match  BM design | ✔
2022 | Engineering Design Hands-on, Move, Match EM design Aerial-BLIMPS, Confined- Mini-QUADRUPEDS | ✔
2023 | Design Development for Aerial platform, Design Development for ground platformer, Robotic Arm and I/F | ✔
2024 | Flying robotic platform, blimps, for aerial motion in Exp cavern BLIMPS DEMONSTRATOR | 
2025 | Motion robotic platform, ground based, for motion in Exp cavern QUADRUPED DEMONSTRATOR | 
2026 | Payloads of the robotic platforms for inspection/manipulation (robotic harm) | 
2027 | Automated Vertex detectors in Primary vacuum  Retractable VERTEX Demonstrator | 
2028 | Motion/inspection robotic platforms implemented in a LHC Exp cavern | 
Collaboration with CERN-BE-CEM-MRO 1 Million Eur includes 2 FTE
MoU with University of Arizona
WP4.2

## Slide 6: New Coolants
4.3 | Environmental friendly, radiation resistant, single-phase and phase-changing coolants for new operative requirements of future detectors <-45⁰C (CO2 limit)
Year | Milestones Deliverables | 
2021 | Investigation of candidate fluids for single-phase and phase-changing applications precision measurements of thermal-fluidic properties of supercritical carbon dioxide (sCO2) | ✔
2022 | Selection of most promising fluids (synthetic and natural) for single-phase and phase-changing use of supercritical fluids at lower temperatures than subcritical carbon dioxide, in particular exploring the possible use supercritical Krypton (sKr) (<-55°C) | ✔
2023 | Understanding and modelling of thermo-fluid properties of the new (selected) natural refrigerant development of Design an innovative thermodynamic cycle capable of bringing Kr in its supercritical region starting from standard conditions while being connected to a detector without causing thermal shocks | ✔
2024 | Validate the Design of hybrid cycle with Krypton (Kr) Readiness of test rig to be used for the new coolants characterization | 
2025 | Modelling and characterization of thermo-fluid properties of skr | 
2026 | Comparative studies of CO2 and sKr cooling performances | 
2027 | Build reduced scale prototypes of the future advanced cooling systems | 
2028 | Completed irradiation campaigns on new classes of synthetic refrigerants | 
Extension program 2024-2028 postponed
due to Group commitment with CO2 planned for LS3 Upgrade.
WP4.3

## Slide 7: Shared objectives

## Slide 8: RESOURCES 2020-2024-2028
 | TRACKER |  |  |  |  |  |  |  | CRYOTANK |  |  |  |  |  |  |  | ROBOTICS |  |  |  |  |  |  |  | NEW COOLANTS |  |  |  |  |  |  | 
Year | Fell |  | Stud |  | Good & Cons |  | Long term inv |  | Fell |  | Stud |  | Good & Cons |  | Long term inv |  | Fell |  | Stud |  | Good & Cons |  | Long term inv |  | Fell |  | Stud |  | Good & Cons |  | Long term inv | 
2020 | 100 |  | 50 |  | 150 |  |  |  |  |  | 50 | xx | 25 |  | xx |  | 100 |  |  |  | 25 |  | xx |  | xx |  |  |  |  |  | xx | xx
2021 | 100 |  | 50 |  | 200 |  |  |  | 100 |  |  |  | 50 |  |  |  | 100 |  | 50 |  | 50 |  |  |  |  |  | 50 |  | 75 |  |  | 
2022 | 100 |  | 50 |  | 200 |  |  |  | 100 |  |  |  | 75 |  |  |  | 100 |  | 50 |  | 75 |  |  |  |  |  | 50 |  | 25 |  |  | 
2023 | 100 |  | 50 |  | 100 |  |  |  | 100 |  |  |  | 75 |  |  |  | 100 |  | 50 |  | 100 |  |  |  |  |  | 50 |  | 50 |  |  | 
2024 | 100 |  | 50 |  | 100 | 50 |  |  | 100 |  |  |  | 25 | 125 |  |  | 100 |  | 50 |  | 100 |  |  |  |  |  | 50 |  | 50 |  |  | 
2025 |  | 100 |  | 50 |  | 200 |  | 100 |  | 100 |  |  |  | 150 |  | 100 |  | 100 |  | 50 |  | 20 |  | 100 |  |  |  | 75 |  | 50 |  | 
2026 |  | 100 |  | 50 |  | 200 |  |  |  | 100 |  |  |  | 150 |  |  |  | 100 |  | 50 |  | 20 |  | 100 |  | 80 |  |  |  | 100 |  | 
2027 |  | 100 |  | 50 |  | 100 |  |  |  | 100 |  |  |  | 50 |  |  |  | 100 |  | 50 |  | 150 |  |  |  | 80 |  |  |  | 100 |  | 
2028 |  | 100 |  | 50 |  | 100 |  |  |  | 100 |  |  |  | 50 |  |  |  | 100 |  | 50 |  | 150 |  |  |  | 80 |  |  |  | 50 |  | 
total | 500 | 400 | 250 | 200 | 750 | 650 | 0 | 100 | 400 | 400 | 50 | 0 | 250 | 525 | 0 | 100 | 500 | 400 | 200 | 200 | 350 | 340 | 0 | 200 | 0 | 0 | 200 | 0 | 200 | 0 | 0 | 0
 |  |  |  |  |  | total | 1500 | 1350 |  |  |  |  |  | total | 700 | 1025 |  |  |  |  |  | total | 1050 | 1140 |  |  |  |  |  | total | 400 | 0
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | TOTAL |  | 3650 | 3515
WP4 Mechanics 2020-2024 3.650,00 CHF includes 6 FTE
2024-2028 3.515,00 CHF includes 6 FTE
2023-2026  1.000,00 CHF includes 2 FTE (from Directorate)

## Slide 9: EP R&D WP4 Detector Mechanics Progress report
WP3, WP8;
CERN-Cryolab – pressure tests at cryo-temperature; EP-DT Composite lab, engineer assessment, EN-MME-NN – CT laminate characterization at cryo temp
Connova – Filament winding and engineering assessment; Workshape- CFRP production
Composite Technology Development (CTD)– Toughened epoxy resin systems at cryogenics
RUAG – Engineering assessment on early stage of the project in order to scale up the production
Leichtbau Zentrum Sachsen GmbH (LZS) – Functionally integrative systematic lightweight construction in multi material design.
Institute of Lightweight Engineering and Polymer Technology (ILK) of TUDresden - Mechanical characterization of material at low temperature..
Technetics – Large metallic seals …
CARBON COMPOSITE CRYOSTAT for HEP Experiment
EP R&D fellow
Low mass mechanics for TRACKERS Massimo Angeletti, Desiree Hellenschmidt, Matheo Dias
EP R&D fellow
EP R&D fellow
EP R&D PhD student
WP1, ALICE, AIDA Innova
CERN-EP-DT-EO design/CO prod/Composite lab sample/FS cooling/TFG PV Deposition /MPT micropattern
EN-MME-MA tomography/MM material TE-VSC permebility
EPFL-CMi microfabrication, Institut Clement Ader/ UPS Toulouse- microvascular, Utrecht Uni- ITS3
Wigner Inst – CFD analysis, St. Pietersburg Uni – gas test cooling, JINR- radiation test
DiscoEurope wafer dicing, SIRRIS laser etching, ERG/ Allcomp carbon foam
Alphacam, Xjet, IKTS Fraunhofer 3d print
Detakta, Microlumen polyimide tubes…
ROBOTICS for HEP experiments
CERN-EP-DT; EO, EP-DT-DI
Petoi BITTLE – provided small quadruped robots, JJ Robot – provided blimps,
Boston Dynamics, AnyBotics – support for the use of quadruped robot in the detector cavern
University of Rome La Sapienza –robotic arm and blimps control and dynamics; University of Zurich, ETH –market survey on flying robot San Jorge Tecnologicas – Collaboration for the design of a non-magnetic blimp/quadcopter; University of Arizona: Robotic student exchange
Coppelia Sim – Support for robotic simulations
NASA, SpaceX: Robotics standard Interfaces
CERN-BE-CEM-MRO – collaboration under definition
Lorenzo Teofili
Francesco Mazzei
EP R&D fellow
EP R&D Technical Student
Maria Soledad Molina Gonzalez
Luca Bernardi (Just Joined)

## Slide 10
BACKUP

## Slide 11: Activity 3: New Coolants for future CERN infrastructure
*[11] FTDM 2022 Frascati – Hybrid cycle with Krypton for cooling of future silicon detectors in HEP – Luca Contiero – link
The temperature domain for future detectors is expected to be around -60 to -80°C [9]
Current CO2 coolant limit -45°C (around -50°C on the primary chiller side)
New environmental-friendly refrigerant
-45 °C
-35 °C
-? °C
Purpose of the research: *[11]
Volumetric Heat Transfer Coefficient (VHTC)
In a detector cooling application the choice of the coolant is twofold:
Having the best thermal performance with the smallest possible cooling pipe
Avoid an uneven temperature distribution along the silicon sensors
Length = 2 [m]; Q = 200 [W] ; Vapor quality change = 0-35%; T = -80 [°C]
Krypton  a possible option under consideration
Same pressure level of CO2, diameter expected to be in the same range
Fluid comparison [10]
Design a special hybrid cycle with Krypton (Kr)
Why?
Selection?
Starting in gas phase (room temperature) requires a special cycle
Supercritical cooldown to avoid thermal shock inside the detector
Delicate components must be cooled down slowly  at high pressure nearly vertical isothermal lines.
Oil-free machine must be used (turbocompressors)
Transcritical-subcritical cycle
 Test on supercritical Kr will be performed at NTNU
 (End 2022) design and procurement of a test rig to compare supercritical CO2 and supercritical Kr thermal performances
→collaboration with
Krypton P-h
*[10] FTDM 2019 Cornell – R&D for a colder future in HEP– B.Verlaat, P.Petagna– link
Transcritical-subcritical cycle
(Supercritical cooldown is required)
20°C