## Slide 1: Muon Collider (solenoid) Magnets Studies
Luca Bottura, F. Boattini, B. Caiffi, S. Mariotto, L. Quettier, M. Statera
on behalf of the Muons Magnets Working Group
KIT 25/1/2023

## Slide 2: Scope of the talk
The solenoid challenges for a muon collider
Technical advances
Work organization
Summary and plans
This is work in progress

## Slide 3: General guidelines
Magnets are relatively power hungry
  The main power consumption for superconducting magnets is for the cryogenic system
  The main power consumption for resistive magnets is to overcome resistive losses (active power, needs to be cooled away) and inductive voltages (reactive power, can be partly retrieved)
Magnets are relatively expensive infrastructure
  Unit cost is large due to the combination of costly materials, complex technology, large mass
  Magnets tend to pave extensively the whole accelerator complex
Seek for practical solutions to minimize capital investment (CAPEX) and operation costs (OPEX). It is unlikely that simple extrapolation of known technology will work, so we still require a large dose of innovation
Produce a credible and affordable accelerator complex design: technology is a mean, not the end of this work

## Slide 4: Magnet specifications
> 40 T, 60 mm
20 T, 200 mm
Radiation heat load ≈ 5…10 kW
Radiation dose: >> 20 MGy
NC ±1.8 T, 400 Hz, 100 mm x 30 mm
SC < 10T, ≈ 100 mm
16 T peak, 150 mm
Radiation heat load ≈ 5 W/m
Radiation dose ≈ 20…40 Mgy

## Slide 5: The solenoid challenges – 1/2
20 T, 200 mm
Radiation heat load ≈ 5…10 kW
Radiation dose: 80 MGy
Large stored energy o(1) GJ, mass o(300) tons, cost o(100) M
Considerable RT and cryogenic heat load: RT power o(1) MW
Radiation dose o(80) MGy and radiation damage o(10-2) DPA

## Slide 6: The solenoid challenges – 2/2
> 40 T, 60 mm
Total 1 km, o(1600) units of solenoid magnets up to o(20) T requires compact windings and careful cost optimization
UHF solenoids, with field beyond state-of-the-art o(40…60) T, calls for novel HTS technology

## Slide 7: Target and capture – 1/4
Attempt to reduce the mass (CAPEX) of the system, and increase operating temperature to improve cryogenic CoP (OPEX)
US-MAP 2010 design
LTS (14 T) + NC (6 T)
US-MAP 2011 design
LTS (14 T) + NC (6 T)
MuCol 2022 design
HTS (20 T, 20 K)
H.G. Kirk, PAC 2011
A. Portone, P. Testoni (F4E)
L. Bottura, A. Kohleimainen (CERN)

## Slide 8: Target and capture – 2/4
A. Portone, P. Testoni, F4E
US-MAP
Proposal
EM = 2.9 GJ
Top = 4.2 K
Mcoils = 200 tons
Mshield = 300 tons
P = 12 MW
EM = 1 GJ
Top = 10…20 K
Mcoils = 110 tons
Mshield = 196 tons
P = 1MW

## Slide 9: Target and capture – 3/4
Operating current: 58 kA
Operating field: 20 T
Operating temperature: 20 K
SOLDERED HTS STACK
COPPER FORMER
COOLING CHANNEL
COPPER SLEEVE
STAINLESS STEEL JACKET
40
25
9
M. Takayasu et al., IEEE TAS, 21 (2011) 2340
Z. S. Hartwig et al., SUST, 33 (2020) 11LT01
HTS conductor design
MIT “VIPER” conductor

## Slide 10: Target and capture – 4/4
Under study (among others)
  Magnetic configuration
  Mechanical support of coils and W-shield (195 tons)
  Integration in a cryostat
  Cooling and cryogenics
  ….
2750 tons
2750 tons
100 tons
100 tons
50 tons
50 tons
A. Kohleimainen (CERN)
A. Portone, P. Testoni, F4E

## Slide 11: Integration work – 1/2
300 mm coil gap for supports and thermal shield
Difficult access to inter-coil space
Limit operations to:
intercoil support installation,
hydraulic connection, and
thermal shield closure
Conical fitting ?
Cold support
Warm support
W-shield upport
A. Kohleimainen (CERN)

## Slide 12: Integration work – 2/2
A. Kohleimainen (CERN)
Max diameter 3.2 m
Bellows for interconnects
Vacuum loads support (70 tons)
Stray fields ?
Magnetic shielding ?

## Slide 13: Many questions still
A. Kohleimainen (CERN)
Target
Coil module
W Shield
Thermal shield
Thermal shield
Pre-compression structure
Vacuum requirements ?
Composition, cooling ?
Beam phisics OK ?
Maintenance ?
On-going discussions, feel free to participate !
e.g. 2/2/2023 https://indico.cern.ch/event/1239921/

## Slide 14: Final cooling – 1/3
Probe the limits of UHF solenoid magnets for the final cooling (performance)
Make windings compact to reduce mass (CAPEX)
I. Dixon, NHMFL
Cartoon design of 40 T, 32 mm user facility solenoid (developmental)
Cross section of
32 T, 32 mm user facility solenoid
at NHMFL
R&D test
achieved 25.4 T
At NHMFL
LTS/HTS hybrids
Images of
32.35 T, 21 mm user facility solenoid
at CAS-IEE

## Slide 15: Final cooling – 2/3
Probe the limits of UHF solenoid magnets for the final cooling (performance)
Make windings compact to reduce mass (CAPEX)
B. Song, SST
REBCO insulated coil
achieved 24.1 T
at CAS-IPP
All-HTS
R&D NI coil achieved 18 T
at PSI
J. Kosse, PSI
J.-B. Song, LNCMI
R&D NI insert coil achieved 32.5 T
at LNCMI

## Slide 16: Final cooling (40 T) – 3/3
B. Bordini, CERN
Inner Ring
Outer Ring
‘Modular’ Coil
1 % Field Homogeneity
Bore
Support Plate
‘Correction’ Coil
T. Mulder, CERN
B. Bordini, CERN
A. Dudarev, CERN
smax = 600 MPa
40 T solenoid design

## Slide 17: 6D cooling
On-axis field and field profile B(s)
Aperture and clearances
Energy deposition, radiation dose, DPA’s
Good starting point, magnet work is starting
https://indico.cern.ch/event/1147941/contributions/4851978

## Slide 18: Scope of the talk
The four main magnet challenges for a muon collider
Technical advances
A digression on HTS
Work organization
Summary and plans

## Slide 19: Tasks
The organization of the tasks overlaps with the EU MuCol study
The scope of the work in most tasks, however, extends beyond the EU proposal (e.g. target solenoid study, HTS tape procurement and measurements, test of HTS pancakes, …)
Most tasks activities also rely on advances and synergy with other projects and programs (e.g. HFM, UHF solenoid R&D, HTS fusion magnets R&D, HTS generators R&D, …)
Task 1
Technical Coordination and Integration
Task 2
Target, Capture and Cooling Magnets
Task 3
Fast Cycled Accelerator Magnets
Task 4
Collider Ring Magnets
Magnet Systems

## Slide 20: The Team and the work – 1/2
Participants
  CERN (LB, SF)
  CEA (LQ)
Activities
  Periodic meeting of the “muons magnets Working Group”
  Machine configuration (“magnet catalogue”)
  Interface to physics, radiation, vacuum, cryogenics, safety and RP
  Review of radiation hardness of superconductors and insulation systems (joint activity with radiation studies)
  Documentation and reporting
Task 1
Technical Coordination and Integration
Task 2
Target, Capture and Cooling Magnets
Task 3
Fast Cycled Accelerator Magnets
Task 4
Collider Ring Magnets
Magnet Systems

## Slide 21: The Team and the work – 2/2
Participants
  INFN (MS)
  CEA (LQ, PhD)
  CERN (AD, BB, TM, LB, AK, CA, AB)
  CNRS (XC)
  F4E (AP, PT)
  KIT (TA)
  PSI (JK)
  SOTON (YY, post-doc)
  UNIGE (CS)
  TWENTE (HTK, AK, post-doc)
Activities (≈ 12 months)
  Conductor review and specification
  Design of target and capture channel solenoids
  Design of final cooling solenoid
  Procurement and electro-mechanical characterization (UHF) of test HTS material
  Pancake model coils, engineering design, manufacturing solutions, mechanical and powering tests
Task 1
Technical Coordination and Integration
Task 2
Target, Capture and Cooling Magnets
Task 3
Fast Cycled Accelerator Magnets
Task 4
Collider Ring Magnets
Magnet Systems

## Slide 22: Muons Magnets WG
Twenty-one meetings to date, with participants from m ost collaborating institutes and universities
Since April we meet:
  to “learn” about the previous work (MAP) and advances in relevant fields,
  to discuss in an informal setting initial ideas and options, and
  in preparation of upcoming activities, in particular the EU MuCol
Site: https://indico.cern.ch/category/13958/
Mailing list: muoncollider-magnets@cern.ch

## Slide 23: Summary and Plans
The grand challenges have been identified, they represent well the envelope of design and performance issues. Work has started to see what are the limits, propose technical solutions and associated R&D
The challenges are aligned with the structure of MuCol (Tasks 7.2, 7.3 and 7.4). This simplifies the forming and coordination work with the team. We plan to continue along these lines
The interaction with the other ”specialties” has started, to discuss specifications, give and receive feedback on feasibility:
  Beam optics
  Impedance limitations
  Radiation heat loads, dose and damage
  Vacuum and cryogenics
It looks like HTS can make a huge difference towards a compact, energy efficient and sustainable collider. Priority will be devoted to this R&D