## Slide 1: EIC User Group Meeting Electronics – Status
Fernando Barbosa (JLab)
28 July 2023
Warsaw, Poland

## Slide 2: EIC Streaming Readout Architecture
Data
Configuration & Control
Power
Detector
FEB
(Front End Board)
RDO
(Readout Board)
DAM + Computing (Data Aggregation Module)
Storage
ASIC
FPGA
Power Supply System
(HV, LV, Bias)
Cooling Systems
Fiber
LVDS ~ 20-30 m*
Analog ~ 20m
Fiber
L ~ 100 m
fiber
Monitoring
BW: O(100 Tbps)
BW: O(10 Tbps)
Goal: O(100 Gbps)
FEB
FEB
RDO
Switch / Server / Link-Exchange: Readout
Switch / Server: Processing
Switch / Server: Buffer
Total
w/ Jin and Kai
Bunch Crossing ~ 10.2 ns/98.5 MHz
Event Rate ~ 2 us/500 kHz
Low occupancy.
Jitter ~ 5 ps
Front-End Electronics
DAQ
GTU
(Global Timing Unit)
*LVDS – ANSI/TIA/EIA-644A standard. Maximum cable length dependent on data rate.

## Slide 3: EIC Readout Chain
Name
Design
Function
Attributes
Adapter
Detector Specific
-HV/Bias Distribution
-HV divider
-Interconnect Routing
-Sensor Specific
-Passive
Sensor
Detector Specific
-Multi-Channel Sensor
-MAPS
-AC-LGAD
-MPGD
-MCP-PMT
-SiPM
-LAPPD
Front End Board
(FEB)
Detector Specific
-Amplification
-Shaping
-Digitization
-Zero Suppression
-Bias Control & Monitoring
-ASIC/ADC
-Discrete
-Serial Link
Readout Board
(RDO)
Few Variants
-Communication
-Aggregation
-Formatting
-Data Readout
-Config & Control
-Clock & Timing
-FPGA
-Fiber Link
Data Aggregation Module (DAM)
Common
-Computing Interface
-Aggregation
-Software Trigger
-Config & Control
-Clock & Timing
-Large FPGA
-PCIe
-Ethernet
Computing
Common
-Data Buffering and Sinking
-Calibration Support
-QA/Scalers
-Collider Feedback
-Event ID/Building
-Software Trigger
-Monitoring
-COTS
-Ethernet
Global Timing Unit (GTU)
-Interfaces to Collider, Run Control & DAM
-Config & Control
-Clock & Timing
On Detector
SMT BGA

## Slide 4: ePIC Readout Channels (w/ Project P6 updates)
Detector System | Channels | Nominal Readout Technology | eRD109 Initiatives
Si Tracking: 3 vertex layers, 3 sagitta layers, 4 backward disks, 5 forward disks | 7 m^2 32 B pixels 5,200 MAPS sensors | MAPS – ITS-3 | 
MPGD tracking: 3 layers | 100k | Strips | SALSA
Calorimeters: (in P6) Forward: LFHCAL pECAL Barrel: HCAL ECAL Backward: ECAL nHCAL | 31640 19000 1536 5760 3256 3240 | SiPM | Discrete/HGCROC
Far Forward: B0: 3 MAPS layers 1 or 2 AC-LGAD layer 2 Roman Pots 2 Off Momentum ZDC: Crystal Calorimeter 32 Silicon pad layer 4 silicon pixel layers 2 boxes scintillator | 3x20cmx20cm (300M pixel) 300k or 600k 1M (4 x 135k layers each) 650k (4 x 80k layers each) 400 11520 160k 72 | MAPS – ITS-3 AC-LGAG AC-LGAD AC-LGAD APD Si PMT/SiPM | EICROC EICROC EICROC Discrete/HGCROC HGCROC Discrete/HGCROC
Far Backward: Low Q Tagger 1 Low Q Tagger 2 2 Calorimeters | 1.3M 480k 700 | AC-LGAD AC-LGAD PMT/SiPM | EICROC EICROC Discrete/HGCROC
PID-TOF Barrel TOF CTTL Hadron Endcap TOF FTTL | 3M-50M | AC-LGAD | EICROC
PID-Cherenkov: dRICH pfRICH DIRC | 5376 69632 69362 | SiPM HRPPD HRPPD | ALCOR EICROC EICROC
Standardization of detector nomenclature?

## Slide 5: eRD109 Status
 | Detector/Technology | Discrete/ASIC | Group | Awarded
A | Calorimeter | Discrete | IUCF | April 2023
B | Calorimeter | HGCROC | ORNL | April 2023
C | dRICH | ALCOR | INFN | April 2023
D | AC-LGAD | EICROC | Omega/IN2P3 | See below
 |  | FCFD | FNAL | June 2023
 |  | Barrel L-M Serv. Hybrid | ORNL | April 2023
 |  | 3rd Party Evaluation | UCSC | Pending Legal
E | MPGD/µRWell | SALSA | CEA | May 2023
 |  |  | USP | May 2023
FY23 - Contract awards have taken much longer than expected.
IN2P3 and OMEGA have committed considerable resources to the design of the ROC ASICs to meet the EIC streaming readout needs.
 | Detector/Technology | Discrete/ASIC | Group
A | Calorimeter | Discrete | IUCF
B | Calorimeter | HGCROC | ORNL
C | dRICH | ALCOR | INFN –BO, TO
D | AC-LGAD | EICROC | Omega/IN2P3/ IJCLab/CEA/IRFU
 |  | Barrel L-M Serv. Hybrid | ORNL
 |  | High Precision Clock Dist. | BNL/Rice/UIC/ORNL
E | MPGD/µRWell | SALSA | CEA/IRFU
 |  |  | USP
FY24 – Proposed and subject to DAC review 28-31 August 2023.

## Slide 6: ePIC Readout Electronics – Present Assessment
Detector Group | Channels | AC-LGAD | SiPM/PMT | MPGD
 | MAPS | AC-LGAD, HRPPD | SiPM/PMT | MPGD
Tracking | 32 B |  |  | 100k
Calorimeters | 50M |  | 67k | 
Far Forward | 300M | 2.3M | 500 | 
Far Backward |  | 1.8M | 700 | 
PID |  | 3M-50M + 140k | 300k | 
TOTAL | 32 B | 7.1M-54M | 370k | 100k
ASIC | ITS-3 | EICROC | Discrete/COTS HGCROC3 ALCOR-EIC | SALSA
eRD109
HRPPD
EICROC and HGCROC families of ASICs have similar interfaces and follow similar developments at IN2P3/OMEGA/IRFU/IJCLab.
Commitment by IN2P3 and OMEGA narrows the ASIC field, favors convergence:

## Slide 7: ROC ASIC Developments
Triggerless, to be checked w/existing chip.
40 MHz operation from external clock with BX 98.5 MHz.
1280 Mbps @ 40 MHz.
Proposed HGCROC (based on H2GCROC3) – ePIROC?
No Change
Modify trig, mem, CLK dist.
Triggered Tests,
N. Novitzky
Proposed EICROC
Different input structure, similar interfaces as HGCROC.
A few variants possible (direct attach BGA, interposer, IC package, # Pixels) to fit detectors.
HGCROC
  1D, 72 ch.
  Cdin: 5-50 pF
  Dynamic Range: 1-10 pC
  Timing: 100-120 ps
  Power: 10-15 mW/ch
EICROC
  2D, 32x32, 1024 ch
  Cdin: 1-5 pF
  Dynamic Range: 1-50 fC
  Timing: 15-20ps
  Power: < 1 mW/ch

## Slide 8: Summary
Delays in awarding FY23 eRD109 contracts but good progress overall.
FY24 eRD109 proposals submitted by 7 July 2023, DAC review late August 2023 – contracts to coincide with FY (October 2023). This will help better align projects with funds and will allow projects to continue uninterrupted.
Gathering and refining detector requirements (ch rates, Cdin, etc.) and services to inform electronics specifications towards final implementations, ~Fall 2023 – proposal by IN2P3/OMEGA/IRFU/IJCLab.
Location/partitioning of electronics under consideration: space, power, radiation, cabling – overall performance:
Project P6 Earned Value (EVMS) tracking is expected to start in August 2023.
by Irakli M.
On-detector for dRICH