## Slide 1
HEMAC meeting #14
19/1/2023
F. Batsch, I. Karpov, H. Damerau
Beam induced power in muon RCS RF systems

## Slide 2
Bunch population 2.54x1012, Trev = 20 µs  I = 20.4 mA
Short-range induced voltage Uind = 1.1 MV
Rough limit estimate per cavity: P = 20.4 mA x 1.1 MV = 22.4 kW
Calculate power loss through loss factor k|| for each simulation step / RF station:
with bunch charge Q and bunch spacing TB = Trev
The geometry of the cavity defines all HOM, i.e. for
single-bunch cases, the short-range wakefield from K.Bane includes
the HOM power losses
As a check, the approximation for short Gaussian bunches gives
n ( for Linac norm)
HOM power for the TESLA cavity:
2
t/4st
Reminder on HOM, from Alexej, see here & paper

## Slide 3
Used parameters: RCS1, 48 RF stations, 696 cavities, 90% survival, bunch length 0.1 ns
The loss factor reaches = - 2.11 V/pC
The power loss per cavity reaches 10.4 kW!
Consistent with upper limit of 22.4 kW
and the loss using  P = 10.0 kW
(comment: this used the fundamental mode, but since short-range and
fund. mode induce the same voltage, this is ok for comparison)
Beam-induced power in RCS1:
3

## Slide 4
RCS2, 48 RF stations:
RCS3, 48 RF stations:
Beam-induced power in the other RCSs:
4
Larger power loss due to shorter bunches:
Larger ring gives smaller average power

## Slide 5
From Heiko’s presentation:
A rough estimate of the short-range power loss per cavity gives:
More under cavities under [link, p.78]
Comparison with ILC:
5
 | ILC | RCS1
Number of bunches, nb | 1312 | 1 each m+ and m-
Bunch length sz | 300 mm | 0.1 ns to 0.02 ns (5 mm)
Bunch spacing, tbs | 554 ns | Trev = 20 ms
Bunch intensity, Nb | 2 ∙ 1010 p/b | 2.5 ∙ 1012 p/b
Average beam current, Ib | 5.8 mA | 2  ~20 mA
[K. Kubo , Link]

## Slide 6
The induced power is very large, above 10 kW for RCS 1&2 per bunch -> bunch crossings?
HOM power capability limit is 3-4 kW
Without other adjustments, the wakefields scale with a², a the iris radius
A factor of 2.5 in power corresponds to √2.5 in iris radius or frequency
1.3 GHz / √2.5 = 822 MHz ?
BUT: The JLAB cryomodule (750 MHz) HOM power capability is estimated to be 20kW per cavity [ref], with 5 HOM waveguide absorbers per cavity: [R.Rimmer]
Need definition of maximal acceptable power level to keep 1.3 GHz or switch to lower frequency
Summary / Discussion:
all from [R.Rimmer]

## Slide 7
Concepts with up to 4 kW and 1.5 GHz presented: see [F.Marhauser2009, PERLE coll. Meeting 2022 ]
Summary / Discussion:
See also Shahnam’s PhD thesis

## Slide 8
Some parameter that change with the FCC-ee 5-cell cavity:
What would look different with 802 MHz cavities?
 | TESLA/ILC | FCC-
Frequency fRF [MHz] | 1300 | 801.58
Cells | 9 | 5
Active length Lactive [mm] | 1038 | 935
Cavity length Lcav [mm] | 1276 | 1291
Gradient [MV/m] | 30 (conservative) | 25
Number of cavities RCS1 | 696 | 835
Straight length RCS 1 | 2334 | 2334
Straight length with RF | 38 % | 46 %