## Slide 1: MPGD technologies 1
Micro Pattern Gaseous Detectors 1
Esther Ferrer Ribas
IRFU/CEA

## Slide 2: MPGD technologies 1
Outline
Birth of Micro Pattern Gaseous Detectors (MPGD)
Gas Electron Multipliers
Micromegas
Micro Resistive Well
Applications

## Slide 3
Birth of Micro Pattern Gaseous Detectors
In the 90’s advances in microelectronics and photolithographic technology on flexible and standard PCB substrates favored the invention
Pitch size of a few hundred microns, an order of magnitude improvement in granularity over wire chambers
First Micro Pattern Gaseous Detector (MPGD): Micro-strip Gas Counter (MSGC) Oed, 1988

## Slide 4
MSGC
Performance
Intrinsic high-rate capability (>106 Hz/mm2),
excellent spatial resolution (down to 30 μm),
multiparticle resolution (∼500 μm),
single photo-electron time resolution in the ns-range,
large sensitive area and dynamic range.
Limitations:
Destructive sparks,
time-dependent gain shifts (substrate polarization and charging up),
deterioration during sustained irradiation (“aging”),
Credit: Sauli « Gaseous Radiation Detectors »

## Slide 5
TPC
Time Projection Chamber
D. R. Nygren et al., 1974
MSGC
Micro-Strip Gas Chamber
A. Oed, 1988
GEM
Gas Electron Multiplier
F. Sauli, 1997
MWPC
Multi-Wire Proportional Chamber
G. Charpak et al., 1968
ANODE
CATHODE
CATHODE
200 µm
MICROMEGAS
MICRO-MEsh GAseous Structure
I. Giomataris et al., 1996
MPGD
Birth of MPGD

## Slide 6
Gas Electron Multiplier (GEM)

## Slide 7
GEM
A thin, metal-clad polymer foil chemically perforated by a high density of holes, typically 100/mm2
Large ΔV between the two sides of the foil creates a high field
Electrons released in the upper region, drift towards the holes acquiring enough energy to provoke ionisations
Large fraction of electrons are transferred into the lower section

## Slide 8
GEM
Full decoupling of amplification stage (GEM) and readout stage (PCB, anode)
Amplification and readout structures can be optimized independently
“Study of long-term sustained operation of gaseous detectors for the high rate environment in CMS”, Jérémie Merlin,
CERN PHD theses, https://cds.cern.ch/record/2155685/files/CERN-THESIS-2016-041.pdf

## Slide 9
Manufacturing of GEM
Details tomorrow « Manufacturing techniques » by Rui de Oliveira

## Slide 10
Performance in single GEM

## Slide 11
Influence of the holes geometry
Effective gain= Detected electrons/Primary electrons
Optimum hole diameter ~ foil thickness
Narrower holes larger fields for a fixed V but losses on the wall compensante for the higher gain
F. Sauli, NIM A 805 (2016) 2-24
Notes: Doble conical shape higher gains but slow gain increase at the start of operation
Cylindrical more stable operation but more prone to discharges at high gains

## Slide 12
Multi-GEM
S. Bachmann et al,
Nucl. Instr. and Meth. A479(2002)294
Cascade of GEM electrodes
Allows attaining higher gain with each GEM at lower voltage
Discharges disfavoured
Notes: Use of three GEM electrodes adn an anode separated by 2mm gaps.
A scheme to distributed the apropriated voltage to all electrodes
The detector gain is characterised with an Fe source.
The maximum safe operating voltage is found and then with an alpha source Radon
Amount of moisture in the gas should be kept below 50 ppm

## Slide 13
GEM Rate capability
J. Benlloch et al, IEEE NS-45(1998)234
5.9 keV X-rays:
> 2.106 mm-2

## Slide 14
GEM spatial resolution
F. Sauli, NIM A 805 (2016) 2-24
Notes: Staggered: pads in every second row are shifted by half pitch

## Slide 15
GEM family
THICKGEM/LEM
GLASSGEM
Cylindrical GEM
GEMPix: a triple GEM structure read by 50 micron pixels
F. Murtas, JINST (2014) 9 C01058
Y. Mitsuya et al., NIM A 795 (2015) 156-159
S. Bressler et al. , Progress Particle and Nuclear Physics 130 (2023) 104029
Notes: Depending on the insulator substrate kapton, pcb, or glass. You can hace standard gem, thick gem also called Large electron multiplier.
You can curve them an obtained a cylindrical GEM or if you coupled GEM electodes to a Medipix chip o Timepix you will have a GEMPIX which is an extremely pixelated structure

## Slide 16
GEM Properties
High Rate Capability  MHz/mm2 (MIP - Minimum Ionizing Particles, 2MeV cm2 /g)
High Gain Up to 105 -106
High Space Resolution <100 mm
Good Time Resolution In general few ns , sub-ns in specific configuration
Good Energy Resolution10-20% FWHM @ soft X-Ray (6 KeV)
Excellent Radiation Hardness
Good Ageing Properties
Ion Backflow Reduction  ~% level, below % in particular configurations
Large size
Low material budget
Low cost

## Slide 17
Micromegas

## Slide 18
Micromegas

## Slide 19
Manufacturing of Micromegas
I. Giomataris et al., NIM. A 560 (2006) 405-40

## Slide 20
Micromegas Gain
David Attié, “Gaseous tracking detectors for academic and societal applications”, Habilitation à diriger des recherches, Octobre 2022

## Slide 21
Micromegas spatial resolution
David Attié, “Gaseous tracking detectors for academic and societal applications”, Habilitation à diriger des recherches, Octobre 2022

## Slide 22
Micromegas rate capability
G. Puill et al., IEEE Trans Nuclear Science, 46 (1999) 6
Current increases with the flux
All curves parallel
Gain independent of the rate
No saturation is observed

## Slide 23
Microbulk
Pitch 100 µm,
Holes 30 µm
Micromesh
5 µm copper
Kapton 50 µm
Readout pads
S. Andriamonje et al. JINST 2010 5 P02001

## Slide 24
Resistive Micromegas
Resistive coating:
  Charge dispersion
  Spark protection
David Attié, HDR, October 2022
T. Alexopoulos et al., NIM 1 640 (2011) 110-118

## Slide 25
Ingrid
Mesh is directly built on the silicon pixel readout chip
High gain and small pixel size allow single electron detection
High resitive silicon oxide layer protection against discharges
M. Chefdeville et al., Nucl. Instr. Meth. Phys. Res. A 556, 490 (2006)
H. van der Graaf, Nucl. Instr. Meth. Phys. Res. A 580, 1023 (2007)

## Slide 26
TWO mechanical entities
Mesh
Readout plane
INTEGRATED:
ONE single entity
Type of mesh
30 µm
Stainless steel
1 µm
Aluminium
5 µm
Copper
Any
type
Advantages
Demontability
Large Surface
Robust
Industrial manufacturing process (PCB)
Intrinsically Flexible
Low mass
Radiopure
Excellent energy resolution
Single electron efficiency
Micromegas family
Classical
1996
Bulk
2003
Ingrid
2005
Microbulk
2006

## Slide 27
Micromegas properties
High gain ( >104)
Good energy (11% @ 6 keV) and time resolution (< 1 ns)
Good spatial resolution (~100 µm)
Reduced ion feedback < 1%
Radiation hardness (1016 p/cm2)
Fast ion collection operation at high flux
Good Ageing Properties
Large size
Low material budget
Low cost
Cope with sparks: resistive coating

## Slide 28
µ-Rwell
The µRWELL is composed of a µ-RWELL PCB + Cathode
µRWELL PCB : amplification stage coupled to the readout PCB through a resistive layer
Resistive layer: Diamond-Like-Carbon with a resistivity 20-100 MOhm/square

## Slide 29
µ-Rwell Low rate: Single resistive layer
Single resistive layer
M. Poli Lener, MPGD 2022
2D current evacuation based on a single resistive layer
Grounding around the active area
For large area: problem the path of the current depends on position=> detectot inhomogeneity
Limited rate capability < 100 kHz/cm2

## Slide 30
µ-Rwell high rate
Double resistive layer
M. Poli Lener, MPGD 2022
Silver grid
PEP (Patterning-Etching-Plating)
Very good performance
Complex manufacturing due to the double matrix of vias
Single DLC layer
DLC grounding from top by kapton etching and plating
No alignment problems
Scalable to large sizes
Good performance
2D evacuation scheme by a conductive grid (screen printed or etched)
Alignment of the conductive grid pattern with the amplification pattern difficult

## Slide 31
MPGD Applications*
*Obviously Not exhaustive

## Slide 32
GEM Implementations
COMPASS
TOTEM
KLOE-2
BONUS RADIAL TPC
Notes: COMPASS 30 x 30 cm2 with 2D readout
TOTEM TWO-ARMS FORWARD TRACKER IN CMS
Cylindrical Inner tracker for the Kloe 2 experiment
BONUS radial TPC at the CLAS experiment at JLAB

## Slide 33
GEM Implementations
ALICE TPC UPGRADE
HBD for PHENIX
LHCB
Notes: Hadron Blind detector for phenix to improve hadron rejection
Upgrade of the ALICE TPC with 4 GEM foils: Two standard pitch GEM and two with larger pitch GEM: energy resolution, ion back flow and spark rate
Triple-GEM detectors for the innermost region of the muon apparatus at the LHCb experiment

## Slide 34
Micromegas Implementations
COMPASS
CAST
NTOF
T2K
CLAS12

## Slide 35
Micromegas implementations
ATLAS-NSW
ND280 upgrade High-Angle TPCs
ACTAR-TPC
MINOS

## Slide 36
Hybrid Implementation: GEM + Micromegas

## Slide 37
Micromegas for axion solar search: CAST and BabyIAXO
Specifications for the detectors:
High detection efficiency in the RoI (0-10 keV)
Very low background < 10 keV: 10-7 c/keV/cm2/s : less than 1 event per 6 months of data taking!
   use of shielding
   radiopurity
   advanced event discrimination strategies
CAST
BabyIAXO
Abeln et al. JHEP 05 (2021) 137

## Slide 38
Micromegas for axion solar search: CAST and BabyIAXO
Standard Micromegas/Floating Mesh
Microbulk

## Slide 39
Micromegas for axion solar search: CAST and BabyIAXO
S. Aune et al., JINST 9 (2014) 9 P01001
F. Aznar et al., JCAP 12 (2015) 9 008
BabyIAXO Microbulk prototype

## Slide 40
Micromegas for axion solar search: CAST and BabyIAXO

## Slide 41
GEM TOTEM T2 Tracker (LHC)
Dedicated to diffractive and forward physics
Measurement of inelastically produced charge particles in Interaction Point 5
Each arm of the telescope 20 triple GEM
Tracking and trigger capabilities
IP5

## Slide 42
GEM TOTEM T2 Tracker (LHC)
Detector requirements
Rate capability: charge particle rates 104 p/mm2/s1
Ageing: 1 year of continuous operation 1011 p/mm2
Discharges : 10 discharges/cm2/year
Time resolution < 10 ns
Spatial resolution < 100 µm
Efficiency > 97%
Half Moon Triple GEM chamber: 40 detectors
Inner diameter 80 mm and outer diameter 300 mm.
Readout: tracking and triggering
Radial strips (accurate track’s anle): 512 strips, 400 µm pitch, 80 µm width
Pad matrix (fast trigger): 1560 pads

## Slide 43
GEM TOTEM T2 Tracker (LHC)
M.G. Bagliesi et al, Nucl. Instr. Meth. A617(2010)134

## Slide 44
Summary
MPGDs are mature technologies
MPGDs today: GEM, Micromegas and µRWell
Versatile, adaptable  wide range of applications
  « MPGD 2 » Eraldo Oliveri
  « MPGD in HEP » Paulo Iengo
  « Applications beyond HEP » Marco Cortesi
  « Applications beyond fundamental research » Jona Bortfeld
Challenging R&D
  Optical readout
  High rates/Aging
  Large areas

## Slide 45
Acknowledgements
D. Attié, F. Jeanneau, E. Oliveri, T .Papaevangelou, F. Sauli, M. Titov, M. Vandenbroucke
Thanks!

## Slide 46
F. Sauli and A. Sharma, «Micro-patern Gaseous Detectors», Ann.Rev.Nucl.Part.Sci. 49 (1999) 341-388
Y. Giomataris, “Development and prospects of the new gaseous detector Micromegas”, NIM A 419 (1998) 239-250
F. Sauli, “The gas electron multiplier (GEM): Operating principles and applications”, NIM A 805 (2016) 2-24
S. Bressler, «The Thick Gas Electron Multiplier and its derivatives: Physics, technologies and applications, Progress Particle and Nuclear Physics 130 (2023) 104029
D. Attié et al., « Current Status and Future Developments of Micromegas Detectors for Physics and Applications”, Appl.Sciences 11 (2021) 12, 5362
Gaseous Radiation Detectors, Fundamental and Applications, Fabio Sauli, Cambridfe Monographs on Particle Physics, Nuclear Physics and Cosmology, Cambridge University Press.
Further reading