## Slide 1: RFKO by Emittance Blowup in CERN Proton Synchrotron
Thomas Bass (SY-ABT-BTP, TECH)
30th January 2023

## Slide 2: Objectives
Masters project as CERN Technical Student (via Royal Holloway Uni. of London)
Studying methods of improving Slow Extraction, especially simulation methods
Specifically looking at using Emittance Blowup (e-BU) to drive radio-frequency knock-out (RFKO) slow-extraction
Emittance BU provided by transverse feedback (TFB) systems
MDs required to obtain benchmarking data for simulation work
Objectives similar to beam studies for CHIMERA, capacity to work in parallel

## Slide 3: MD Process
Using CPS MD9044_IEAST_Pb_750
  Lead+54 ions
  750 MeV Ek/nucleon at T8 east area -> equivalent to 4.535 GeV Ek Protons
  Extraction to east dump
Use Qmeter2 TFB, repeated sweeps across 1/3rd integer resonance (“chirps”)
Monitoring extracted beam at East F61 with BXSCINT
  Gas Beam Current Measurement (F61.BCGAA023)
Q=1/3
n turns
t interval
frequency
time
n measurements
time
frequency/amplitude

## Slide 4: MDs completed in 2022
MD 8923 – 1st & 3rd Nov 22 – 12h
Work completed with Eliott Johnson (SY-ABT-BTP)
First attempts at using Qmeter2 TFB to drive slow extraction
Using ions, extracting to East area dump
Established basic configuration for successful extraction
Found improvements with data acquisition methods
    BXSCAL could not provide accurate data
    BXSCINT was used instead
MD 9044 – 16th to 23rd Nov 22 – 36h
Worked with Tom Levens (SY-BI-IQ) and Gerd Kotzian (SY-RF-FB) to implement new TFB signal generator
Enabled chirps with intervals below 1ms
    Qmeter2 has a 1ms interval limitation
    New signal generator installed to create frequency modulated chirps at a sub-1ms interval
Successfully extracted beam using sub-1ms intervals
Successfully performed parameter scans to obtain transfer functions

## Slide 5: 2022 MD Results
MD 8923
Basic Method Investigation & Verification
A smaller chirp interval – at a constant chirp time – produces higher intensity, as more time is spent near resonance
Chirps between 1ms and 20ms
Spill signals from BXSCINT Gas Scintillator clearly show presence of driving interval frequency.

## Slide 6: 2022 MD Results
MD 9044
Parameter scans completed using Qmeter2
Successfully shown chirp interval effect on spill quality
Fixed-amplitude transfer function obtained

## Slide 7
New Signal Generator
Qmeter2 is limited to 1ms minimum interval
New signal generator installed to control TFB
Allows for sin-wave frequency modulated by ramp/saw wave
Frequency of ramp/saw wave = interval frequency
Implemented by Tom Levens and Gerd Kotzian with Eliott Johnson

## Slide 8: 2022 MD Results
MD 9044
Parameter scans completed using custom signal generator to achieve chirp intervals below 1ms
Successfully shown chirp interval effect on spill quality

## Slide 9: Goals for 2023
Obtain more data when Ions are available in PS
  Parameter scans over wider ranges
  Multiple repeats for higher confidence
Explore faster (sub-1ms) chirp interval
Amplitude-modulated chirp signal to improve spill quality
  Spill shape appears to change with gain
  Higher gain creates higher initial spill, then a decay; Lower gain creates a slow rise to plateau
  Need better results to quantify this, and explore amplitude modulation to achieve constant spill
All with the aim of verifying simulations of Slow Extraction with Xsuite/MAD-X
MD Requests
4.53 GeV Protons at PS to East Area
    Equivalent to 0.75 GeV Pb+54 ions
Four to eight MD slots (projected)