## Slide 1: High-intensity LHC beam study campaign in PS (Quadrupolar coupled-bunch feedback)
Jan Paszkiewicz, Ben Woolley, Heiko Damerau, Alexandre Lasheen
Injectors Performance Panel MD Days, 31 January 2023

## Slide 2: Coupled-Bunch Feedback Overview
  Dipole-mode feedback necessary for multi-bunch LHC beam.
  Quadrupole-mode feedback relevant for high intensities: good beam quality with 3.15×1011 p/b with LHC25ns beam in the PS (NB: no bunch rotation at this intensity due to large beam loading on 40 & 80 MHz cavities)
  Frequency-domain approach: one channel per frev harmonic pair: 10 channels for h=21 beam.
  4 PS One-Turn Feedback boards with 4 channels each, Finemet longitudinal kicker.
No CBFB
Dipole FB only (no 40 MHz cav.)
Dipole & quad FBs (no 40 MHz cav.)
3.15e11 p/b equiv.
Nominal
LIU baseline

## Slide 3: Internal Acquisition
Record baseband data for each channel
  ±2 kHz about each frev harmonic.
  2 modes per channel can be obtained from IQ data.
  Dipole and quadrupole mode data.
Powerful diagnostic tool
  Example shown here with dipole FB on and quadrupole FB on.
  Features such as growing instability, SPS synchro loop kick, start of splittings visible.
  Good correlation with mode spectra obtained from processing tomoscope data.
  Can observe the whole cycle for every cycle.
  Data available PPM.
Correlation between internal signal and tomo-derived data:
Dipole mode spectrum vs. time:
Quad. mode spectrum vs. time:
Quadrupole mode spectrum from processing tomoscope data:

## Slide 4: CBFB Architecture (One Module, 4 Channels)
Out
FIR
↓4
Beam
Peak filter
sin(2πfrevhint)
FIR
↓4
Feedback channels
Feedback channels
Feedback channels
Feedback channels
Comp. filter
FIR
↑4
FIR
↑4
Σ
Dipole-mode feedback
Quadrupole-mode feedback
Internal FGC
4
4
4
4
Feedback channels
Feedback channels
Feedback channels
Feedback channels
Dipole gains
Quadrupole gains
Gain scaling functions

## Slide 5
Smooth reduction of feedback gain to zero during splitting
  CB oscillations during splitting can cause bunch to bunch charge variation.
  Only abrupt stop was possible in previous iterations.
  CBFB gain can now be reduced gradually as the h=21 accelerating voltage is reduced during the splitting.
  Quadrupole feedback off.
CBFB During Splittings
CBFB gain scaling
CTime
h=21
h=42
First 2-split
Second 2-split
Boards 0,1,2
Abrupt stop at C2710:
Smooth taper to zero:

## Slide 6
Dipole feedback on h=21 after first double splitting
  Coupled-bunch modes during splittings thought to contribute to beam halo, implications on PS-SPS transfer and losses in SPS.
  Configure board 3 to stabilize h=42 beam: π-mode at h=42 corresponds to signal at h=21
Possibly extend this to second 2-split (h=84) if sufficient motivation exists.
  Might prove more challenging.
  Low impedance of Finemet at these frequencies
  Decimation to h=64 in firmware will need to be removed.
CBFB During Splittings
Chart: MHz
Finemet kicker S21 (Matthias Haase)
CBFB gain scaling
CTime
h=21
h=42
First 2-split
Second 2-split
Boards 0,1,2
Board 3
Damping of π-mode after first 2-split

## Slide 7: Next Steps
Dipole and quadrupole-mode coupled-bunch feedbacks are now operational.
  Good performance in damping longitudinal CB oscillations at high intensities.
  FESA classes and basic Inspector panel deployed, PyQt GUI in development.
  Baseband acquisition: try to find applications as a general diagnostic.
2023 MDs:
  Optimisation of feedback during splittings, determine implications on PS-SPS transfer.
  Application of CBFB before transition to MTE beam (next slide).
  Find optimal combination of dipole and quadrupole gains.
  Study higher modes (e.g. sextupole and octupole) which are seen occasionally.
  Simultaneous Finemet cavity feedback and CBFB (Requires firmware change and retuning).

## Slide 8
Dipole instabilities seen before transition in h=8 MTE beams.
Applying CBFB not attempted yet but could be set up without firmware modifications.
Input and output harmonics are programmable PPM.
  E.g. h=7 → h=1 for MTE beam, h=20 → h=1 for LHC beam.
Coupled-Bunch Instability Before Transition
Dipole oscillations in MTE beam (Mihaly Vadai)