## Slide 1
The LHC: How does it work?
Dutch Language Teacher Programme
30 November 2023
Accelerating Science and Innovation Jan Uythoven, CERN
Notes: 1

## Slide 2
How does the accelerator work?
  Magnets
  Radio Frequency
  …
Energy in the beam
The future
Compact Muon Solenoid
Cern Control Centre

## Slide 4: The LHC
Very big
Very cold
Very high energy

## Slide 5: The LHC
Two beams of trillions of protons race around the 27 km ring at 0.999999991 times the speed of light in opposite directions…
So a particle goes around the LHC 11’000 times per second !

## Slide 6: LHC tunnel
Circumference = 26.7 km
Depth = 70-140 m
Slope = 1.4 %

## Slide 7: LHC Injector Chain
7
Normal operation with protons, but every year few weeks of operation with heavy ions (Pb82+)
New Linac4 in 2020: H-
0.16
2.0

## Slide 8: Where do the Protons come from?

## Slide 9: Basic ingredients of a particle accelerator
Magnetic field to
  Bend the beam around the circle (dipole magnets)
  Keep the particles together (quadrupole magnets = lenses)
Electric field to accelerate the particles
  Very fast varying electric fields = Radio Frequency cavities

## Slide 10: Dipole Magnets
Bend the beam around the circle
Number of dipoles 1232
Dipole field at 450 GeV 0.535 T
Dipole field at 7 TeV 8.33 T
Bending radius 2803.95 m
Main Dipole Length 14.3 m
Openings (full aperture) 56 mm
I
I
I
B
SUPERCONDUCTING! Cooled with superfluid helium at 1.9 K

## Slide 11: The superconductor
Strand
Filament
Cable
Used 1200 tonnes/7600 km of cable Single cable carries current up to 12 kA
Niobium-titanium Rutherford cable

## Slide 12: More than just some coils…
12

## Slide 13: During construction: Dipoles all over

## Slide 14: In the LHC tunnel
?
?
?
?
?

## Slide 15: Beam is divergent
Many particles many initial conditions
Vertical
displacement
Many different angles
 s
Quadrupole magnet

## Slide 16: Quadrupole magnets
A quadrupole magnet will focus in one plane and de-focus in the other.
Convention: a “focusing” quadrupole focuses in the horizontal plane

## Slide 17: Alternate gradient focusing
(and similarly for the vertical plane y)
The general linear magnet lattice can be parameterized by a ‘varying spring constant’, K=K(s).
K(s) describes the distribution of focusing strength along the lattice and is periodic.
This is Hill’s equation.
s
x

## Slide 18: Squeeze
Beam 1
Beam 2
Focus beam down to very small sizes in the experiments using quadrupole magnets

## Slide 19: Accelerating the Particles
LHC: beams with an energy of 6.8 TeV
=
6 800 000 000 000 V
Tera Giga Mega kilo

## Slide 20: Radio Frequency Cavities
RF = Oscillation of field at 400 MHz (Radio Frequency)
Use the Electrical Field at each passage
4 cavities/module - 2 modules/beam - 16 MV (5.5 MV/m)
Superconducting to reduce Beam Impedance
4 Cavity RF Module

## Slide 21: Lots of bunches
25 ns = 7.5 m
In 2023 the LHC has been operation with up to 2500 bunches per beam, separated by 25 ns
Transverse size typically 1 mm

## Slide 22
12 micron
Up to 50 collisions per crossing
11’000 crossings per second
2200 bunches per beam (2016)
1 Billion Collissions Per Second  GRID

## Slide 23: Luminosity

## Slide 24: Luminosity
N | Number of particles per bunch
kb | Number of bunches
f | Revolution frequency
σ* | Beam size at interaction point
F | Reduction factor due to crossing angle
ε | Emittance
εn | Normalized emittance
β* | Beta function at IP

## Slide 25: It is all about Luminosity
2018
2023: not a record breaking year
IT.L8 leak
Ion operation

## Slide 26: Energy in the Beam
Electric Energy (RF cavity)  Kinetic energy
E-beam | 6.5 TeV = 6.5e12 eV
1 eV | 1.6e-19 Joules
Number of bunches | 2300
Number of protons per bunch | 1.3e11 protons
Energy | 311 MJoules
What would be the speed of a car to have the same kinetic energy ?

## Slide 27: Car Versus Beam
E-beam | 6.5 TeV = 6.5e12 eV
1 eV | 1.6e-19 Joules
Number of bunches | 2300 (for 2016)
Number of protons per bunch | 1.3e11 protons
Energy | 311 MJoules
Electric Energy of the beam  Kinetic energy
Mass car | 1800 kg
Kinetic energy | 306 MJoules
V | 583 m/s
V | 2100 km/h
Kinetic Energy of the car
But at the size smaller than a hair ….

## Slide 28: Don’t break the machine!
Energy per beam up to 360 MJ
British aircraft carrier at 12 knots
Thread through a very cold, very dark, very small hole...
28
28

## Slide 29: Beam dump block (TDE)
700 mm  graphite core, with graded density of 1.1 g/cm3 and 1.7 g/cm3
12 mm wall, stainless-steel welded pressure vessel, at 1.2 bar of N2
Surrounded by ~1000 tonnes of concrete/steel radiation shielding blocks
0.7 m
3.5 m
3.5 m
1.7 g/cm3
1.1 g/cm3
1.7 g/cm3
beam
29
29

## Slide 30: Quench Limit of LHC Super-Conducting Magnets
Beam
360 MJ
SC Coil: quench limit
5-30 mJ/cm3
56 mm
Nominal design at 7 TeV

## Slide 31: Collimation
beam
1.2 m
Almost 100 collimators and absorbers.
Alignment tolerances < 0.1 mm to ensure that over 99.99% of the protons are intercepted.
Primary and secondary collimators are made of reinforced graphite – robust.
31
31

## Slide 33
Beam dumps
RF
Collimation
Collimation
1720 Power converters
> 9000 magnetic elements
7568 Quench detection systems
1088 Beam position monitors
~4000 Beam loss monitors
120 tonnes of Helium, down to 1.9 K
360 MJ stored beam energy per beam
11 GJ total stored energy in magnetic systems
LHC: big, cold, high energy
Injection B2
Injection B1

## Slide 34: Machine Elements
Magnets: guidance and transverse ‘stability’
  Dipoles, Quadrupoles, Sextupoles, Octupoles
Radio Frequency – Longitudinal motion
  Acceleration
  Feedback
Injection and Beam Dumping Systems
  Fast Pulsed Magnets (‘Kicker Magnets’)
  Septum Magnets
  Beam dump block
Machine Protection
  Collimation System, other absorbers, Interlock Systems
Beam Diagnostics & Protection
  Beam Position, Beam Loss Monitors, Tune Measurement, Synchrotron Light Measurements, Beam Size Measurements
Cryogenics & Vacuum

## Slide 35: Operational cycle
Beam dump
Ramp down/precycle
Injection
Ramp
Squeeze
Collide
Stable beams
Ramp down | 35 mins
Injection | ~30 mins
Ramp | 12 mins
Squeeze | 15 mins
Collide | 5 mins
Stable beams | 0 – 30 hours
Turn around from stable beams to stable beams - 2 to 3 hours on a good day, followed by Stable Beams, average 6 hours.

## Slide 36
Luminosity
Beam intensity

## Slide 37: Magnet Training to reach 7 TeV Beam Energy
During the training after LS2 (2021) we needed 3x a sector warm-up – delay of about 3 months each time, partly in parallel
Present Operation
‘Nominal’
6.5 TeV = Operation <= 2018
6.8 TeV

## Slide 38: Magnet Training to reach 7 TeV Beam Energy
During the training after LS2 (2021) we needed 3x a sector warm-up – delay of about 3 months each time, partly in parallel
Present Operation
‘Nominal’
6.5 TeV = Operation <= 2018
6.8 TeV
6.8 TeV

## Slide 39: What’s Next ? High-Luminosity LHC
Injectors upgrade and LHC civil engineering
HL-LHC upgrade

## Slide 40
UA57
US57
UR55
UL57
UPR57
PC IT
PCs IT Trims
DFX
DSHX
DFHX
CDBs
PIC,BIS
QDS
CLIQ
Warm Diodes
DCM
Q1
Q2A
Q2B
Q3
CP
D1
OC PCs
D1 PC
Cold Diodes
OC EE
DSHM
D2 PC
D2 OC EE
Cold box
CDBs
DFM
DFHM
DQHDS
D2
Q4
Q5
Q6
Valve box
D2 OC PCs
Crab
Cavities
RF Powering
UW57
TAXN
Cooling and Ventilation
Prepare the machine for operation beyond 2025 and up to ~2041
Operation scenarios for a total integrated luminosity of 3000 fb-1
High Luminosity LHC

## Slide 41
HL-LHC: IR magnets
Final focus
quadrupole (MQXF)
Separation/recombination dipoles
Dipole correctors
Higher order correctors
New wide-aperture superconducting magnets for the interaction regions
Nb3Sn technology  Larger operational peak fields (~12 T)
Large aperture: 150 mm
  Allows for smaller beam size at the experiments
  Allows introducing tungsten shielding to protect the magnet from radiation generated by collisions
Series production in progress
Final focus quadrupoles

## Slide 42: The Future @ CERN after the HL-LHC

## Slide 43: European Strategy for Particle Physics Update 2020
“An electron-positron Higgs factory is the highest-priority next collider.”
“For the longer term, the European particle physics community has the ambition to operate a proton-proton collider at the highest achievable energy.”
“Europe, together with its international partners, should investigate the technical and financial feasibility of a future hadron collider at CERN with a centre-of-mass energy of at least 100 TeV and with an electron-positron Higgs and electroweak factory as a possible first stage.”
e+e- machine as a Higgs factory
High energy hadron collider

## Slide 44
Really going to have make the case because…

## Slide 45
FCC integrated program: inspired by LEP- LHC
FCC-ee
2020 - 2040
2045 - 2063
2070 - 2095
FCC-hh
Comprehensive long-term program maximizing physics opportunities:
Stage 1: FCC-ee (Z, W, H, ) as Higgs factory, electroweak & top factory at highest luminosities
Stage 2: FCC-hh (~100 TeV) as natural continuation at energy frontier, with ion and eh options

## Slide 46
46
PA: Experiment
PB: technical
PD: experiment
PF: technical
PG: experiment
PH: technical
PJ: experiment
PL: technical
Major achievement: optimization of the ring placement
Layout chosen out of ~100 initial variants, based on geology and
surface constraints, environment, infrastructure.
Lowest-risk baseline: 90.7 km ring, 8 surface points,
4-fold superperiodicity, possibility of 2 or 4 IPs
Whole project now adapted to this placement
Number of surface sites | 8
LSS@IP (PA, PD, PG, PJ) | 1400 m
LSS@TECH (PB, PF, PH, PL) | 2032 m
Arc length | 9.6 km
Sum of arc lengths | 76.9 m
Total length | 90.7 km
Optimized placement and layout for feasibility study

## Slide 47
Power consumption and electrical grid infrastructure
Powering concept and max power load by sub-stations:
The loads could be charged on the three sub-stations (optimum connections to existing regional HV grid):
Point D, with a new sub-station covering PB – PD – PF – PG
Point H with a new dedicated sub-station for collider RF
Point L, with a sub-station covering PJ – PL – PA
 Alternative to new sub-station at Point L is reusing the existing CERN Prevession station to PA
All options pursued with RTE
Powering concept and max. power rating of the three sub-stations compatible FCC-hh.

## Slide 48: Integration of environmental challenges in future accelerators
Future machines – full lifecycle
    Starts with choice of fundamental design and technology
    Least resource-heavy designs compatible with the long-term scientific goals
    Footprint given by full lifecycle, civil engineering, construction…
Technology – energy efficiency
  SRF, klystrons, magnets (SC, HTS, permanent) etc. etc.
  Technical infrastructure: efficiency, heat recovery…
Operations
  Source renewable power
  Dynamically follow renewable power availability
Innovative technology
    Power/energy distribution (HTS, smart grids, hydrogen…)
    Energy storage (SC magnets, hydrogen…)
Support to alternatives
    Fusion – ITER
    ADS, thorium – MYRHHA
Procurement
  Energy use considered in system design, specifications, arbitration
Very much work in progress

## Slide 49: Muon Collider
> 40 T, 60 mm
RCS
20 T, 200 mm
Radiation heat load ≈ 5…10 kW
Radiation dose: 80 MGy
NC ±1.8 T, 400 Hz 100 mm x 30 mm
SC < 10T
100 mm x 30 mm
SC dipole
NC dipole
NC dipole
SC dipole
16 T peak, 160 mm
Radiation heat load ≈ 5 W/m
Radiation dose ≈ 20…40 MGy
Luca Bottura

## Slide 50
LEGEND
FCC
Muon Collider ring
Muon Collider
LHC
CERN ExistingLHC
CLIC
CLIC
FCC
Muon Acceleration ring

## Slide 51: Compare FCC to the LHC timeline …

## Slide 52
2009
2010
2011
2012
2013
Trial/descent in the underworld
November 29, 2009
Resurrection and rebirth
March 30, 2010
First collisions at 3.5 TeV
Ascension
Apotheosis and atonement
4 July, 2012
Heroic subplot
Nobel Price and HL-LHC for years to come …

## Slide 53
Bedankt voor jullie aandacht !
Accelerating Science and Innovation
Notes: 53

## Slide 54: SPARE SLIDES

## Slide 55: CMS: heavier than the Eifel tower

## Slide 56: ATLAS: large as a building of 5 floors

## Slide 57: ALICE: very sensitive, optimised for ion collisions

## Slide 58: LHCb: asymmetric, B-physics

## Slide 59: Aim of the game
We want to deliver maximum number of collisions at the maximum beam energy for maximum physics reach
E = m c 2

## Slide 60: The Higgs field gives mass to other particles

## Slide 61: Why is the Higgs so special?

## Slide 62: Reduced Energy – the history
10th September 2008: First circulating beams – all smiles

## Slide 63: Reduced energy – the history
19th September 2008: electrical arc ruptured bus-bar interconnection during tests without beam – violent He blow-off

## Slide 64: Reduced energy – the history
Major damage over a few hundred meters. Back in operation 1 year later.

## Slide 65
2013 – 2014: Long Shutdown to repair defective connections between superconducting magnets
2015: Restart with beam energy of 6.5 TeV

## Slide 66: Next 10 years
The LHC has a long future ahead ….
Followed by many years of HL-LHC running

## Slide 67: The HL-LHC Project
New IR-quads Nb3Sn (inner triplets)
  New 11 T Nb3Sn (short) dipoles
  Collimation upgrade
  Cryogenics upgrade
  Crab Cavities
  Cold powering
  Machine protection
  …
Major intervention on more than 1.2 km of the LHC

## Slide 68
High Luminosity LHC Participants

## Slide 69
29 Countries – over 70 Institutes
Accelerator collaboration
Detector collaboration
Accelerator + Detector collaboration
CLIC Collaboration

## Slide 70: CERN: Particle Physics and Innovation
Interfacing between fundamental science and key technological developments
CERN Technologies and Innovation
Detecting particles
Accelerating particle beams
Large-scale computing (Grid)
Notes: 70

## Slide 71: Medical Application as an Example of Particle Physics Spin-off
Combining Physics, ICT, Biology and Medicine to fight cancer
Accelerating particle beams
~30’000 accelerators worldwide
~17’000 used for medicine
Hadron Therapy
Leadership in Ion Beam Therapy now in Europe and Japan
Tumour Target
Protons
light ions
>70’000 patients treated worldwide (30 facilities)
>21’000 patients treated in Europe (9 facilities)
X-ray
protons
Detecting particles
Imaging
PET Scanner
Clinical trial in Portugal for new breast imaging system (ClearPEM)
Notes: 71

## Slide 72
CERN Education Activities
Scientists at CERN
Academic Training Programme
Young Researchers
CERN School of High Energy Physics
CERN School of Computing
CERN Accelerator School
Physics Students
Summer Students
Programme
CERN Teacher Schools
International and National Programmes
Latin American School
Natal, Brazil, 2011 Arequipa, Peru, 2013
NEW:
Asia-Europe-Pacific School of High-Energy Physics
Fukuoka, Oct 2012
India, 2014
CERN School of Physics Hungary, June 2013

## Slide 73
2008
2009
2010
2011
LHC Timeline
September 10, 2008
First beams around
September 19, 2008
Disaster Accidental release of 600 MJ stored in one sector of LHC dipole magnets
August 2008
First injection test
August, 2011
2.3e33, 2.6 fb-1
1380 bunches
October 14 2010
1e32
248 bunches
November 2010
Ions
March 30, 2010
First collisions at 3.5 TeV
1380
June 28 2011
1380 bunches
November 29, 2009
Beam back
2012
18 June, 2012
6.6 fb-1
to ATLAS & CMS
6 June, 2012
6.8e33
4 July, 2012

## Slide 74
The highlight of a remarkable year 2012

## Slide 75
Nobel Prize in Physics 2013
The Nobel Prize in Physics 2013 was awarded jointly to François Englert and Peter W. Higgs "for the theoretical discovery of a mechanism that contributes to our understanding of the origin of mass of subatomic particles, and which recently was confirmed through the discovery of the predicted fundamental particle, by the ATLAS and CMS experiments at CERN's Large Hadron Collider”.

## Slide 76
The Worldwide LHC Computing Grid
Tier-1: permanent storage, re-processing,
analysis
Tier-0 (CERN): data recording, reconstruction and distribution
Tier-2: Simulation,
end-user analysis
> 2 million jobs/day
~250’000 cores
173 PB of storage
nearly 160 sites, 35 countries
10 Gb links
An International collaboration to distribute and analyse LHC data
Integrates computer centres worldwide that provide computing and storage resource into a single infrastructure accessible by all LHC physicists

## Slide 77: Verification of Dump Protection
Switch off the RF
  Debunching fills the abort gap
Dump Beam
  Loss in point 6 on absorber elements
  Some losses collimation
  Clean at experiments: factor 1 : 10 000
Dump
Collimation
Rest of the machine is clean
Measured Beam losses around the whole Machine
Image of the dumped beam
77
77

## Slide 78: Only one way to safely get rid of the beam
LHC Beam Dumping System
Extraction Kickers 2 x 15 Systems
TCDQ
TCDS
10 Dilution kickers MKB
78
78

## Slide 79: Beam dump block (TDE)
700 mm  graphite core, with graded density of 1.1 g/cm3 and 1.7 g/cm3
12 mm wall, stainless-steel welded pressure vessel, at 1.2 bar of N2
Surrounded by ~1000 tonnes of concrete/steel radiation shielding blocks
0.7 m
3.5 m
3.5 m
1.7 g/cm3
1.1 g/cm3
1.7 g/cm3
beam
79
79

## Slide 80: Extraction kicker – Abort Gap
Synchronised dump trigger
3.0 ms
particle-free
abort gap
Extraction kicker MKD deflection
LHC
Beam
Within 3 turns of dump request
80
80

## Slide 81: At every dump: Check the Extraction Kickers
3 µs ‘Abort Gap’ without beam
81
81

## Slide 82: At every dump: Check the Dump Pattern
82
82

## Slide 83: At every dump: Check the Beam Losses
83
83

## Slide 84: Protection against ‘Kicker Sweep’
Beam in the Abort Gap
Asynchronous beam dump  quench or damage
  Several failures possible (synchronisation, MKD erratic)
Precautionary measures include:
  TCDS (fixed) – 6 m long diluter protects extraction septum
  TCDQ/TCS (mobile) – 7 m long diluter kept at about 7-8 s from the beam at all times
84
84