## Slide 1
A. Bertarelli, C. Accettura, B. Bordini, A. Kolehmainen, F. Sanda
CERN
Mechanical Concepts for Final Cooling Solenoid

## Slide 2: Outline
Introduction
Analytical Calculations
Finite Element Simulations for several Mechanical Concepts
  Concept 1 – Shrink-fitted cylindrical shell
  Concept 2 – Conical shrink disk
  Concept 3 – Hybrid configuration
Mechanical Concepts Pros and Cons
What’s Next?

## Slide 3: Main Specs & Design Principles
Main Specs: 1) Bore field > 40 T 2) Aperture 50 mm; 3) magnetic field homogeneity 1 % over 0.5 m
Principles guiding this conceptual design study (based on a stationary analysis - dynamic studies to be performed at a later time)
  Non-insulated coils (protection, mechanical robustness)
  Avoid tensile radial stresses (minimize the risk of critical current degradation)
  Modular single layer pancakes (design as simple and flexible as possible)
  Use as wide as possible tapes (12 mm, to limit the number of pancakes)
  Intercept axial Lorentz forces between pancakes via support plates (minimize the pancakes mechanical interactions)
  In the ‘modular’ coils, maintain, as much as possible, the magnetic field lines parallel to the tapes (minimize axial Lorentz forces and maximize the conductor critical current) . Current per tape < 1000 A < estimated Ic (4.2 K, B⫽ 50 T)
  Radially support each coil via an outer ring that could eventually apply a precompression on the coil (limit the hoop stress and to avoid tensile radial stresses)
Introduction
Ref. B. Bordini, 1st MuC Collaboration Meeting – Oct. 2022

## Slide 4: Basic Assumptions
A high radial compression is necessary to reduce hoop stresses and prevent tensile radial stresses on the HTS coil
Mechanical concept is based on encapsulating HTS pancake coils in an external structure, generating high radial compressive stresses
Anistropic nature of HTS tape complicates stress analysis and assessment
Based on (incomplete) literature review, main assumptions for HTS tape are:
  In-plane tension limit is high ( > 700 MPa)
  Hoop tensile strain limit is ~ 0.4%
  In-plane compression limit is not known but should be higher than 100 MPa
  Radial tensile stress components to be avoided (what about 10-100 MPa limit?)
  Shear stress limit is low though not zero (> 19 MPa?)
  Given limited/unknown reliability of many of these assumptions, convenient safety margins should be adopted, particularly for shear and out-of-plane stresses
Introduction
Hideaki Maeda and Yoshinori Yanagisawa IEEE TAS, VOL. 24, NO. 3, JUNE 2014

## Slide 5: Hypotheses for Analytical Calculations
Analytical calculations of stresses and deformations performed for an inner cylinder submitted to EM forces and radial preload from an external thick cylindrical shell, linearly superposing effects of preload, EM forces (and restoration of Boundary Conditions)
Assumptions
  Axial symmetry, plain strain (i.e. infinitely long solenoid)
  Linear elasticity. Homogeneous material. Both isotropic and orthotropic cases studied.
  Ideal, uniform current distribution
Main parameters and material properties:
  Magnetic Field
  Coil Dimensions : Inner Radius Outer Radius
  Current density
  Shell Properties (Steel Outer Shell )
  HTS Tape Geometry: width 12 mm; thickness
  Wire Elastic properties from rule of mixtures with 50 µm Hastelloy, 10+10 µm Copper plating, 5 µm Silver 
  Interference (thermally induced) between Coil and Shell
Analytical Calculations

## Slide 6: Results of Analytical Calculations
Results
Radial effects
  Shrink Fitting Pressure (at cold)
  Coil Radial stresses are always compressive, both for shrink-fitting and energization
  Min coil radial stress at energization in the vicinity of Coil OD. Final pressure
  Coil Radial Displacement is always negative after shrink-fitting and becomes positive after energization

## Slide 7: Results of Analytical Calculations
Hoop Stresses
  Min coil hoop stress (ID) after shrink fitting (at cold)
  Max shell hoop stress (ID) after shrink fitting (at cold)
  Max coil hoop stress (ID) at energization (total)
  Max shell hoop stress (ID) at energization (total)
Analytical Calculations

## Slide 8: Concept 1 – Shrink-fitted Thick Cylindrical Shell
The baseline concept is based on encapsulating HTS pancake coils in a thick cylindrical shell, relying on thermally-induced shrink fitting
Linear Elastic Materials; orthotropic, homogenized HTS properties
Thermal condition
    ∆Tshell = 200 °C
Electromagnetic Forces
    Ideal Solenoid ( = 531 A/mm2)
    Real Solenoid ( = 620 A/mm2)
Finite Element Calculations

## Slide 9: Concept 1 – Hoop and Radial Stresses: Preload and Cooldown
Achievable pre-compression, due to differential heat contraction and shell pre-heating
Single and double shrink-fit shells studies (to limit high temperature on HTS)
Finite Element Calculations
20 μm of Cu (750 turns)
40 μm of Cu (600 turns)
Step 1: Hot cerclage (∆T=200°C) similar results with double layer shellwith double layer shell
Step 2: Cool-down

## Slide 10: Concept 1 – Hoop and Radial Stresses: Energization
Final stresses due to energization:
Finite Element Calculations
20 μm of Cu (750 turns)
40 μm of Cu (600 turns)
Ideal Solenoid (no support plate)
Real Solenoid maximum strain 0.33%

## Slide 11: Concept 2 – Conical shrink disk
Alternative concept is based on a pair of adjustable shrink-discs with conical surfaces
Thicker coils packs can be assembled (up to 8 x 12 mm coils)
Finite Element Calculations
Symmetry Plane (XZ)
High Strength Inconel 718 Disk and Wedge
16 x M16x1.5 High Strength Bolts (not shown)
2 x 4 HTS Coils (12 mm tape)
Stainless Steel Spacers (2 mm)
OFS Copper Sheath (2 mm) (elastic-plastic behaviour)

## Slide 12: Concept 2 – Conical shrink disk: Geometry
Finite Element Calculations
Main Dimensions
Coil ID 60 mm
Coil OD 180 mm
Disc OD 500 mm
Coil Pack Height 112 mm

## Slide 13: Concept 2 – Conical shrink disk: Boundary Conditions
Results
615 A/mm2 Uniform Current Density (24.1 N/mm3 Peak Force)
Imposed Displacement: 5 mm

## Slide 14: Concept 2 – Conical shrink disk: Hoop Stresses and Strains
2 Load Steps:
  Shrink Disk displacement (5 mm)
  Energization
Max. Hoop Stress (after energization): 620.4 MPa
Max. Hoop Strain (after energization): 0.344 %
Finite Element Calculations

## Slide 15: Concept 2 – Conical shrink disk: Shear Stresses
Shear Stresses globally lower than 15 MPa
However, locally they can reach after energization ~ MPa
Finite Element Calculations

## Slide 16: Concept 3 – Hybrid Solution (Shell and Shrink Disk)
To limit shear stresses, an intermediate steel shell is added (ID 184 mm; OD 224 mm)
~ 150 µm interference with coil pack created by differential heating
3 Load Steps: 1. Shell/Coil Interference; 2. Shrink Disk Displacement (2.2 mm); 3. Energization
Finite Element Calculations
Stainless Steel Intermediate Shell (2 mm)

## Slide 17: Concept 3 – Hybrid Solution: Hoop Stresses and Strains
Min. Hoop Stress after shrinking: -426 MPa
Max. Hoop Stress after energization: 598 MPa
Max. Hoop Strain after energization: 0.332 %
Finite Element Calculations

## Slide 18: Concept 2 – Conical shrink disk: Shear Stresses
Local peak shear stress ~ 10 MPa
Max Shear after energization MPa
Finite Element Calculations

## Slide 19: Mechanical Concepts Pros and Cons
Concept 1 - Pros
  Simple
  Limit shear stresses
Concept 1 - Cons
  Requires tight tolerances (~ 2 MPa/µm)
  Cannot be adjusted
  Several coaxial shells necessary to limit Tmax on Coil (if overheating is applied)
Concept 2 – Pros
  Easily adjustable
  Tolerances less critical
  Thicker coil packs can be assembled (up to 8 × 12 mm coils)
Concept 2 – Cons
  High shear stresses locally induced
  Requires control of friction coefficient between conical surfaces  if lubrication not admissible, hard coatings likely required
Concept 3 – Pros
  As concept 2 with limited shear stresses
Concept 3 – Cons
  Somehow similar to concept one, though lower temperatures and less tight tolerances are required (thanks to adjustment)
Proposal

## Slide 20: What’s next?
Further design optimization necessary, particularly to limit shear stresses
For concepts 2 and 3, key to limit friction coefficient on sliding surfaces (0.1 assumed): R&D on hard coatings to be launched
Reliability/applicability of admissible limits found in literature to be confirmed
Necessary to characterize mechanical properties of representative coil samples to validate this concept  a compressive jig with controlled compressive force is proposed to test pancake coil (customized design based on Shrink Disc concept) at EN-MME Mechanical Measurement Lab
Proposal

## Slide 21
Thanks for your attention

## Slide 22: Magnetic Field with Double Symmetry BC (Long Solenoid)
Finite Element Calculations