## Slide 1
YETS 2022-2023
LHC Beam vacuum activities
Cesar Vazquez Pelaez
on behalf of TE/VSC/BVO
04.07.2023

## Slide 2
Outline
LHC vacuum system
YETS Framework
3. Activity overview
HL-LHC
General activities
4. Summary
4th July 2023

## Slide 3
LHC vacuum system
RF accelerating cavities (P4)
Transfers lines (TI2, TI8)
4 main experiments
2 DUMP lines (P6)
Cleaning insertions (P3, P7)
4th July 2023

## Slide 4
LHC vacuum system
5.8 km of baked system
  85% are NEG coated chambers
Up to 186 vacuum sectors
  Twin (2 separate beampipes)
  Combined (common beampipe)
Room temperature areas:
8 Long Straight Sections (~528 m. each)
Cryogenic areas:
Stand-Alone Magnets (cold bore @4K)
Inner Triplets (cold bore @1.9K)
~1.4 km of cryogenic vacuum pipes
Up to 82 vacuum sectors
4th July 2023
Twin sectors
Combined sectors
(both sides of Experiments)

## Slide 5
LHC vacuum system
8 ARCs (~ 2.8 km each)
Superconducting “bending” magnets
Cold bore @1.9K, beam screen @5-20K
~48 km of cryogenic vacuum pipes
Up to 18 vacuum sectors
TCLD collimators
2 vacuum sectors
Cryogenic areas:
Room temperature areas:
4th July 2023

## Slide 6
YETS Framework
28th November 2022
10th March 2023
27th March 2023
HL-LHC upgrade
WP13
WP5
WP14
WP17
Maintenance & Operation
Cryogenics
Cooling and ventilation
Vacuum
Electrical systems
Survey
Optics
…
Consolidation & other
Optical fibre
Telecom cable campaign
…
YETS (Year End Technical Stop) 2022-2023
Works from 28th November to 10th March (P7 from 8th January)
Beam back on 27th March
4th July 2023

## Slide 7
YETS Framework: Planning
Electrical tests = power cuts
Activities in parallel
Access constraints
Co-activity
4th July 2023
VSC

## Slide 8
YETS 22-23 activities: Overview
LSS8
MKI cool prototype (WP14)
A4L8.C Replacement TCTPV.4L8.B1
LSS4
BGC phase II (WP13)
2 BWS maintenance
E5R4.R RF-finger problem suspicion
LSS7
2 TCPC crystal collimators (WP5)
4th July 2023
VSC-led activity
LSS6 - DUMP BTD62
Replacement MKBV.B2
MKBs Pumping upgrade
HL-LHC activities
General activities

## Slide 9
HL-LHC activities
4th July 2023

## Slide 10
LSS4 | BGC Phase II
See Cristina’s seminar
from March 21st
BGC (Beam Gas Curtain) phase II installation completed and instrument fully operational for 2023 run
Beam Gas Curtain: a new instrument for LHC Run 3 - YouTube
First injections done during stable beams
Removal of BGI table and installation of new gas injection system
Integration of injection and dump chambers
5 turbomolecular pumping groups + 1 dry pump for injection line
New PLC controls + SCADA int.
WP13
LHC-BGC-EC-0005
LS2
(phase I)
YETS 22-23
(phase II)
Independent compressed air supply (new line)
New gauges
4th July 2023

## Slide 11
LSS7 | TCPC Crystal collimators
Upgrade of the crystal collimation test stand in IR7
YETS 21-22: Replacement of 2 TCPCV in sectors B5L7.B and B5R7.R
YETS 22-23: Replacement of 2 TCPCH in sectors A4L7.B and A5R7.R
Opening of vacuum sector and releasing of collimators from their slot
Connection of new collimator
Sector reconditioning: Pump + bake + NEG activation
WP5
LHC-TC-EC-0015
4th July 2023

## Slide 12
Last minute removal of TCPCH.A4L7.B1
In March, during OP commissioning tests, the crystal remains blocked halfway in (no beam circulation possible)
Prompt action to vent the sector for an inspection (SY/STI)
Mechanical failure (roller cage jammed). Repair in situ not possible
Crystal collimator removed and slot closed with a vacuum chamber
Reconditioning of the sector: Pump, re-bake + NEG activation
Total intervention time: 6 days (very challenging)
Reinstalled two weeks ago during TS1 – 5 days
Inspection of TCPC by SY/STI
LSS7 | TCPC Crystal collimators
Sector opening (TE/VSC)
4th July 2023

## Slide 13
LSS8 | MKI cool
First MKI cool prototype installed during YETS 22-23 (1 out of 8)
Activities in surface
Acceptance test of the MKI cool subcomponents
Acceptance test of the MKI cool tank assembly + bake-out
Activities in tunnel
Adjacent sectors (G5R8 & I5R8)
  Removal/reinstallation of 4 vacuum assembly modules
  Reconditioning: Pump + bakeout
Acceptance test of the MKI cool in Bldg.867
MKI cool transport
MKI8D
WP14
LHC-MKI-EC-0004
4th July 2023

## Slide 14
LSS8 | MKI cool
Accidental dry nitrogen inrush inside all the MKI tanks
Bake-out of MKI8C
Pump-down restarted with fast recovery of vacuum
Bake-out cycle of MKI8C
Reconditioning completed and nominal pressures recovered (<1x10-11 mbar). No need of additional bake-out in rest of MKIs sectors
HV test of all MKI performed by SY-ABT. No issues identified
Additional safety measures implemented
Validation check before interventions
Already implemented during YETS 22-23 in other all sectors
~5x10-6 mbar
~2x10-2 mbar
~4x10-1 mbar
MKI8A
MKI8B
MKI8C
~4x10-1 mbar
MKI8D
4th July 2023

## Slide 15
General activities
4th July 2023

## Slide 16
Maintenance of 2 BWS (Beam Wire Scanner) in sectors E5L4.R and E5R4.B
E5L4.R (outer beam line): additional mechanical intervention requiring opening and disconnection of the tank from the beamline
Intervention by SY-BI : C-wire inspection (exchange) + functional tests
Vacuum reconditioning: Pump + bake + NEG activation
LSS4 | BWS maintenance
E5L4.R (outer beam pipe)
E5R4.B (inner beam pipe)
4th July 2023

## Slide 17
LSS4 | E5R4.R RF-finger problem suspicion
Pressure spikes up to 10-6 mbar detected during beam operation in two adjacent penning gauges
Objective during YETS: Discard any aperture restriction (ULO, RF-finger damaged, etc.)
Opening of the sector for visual inspection of BQS (Schottky Monitor) and adjacent vacuum chambers 
E5R4.R
F5R4.B
D4Q5-R4
Penning gauges
Sector valve
Warm modules
X-ray (EN-MME) on 4 warm modules 
BQS
Additional X-ray (EN-MME) on sector valve 
4th July 2023

## Slide 18
LSS6 DUMP | MKB exchange
CapaciTorr HV 2100 (ZAO alloy)
Plasma screen coated
New tank upgraded with 2 modifications:
Replacement of the MKBV (C+D) in BTD62 due to an electrical flashover during operation
Also implemented in all other 5 tanks in BTD62
BTD68 upgrade planned for EYETS 23-24
New interconnection end cap plasma screens with aC coating (SY-ABT)
Additional pumping: 2 NEG cartridges per tank (TE-VSC)
4th July 2023

## Slide 19
~5x10-11 mbar
~2x10-9 mbar
Pressure increase detected in sector A4L8.C over a period of months
Complex and long vacuum sector (>50 m, recombination area, chambers ID 212 mm)
Leak confirmed at the beginning of YETS
Leak rate of ~10-6 mbar.l/s detected on an edge welded bellow of a collimator (TCTPV) motor
27 June 2023
LSS8 | A4L8.C replacement TCTPV

## Slide 20
On surface, series of validation done by different groups (including vacuum acceptance test)
New collimator installed
Base pressures recovered after bakeout
Vacuum acceptance test of spare TCTPV in bldg.867
LSS8 | A4L8.C replacement TCTPV
Replacement of TCTPV.4L8.B1 by spare one
4th July 2023

## Slide 21
Consolidation and non-conformities
12x old ion pumps (VPI) exchanged by new pumps (VPIAN) with HV Fischer feedthrough
2x non-conform Penning gauges (VPGB) exchanged
4th July 2023

## Slide 22
Bake-out
But not only…
LHC Vacuum sectors baked: 9
Length of beamlines baked: 182 meters
Example of instruments equipped:
MKI
Crystal collimators (TCPC)
Beam Wire Scanners (BWS)
BRANB
TCLIA, TCTPV and TCTPH
AWAKE expansion volume
Some numbers:
Bake-out racks used: 27
Injectors Vacuum sectors baked: 3
Length of beamlines baked: 45 meters
AWAKE expansion volume
Crystal collimator
4th July 2023

## Slide 23
Summary
All activities planned have been performed in time with no impact for the restart of the machine.
More activities with respect to baseline including last minute interventions (crystal collimator removal) but well-executed.
Challenging management of the bakeout activities due to implication of the involved team in parallel activities in the Injectors complex.
4th July 2023

## Slide 24
    Thanks to all TE/VSC participants, FSU and AL4030 colleagues!
TE/VSC/BVO
D.Digonzelli
C.Moreillon
Industrial support
P.Caseiro
P.Ouvrier
FSU
G.Bregliozzi
J.Finelle
G.Cattenoz
K.Owens
N.Zelko
E.Page
J.Hansen
O.Santos
I.Wevers
K.Henneli
TE/VSC/ICM
L.Zygaropoulos
J.De la Gama
I.Lobato
…and more
J.Sestak
4th July 2023

## Slide 25
Any questions?
Thank you for your attention

## Slide 26
Spares
4th July 2023

## Slide 27
LHC vacuum system
Component | Quantity
Vacuum sectors (cryogenic / RT) | 88 / 186
Vacuum sectors valves (all LHC) | 241
Roughing valves (LSS) | 348
Ion pumps (special / 30 / 60 / 350 / 400 l/s) | 12 / 625 / 177 / 36 / 35
NEG cartridges (D400 / D2000) | 257 / 0
Bayard-Alpert gauge (LSS) | 201
Penning gauges (LSS) | 571
Pirani gauges (LSS) | 331
Item in LSS | Length (m) | % wrt total
SAMs & ITs @ cryogenic T | ˜ 1365 | 19
LSS @ RT baked | ˜ 1000 | 14
LSS @ RT with NEG chambers | ˜ 4800 | 67
Total length under vacuum | ˜ 7200 | 100
˜ 85% of the baked vacuum system is NEG coated |  | 
LHC in numbers: Vacuum
4th July 2023

## Slide 28
The way we work
Vacuum reconditioning
- Pump-down
- NEG activation
Quality control 1
Quality control 2
Preparation
- ECR / ARR
- Layout modification
- Integration
- IMPACT
- VIC
- Logistics
- WOs
…
Mechanical intervention
Vacuum controls
(ICM)
Work in the tunnel
ECR: Engineering change request
ARR: Asset replacement request
VIC: “Visite d’Inspection Commune”
No layout modifications required during this YETS
4th July 2023

## Slide 29
LS2
YETS 22-23
LSS4 | BGC Phase II
4th July 2023

## Slide 30
LSS4 | BWS maintenance
New sector valve
Sector valve
BWS
36.5 m
6.6 m
BWS
Before LS2
After LS2
Sectorization during LS2
4th July 2023

## Slide 31
LSS4 | E5R4.R RF-finger problem suspicion
X-ray on sector valve
4th July 2023
Feasibility study on random valve (on surface )
VVGSH.1174.5R4.R

## Slide 32
LSS4 | E5R4.R RF-finger problem suspicion
X-ray on sector valve
4th July 2023
VVGSH.1174.5R4.R