## Slide 1: Picosec Micromegas for the Muon Collider Detector
D. Fiorina – INFN Pavia
On behalf of the Muon Collider Collaboration

## Slide 2: Index
Introduction to the Muon Collider
  Requirement for Muon timing in Muon collider
Test Beam results
  Photoelectrons measurement
  Timing measurements
Rate capability (preliminary results)
Eco-friendly gas (preliminary results)

## Slide 3: Muon Collider facility
Simulations available for √𝑠=1.5TeV
Production ongoing for √𝑠= 3TeV

## Slide 4: Muon Collider Detector
Design phase of the Muon Collider Detector
For the muon endcaps, a Muon tracking and timing station based on Picosec+MPGD has been proposed
Shielding from Beam Induced background (from decaying muons) limits the coverage in eta (θ>8°, η<2.7 available)

## Slide 5: Muon endcap
Out-to-In muon tracking approach currently under study
Resolve muon in the muon system to close the track in the tracker system reducing the combinatory background
Time resolution ~100ps
Tracker
Time seed
Picosec
Tracking MPGD
Rate capability (√𝑠=1.5TeV):
  60 kHz/cm2 8°<θ<12°
  2 kHz/cm2 θ>12°
6.5m
Endcap – not in scale
0.6m
0.9m
12°
8°
Operation in a heavily ionising particle environment

## Slide 6: Picosec Micromegas
Cherenkov radiator
Photo
cathode
Gas Mixture
MgF2 3mm
CsI 18nm
200µm
128µm
18µm wire
Gas Mixture:
Ne/C2H6/CF4
80/10/10
Look at Cherenkov, not the ionisation
  Photo-electrons created promptly with the MIP passage
Remove the ‘drift’ gap and start the avalanche as soon as possible
  Avalanche propagate faster
Cherenkov radiator MgF2:
  Optimal UV transparency, high cost, no technology for large windows, fragile
Photocathode CsI:
  Best UV QE, radiation damage, Hygroscopic
Gas Ne/C2H6/CF4:
  High quenching, high-cost, non-eco-friendly

## Slide 7: Test Beam Setup
Test beam, 19Oct-1Nov 2022
Profited of the RD51 GEM-based tracker
Participated to full RD51 R&D campaign
  First beam time with a dedicated detector for muon collider R&D
Single-channel:
Test the detector operation on the beam
Measure different radiator+photocathode combination yield (photoelectrons/MIP) and compare
Measure time resolutions with different radiator+photocathode combination
Comparison between non-resistive MM (amplification 150um) and resistive MM (amplification 128um)
MCP for time reference σt≈5ps

## Slide 8: Single-channel setup - Photoelectrons/MIP measurement-
Charge amplifier
Waveform saved for processing
Charge spectrum with UV LED  single photoelectron spectrum
Charge spectrum with beam  photoelectrons from beam spectrum
  Geometrical cut essential to select only fully contained Cherenkov cones
Integral of the signal
-or-
Just the amplitude
Polya function (negative binomial)
Describe well the gain fluctuation when the primary charges are low
Single PE
Multi PEs

## Slide 9: Photoelectrons per Muon
The ratio among the mean amplitudes gives the average number of photoelectrons per incoming muon.
We don’t know precisely the amount of aging of the CsI photocathode in orange, but it was handled in the air multiple times (collected humidity damage). CsI is prone to degradation if exposed to humidity and heavy ion bombardment
Quartz is not a good radiator. Its yield is an order of magnitude lower than MgF2. May create some inefficiencies
B4C is very promising (12nm demonstrated the best performance https://indico.cern.ch/event/1219224/contributions/5130512/attachments/2565710/4423222/Marta Lisowska - PICOSEC Micromegas - MPGD2022.pdf). Moreover is resistive (spark protection) and easy to handle.
MgF2 radiator
Quartz radiator

## Slide 10: Single-channel setup -Timing measurement-
Fast electron peak
Slow ion tail
Current amplifier
To preserve the rising edge!
Logistic function fit on Picosec signal
 CFD on fit  Signal Arrival Time
Logistic function fit on MCP signal
 CFD on fit  Signal Arrival Time
Δt between the SATs gives the time resolution!
The geometrical cut on the fully contained cones is fundamental also in timing.

## Slide 11: Timing Results
Chart: Drift field (V/um)
| 2 | 2.0416666666666665 | 2.0833333333333335 | 2.125 | 2.1666666666666665 | 2.2083333333333335 | 2.25 | 2.2916666666666665 | 2.3333333333333335 | 2.2083333333333335 | 2.25 | 2.2916666666666665 | 2.3333333333333335 | 2.375
Aged CsI D=240um | 104.7 | 105.8 | 98 | 98.3 | 87.7 | 71.4 | 65.3 | 59.2 | 54.6 | 75.7 | 65.6 | 61.8 | 59.1 | 60.3
B4C 14nm D=150um | 92.3 | 86.7 | 75.4 | 61
new CsI D=150um | 61 | 51.2 | 53.5 | 43.4
B4C 6nm D=150um | 114.2 | 83.3 | 81.7 | 72.7
Chart: Drift field (V/um)
| 3.2666666666666666 | 3.2 | 3.1333333333333333 | 3.4
Quartz CsI 150um NEW MM | 82.5 | 90.2 | 99.2 | 81.1
new CsI D=150um NEW MM | 23.9 | 24.7 | 27
non-resistive MM 150um 1.84 V/um
Resistive MM 128um 2.15kV/um
The timing performance reflects the number of PEs/MIP
All the combinations may be suitable for Muon Collider application (<100ps)

## Slide 12: Rate capability to single PEs -work in progress-
Irradiation with UV LED to generate single-photoelectrons signals
CsI photocathode
Counts signals and measures the average amplitudes
Drift field: 3.13 V/um
Detector performance stays stable up to 2MHz/cm2 for single-photoelectron
One can roughly scale a factor of 10 for Muons
We can go higher with the rate, but we have to fight against CsI degradation
Amplification field:
2V/um
1.9V/um
1.8 V/um
Example of an amplitude spectrum
Example of 1.6ms of acquisition 

## Slide 13: Eco-friendly gases -work in progress-
LED irradiation  single Photoelectrons signals
Gas: Ar/CO2 93/7
Drift: 150um, Amplification: 150um
Drift: 380V, Amplification 480V (max voltages achievable with such mixture)
Many of the signals do not present the expected electron-peak/ion-tail ratio
Multiple signals on the same rising edge
Probably caused by some feedback process because of the low quenching gas?
Any suggestion on that is very welcomed 

## Slide 14: Conclusions
Muon Collider requirement
~100ps time resolution
60kHz/cm2 rate capability
Spark and radiation hard detector
Scalable technology up to ~m2 (baseline option is to tile a large surface with small detectors)
Test Beam results
All configurations satisfied the ~100ps time resolution
Quartz+CsI and MgF2+Chromium may lead to inefficiencies because of the low number of photoelectrons
CsI is the best photocathode but can be easily damaged by ion bombardment and humidity
B4C is a very promising candidate (resistive and easy to handle)
  Not suitable for Muon Collider because of neutrons, but DLC should have a similar performance
Rate capability
Detector response to single photoelectrons stable up to 2MHz/cm2
Operational limit will be tested soon!
Eco-friendly gas
Ar/CO2 (93/7) seems to have a too-small quenching factor for good performance in a single photoelectron case
New gases will be tested in Pavia (Ne, Ar, C2H6, C4H10, R1234ze…)
DRD1 transition:
Pavia group is the ‘watcher’ in the Muon Collider Collaboration for the new DRD1
Expression of interest in RPC, straw tubes and MPGDs (Picosec but not only)

## Slide 15: BACKUP

## Slide 16: Timeline

## Slide 17: Simulation background
Background interaction with the detector was simulated in Geant4
Convoluted with the response of different gaseous detector technologies (hit when a charged particle is found in the drift gap)
Simulated Picosec: 3mm MgF2 radiator, 18nm CsI photocathode, 200um drift gap
Picosec can potentially operate in high-rate environments and give timing information with higher precision wrt other technologies

## Slide 18: BIB spectrum

## Slide 19: BIB neutrons

## Slide 20: Selection of detectors for MIP timing
Detector | Space resolution | Time resolution | Rate capablity | Longevity | Cost (CHF/cm2) | Reference
MRPC ALICE ToF | ≈3cm* | ≈60ps** | 500Hz/cm2** | No issue after 20 years operation** | ≈1 | alice_toftdr.pdf (cern.ch) 1806.03825.pdf (arxiv.org)
LGAD ATLAS HGTD | ≈1mm* | ≈30ps ≈70ps end of life | - | 2.5x1015neq/cm2 | ≈38 | HGTD TDR (cern.ch)
LGAD CMS MTD endcap | ≈1mm* | ≈30-40ps 50-60ps end of life | - | 1.5x1015neq/cm2 | ≈62 | CMS Technical Design Report for the Phase-2 Timing Upgrade (cern.ch)
Picosec 10x10cm2 prototype | ≈1cm* | ≈24ps | Tested on ≈50kHz/cm2 laser beam and ≈100Hz/cm2 muon beam NO LIMIT REACHED | - | ≈70 Cost of one 100cm2 prototype | 
Micromegas ATLAS NSW | <100µm | ≈7ns | >15kHz/cm2 required ≈1MHz/cm2 max | >230mC/cm2 | ≈1 | ATLAS-TDR-020.pdf (cern.ch) pdf (iop.org) 47d84fb8700bff3c5787574218f71972 (inspirehep.net)
*estimated from pad size
**from real operation
Picosec potential:
High rate capability wrt MRPC
Low cost wrt to LGAD

## Slide 21: R&D Plan: Cherenkov Radiator
Cherenkov radiator
Photo
cathode
Gas Mixture
Cherenkov radiator – Baseline MgF2
High UV transparency (>120nm)
Fragile
High cost (12€/cm2)
No technology for large areas (100cm2 max)
Quartz (5€/cm2, >180um)
Sapphire (6€/cm2, hard, large area, >170um)
other F-based crystals have to be studied!
Broken MgF2 crystal

## Slide 22: R&D Plan: Photocathode
Photocathode – Baseline CsI
High quantum efficiency to UV (≈10p.e./MIP)
Easy to coat by Chemical Vapour Deposition
Hygroscopic (sealed operation, dry gas)
Damage by ion bombardment
Metallic (Al, Cr, Au…)  easy to coat, non-resistive (pro and cons), lower QE (1-2 p.e./MIP)
Carbon-based (DLC, B4C)  dedicated sputtering machine, resistive (pro and cons), lower QE (factor 3-4 p.e./MIP)
Damaged CsI
Photoelectrons generated per MIP (p.e./MIP) with 3mm MgF2 radiator
Cherenkov radiator
Photo
cathode
Gas Mixture

## Slide 23: R&D Plan: Gas Mixture
Gas Mixture– Baseline Ne/C2H6/CF4
High gain and discharge quenching (up to 2-3x105)
High drift velocity (>5 cm/µs)
Very costly (Ukraine was the main producer of Ne, CF4 is heavily taxed for its GWP)
Not eco-friendly (GWP≈740)
C2H6 (3k€ bottle, GWP=10.2) can be substituted with other quenchers :
CO2 (0.7k€ bottle, GWP=1, small quenching)
iC4H10 (1.5k€ bottle, GWP=3, good quenching)
CF4 (4k€ bottle, GWP=7390) is difficult to replace:
drop it
R1234ze (1.5k€ bottle, GWP=7, candidate substitute for fluorinated gas in RPC and CMS-CSC)
New mixtures with new gases
ALICE TPC GEM Ne-N2-CO2 (relatively high drift velocity, negligible GWP)
Cherenkov radiator
Photo
cathode
Gas Mixture