## Slide 1: US Contributions to FCC FCC-US Workshop Tor Raubenheimer April 24, 2023
SPACE FOR ADDITIONAL LOGOS

## Slide 2: FCC-ee Layout
Double ring e+e- collider with 91 km circ.
Common footprint with FCC-hh, except around IPs
Perfect 4-fold superperiodicity allowing 2 or 4 IPs; large horizontal crossing angle 30 mrad, crab-waist collision optics
Synchrotron radiation power 50 MW/beam at all beam energies
Top-up injection scheme for high luminosity Requires booster synchrotron in collider tunnel and 20 GeV e+/e- source and linac
Or MR RF?
Or Booster RF?

## Slide 3: Present US Engagement in FCC Accelerator

## Slide 4: Opportunities for increased engagement
Some R&D topics match to unique US technical expertise: bulk Nb SRF, compact SC IR magnets, …
Many other topics leverage US capabilities: beam physics, RF power sources, waveguides, and couplers, power convertors, HTS magnets, beam instrumentation and feedback, controls, ….
Other topics could engage US industry: 270 km vacuum chamber and associated components, dipole magnets for main ring and booster, supports and girders, ….

## Slide 5
F. Peauger and O. Brunner

## Slide 6
F. Peauger and O. Brunner

## Slide 7: FCC-ee SRF R&D
400 MHz Cu/Nb cavities with Q0 of >3e9 at 12 MV/m and 4.5K
  Require strong damping of single-cell cavities to reduce HOMs at Amp-level current
  Coupler design for ~MW RF power
  Compact cryomodule design for W, Zh, and t-tbar
800 MHz Nb cavities with Q0 of >3e10 at 25 MV/m and 2K
  Require strong damping of HOMs in 5-cell cavities for 100 mA
  Recently increased Q0 spec from 2e10 to >3e10
  Coupler design for 250 kW RF power
  Compact cryomodule design for t-tbar

## Slide 8: High Q0 SRF Systems – US expertise
LCLS-II developed new N2 doping approach  is operating cryomodules at 1.3 GHz with Q0 = 2.7x1010 at 16 MV/m
PIP-II is developing high Q cavities at 650 MHz
LCLS-II-HE will build 23 cryomodules with Q0 = 2.7x1010 and >21 MV/m
LCLS-II
PIP-II

## Slide 9
Complicated integration with SC quadrupoles, solenoids, IR chamber, LumiCal, shielding, and diagnostics
Quadrupoles thanks to M. Koratzinos
M. Boscolo, M. Koratzinos, B. Parker
FCC-ee IR Magnet R&D

## Slide 10: IR Magnets
Challenging IR magnets embedded in the detector with 2.2 meter L*
Similar requirements to Linear Colliders
Small aperture with modest pole-tip field
Design and requirements have significant impact on detectors
BNL Direct Wind in Action Closeup View

## Slide 11
Many similarities with EIC IR
FCC-ee IR Magnet R&D
Direct Wind Tapered Double Helical Coil
EIC Tapered Quadrupole R&D Example
H. Witte
Double Helical CCT
Grooved Double Helical Coil Support
M. Koratzinos
FCC R&D CCT Magnet
Baseline FCC-ee Coils and Beam Pipe

## Slide 12
IP chamber: critical for performance, MDI
1) Central IP vacuum chamber (test cooling and vacuum systems), AlBeMet162 & steel transition (shape of transition, EBW process), Bellows (vacuum and thermal tests), Welding (EBW for elliptical geometry), C-fibre support structure
2) Elliptical vacuum chamber with remote vacuum connection, first quadrupole QC1, cryostat, beam pipe and quadrupole and cryostat support, vibration & alignment sensors
M. Boscolo, F. Fransesini, F. Palla, et al.
bellows assembly
support tube with carbon fiber cylinder
FCC-ee IR Mockup

## Slide 13
Collaboration between PSI and CERN with external partners: CNRS-IJCLab (Orsay), INFN-LNF (Frascati), KEK/SuperKEKB as observer, INFN-Ferrara – radiation from crystal
P3: PSI e+ production experiment with HTS solenoid at SwissFEL
planned for 2024/25
Latest FCC-ee pre-injector layout
P. Craievich, A. Grudiev, C. Milardi, A. De Santis, et al.
FCC-ee Pre-Injector R&D
e+ requirements ~2x SLC
20 GeV linac to Booster

## Slide 14: FCC-ee Accelerator Layout
The arc cells are repeated 2000 times around the ring
  Critical to understand and optimize the layout for cost, installation, alignment, operation, and maintenance
  Includes placement of the main rings and the Booster
  6000 11-meter twin-bore dipoles and 3000 3-meter twin-bore quadrupoles plus the booster
Preliminary single cantilever dipole supports
Common girder for main collider quadrupoles & sextupoles
HL-LHC jacks
Common support for booster’s quadrupoles & sextupoles
HL-LHC 2t Universal Adjustment Platform (UAP)
C. Tetrault
F. Carra et al

## Slide 15: FCC-ee Vacuum System

## Slide 16: FCC-ee Vacuum System
The arc cells are repeated 2000 times around the ring
  Critical to understand and optimize the layout for cost, installation, alignment, operation, and maintenance
  Includes placement of the main rings and the Booster
  6000 11-meter twin-bore dipoles and 3000 3-meter twin-bore quadrupoles plus the booster
Preliminary single cantilever dipole supports
Common girder for main collider quadrupoles & sextupoles
HL-LHC jacks
Common support for booster’s quadrupoles & sextupoles
HL-LHC 2t Universal Adjustment Platform (UAP)
C. Tetrault
F. Carra et al

## Slide 17: Planning US Engagement
Working to develop an R&D budget request for P5
  Expect that OHEP will establish a funding path for FCC-ee accelerator and detector R&D and we’re developing a placeholder to provide guidance
FCC-US meeting is an opportunity to start thinking about details
  Focus on technologies other than SRF right now: IR magnets, collimation, backgrounds, beam physics, ….
Lots more detail will be discussed at FCC Week 2023
  Join us there!

## Slide 18: FCC-ee US Engagement Summary
US has been engaged in the FCC-ee design
Many opportunities for engagement in R&D stage which will continue into 2030’s – many synergies with EIC
A decision on FCC-ee will be presumably made on 2027 timescale  increased engagement with R&D, engineering, and fabrication
Assuming the project moves ahead, the US contribution could be B$-scale

## Slide 19: Thank you for your attention.
19
SPACE FOR ADDITIONAL LOGOS
Name of the speaker/author
Date / Name of the event

## Slide 20: Management and Advisory