## Slide 1
EIC Collimation Studies
Matthieu Valette (BNL)
in collaboration with :
A. Drees, G. Robert-Demolaize
J. Bellon, A. Blednyk, C. Hetzel,
S. Seletskiy, N. Tsoupas
US FCC Workshop

## Slide 2: Context
The EIC will feature powerful beams
  10x the stored energy of RHIC
  2x Super KEK-B target stored energy in the ESR with 1/2 the bunches
Collimators accomplish 2 main missions
  Beam cleaning to reduce radiation & backgrounds from lost particles
  Machine & Detector protection from accidental beam loses (CCs, kickers, instabilities, …)
Constraints
  Impedance budget
  Beam lifetime
  $ budget
Light Sources

## Slide 3: Introduction
The e- bunches will be very dense (0.5 mm2) and melt metals in case of normal impact.
The p+ beam will have similar parameters as the post-LIU SPS.
Other complexes have reported issues limiting performance:
  Super KEK-B experienced instabilities causing collimator damage and limiting beam currents.
  HL-LHC will switch to coated collimators (MoGr) to reduce impedance.
Assuming SKEKB-like tails

## Slide 4
Special constraints:
  Different loss behavior for protons/ions
  Cold ring requires good cleaning efficiency in the arcs
  More flexibility on the optics
We can benefit from RHIC and LHC experience.
Planned in IR12 :
  issues with other users due to radiation
  switchyard doubles the second secondary
Momentum collimators are planned for the sector 12 ”D7” dummy.
Courtesy of G. Robert-Demolaize
HSR Collimators

## Slide 5: ESR collimation
IR2 - Horizontal
IR4 – Vertical
Focus on the 10 GeV case with the most stored energy.
Planned in IR2 & 4 :
  1 double-sided primary
  2 double-sided secondary for cleaning and flexibility with phase advances and optics
  Possibility to double each set for redundancy and extra flexibility
Collimators Quadrupoles
Dipoles
Dump kickers & Lambertson
HSR crossover

## Slide 6: ESR collimation (continued)
Electron bunches have a short polarization lifetime (~35 min) and will be replaced every 10 minutes. The ~250 J of the used bunch will be absorbed in-vacuum.
The Titanium transfer-absorber will be in IR12 with 2 jaws for injection failure cases.
IR12 is also the location with the largest dispersion and the most suitable for momentum collimation.
IR12 – Injection protection

## Slide 7: Collimation hierarchy
secondary
Arc
Triplet
primary
secondary
Triplet
Exp. detector
primary
IR2
secondary
secondary
Horizontal
Vertical
13σ
14σ
45σ
17σ
17σ
19σ
70σ
25σ
Exp. detector
e- beam
IR4
Arc
Masks
Imposed by squeezed optics in the IRs
Retraction from prim -> sec -> aperture based on orbit stability
Arc is tighter than experiment in the horizontal plane
Masks upstream of IRs will prevent losses into the focusing quads from showering to the detectors
48σ
63σ
18 GeV optics

## Slide 8: Optics considerations
Phase advances :
  key to protect against kicker failures
  important to ensure cleaning efficiency with secondaries
  Orbit/optics will have to be monitored to ensure protection/cleaning
Orbit stability, β-beat, errors, … will affect collimations hierarchy and retraction margins.
Failure case simulations are needed once powering circuits are being finalized.
We are following developments at KEK-B closely to learn from their experience.

## Slide 9: Mechanical design
The HSR will feature long LHC-like collimators.
  The jaws will be several meters long and made of amorphous Carbon
The ESR will feature short KEKB-like collimators.
  Coated Carbon would benefit energy absorption and impedance.
  Composite materials are also under consideration (MoGr).
  All collimators will feature the same design for replaceability.
Horizontal e-col
Vertical e-col

## Slide 10: Tracking simulations
Xsuite + BDSIM used as a tracking tool.
Sample loss maps for the ESR are ready and allow design validation.
  More elaborated simulations will follow, including SR, beam-gas and generation of secondary particles.
Special thanks go to CERN’s collimation team : Frederik, Andrey, Pablo and Stefano for their help.

## Slide 11: Summary
Sector 12 H Momentum Collimation (D7 ‘dummy’)
IR12 e Injection absorbers
IR4 e Vertical Collimation
IR2 e Horizontal Collimation
& Abort System
H Injection protection
(note: not actual inj. location)
electron : 6 collimators
Hadrons : 8+1 collimators
+absorbers and masks
Sector 12 H Betatron Collimation (both planes)
Hadron Abort System (already there)
Masks

## Slide 12: Conclusion & Outlook
Collimation system design :
  Space, impedance and budget constrains are included to ensure background reduction and protection from failure cases.
  Global/Local optics requirements are defined for the lattice integrators.
  IR4 optics are being finalized and moveable mask location conflict need to be ironed-out.
Tracking simulations :
  ESR : preliminary loss maps are ready, more detailed studies on cleaning inefficiency and errors are next
  HSR : pending software functionalities
  A dedicated simulation sever is being purchased
Failure simulations will follow once some design parameters are settled.