## Slide 1: Mechanical Integration of the IDEA detectors in the FCC-ee interaction region
Fabrizio Palla1
Manuela Boscolo 2, Filippo Bosi 1, Francesco Fransesini 2, Stefano Lauciani 2
1INFN Sezione di Pisa, Italy
2INFN Laboratori Nazionali di Frascati (RM), Italy
First Annual U.S. Future Circular Collider Workshop
BNL, April 24-26, 2023

## Slide 2: The IDEA Concept
See talk by P. Azzi and N. De Filippis in the “Detector”
parallel session

## Slide 3: Requirements
Interaction region detectors must be integrated with the beam pipe
  The vertex detector innermost radius should profit of the reduced beam pipe diameter (2 cm) and should cover
  Must not interefere with the Luminosity Calorimeter (clearance of ~120 mrad)
  The mounting of the vertex and the outer tracker must be done inside the support tube
  Minimize the radiation lengths

## Slide 4: Vertex and Outer Trackers
Inside the same volume of the support tube that holds also the LumiCal
  Vertex detector supported by the beam pipe
  Outer Tracker (1 barrel and 6 disks) fixed to the support tube
Minimal number of detector module variants
  One module type only for the Vertex
  One module type only for the Outer barrel and disks
See talk by M. Boscolo for the interaction region layout

## Slide 5: Conceptual Tracker layout
Vertex detector:
Modules of pixel size
3 barrel layers at
13.7, 22.7 and 33 mm radius
Outer tracker:
Modules of pixel size
Intermediate barrel at 13 cm radius (improved reconstruction for)
Outer barrel at 31.5 cm radius
3 disks per side
DRIFT CHAMBER
EXSTERNAL CILINDER
OUTER TRACKER
MEDIUM TRACKER
INNER TRACKER
DISK 3
DISK 3
DISK 1
DISK 1
DISK 2
DISK 2

## Slide 6: Vertex detector modules
Chip 1
Chip 2
32 mm
8.4 mm
Readout
Module concept inspired by ARCADIA INFN R&D
  Depleted Monolithic Active Pixel Detectors (DMAPS) sensor and back-side processing already tested on silicon
  Pixel size 25x25 µm2 , 50 µm thick
  Active area 640 pixel (16 mm) in z and 256 pixels (6.4 mm) in
  Chip periphery plus an inactive zone: total of 2 mm in
  Chips are side-abuttable in z
Composed of 2 pixelated parts: total of 8.4 mm 32 mm (z)
  Power budget not established yet: assume (reasonably)
z 640 pixel
R-phi 256 pixel

## Slide 7
Layer 1
15 overlapping staves of 6 modules each
Pinwheel geometry: all modules at the same (smallest) radius
Power budget ~12 W
Total weight ~22 grams
Total thickness 0.25% X0
Silicon: 0.053% X0
Power and readout bus: 0.056% X0

## Slide 8
Layer 2
24 overlapping staves of 10 modules each
Pinwheel geometry
Counter-rotated wrt layer 1 to mitigate charge-asymmetry effects in track reconstruction
Power budget
~32 W
Total weight ~63 grams
Total thickness 0.25% X0

## Slide 9
Layer 3
18 overlapping staves of double 16 modules each
Lampshade geometry.
Charge symmetric track reconstruction
Total weight ~150 grams
Total thickness 0.25% X0
Power budget
~77 W

## Slide 10: Overall Vertex layout
Total power ~120 W – Air cooled
Total weight ~230 grams

## Slide 11
Vertex detector supporting conical structure
Weight ~ 460 grams

## Slide 12: Outer layers modules
Based on ATLASPIX3 R&D
  DMAPS
  50 x 150 µm2
  Up to 1.28 Gb/s downlink
  TSI 180 nm process
  132 columns of 372 pixels
  Active (total) length (r-phi x z)
    18.6 (21) mm x 19.8 (20.2) mm
  Module is made of 2x2 chips – total length:
    size 42.2 mm x 40.6 mm
  Power budget not established yet:
    assume
Power
Data IN/OUT
HV

## Slide 13
Intermediate Tracker Barrel
At 13 cm radius
22 staves of 8 modules each.
Lightweight reticular support structure (ALICE/Belle-II like)
Readout chips either side
Power budget
~342 W
Total weight ~1 kg
Water cooled (2 pipes of 2 mm diameter)

## Slide 14
Outer Tracker Barrel
At 31.5 cm radius
51 staves of 16 modules each
Lightweight reticular support structure (ALICE/Belle-II like)
Total weight ~3.7 kg
Readout chips either side
Power budget
~1400 W
Water cooled (2 pipes of 2 mm diameter)
Notes: NB. Qui la struttura reticolare deve stare giù perché sennò non si riesce ad ottenere il raggio esterno più grande e vicino alla DCH.

## Slide 15
Outer Tracker Disk 1
2 sides (front and back) each with 4 petals.
One petal is made of different staves of overlapping modules
Total modules per disk: 196
Total weight ~850 grams
Power budget ~ 336 W
Cooling using 1 water pipe (2 mm diameter)
Similar geometry for the other two disks (only change the inner radius)

## Slide 16: Support cylinder
All elements in the interaction region (Vertex, Tracker and LumiCal) are mounted rigidly on a support cylinder that guarantees mechanical stability and alignment
  Once the structure is assembled it is slided inside the rest of the detector

## Slide 17: Support tube – description
The structure is made with a multiple layer structure:
1mm Carbon Fibre + 4mm Honeycomb + 1mm Carbon Fibre
6 reinforcement ribs to support of the disks
Split in two halves to simplify the assembly procedure
The Aluminum endcaps support the LumiCal and the beampipe
Supporting system of the LumiCal under study
Aluminium ribs
Aluminium endcaps

## Slide 18: LumiCal integration
Currently under study the possibility to include LumiCal as a single object
The main modification consists into the creation of an annulus:
  18 mm along z (a multiple of 3.5 mm W (1X0) + 1.0 mm gap for Si pads)
  20 mm along the radius of the Lumical
A different design is being evaluated as different cut dimension or a conical cut on the LumiCal shape

## Slide 19: Support tube – Structural analysis – results
 | Maximum stress [MPa]
Aluminium flanges | 2.70
Aluminium ribs | 0.20
Honeycomb | 0.02
Carbon fiber | 0.50
 | Maximum displacement X [µm]
Aluminium flanges | 13
Aluminium ribs | 22
Composite | 23

## Slide 20
Assembly sequence

## Slide 27: General integration

## Slide 28: Conclusions
A first layout of the interaction region with LumiCal, vertex and outer tracker of the IDEA detector is being engineered
  Feasibility studies of integration successfully done including mounting sequence
Next steps:
  Vertex detector
    Study the routing of the services (readout and power cables)
    Dimensioning the air cooling system
  Outer Tracker
    Study the routing of the services (readout and power cables, cooling manifolds)
  Lumical
    Engineering and assembly
  Tracker support tube
    Study the anchoring to the detector
  Insert the layout in the GEANT simulation ongoing

## Slide 29
Thank you for your attention

## Slide 30: Backup

## Slide 31: Half-ladder layout – layer 1
z=0
Chip 1
Chip 2
Chip 1
Chip 2
96.5 mm
0.2 mm
Chip 1
Chip 2
8.4 mm
0.1 mm
Layer 1 ladders are placed at 13.7 mm radius

## Slide 32: Half-ladder layout – layer 2
z=0
Chip 1
Chip 2
Chip 1
Chip 2
160.9 mm
0.2 mm
Chip 1
Chip 2
8.4 mm
Chip 1
Chip 2
Chip 1
Chip 2
8.4 mm
0.1 mm
Layer 2 ladders are placed at 22.7 mm radius

## Slide 33: Half ladder layout – layer 3
16.3 mm
Layer 3 ladders are placed between 30.5 and 35.55 mm radius
Overlapping in 2 parallel ladders separated by 500 µm
- see engineering drawings later
Passive parts on the sides
z=0
Chip 1
Chip 2
Chip 1
Chip 2
Chip 1
Chip 2
Chip 1
Chip 2
Chip 1
Chip 2
Chip 1
Chip 2
Chip 1
Chip 2
Chip 1
Chip 2
0.2 mm
0.2 mm
0.2 mm
0.2 mm
z=0
257.5 mm
z=0
Chip 1
Chip 2
Chip 1
Chip 2
Chip 1
Chip 2
Chip 1
Chip 2
Chip 1
Chip 2
Chip 1
Chip 2
Chip 1
Chip 2
Chip 1
Chip 2
0.2 mm
0.2 mm
0.2 mm
0.2 mm

## Slide 34: Layer 1 stave detail
Reticular lightweight support to provide stiffness
Thin carbon fiber walls interleaved with Rohacell
2 buses (data and power) 1.8 mm wide and 250 µm thick (50 µm Al, 200 µm kapton) per side
Sensors facing interaction point w/o any other material in front
Readout chips either sides
Air cooled

## Slide 36: Vertex on the beam-pipe

## Slide 37: Air cooling for Belle-II upgrade

## Slide 38
Similar structure of Belle-II oVTX L5

## Slide 39: Overall layout

## Slide 41: OUTER TRACKER

## Slide 42: MEDIUM TRACKER

## Slide 43: Stave detail

## Slide 44: DISK 2

## Slide 45: DISK 3

## Slide 46: Typical disk module stave
Cooling pipes
Lower modules
Upper modules
Front
Carbon fibre spacer
Carbon fibre pacers
Back
Electrical bus

## Slide 47: Support tube – Updated structural analysis
The aim of this analysis is to calculate the stress and displacement in each part of the cylinder (Al reinforcement, carbon fiber, honeycomb).
It is necessary to set:
Constraint configuration  double fixed ends
Loads configuration
Chamber | 50 kg
LumiCal | 70 kg + 70 kg
Disk | 52 kg
Outer tracker | 11
Medium tracker | 3
Including estimates of the services running from the detectors to the end of the support tube | 
Loads applied to remote point to distribute
Carbon fiber/ honeycomb creation  layered section

## Slide 48
Loads configuration
Layered section

## Slide 49: Support tube – Rail
The support tube needs to be inserted into the main detector; the idea is to use a rail, starting from the outside of the detector to allow the sliding of the cylinder.
To assure a good precision and appropriate support it is necessary to use the linear bearings; different types are available, the choice has to be made considering:
Required positioning precision
Weight of the whole structure
Necessary degrees of freedom
SECTION

## Slide 50
Under study:
Rail support
Rail anchoring
Rails length
Geometry of the rail section
Linear bearing type
Positioning system
To continue the design, it is necessary to know:
Allowable anchoring point from detector side
Allowable space (internal detector diameter and geometry)

## Slide 51: LumiCal – Support proposal
LumiCal are held by the two support tube endcaps.
A hexapod structure allows to limit the axial footprint.
Hexapod positioner has 6 DOF and high-precision positioning (m).
Actuators could be manual or automatic for a remote positioning.
The adoption of this solution depends on many factor:
Active or passive alignment system
Detection positioning system
Actuator system (manual, pneumatic, piezoelectric, step-motor, etc.)
Anchoring system

## Slide 54: Low impedance vacuum chamber
Inlet/outlet for paraffin cooling (copper)
Two halves AlBeMet pipe
Transition
Bellows
Electron Beam Welding
Thick copper deposition
Material | thickness
AlBeMet162 (62% Be and 38% Al alloy) | 0.35 mm
Paraffin (coolant) | 1 mm
AlBeMet162 | 0.35 mm
Au | 5 mm
warm and cooled
  Inner radius 10 mm
  Outer radius 11.7 mm
Geometry studied to integrate the central chamber with the vertex detector
To reduce the cooling material, the design provides five channels for each side; in this way is possible to use the needed quantity of coolant and reduce the material, creating a light structure.
Starting from 90 mm to 1190 mm from IP
The cooling is based on an asymmetric solution, using the 50 mrad cone as the cutting profile, to assure the respect of the spatial constraint due to the LumiCal requirement.
Notes: central chamber we are working at the moment