## Slide 1: Review of beam diagnostics R&D @ CLEAR
S. Mazzoni for the BI teams
CLEAR scientific board meeting, 1/2/2023

## Slide 2: BI R&D @ CLEAR in 2022
Optical BLM tests (U. Huddersfield)
ChDR BPM tests (U. Oxford)
ChDR – based bunch length measurement (U. Manchester)
Electro optical sampling of ChDR (TU. Vienna)
Rad-hard fibres tests for FLASH and CERN Exp. Areas

## Slide 3: Loss detection and localization by Cherenkov oBLM
Losses produced by screen insertion and steering magnets along the line.
Screen locations
Steering magnet locations
Calculation method: Upstream relative arrival times comparison
30 bunches
PhD thesis of S. Benitez (U. Huddersfield)
30 bunches
Further steps about the localization of SPS beam losses are being investigated.

## Slide 4: ChDR BPM tests
Test of horizontal plane of AWAKE ChDR BPM PUs in-vacuum in location ~7m upstream of THz setup
Characterization of PUs with signal processing at three different frequency ranges: 26.5-40 GHz, 50-75 GHz, 75-110 GHz
Example set-up and signals with Ka band (26.5-40 GHz) detection, and the difference over sum of the input voltage to the Schottky diodes.
Sensitivity 3.1 %/mm
PhD thesis of C. Pakuza (U. Oxford)

## Slide 5: ChDR bunch length monitor for AWAKE run 2
RMS bunch length measurement using 2 different Schottky detectors working in different frequency bands (WR-12 (60-90) GHz & WR-1.9 (400-600 GHz))
PhD thesis of C. Davut, U. Manchester

## Slide 6: ChDR bunch length monitor for AWAKE run 2
Martin – Puplett Interferometer scan with 0.5 ps electron bunch @5 mm impact parameter
Frequency Selective Surface (>80 GHz high pass filter) used to prevent low frequency domination of the ChDR spectrum.
PhD thesis of C. Davut, U. Manchester

## Slide 7: ChDR with Electro-Optical probes
Characterization of ChDR from an 36 mm diameter Alumina radiator using EO-probes from KAPTEOS (BW up to 10 GHZ)
Successfully measured:
Lower limit for the absolute e-field strength  benchmarking CST simulations
Linear polarization of ChDR travelling through radiator
e-field distribution on radiator surface
Low cut-off frequency of 36 mm diameter radiator
Impact parameter dependence at low frequencies
PhD thesis of A. Schloegelhofer, TU. Vienna

## Slide 8: Silica Fibre tests for FLASH Therapy Beam Instrumentation
Tested different radiation-hard optical fibres
  Silica fibres with varied diameters
  Glass capillaries filled with liquid scintillators
Coupled to si-pm and pmt
Single bunch and multi bunch scans
Saturation occurs during multi bunch scans
Repeated measurements using optical filters and saturation still occurs
200𝜇m Diameter FIbre
si-pm
si-pm
PMT
E. Buchanan, I. O. Ruiz and J. Bateman

## Slide 9: BI tests in 2023
Beam Time Requests for BI tests in 2023 have been submitted:
  ChDR BPM follow-up
  Electro-optical sampling of ChDR
  ChDR Bunch length follow-up (interferometer scans)
  EOSD tests in air (two proposals from CERN and KIT)
For second half of CLEAR operation year:
  oBLM follow-up
  cavity BPM studies (A. Lyapin, RHUL)
CLEAR remains an essential facility for instrument development and formation of students !