## Slide 1: Optimisation of the MIRACLS components for MR-ToF mass separation
Franziska Maria Maier
CERN PhD Student

## Slide 2: MR-ToF devices are highly selective mass separators.
Ion mixture
time-of-flight separation in multiple revolutions
separated ion species
ion trajectory
Downstream experiments
Fig. courtesy R. Wolf
Notes: Pps pulse per second

## Slide 3: MR-ToF devices are highly selective mass separators.
Ion mixture
time-of-flight separation in multiple revolutions
separated ion species
ion trajectory
Downstream experiments
Fig. courtesy R. Wolf
A=149
Notes: Pps pulse per second

## Slide 4: MR-ToF devices are highly selective mass separators.
Ion mixture
time-of-flight separation in multiple revolutions
separated ion species
ion trajectory
Downstream experiments
 | current MR-ToF devices | MIRACLS 30-keV Device | Magnetic mass separators
R = (2-3) x m/Δm | > 100,000 | > 100,000 | a few 1000
Processing time | (tens of) ms | 3 ms | continuous
Ion flux | ~103-107 ions/s depending on m/Δm | ~105-109 ions/s depending on m/Δm | 1013 pps
Fig. courtesy R. Wolf
Notes: Pps pulse per second
30,000 for next generation mass separators, CARIBU, SPIRAL2/DESIR, CANREB

## Slide 5: MR-ToF devices are highly selective mass separators.
Ion mixture
time-of-flight separation in multiple revolutions
separated ion species
ion trajectory
Downstream experiments
 | current MR-ToF devices | MIRACLS 30-keV Device | Magnetic mass separators
R = (2-3) x m/Δm | >100,000 | > 100,000 | a few 1000
Processing time | (tens of) ms | 3 ms | continuous
Ion flux | ~103-107 ions/s depending on m/Δm | ~105-109 ions/s depending on m/Δm | 1013 pps
Fig. courtesy R. Wolf
Notes: Pps pulse per second
30,000 for next generation mass separators, CARIBU, SPIRAL2/DESIR, CANREB

## Slide 6: MR-ToF devices require bunched beams.
Paul-trap cooler-buncher installed upstream.
Time-of-flight
cooling laser
ions
Counts
S. Sels, F. Maier et al., Phys. Rev. Research 4, 033229 (2022).
Notes: Properties of bunched beams define performance of MR-ToF devices , small peak width for fast R sep
Additionally we also see that our simulations of the cooling process are in good agreement with exp. data.

## Slide 7: MR-ToF mass resolving power
∆t0 mainly defines how long it takes to reach given R.
Paul trap setting 1
∆t0=19 ns
Paul trap setting 2
∆t0=106 ns
Simulations (dashed) and experiment (points) are in good agreement.

## Slide 8: Development of a new Paul trap
Cern photograph, 2021.

## Slide 9: MR-ToF mass resolving power
1.5 keV, setting 1
1.5 keV, setting 2
30-keV
R=105 is reached in 3 ms.

## Slide 10: MR-ToF mass resolving power
30-keV
1.5-keV, settings 2
1.5-keV, settings 1
Finally reachable R is limited by broadening effects of ∆t0 over revolution number.

## Slide 11: MR-ToF mass resolving power
30-keV
1.5-keV, settings 2
1.5-keV, settings 1
isobaric pure 132Sn
isobaric pure 28-34Mg
isobaric pure 128Sn
Notes: 132Sn vs 132Sb:
m/Δm = 40,000
132Sn vs 132Cs:
m/Δm = 12,000
132Sn vs 132Sb:
m/Δm = 94,000
Mg vs Na (A=28-34):
m/Δm < 2,500

## Slide 12: MR-ToF devices are highly selective mass separators.
Ion mixture
time-of-flight separation in multiple revolutions
separated ion species
ion trajectory
Downstream experiments
 | current MR-ToF devices | MIRACLS 30-keV Device | Magnetic mass separators
R = (2-3) x m/Δm | > 100,000 | > 100,000 | a few 1000
Processing time | (tens of) ms | 3 ms | continuous
Ion flux | ~103-107 ions/s depending on m/Δm | ~105-109 ions/s depending on m/Δm | 1013 pps
Fig. courtesy R. Wolf
Notes: Pps pulse per second
30,000 for next generation mass separators, CARIBU, SPIRAL2/DESIR, CANREB

## Slide 13: Coulomb interactions limit ion flux.
Peak coalescence effect
Ion throughput is limited.
Experimental studies with m/Δm ≈ 2500:
Ion intensity
A few 100 ions/bunch
A few 1000 ions/bunch
L. Schweikhard, X LASNPA, 2013.
Time-of-Flight (µs)
Counts
Notes: We see that the limited ion flux is hence a real challenge for MR-ToF device. Before we now tackle this challenge, we will talk about…

## Slide 14: MR-ToF ion flux
0 20k 40k 60k 80k 100k 120k 140k
m/Δm
Existing low-energy devices

## Slide 15: MR-ToF ion flux
1.5-keV MIRACLS simulated
Existing low-energy devices
0 20k 40k 60k 80k 100k 120k 140k
m/Δm

## Slide 16: MR-ToF ion flux
0 20k 40k 60k 80k 100k 120k 140k
30-keV MIRACLS simulated
m/Δm
0 20k 40k 60k 80k 100k 120k 140k
1.5-keV MIRACLS simulated
Existing low-energy devices

## Slide 17: MR-ToF ion flux
0 20k 40k 60k 80k 100k 120k 140k
30-keV MIRACLS simulated
m/Δm
0 20k 40k 60k 80k 100k 120k 140k
isobaric pure 132Sn
isobaric pure 28-34Mg
isobaric pure 128Sn
1.5-keV MIRACLS simulated
Existing low-energy devices

## Slide 18: Simulation Results
 | MIRACLS 30-keV Device
R = (2-3) x m/Δm | > 100,000
Processing time | 3 ms
Ion flux | > 105-109 ions/s depending on m/Δm

## Slide 19: The new ISOLDE MR-ToF mass separator
Floor space: ca. 3 m x 1 m

## Slide 20: The new ISOLDE MR-ToF mass separator
Identical to MIRACLS 30-keV MR-ToF device for CLS studies (except of drift tube length and shortened injection optics)
Worldwide first MR-ToF device operating at ion beam energies exceeding a few keV
Floor space: ca. 3 m x 1 m

## Slide 21: Summary
 | MIRACLS 30-keV Device
R = (2-3) x m/Δm | > 100,000
Processing time | 3 ms
Ion flux | > 105-109 ions/s depending on m/Δm
Paul trap settings
Injection optics
MR-ToF settings
30-keV beam energy

## Slide 22: Thanks!
https://miracls.web.cern.ch/
F.M. Maier (CERN, U. Greifswald)
F. Buchinger (McGill University)
L. Croquette (McGill University)
P. Fischer (U. Greifswald)
S. Freeman (CERN)
H. Heylen (CERN)
F. Hummer (CERN, McGill University)
C. Kanitz (CERN)
S. Lechner (CERN, McGill University)
E. Leistenschneider (CERN)
G. Neyens (CERN, KU Leuven)
P. Plattner (CERN)
A. Roitman (McGill University)
M. Rosenbusch (Wako)
L. Schweikhard (U. Greifswald)
S. Sels (CERN)
M. Vilen (CERN)
F. Wienholtz (CERN)
S. Malbrunot-Ettenauer (CERN, TRIUMF, Toronto)
Relevant literature:
S. Sels, F. Maier et al., Phys. Rev. Research 4, 033229 (2022)
F. Maier, M. Vilen et al., NIM A 1048, 167927 (2023).
F. Maier et al, to be submitted to NIM A.

## Slide 23: Simulated performance
30-keV, ~300 K
1.5-keV, Doppler cooling
1.5-keV, ~300 K
1.5-keV MIRACLS simulated
Existing low-energy devices
30-keV MIRACLS simulated
0 20k 40k 60k 80k 100k 120k 140k

## Slide 24: Study of the interaction of two ensembles of different ion species
Simulations with m/Δm ≈ 2500:
Peak coalescence effect
Ion throughput is limited.

## Slide 25: Space charge studies in MIRACLS low-energy setup.
Collisional excitation measurements:
Inelastic collisions between Mg ions and residual gas particles  fluorescence
Notes: Study large cloud of ions by technique of coll exc.

## Slide 26: Collisional excitation measurements
24Mg
25Mg
26Mg
0th
1st
2nd
3rd
4th
Tracking of the evolution of the ion bunch’s temporal width over revolution number
Understand ion dynamics within MR-ToF device for varying numbers of stored ions
S. Lechner et al., Hyperfine Interact. 240, 95 (2019).
F. Hummer, BSc thesis, 2019.

## Slide 27: Simulations vs experiment
24Mg+, 34th revolution
≈ 4000 ions
≈ 20,000 ions
Time of flight (µs)

## Slide 28: Simulations vs experiment
Coulomb interactions influence ion dynamics, e.g. selfbunching effect for large ion densities.
24Mg+, 34th revolution
≈ 4000 ions
≈ 20,000 ions
Time of flight (µs)
Notes: Simulations reproduce space charge effects.

## Slide 29: Simulations vs experiment for different operation modes.
Isochronous mode: dt1/dE ≈ 0
Smallest dispersions/turn
largest mass resolving power
typical mode for mass measurements and separation
Dispersive mode: dt1/dE < 0
Selfbunching mode: dt1/dE > 0
high N
high N
high N
low N
low N
low N

## Slide 30: Dependence on mass and abundance ratio is very small.
m/Δm = 25,000

## Slide 31: Place MR-ToF device close to ToF focus.
Figure courtesy: A. Finlay
Time focus

## Slide 32: Place MR-ToF device close to ToF focus.

## Slide 33: Isochronous operation
Penetration depth difference ∆x needs to allow to achieve dt1/dE ≈ 0.
Only possible for certain MR-ToF geometries and potential distributions.
Energy spread tolerance: ΔE/E ≈ 1%

## Slide 34: Does faster MR-ToF mass separation increase ion flux?
Initial time spread ∆t0 mainly governed by Paul trap preparation
Storage time ts needed to obtain R=5000
Max. ion number Nmax to be able to mass separate > 93% of the ions
Ion flux = Nmax/ts (as defined for our purposes)
Exemplary simulation studies with m/Δm=2500, m=24 u, abundance ratio 9:1

## Slide 35: Does faster MR-ToF mass separation increase ion flux?
Initial time spread ∆t0 mainly governed by Paul trap preparation
Storage time ts needed to obtain R=5000
Max. ion number Nmax to be able to mass separate > 93% of the ions
Ion flux = Nmax/ts (as defined for our purposes)
Exemplary simulation studies with m/Δm=2500, m=24 u, abundance ratio 9:1

## Slide 36: Does faster MR-ToF mass separation increase ion flux?
Initial time spread ∆t0 mainly governed by Paul trap preparation
Storage time ts needed to obtain R=5000
Max. ion number Nmax to be able to mass separate > 93% of the ions
Ion flux = Nmax/ts (as defined for our purposes)
Exemplary simulation studies with m/Δm=2500, m=24 u, abundance ratio 9:1

## Slide 37: Does faster MR-ToF mass separation increase ion flux?
Initial time spread ∆t0 mainly governed by Paul trap preparation
Storage time ts needed to obtain R=5000
Max. ion number Nmax to be able to mass separate > 93% of the ions
Ion flux = Nmax/ts (as defined for our purposes)
Exemplary simulation studies with m/Δm=2500, m=24 u, abundance ratio 9:1

## Slide 38: Does a larger beam energy increase ion flux?
A=24
A=28-152
A=132
0 20k 40k 60k 80k 100k 120k 140k
30-keV MIRACLS simulated
m/Δm
0 20k 40k 60k 80k 100k 120k 140k
1.5-keV MIRACLS simulated
Existing low-energy devices

## Slide 39: Important notes
Simulated dispersions/turn are multiplied by factor 3 to achieve a good agreement with exp. data for all shown figures of mass resolving power versus storage time. This mismatch is attributed to residual gas present in the experimental setup but not in the simulations.