## Slide 1: FCC-hh ring design meeting #2
M. Giovannozzi
Acknowledgements: A. Abramov, W. Bartmann, R. Bruce, S. Calatroni, F. Cerutti, R. Lopez, N. Mounet, G. Perez-Segurana, T. Risselada, P. Thonet, E. Todesco

## Slide 2
Outline
On-going activities:
  PA31V3.0
  Optics design
  Transfer lines in ring tunnel
  Operating temperature of beam screen
  General points

## Slide 3
On-going activities: PA31V3.0
New layout
  The ring circumference will be further shortened for matching the harmonic number of FCC-hh and its injector and for improving the ring placement.
V2.0
  Lcell = 215.294 m; LCirc = 91104.686; Ncell = 42;
  Lss = 1400 m; Lss = 2143 m;
  q0 =+10.88 deg; PAlat = 46.2467465 deg; PAlon = 6.09718737 deg;
V3.0 (beam energy for 16 T is approximately 47 TeV)
  Lcell = 215.294 m; LCirc = 90657.886; Ncell = 42;
  Lss = 1400 m; Lss = 2032 m;
  q0 =+10.90 deg; PAlat = 46.2466 deg; PAlon = 6.0981 deg;
V3.1
  Same as V3.0, but with the experimental IPs radially displaced match those of the FCC-ee rings.

## Slide 4
On-going activities: PA31V3.0
The comparison of the FCC-hh ring and the corresponding FCC-ee ring showed large displacements that should be fixed in the future.

## Slide 5
On-going activities: optics design
V1.0
  It includes new optics for collimation insertions and new PB optics.
  Preparation of a thin lens lattice for collimation studies to validate the new optics.
V3.0
  Development of a 16-dipole cell design: see presentation by Gustavo.
  The decision has been taken to injection the beams in the outer channel.
  Decision to replace normal conducting separation dipoles in experimental insertions with superconducting ones. At present, HL-LHC performance is assumed, but following aperture studies we will better specify the magnets. This would enable gaining useful space in the insertion.

## Slide 6
On-going activities: transfer lines in ring tunnel
Optics design:
  Same regular cell as that of the FCC-hh ring. This design will be used also for the part of the transfer lines outside of the ring tunnel.
Magnet design:
  Two solutions available:
    Normal-conducting magnets
    Permanent magnets
  Overall magnet design available, integration studies to be launched.

## Slide 7
On-going activities: beam screen temperature
Thanks to the decision to perform a coating of the beam screen (with amorphous carbon) it is possible to operate the beam screen at higher temperature.
The best choice seems to be 70 K
Using the information in
  L. Tavian, Cryogenics, FCC Collider Kickoff Meeting, Univ. Geneva, Switzerland (2014), https://indico.cern.ch/event/282344/contributions/1630775/
  It is possible to estimate the gain with respect to the CDR

## Slide 8
General points
HTS coating of beam screen
  Excellent progress by the collaboration working on this topic.
  N. Mounet has joined our team to support beam dynamics aspects of these activities.
Collimation and beam dynamics simulations
  Possibility to collaborate with Pakistan Atomic Energy Commission (PAEC). Details are being worked out.

## Slide 9: Thank you for your attention!