## Slide 1: IMCC Annual Meeting 2023 - Orsay Design of the target system and shielding
by Rui Franqueira Ximenes (CERN-SY-STI-TCD)
M. Calviani1, F. Saura1, Christophe Y. Mucher1,
Anton Lechner, Daniele Calzolari CERN – Systems Department, Sources Targets Interaction (STI), Targets Collimators Dumps (TCD)
2023/06/20

## Slide 2: Outline
WP4.2 - Target system development
Establish a baseline target
Identify technological limits and R&D.
Define a system conceptual design
Estimate pion yield, target lifetime, heat load on the surrounding magnets.
Define the required shielding and associated magnet aperture

## Slide 3: Carbon target & target systems considerations
  Energy deposition & dpa studies on the Target, windows, shielding, magnets, chicane
  Parameterization study in view of pion/muon yield optimization
  Conceptual Engineering study of Target & Target Systems, shielding, p+ dump -> feasibility
  ++ iteration loops with p+ driver, magnets, cooling
Production target
Tapering region
Chicane
Eventually p+ dump

## Slide 4: TARGET SYSTEM & SHIELDING DESIGN & INTEGRATION

## Slide 5: Target System & shielding
5
Shielding (Tungsten)
HTS
Neutron absorber (water and boron carbide layer)
Target Titanium vessel
Stainless Steel wall
Cooling Helium
Titanium Outer Vessel
Vacuum
170
590
171
548
Static Helium
150
R15
C-Target
800
P+ Beam
Target He coolant (RT)
Shielding He coolant (RT)
Thermal Radiation shield
Stainless Steel Shielding vessel
water moderator
Target p+ beam pipe
Non cooled shielding
To be optimized with WP4 & WP7
Inside solenoid cryostat
Outside solenoid cryostat

## Slide 6: Carbon Target Systems
6
Integration of Target System in cryostat*
*Solenoid cryostat design >> See Carlotta Accettura & Antti Kolehmainen
presentation (WP7)

## Slide 7: Carbon Target: engineering feasibility
  Target Cooling
  Due to high T and sublimation of graphite, an enclosed ‘pressurized’ atmosphere is required.
  However, active cooling can be made indirectly. Heat dissipation mostly via radiation and natural convection. → target confinement / separation of cooling system is advantageous (maintenance, RP, disposal, cooling services requirements).
Maximum temperature and power deposition for 1.5 MW as function of the beam sigma.
Direct cooling considerations
Old concepts

## Slide 8: Carbon target
8
Inner vessel
Outer vessel
Vessel support
Target rod
Muon/ Downstream Beam window
Water OR Helium cooling connections
Static He
Target support structure
P+ Beam
Centring rings
Target beam pipe
Flange
Static He
Welded connections
CERN’s CNGS Target

## Slide 9: Carbon target
9
Target cooling system routed upstream.
Either contained in outer tube or “free”
P+ window outside cryostat assembly
More accessibility for maintenance, replacement, etc
Inside solenoid cryostat
Outside solenoid cryostat
Look-alike services routing at CERN’s SPS internal dump (TIDVG5)
All welded connections, except downstream target flange
Plenum for He distribution

## Slide 10: Beam windows
  For these beam parameters, C-Target seems feasible.
  However, for the p+ beam window :
  Fatigue: extensive load cycles to be experienced by the target & windows (108 /y) at very high temperature.
  DPA: >>1 dpa levels on the beam windows.
    Possible strategies: windowless, blown-up beam somewhere upstream, dual bunch, rotating window “dilution”, frequent window exchange.
  High power deposition: 50-650 W (0.1 – 1 mm)
Carbon Target
DPA on proton beam window.
Ti, 2 MW, 200 days of operation
DPA on proton beam window.
Be, 2 MW, 200 days of operation is approximately 50x lower! Work on going

## Slide 11: Beam windows
11
P+window
Location:
  P+ window outside cryostat assembly
  More accessibility for maintenance, replacement, etc
Beam dilution
  Mechanical dilution (window moves periodically)
  Beam position change
  Wide beam spot size. How much is reasonable?
  Multi bunch pulse?
Materials
  Low density. Be, Al, Glassy Carbon?
  Radiation damage robustness. Inconel 718 ?
Cooling
  Dedicated, shared with Target?
Carbon Target
P+
Beam window
……
Cryostat

## Slide 12: Target Shielding
Energy deposition
The energy deposited on the target is only 5.6 % (D30xL800 mm) of the total beam power
Most of the thermal energy is deposited on the shielding (33.7 %).
Power deposition provided by Daniele Calzolari SY-STI-BMI
https://indico.cern.ch/event/1176034/contributions/4939053
Parameter | Thermal power | % of Beam Power
Shielding | 674 kW | 33.7 %
Target | 111 kW | 5.6 %
Ti Vessel | 24 kW | 1.2 %
Water* | 11 kW | 0.6 %
Helium** | ~0 kW | ~0 %
TOTAL | ~820 kW | ~41 %
*New baseline is He cooled Target
**He coolant of the shielding
2 MW
Beam power

## Slide 13: Target Shielding
Shielding water cooled
Cooling of the shielding is required but not a showstopper
Example of reasonable parameters: (1.5MW, initially study)
Shielding
26 pipes w/ RT water @ 3m/s
max T = 350 °C
External max T = 80 °C
Target
Annular RT water @ 3m/s
Max T = 2530 °C
Al vessel max T: of = 40 °C
Challenges
Radiolysis
Pressure bursts during pulse
Requirement of corrosion-erosion protection of W
Water cooled
1.5 MW (initially assessment)

## Slide 14: Target Shielding
Shielding He cooled: Feasible for 2 MW
Shielding “pie slices” + He via holes
He (gas cooled, 3-5kg/s at few bar)
Frame with 40 mm square SS profiles
Temperatures below 100 °C
Shielding “pie slices” + He in outer Diameter
He (gas cooled, 3-5kg/s at few bar)
Frame with 40 mm square SS profiles
Temperatures 150 – 750 °C
Shielding “donuts” + He in pipes & outer Diameter
150x D5mm pipes; 0.0022 kg/s/pipe; 10 bar; Mach 0.1 (high HTC); 570 C max W temperature.
Tunning cooling parameters (HTC, pressure drop, speed, mass flow)
He cooled
>> See Francisco Esteban presentation tomorrow

## Slide 15: Target Shielding
Possible optimization to reduce radiation damage in HTS coils:
With neutron absorber, DPA reaches values of 8×10-4 DPA after 1 year
However, due to less W the Ionizing dose increases: >70 MGy after 10 years (3 cm H2O)
1.5 MW (initially assessment)

## Slide 16: Target Shielding
16
Conceptual Design
Donut + Pie blocks due to manufacturing limitations & to ease assembling.
Inner holes for bulk cooling. Return circuit on the outer radius.
Longitudinal slots for locking & alignment pins.
…
Considerations
Material choice (W, W heavy alloys)
Manufacturing & machining
Handling
Integration of cooling system
Shielding assembly

## Slide 17: Target Shielding
17
Conceptual Design
Holding the assembly (23 tonnes).
  Self-holding assembly, e.g. puzzle-like shape.
  Alignment pins & structural rods
He distribution
Water moderator & neutron absorber
He plenum
He return outlet
H2O moderator
Inlet guide plate & tubes
Boron carbide

## Slide 18: Target Shielding
18
Shielding vessel
Two half-shells pressed and welded; Loose fitting seamless/welded, other..
Shielding (vessel) supported via structural beam+ feet at the extremities of the cryostat. Avoid mechanical and thermal load on the solenoid
e.g. 11 tesla magnets pressed + welded half-shells

## Slide 19: Conclusions
Main objective is to have a high-level design, integrated with WP3 and pinpoint key design, manufacturing and integration directions. Potentially identify key constrains and limitations of the whole assembly and possible prototyping directions.
Conceptual 3D design of the target systems & integration in the solenoid cryostat just started.
  Mostly de-coupled Target and shielding assemblies
  Services routed upstream. Fine integration of connections with the cryostat vessel is required
  Target assembly with p+ beam window outside cryostat for easier maintenance/replacement & possibly to allow implementing a solution for the high yearly radiation damage & thermal power during operation.
Integration of P+ dump to be addressed.
19

## Slide 20
Thank you very much for your attention

## Slide 21: Proton dump beam extraction
  Extraction in the chicane is very challenging.
  Tilted beam required to extract in the tapering region

## Slide 22: Proton dump beam extraction
  9 deg angle to extract before chicane.
  Integration with the magnets to be done (~10x10cm aperture)
  Target response to be checked
Particle fluence profile (axial direction & transverse direction)
by Daniele Calzolari https://indico.cern.ch/event/1256505/contributions/5277355/

## Slide 23: Conclusions
Interaction between different groups (proton driver, magnets, target, muon cooling, service groups) is key for efficient feasibility studies and optimization.
Possible to select range of beam parameters compatible with C-Target (both thermally and structurally). Pion/muon yield near optimal range following parametric study.
Fatigue and radiation damage will be a major challenge of a solid target and of the beam windows. Topic to be discussed in the framework of the RaDIATE Collaboration
Shielding design highly coupled with Target/solenoid design and respective radiation damage limitations. (O)700kW cooling needs for 2 MW facility.
P+ dump required. Challenging integration.
Feasibility of liquid lead target being studied (ongoing collaboration between CERN-STI & ENEA). Alternative for > 2MW range operation, but with challenges to be addressed.
W powder target studies to ramp-up, built on current experience at RAL.

## Slide 24: Prospects
Develop the conceptual design of the target systems (Target, Shielding, cooling, etc) and its integration in the solenoid cryostat.
Address the high levels of dpa in the proton window & cooling needs.
Assess the mechanical response of the target vessel and shielding assembly.
Continue interaction/iterations with WP7 & WP3.
Carry-on the required energy & dpa studies through the target complex & provide pion/muon yield calculations to the cooling team.
Continue the development of the liquid Pb curtain target
Ramp-up fluidized W target studies