## Slide 1: RF in strong B-field test stand motivation and requirements
Claude Marchand
CEA Paris-Saclay
IMCC Annual Meeting
June 20, 2023

## Slide 2: Outline
Claude Marchand / IMCC annual meeting 2023
Problematic of NC RF cavities for the muon cooling complex in high magnetic fields:
  Overview of MTA (Mucool Test Area) experimental results:
  MICE 201 MHz and Mucool 805 MHz cavities in B field up to 4T
  Model(s) that explain existing RF BD results in magnetic field
Further tests are needed to consolidate models and test new BD mitigation solutions:
  Different cavity materials, operating temperatures, frequencies, RF pulse length …
  Calls for new RF test stand(s) à la MTA: cavity, RF power source, solenoid field …

## Slide 3: RF system for 6D cooling (MAP study)
Rectilinear channel contains some of the most challenging
NC cavity designs in terms of required RF gradient and B-field
Before bunch merge
After bunch merge
B field
[T]
Claude Marchand / IMCC annual meeting 2023

## Slide 4: Summary of NC RF cavities tests in high B field (MTA)
State of the art (not complete):
MICE 201 MHz RF module prototype (beryllium windows):
5T fringe field, 11 MV/m, 1ms@1Hz
MUCOOL 805 MHz pill box cavity,
Cu & Be windows:
Cu: 3T, 13 MV/m, 30ms@10Hz
Be: 3T, 50 MV/m
MUCOOL Gas filled RF cavity:
  3 T, 65 MV/m 805 MHz molybdenum cavity
44cm
28.4cm
Claude Marchand / IMCC annual meeting 2023
(comprehensive review by Derun Li, CERN LDG meeting 2021)

## Slide 5: Summary of NC RF cavities tests in high B field (MTA)
State of the art (not complete):
MICE 201 MHz RF module prototype (beryllium windows):
5T fringe field, 11 MV/m, 1ms@1Hz
MUCOOL 805 MHz pill box cavity,
Cu & Be windows:
Cu: 3T, 13 MV/m, 30ms@10Hz
Be: 3T, 50 MV/m
MUCOOL Gas filled RF cavity:
  3 T, 65 MV/m 805 MHz molybdenum cavity
Claude Marchand / IMCC annual meeting 2023
(comprehensive review by Derun Li, CERN LDG meeting 2021)

## Slide 6: Some initial results on 805 MHz PB cavity with Cu
Claude Marchand / IMCC annual meeting 2023
A. Moretti et al., Phys.Rev.Acc.Beams 8, 072001 (2005)
Fowler-Nordheim Enhanced Field Emission current:
+
-
+
-
-
-
+
+
bm/
where is the enhancement factor
due to microscopic emmiter sites

## Slide 7: Breakdown model: beamlet focused by magnetic field
Model developed by US labs, checked against measurements in high . papers: Palmer et.al PRAB 2009, Stratakis et.al NIMPR 2010, Bowring et.al PRAB 2020
Model predicts local temperature rise due to electron bombardment
Breakdown occurs when
Heating due to electron bombardment
Numerical simulations conducted by SLAC collaborators showed trajectories of beamlets in the presence of the 805 MHz pillbox cavity
Thermal diffusion
Electron beamlet
: 38 °C for Cu, 129 °C for Be, 224 °C for Al
Claude Marchand / IMCC annual meeting 2023

## Slide 8: MuCool 805 MHz cavitiy test with modular plates
Be: 0 & 3 T
Cu: 0 T
Cu: 3 T
modular plate
Claude Marchand / IMCC annual meeting 2023

## Slide 9: MuCool 805 MHz cavitiy test with modular plates
Be: 0 & 3 T
Cu: 0 T
Cu: 3 T
modular plate
Claude Marchand / IMCC annual meeting 2023
End of the game ?
(cf. Stratakis statement yesterday):

## Slide 10: MuCool 805 MHz cavitiy test with modular plates
Be: 0 & 3 T
Cu: 0 T
Cu: 3 T
modular plate
Claude Marchand / IMCC annual meeting 2023
Or need for more ?
(Bowring 2020 paper left)

## Slide 11: Scaling using no-diffusion beamlet model
No diffusion
Diffusion
The breakdown model can be simplified: for short pulses
) we can neglect heat diffusion in the wall.
Then the breakdown condition is given by (S. Arsenyev, 2021):
Magnetic field at breakdown
Wall material properties
Field Emission current
Electron energy loss
Pulse length
Cavity-dependent constant
This equation provides scaling laws of on different parameters. Mitigation solutions that follow from this equation:
Very short pulse (sub )
Different wall materials (Al, hard copper alloys)
Low temperature (nitrogen cooling 70 K)
Cavity shape optimization
When combined, benefits from different solutions would multiply
Claude Marchand / IMCC annual meeting 2023
DTplastic

## Slide 12: Benefits of short sub-µs pulse
6 increase in B
3 increase in E
Going down from 10 ms to 300 ns pulse would dramatically improve cavity breakdown performance
300 ns pulse length needs an over coupled cavity and a 23 MW klystron (only a factor of 2 increase from Litton 805 MHz 12 MW klystron)
Claude Marchand / IMCC annual meeting 2023

## Slide 13: Comparing breakdown mitigation ideas
Benefits of short pulse and aluminum multiply
Aluminum cavity with a short pulse looks very promising
This plot is not intended to give absolute values for breakdown threshold, but only a feeling of which solutions can be more promising. We scale curves from MUCOOL cavity study ( so the no-diffusion model applies only approximately)
Scaled from the first 3 curves using the scaling model (slide 7)
Claude Marchand / IMCC annual meeting 2023

## Slide 14: R&D directions for NC RF cavities tests in high B field
Need high gradient RF test stand(s) with B field up to ~10T Test cavities for technology development
  Frequency: ideally 300 to 700 MHz range
    tests at higher frequencies useful, but need some rescaling to MCC f range
  Gradients from 25 to 50 MV/m
  Short RF pulses (~ms)
  Magnetic field: 0 – ~10T, different field configurations
  Different materials: Cu, Be, Al, …
  Different temperatures: 300K -> 70K ->…
  Different cavity shapes ?
Claude Marchand / IMCC annual meeting 2023

## Slide 15: General layout of the RFMF test station
Preliminary design is aimed at fitting a cavity of the size up to a 700 MHz system
Minimum bore of the split coil
   600 RT free bore for RF  700 mm minimum SC coil diameter
Scheme 1: single cryostat
Scheme 2: split cryostat
WP8 - RFMF test station - L. Rossi et al. UMIL&INFN
Claude Marchand / IMCC annual meeting 2023

## Slide 16: CEA setup with the 4T MICE AFC magnet
MUCOOL setup
5T magnet, 805 MHz
CEA setup
4T magnet, 704 MHz
47 cm bore of the MICE AFC magnet will tightly fit the cavity
47 cm
B-field
32.6cm
44cm
28.4cm
Claude Marchand / IMCC annual meeting 2023

## Slide 17: Effect of the RF frequency in beamlet model (Stratakis)
Claude Marchand / IMCC annual meeting 2023
-> E805/E201=1.58
Factor 2.6
While classical RF BD
(Wang&Loew 1997) predicts less frequency dependence:

## Slide 18: Effect of the RF frequency (G. Ferrand).
A few simulations of particle in pillboxes with Matlab. Example at 0.5 T.
Simulation at 700 MHz, 0.5 T, 30 MV/m
Simulation at 2 100 MHz, 0.5 T, 30 MV/m
At 2.1 GHz, an identical focusing of the electron beam than at 700 MHz occurs at 2xB.
Claude Marchand / IMCC annual meeting 2023

## Slide 19: RF test stand requirements
Frequency:
  Ideally the ones chosen for the 6D cooling (325-352/650-704 MHz)
  But the lower the frequency, the bigger the solenoid bore diameter and $$$
  -> tempting to perform BD tests at higher f (3 GHz), but have to rely on models to rescale to MCC frequencies
Magnetic configuration:
  two coils SC solenoid, B up to 5T min, ideally 10T, same and opposite polarization (~20T/m)
  Bore diameter depends on frequency and exact cavity design (w/wo 70 K cooling)
  -> e.g. for 704 MHz, 60 cm free RF bore desired
RF power sources:
  ~10’s MW range: depends on cavity Q factor and highest needed RF gradient
  -> e.g. for a PB cavity at 704 MHz (Cu) and 50 MV/m : ~7 MW peak
  Pulses from sub ms to ~0.1 ms, the higher the rep. rate, the faster the cavity conditioning
Test stand shielding:
  Radiation shielding against high FE at highest RF gradients
  May also need magnetic shielding due to extended solenoid stray field
Claude Marchand / IMCC annual meeting 2023

## Slide 20
Thank you
for attention