## Slide 1: LINAC Activities at CERN
Alessandra Lombardi and the Hadron Sources and Linac team
The Superconducting Proton Linac (SPL)
Achievements with LINAC4
Activities on RFQ redesign
Conclusions and outlook
Radio Frequency Quadrupole 352MHz
Fast Chopper – 1MHz
source
Emittance metre
Solenoid
Source test stand

## Slide 2: LINACs for ν-fact or µ-collider – CERN 2010
352MHz
704 MHz
7 Dec 2020
SPL parameters

## Slide 3: Building blocks of the superconducting part

## Slide 4
Frequency : 352 MHz
Duty cycle for PSB : 0.06 %
Max duty cycle : 5%
Located 12m underground
Notes: Add lines to indicate the PSB and the PS

## Slide 5: Baseline beam parameters
LINAC4 – CDR -2006 | LINAC4 – achieved (2016) | Comments – general | Comments – mucoll specific
H- | Stripping and more tested in Half Sector Test |  | 
70mA peak at the source 65 ma peak at 3 MeV 40 mA after chopping | 50mA peak (in twice the acceptance of the RFQ) 30 mA peak at 3 MeV (record) 20 mA after chopping | Peak current from the source Average beam current after chopping (LEBT and RFQ transmission and chopping factor) | Missing a factor 2 for the high current
160 MeV | 160.48 MeV | All RF structures performing to specs | 
0.4 π mm mrad | 0.3 π mm mrad (at 160MeV) | Smaller emittance , allows for more turns injected | 
400 µsec 1Hz (4 rings) | Up to 600 µsec 1Hz | Longer injection in the PSB (100-150turns) | Longer pulse and ducty cycle is possible
Fast Chopping at 3 MeV 2µsec inj kicker rise-time | Demonstrated , including transmitted beam quality | Unprecedented flexibility, to be exploited Beam from 1µsec to 150µsec | Repetition rate (40MHZ) not demonstrated
Energy painting with the last accelerating modules |  |  | Flexibility in the longitudinal plane

## Slide 6: Measuring at 3 MeV : CHOPPING removing microbunches (150/352) to adapt the 352MHz linac bunches to the 1 MHz booster frequency
Match from the RFQ
Match to the DTL
Chop
Meas 2014
Beam current downstream the dump

## Slide 7
Beam to the LBE !
LBE
Beam phase spread at 160 MeV – in specs.
96% transmission from 3 MeV to the LBE – 23mA suitable for all pre-LS2 beams
Emittance measurements in LBE – as expected
Availability
93.9%
Pre-injector
Accelerator
Transfer Lines

## Slide 8: Pulse Flatness and chopping
600 μs long 25.5 mA pulse just upstream the LINAC4 dump (red curve). The pulse flatness meets the specification for each of the 4 Booster rings
Zoom into start of Ring 4 with nominal chopping pattern;
Top: BCT in transfer line; bottom: output voltage (neg./pos.) of chopper plates.

## Slide 9: Longitudinal stability and painting
Measured phase variation for 100 μs long pulse when a energy variation is programmed along the pulse –proof of principle of energy painting
The beam phase spread along the pulse is within specs – RF regulation is ok

## Slide 10: Beam Intensity and Transmission
Excellent transmission from 3 MeV to the LBE
Routinely 23mA (un-chopped) that allows the production of all the pre-LS2 beams
H- beam intensity on the 15 transformers along the linac and transfer lines
Pre-injector
Accelerator
Transfer Lines

## Slide 11
2013: Comparison of measured emittance (yellow) and RFQ acceptance (pink). The expected transmission thru the RFQ is 75%. (PARMTEQ + TOUTATIS).
16mA
IS-O2
(25mA in RFQ acceptance)
IS-04
(50mA in RFQ acceptance)
IS-O3
(35mA in RFQ acceptance)
3m high-field (2018)
RFQ3
2021
Source redesign
RFQ redesign
CERN 2013 : pre-injector challenge
Edgar Sargsyan talk

## Slide 12
2013: Comparison of measured emittance (yellow) and RFQ acceptance (pink). The expected transmission thru the RFQ is 75%. (PARMTEQ + TOUTATIS).
16mA
IS-O2
(25mA in RFQ acceptance)
IS-04
(50mA in RFQ acceptance)
IS-O3
(35mA in RFQ acceptance)
3m high-field (2018)
RFQ3
2021
Source redesign
RFQ redesign

## Slide 13: Common design guidelines
Input/output energy : 45 keV/3MeV;
a two-term potential vane profile, a constant average aperture radius and a constant transverse radius of curvature for an easier tuning and the possibility of machining with a 2D cutter;
Constant voltage profile;
Transmission higher than 90% for emit=0.5µm rms normalised I=70mA

## Slide 14: RFQ design – copper
General Guidelines:
Stay below the RFQ1 line
Transmission>90 for emit=0.5 mm mrad and I=70mA
rho/ro=0.7 -1
Two versions
  L=4.5 m to avoid dipole rods
  L=as short as possible.

## Slide 15: 4.5 m
RFQ parameters | 
Length m | 4.5
Vane voltage kV | 79
Max electric field (MV/m) | 33
Peak RF power kW | 750
Average aperture (r0) mm | 3.2
Transverse radius (ρ) | 2.7
Maximum modulation | 1.5
Minimum aperture mm | 2.5
Focusing parameter (B) | 5.87
Phase at gentle buncher deg | -35
Transmission % (70mA , 0.5 mm mrad) | 93.2
Chart: modulation, aperture and phase vs length (cm)
Chart: pole tip max field (MV/m) vs length (cm)

## Slide 16: Beam dynamics – 70mA emit =0.5mm mrad
Transverse (x, y top) and longitudinal planes (phase, energy spread) along the RFQ
Beam at the RFQ output plane

## Slide 17: 3.9 m
RFQ parameters | 
Length m | 3.9
Vane voltage kV | 79
Max electric field (MV/m) | 33
Peak RF power kW | 650
Average aperture (r0) mm | 3.2
Transverse radius (ρ) | 2.2
Maximum modulation | 1.8
Minimum aperture mm | 2.2
Focusing parameter (B) | 5.76
Phase at gentle buncher deg | -32
Transmission % (70mA , 0.5 mm mrad) | 95.4
Chart: modulation, aperture and phase vs length (cm)
Chart: pole tip max field (MV/m) vs length (cm)

## Slide 18: Beam dynamics – 70mA emit =0.5mm mrad
Transverse (x, y top) and longitudinal planes (phase, energy spread) along the RFQ
Beam at the RFQ output plane

## Slide 19: RFQ design – new material
General Guidelines:
Field up to 50MV/m for 78 kV (cryo-copper)
Respect scaling –
  120kV and 42.3 MV/m
  140kV and 39.3 MV/m
Transmission > 90% for emit=0.5 mm mrad and I=70mA
rho/ro=0.7 -1
L as short as possible
Best beam quality

## Slide 20: 2.5 m 120 kV
RFQ parameters | 
Length m | 2.5
Vane voltage kV | 120
Max electric field (MV/m) | 44
Peak RF power kW | 960
Average aperture (r0) mm | 4.1
Transverse radius (ρ) | 4.1
Maximum modulation | 2.2
Minimum aperture mm | 2.4
Focusing parameter (B) | 5.54
Phase at gentle buncher deg | -32
Transmission % (70mA , 0.5 mm mrad) | 91.2
Chart: pole tip max field (MV/m) vs lenght (cm)
Chart: modulation, aperture and phase vs length (cm)

## Slide 21: Beam dynamics – 70mA emit =0.5mm mrad
Transverse (x, y top) and longitudinal planes (phase, energy spread) along the RFQ
Beam at the RFQ output plane

## Slide 22: Comparison of performance-method
Comparison of performance
    Simulations
    Current through the RFQ
Parameters :
  emittance at the RFQ input plane : 0.2 to 0.9 µm
  Matching :
  Transverse beam distribution : uniform, parabolic, gaussian
  Current : range 0-60mA
  Energy dispersion

## Slide 23: Comparison of performance – results
Current of 60 mA needs to fit in an emittance of 0.4 for RFQ1 vs in an emittance of 0.8 for RFQ3 to give 48mA out of the RFQ
Chart: transmission vs emittance at fixed current - 40 mA
| 0.9 | 0.8 | 0.6 | 0.4 | 0.2
RFQ1 | 57 | 67 | 77 | 86 | 95
RFQ3-4.5m | 76 | 82 | 92 | 97 | 99
RFQ3-3.9m | 69 | 77 | 88 | 96 | 99
RFQ3-2.5m | 79 | 86 | 94 | 98 | 99
Chart: transmission vs emittance at fixed current - 60 mA
| 0.9 | 0.8 | 0.6 | 0.4 | 0.2
RFQ1 | 54 | 64 | 74 | 82 | 91
RFQ3-4.5m | 73 | 80 | 91 | 96 | 98
RFQ3-3.9m | 67 | 74 | 87 | 95 | 97
RFQ3-2.5m | 75 | 81 | 91 | 96 | 97

## Slide 24: Summary
The SPL design of 2010 still holds
The normal conducting part of the proton driver (LINAC4) is almost fit for high power linac : main issue is brightness of the pre-injector.
Chopping should be upgraded to faster rep rate
Substantial progress on the source brightness : next talk by Edgar Sargsyan
There are 3 designs for an RFQ that fits the specifications of LINAC4 at higher beam current and emittance. All designs have a transmission of more than 90% for a beam of 70mA with rms emittance 0.5 mm mrad. Two of the RFQ designs are based on RF parameters similar to RFQ1 whereas a very short RFQ is based on a surface field higher than what is attainable with room temperature copper.