## Slide 1
H- stripping:
Operational issues and
Challenges at high-energy,
high-intensity stripping

## Slide 2
Background of this talk
A high-energy and high-intensity SC H- linac with successive charge-exchange
injection into a storage ring* are in consideration.
(* A rapid cycling synchrotron (RCS) could also be an option)
Overview of the operational issues in a high-intensity proton driver
(J-PARC RCS) and high-energy stripping challenges are presented.
A high intensity proton driver is needed for the Muon Collider.
Intensity: ~ 2 MW  Higher than existing to date.
The challenges are thus beyond those facing in the running machines to date.

## Slide 3
The H- charge exchange injection (CEI) is an efficient way to increase the proton
beam power with multi-turn injection into a synchrotron or storage ring.
The beam loss can be kept sufficiently lower as compared to p injection.
A stripper foil is conventionally used for an H- stripping to proton.
However, this becomes complicated and have several following issues,
especially dealing with high-intensity beam.
• Lifetime of the stripper foil.
• Maintaining and controlling the partially stripped (H0) and unstripped
H- and their proper disposal.
• Excited state of H0 and the beam loss from H0* decays outside the aperture.
• Stripped electron collections.
• Beam loss, especially uncontrolled ones caused by the foil scattering.
An optimum transverse painting (TP) at injection is needed to minimize
foil hitting of the circulating beam during multi-turn injection.
. . . . . . . . . . .
High-power H- charge-exchange challenges

## Slide 4
Overview of running high-intensity (MW class)
proton machines
Parameter | SNS in Oak Ringe | J-PARC RCS
Type | Storage ring | Synchrotron
H- IS peak (mA) & inj. beam power (MW) | < 40 1.4 | > 50 0.133
Inj. pulse (ms) | 1 | 0.5
H- stripping type & stripping efficiency (%) | Multi-turn H- CEI by foil 95% | Multi-turn H- CEI by foil 99.7%
Ein / Eout (GeV) | 1 / 1 | 0.4 / 3
Beam power (MW) | 1.4* (1.5 E14/pulse) | ~1** (~1E14/pulse)
SC tune shift | ~0.1 | ~0.15
* 1.55 MW to date. Upgrading for > 2 MW (By increasing inj. beam energy and peak current)
** ~ 1 MW to date. Demonstrated 1.5 MW potential. Studying towards 2 MW!
(By increasing injection pulse length & peak current)
◆ SNS in Oak Ridge: 1.4 MW designed
◆ RCS at J-PARC : 1 MW designed
● A multi-MW beam power is thus not that far!
● A higher injection energy has a significant benefit for SC mitigation.

## Slide 5
Beam survival rate
Painting parameter ID
○ Einj=181 MeV, 539 kW-eq. intensity
○ Einj=400 MeV, 553 kW-eq. intensity
By longitudinal
painting
By adding 100p
transverse painting
No painting
Higher injection energy benefits for SC mitigation
This experimental data clearly show a significant gain from a higher
injection energy as well as excellent ability of injection painting.
Space-charge mitigation
by higher injection energy
ID | etp (p mm mrad) | RF V2/V1 (%) | f2 (deg) | Dp/p (%)
1 | - | - | - | -
2 | 100 | - | - | -
3 | - | 80 | -100 | -0.0
4 | - | 80 | -100 | -0.1
5 | - | 80 | -100 | -0.2
6 | 100 | 80 | -100 | -0.0
7 | 100 | 80 | -100 | -0.1
8 | 100 | 80 | -100 | -0.2
Expanded view
Laslett tune shift at inj. energy:

## Slide 6
RCS
(H-  p)
0.43 GeV
MR
330 GeV (p)
H- Linac
(0.4 GeV)
MLF
For NU
experiment
For HD
experiment
Stripping foil
J-PARC Accelerator facility
J-PARC 3-GeV RCS
Beam power: 1 MW
Circulating
beam
Ring
Collimators
ISEP1
ISEP2
PBH1
PBH2
QFL
SB1
SB2
SB3
SB4
QDL
DSEP1
DSEP2
DUMP-Q
QFM
H0 Dump
(4kW)
1st Foil
3rd Foil
2nd Foil
PBH3
PBH4
waste beam
MWPM3
MWPM4
MWPM5
MWPM6
MWPM2
H- beam
PBV1
PBV2
PSTR1
PSTR2
H- beam energy: 0.4 GeV
◆ Stripping foil thickness: 333 mg/cm2
◆ Stripping efficiency (p) : 99.7%
Partially stripping H0 : 0.3% (0.4 kW)
Unstripped H- : 1E-5%
SB 1~4 : Chicane bump
PBH1~4 : Hori. painting bump
PBV1~2 : Vert. painting bump
H- stripping injection at J-PARC

## Slide 7
J-PARC H- stripping issues at high-intensity operation
• Unstripped H- (Controlled)
Determine by the foil thickness and those missing the foil.
Initially negligible (1E-5%), but problems when a foil degradation occurs and using a
smaller size foil. Operational limit from the waste beam dump temperature.
• Partially stripped H0 and their excited states (H0*) losses (Partially uncontrolled):
H0 yield depends on the foil thickness. H0* decays determined by the injection chicane design.
H0 yield: 0.3% (400 W). H0* decay outside the aperture : 6W (Extreme case)
Recently chicane bump field is reduced by 20%.
At the SNS: Foil inside a magnet. Decays immediately. Loss negligible.
Otherwise > 2000 W loss could occur!
• Stripped electron collection (Controlled):
No issues so far. (SNS had problems at earlier commissioning stage)
• Foil lifetime (Controlled so far) P.K. Saha et al., PRAB 23, 082801 (2020)
Foil degradation determines the practical foil lifetime.
Temporary solution: Inserting the foil more to the beam. Foil hitting (scattering) rate increases.
At present ~1 month at 0.9 MW opr. Foil magazine can hold 15 foils.
◆ Foil scattering beam losses (Partially uncontrolled):
Several sources/mechanisms. Determined by the foil thickness & size, and foils hits.
TP minimizes the foil hits.
ー Single Large angle Coulomb scattering: An additional injection collimator was installed in J-PARC.
ー Energy straggling, Multiple scattering, Nuclear interaction: Determined by the foil thickness.
ー Foil hitting rate of the circulating beam: Minimized by the trans. inj. painting and the foil size.
 One of the main issues at J-PARC at high-intensity operation.

## Slide 8
Foil scattering beam loss issues
Fast extraction
­- 1 MW
- 0.87 MW
- 0.77 MW
- 0.5 MW
- 0.3 MW
- 0,1 MW
Measured circulating
beam intensity
• Already achieved the designed 1 MW beam power and tested for a short time operation.
• Maximum Longitudinal and Transverse paintings (LP and TP) are applied for SC mitigation.
• The TP creates uniform beam distributions and also minimize foil hitting rate.
A higher TP reduced foil hitting rate, but TP area depends on the machine aperture,
lattice design, realistic machine errors and imperfections.
 Barely reached to the design TP of 216p mm mrad. The average foil hits/proton is ~ 7.
Time structure of the beam loss
Beam loss occurs only
at injection energy (and
Localized almost at the
Collimator section).
● Estimated beam loss at 1MW: ～0.2% (0.3 kW ) << Collimator limit (4 kW)!
◆ However, residual radiation at the injection area caused by the uncontrolled beam loss due to foil scattering of the circulating beam is rather high.
◆ Reduction of the foil scattering beam loss is a top priority!

## Slide 9
Reduction of the foil scattering beam losses
×
y
y’
Circulating beam
(painting emittance)
Inj. beam
×
Optimization of vertical painting matching
with injection beam. (y’ : -3.3  2.82 mrad)
Minimize number of large amplitude particles.
 Reduce beam loss.
Optimize vert. transverse painting
w.r.t. the smaller inj. by.
・Minimize vert. inj. beam size by manipulating
vert. beta (by) of the injection beam.
・Minimize vertical size of the stripper foil.
+
Foil hitting rate (uncontrolled beam loss) 30% reduced.
The total beam loss at the injection, collimator and 1st arc
sections are 40% reduced in average.
Measured foil scattering beam loss

## Slide 10
Latest beam loss mitigation at 1 MW
◆ The residual beam loss is estimated to be ~0.05%.
 The residual beam loss is dominated by the foil scattering.
◆ We will try to further reducing the foil size.
 Unstripped H- beam power at the waster beam dump is an issue.
Time structure of the beam loss
Comparison: 2020 & 2022
Based on numerical simulations and extensive beam studies following optimizations were implemented.
Minimized injection beam and the foil sizes.
Optimized betatron tunes.
Optimized transverse and longitudinal paintings.
Optimized correction of nx -2ny = -6 resonance.
Reduced 3nx = 19 effect by SB ×0.8 field
(reduced K2 field intrinsic in the SB, H0* decays)
◆ To eliminate foil scattering beam losses and foil lifetime issues,
we are developing laser stripping of H- charge-exchange injection.
1 MW operation can be achieved with a negligible
beam loss!!

## Slide 11
Earlier studies: Project-X design study at Fermilab (HB 2008, 2010 WS, David Johnson)
H- energy : 8 GeV with stripping injection
H- stripping challenges at high-energy & high-intensity
MC case: 5-10 GeV, 2 MW
Kazami Yamamoto et al., PRAB15, 120401 (2012)
Higher secondary particles, hadronic flux at
higher energy.
Residual dose rate around the foil:
1.6 times higher at 1 GeV as compared to 0.4 GeV!
Lorentz stripping:
Curvature radius of the injection magnets
should be long enough to keep a lower
Lorentz stripping of the H- beam.
Needs careful injection design:
・Project-X (8 GeV) inj. case. David Johnson, HB 2008
・H2 should be moderate.
・H3 should be stronger to stripping H0* immediately.
Additional concerns:
Foil scattering and foil lifetime issues
should be further seriously concerned!

## Slide 12
Stripping efficiency and H0 excited states loss
Some of the H0 are in excited states (H0*).
Decays passing through a magnetic field
due to E = b g c B
E is higher for a high-energy beam.
The decay rates depend on the strength of the
magnetic field.
 Higher at higher H- energy
At 8 GeV, H0* > 2 are subjects to concern.
Stripping efficiency of 8 GeV H- as a
function of foil thickness
(Cross sections ref. W. Chou et al.,
NIMA 590, 1-12 (2008))
A foil thickness of 700 mg/cm2 gives
H+ : 99.79%
H0 : 0.21%
H- : ~10-6%
Mike Plum, HB 2016

## Slide 13
To overcome the issues and limitations associated with foil stripping
as well as to realize next-generation multi-MW proton accelerator,
we have to established an alternate method of H- stripping.
 Laser stripping?
Next generation H- stripping injection

## Slide 14
Laser stripping (LS) of H- beam
PRL 118, 074801 (2017)
H-
p
10 ms
H-
H0
H0*
p
e-
e-
e-
UV laser
l= 213 nm
Step 1:
Photo-detection
H- + g → H0 + e-
Step 2:
H0 excitation
H0 + g → H0* (n=3)
Step 3:
photo-ionization
H0* + g → p + e-
YAG Laser
l=1064 nm
YAG Laser
l=1064 nm
e-
SNS (Oak Ridge): Laser-assisted H- stripping
・High field magnets for stripping.
・UV laser (355 nm) for H0 excitation.
・10 ms stripping demonstrated.
・Studies for implementation are underway.
J-PARC: H- stripping by using only lasers
・IR lasers for stripping. Deep UV laser (~200 nm) for H0 excitation.
・Demonstrated 40 ms H- neutralization at 3 MeV.
・A POP test at 400 MeV stripping expected in 2024.
8 GeV H0 excitation. Higher H- energy is suitable.
David Johnson
HB 2010
To reduced the laser energy, a multi-reflection cavity
systems has been developed at J-PARC.
Seeder energy ～1/N, where, N = no. of reflections.
N = 32 achieved. Next trail for N = 64.
Tiny spot focused at the IP  Higher flux
Bigger spot at the mirrors  Reduce mirror damage

## Slide 15
Summary
• The H- stripping injection issues associated with stripper foil at J-PARC are discussed.
• The beam loss at the designed 1 MW has been reduced to an extremely low level
to remain mainly the foil scattering beam losses.
• The foil scattering uncontrolled beam losses and the corresponding residual
radiation at high-intensity operation is one of the concerning issues.
• To overcome the foil issues, a laser stripping of H- is under development.
• Based on the J-PARC and SNS results so far, a multi-MW beam power for
the MC can be achieved without serious issues.
• However, the H- stripping at higher energy and higher intensity becomes more
complicated and challenging.
• The injection system has to be designed more carefully.
• A laser stripping at higher H- energies would be more feasible.

## Slide 16
Extra slides

## Slide 17
Implementation of a smaller by and a smaller foil
Beam loss:
40% reduction at the injection, collimator and 1st arc sections.
Measured foil hits: 30% reduced
Implemented to RCS
operation from 700 kW
Residual radiation
accordingly reduced
by = 8 m
by = 2.4 m
P. K. Saha
s = 2 mm
s = 1 mm
20 mm
For by = 8m
14 mm
For by = 2.4m