## Slide 1: Longitudinal tracking studies for the entire RCS chain
Fabian Batsch, Rama Calaga, Heiko Damerau, Ivan Karpov
Acknowledgements: David Amorim, Scott Berg, Fulvio Boattini, Luca Bottura, Christian Carli, Antoine Chancé, Alexej Grudiev, Elias Metral, Ursula Van Rienen, Daniel Schulte, Sosoho-Abasi Udongwo
IMCC Annual Meeting, Orsay, 21/6/2023
Funded by the European Union under Grant Agreement n.101094300

## Slide 2: Outline
Longitudinal emittance definitions
Bunch length during acceleration
Synchronous phase optimization
Beam-induced voltages and HOM power estimates
Outlook
  emittance growth and budget
  multi-turn effects and induced voltages calculations
Summary
F. Batsch

## Slide 3: Reminder on design baselines
Base for the work is the US Muon Accelerator Program (MAP)
High energy complex consist of a chain of rapid cycling synchrotrons (RCS)
F. Batsch
Part of interest for us
1 bunch per beam

## Slide 4: The RF challenges: Voltage
Installed voltages in lepton rings:
 Even more RF voltage than any other circular collider
 Much fewer turns
 | RCS1 | LEP2 | FCC-ee
Circumference, 2pR [m] | 5990 | 26658 | 91106
Energy factor, Eej/Einj | 5 | 4.8 | n/a
Repetition rate, frep [Hz] | 5 (asym.) | Slow (min.) | n/a
Number of turns | 17 | few 108 | 108
Max. RF voltage, VRF [GV] | 21 | 3.6 | 11.3
Energy gain per turn, DE [GeV] | 14.8 | 3.49 | 10
From talk by H. Damerau

## Slide 5: The RF challenges: Intensity
High bunch charge and current:
Average beam current more than three times (2) above ILC
Very strong transient beam loading
During first turn in RCS1 energy gain is about 20% of beam energy
From talk by H. Damerau
F. Batsch
 | ILC | RCS1 (and RCS2)
Number of bunches, nb | 1312 | 1 each m+ and m-
Bunch spacing, tbs | 554 ns | Trev = 20 ms
Bunch intensity, Nb | 2∙1010 p/b | 2.7 (2.5)∙1012 p/b
Average beam current, Ib | 5.8 mA | 2 x 20 mA

## Slide 6: General parameter table
Detailed parameter table: https://cernbox.cern.ch/index.php/s/I9VpITncUeCBtiz
 | RCS1314 GeV | RCS2750 GeV | RCS31.5 TeV
Circumference, 2pR [m] | 5990 | 5590 | 10700
Energy factor, Eej/Einj | 5.0 | 2.4 | 2.0
Repetition rate, frep [Hz] | 5 (asym.) | 5 (asym.) | 5 (asym.)
Number of bunches | 1m+, 1m- | 1m+, 1m- | 1m+, 1m-
Bunch population | >2.5∙1012 | >2.3∙1012 | 2.2∙1012
Survival rate per ring | 90% | 90% | 90%
Acceleration time [ms] | 0.34 | 1.04 | 2.37
Number of turns | 17 | 55 | 66
Energy gain per turn, DE [GeV] | 14.8 | 7.9 | 11.4
for survival [MV/m] | 2.4 | 1.3 | 1.1
Acc. field in RF cavity [MV/m] | 30 (45 optimistic) | 30 | 30
Max. for fs=45° [GV] | 20.9 | 11.2 | 16.1
 | RCS1314 GeV | RCS2750 GeV | RCS31.5 TeV
Circumference, 2pR [m] | 5990 | 5590 | 10700
Energy factor, Eej/Einj | 5.0 | 2.4 | 2.0
Repetition rate, frep [Hz] | 5 (asym.) | 5 (asym.) | 5 (asym.)
Number of bunches | 1m+, 1m- | 1m+, 1m- | 1m+, 1m-
Bunch population | >2.5∙1012 | >2.3∙1012 | 2.2∙1012
Survival rate per ring | 90% | 90% | 90%
Acceleration time [ms] | 0.34 | 1.04 | 2.37
Number of turns | 17 | 55 | 66
Energy gain per turn, DE [GeV] | 14.8 | 7.9 | 11.4
 | 2.4 | 1.3 | 1.1
Acc. field in RF cavity [MV/m] | 30 (45 optimistic) | 30 | 30
 | 20.9 | 11.2 | 16.1

## Slide 7: The 1.3 GHz TESLA cavity
Relevant beam parameter
  Bunch population >2.2∙1012 large intensity effects
  Ib = 20.4 / 18.8 / 10.0 mA in RCS1/2/3  2x430 kW per cavity
  700 / 370 / 530 cavities distributed over nRF RF stations
  fs = 45° (above transition: gtr = 20.41, 600 < g < 14200)
Cavity parameter (9 cells, L=1.06 m):
  Harmonic number h = 25957 to 46367
  R/Q = 518 W, total Rs = 306 GW
  Gradient of structure 30 MV/m
  QL = 2.2e6 (for beam loading compensation with f = 320 Hz, [ref])
From design report
(with Gacc = 30 MV/m)
(From design report)

## Slide 8: Outline
Longitudinal emittance definitions
Bunch length during acceleration
Synchronous phase optimization
Beam-induced voltages and HOM power estimates
Outlook
  emittance growth and budget
  multi-turn effects and induced voltages calculations
Summary
F. Batsch

## Slide 9: Longitudinal emittance
tyh@fdg.com
Different definitions of the longitudinal emittance and different units co-exist:
Encircling, 1s, 4s, FWHM,…
[eV-s], [MeV-m], [mm] can be converted converted:
F. Batsch
Parameter table from webpage:
MeVm ≙ 0.025 eVs eVs for 4ellipse
[see technical note on unit conversion]
tyh@fdg.com
1st
2st
1sE
2sE
Parameter | Unit | 3 TeV | 10 TeV
L | 1034 cm-2s-1 | 1.8 | 20
N | 1012 | 2.2 | 1.8
fr | Hz | 5 | 5
<B> (average) | T | 7 | 10.5
εL (norm, 1σzσE) | MeV m | 7.5 | 7.5
σE / E | % | 0.1 | 0.1
σz | mm | 5 | 1.5

## Slide 10
The tails must be defined. Equal FWHM bunch lengths but different tail definitions give different encircling emittances:
Tails increase eL by factor of 2
 Increased voltage requirements to increase bucket area
The longitudinal profile definition
µ = 0.5, tL = 4 st
µ = 1 (parabolic)
µ = 2
µ = 3
FWHM,
µ = 1
FWHM,
µ = 2.5
Encircling ,
µ = 1
4s,
µ = 2.5
eL = 0.22 eVs
eL = 0.31 eVs, 4sL = 0.16ps
eL = 0.69 eVs , 4sL = 0.20ps
eL = 0.22 eVs
fs = 30°
(^(µ+1/2) in BLonD)
F. Batsch

## Slide 11
The tails must be defined. Equal FWHM bunch lengths but different tail definitions give different encircling emittances:
Tails increase eL by factor of 2
 Increased voltage requirements to increase bucket area
The longitudinal profile definition
µ = 0.5, tL = 4 st
µ = 1 (parabolic)
µ = 2
µ = 3
FWHM,
µ = 1
FWHM,
µ = 2.5
Encircling ,
µ = 1
4s,
µ = 2.5
eL = 0.22 eVs
eL = 0.31 eVs, 4sL = 0.16ps
eL = 0.69 eVs , 4sL = 0.20ps
eL = 0.22 eVs
fs = 30°
(^(µ+1/2) in BLonD)
F. Batsch
fs = 45°, used in simulations:

## Slide 12
From the dynamics point-of-view, muons behave more like protons  Chose m = 2.5 for now:
The longitudinal profile after cooling would be an important input
Side note: examples for muons exist but not for a collider application:
The longitudinal profile definition
F. Batsch
[source]
eL =bg*sz * sDp/p = 24 mm
Bucket at injection in RCS1

## Slide 13: Outline
Longitudinal emittance definitions
Bunch length during acceleration
Synchronous phase optimization
Beam-induced voltages and HOM power estimates
Outlook
  emittance growth and budget
  multi-turn effects and induced voltages calculations
Summary
F. Batsch

## Slide 14
In the 1.5 TeV collider, bunch length sz = 5 mm
In simulations, the bunch length at injection in RCS1 sz = 13 mm
The 1 sigma bunch length decreases during acceleration in all 3 RCs:
Final bunch length is sz < 7 mm, bunch rotation might be required
Bunch lengths during acceleration
F. Batsch
RCS1 RCS2 RCS3
Note: initial variations due to mismatched bunch

## Slide 15: Outline
Longitudinal emittance definitions
Bunch length during acceleration
Synchronous phase optimization
Beam-induced voltages and HOM power estimates
Outlook
  emittance growth and budget
  multi-turn effects and induced voltages calculations
Summary
F. Batsch

## Slide 16
Bucket filling factor defines stable phase
The synchronous phase itself directly impacts the main RF requirements:
Energy gain of the synchronous particle 14.75 GeV per turn. For  GV, i.e., large overvoltage
The bunch length changes with , which affects the HOM power to a small extend
Increase the synchronous phase and consequently reduce bucket area to possibly decrease VRF
F. Batsch
The synchronous phase and its influence

## Slide 17: Over-voltages due to fs
Independent of the cavity frequency or RCS, the overvoltage in the RF voltage , compared to is:
F. Batsch
Relative change in VRF
Absolute change in VRF

## Slide 18: Over-voltages due to fs
Independent of the cavity frequency or RCS, the overvoltage in the RF voltage , compared to is:
F. Batsch
Relative change in VRF
Absolute change in VRF
zoomed
zoomed

## Slide 19
Bucket areas for each RCS:
Intensity effects decrease the bucket area slightly
Relaxed voltage requirements and longer bunches (reduces HOM power)
Synchronous phase optimization
F. Batsch
RCS1 RCS2 RCS3
eVs
eVs
eVs

## Slide 20
Possibility to use the muon loss as a criteria
The beam losses increase gradually with the shrinking bucket
 Used single bunch for fs = 45° and “injected” it in all cases to avoid that the matching routine shrinks the bunch:
Synchronous phase optimization
F. Batsch
Between fs = 50° and 55 seems to be the limit
Further studies to come after optimization of the RF voltage and ramping

## Slide 21
The same scan can be repeated for nonlinear ramping function
Example of an older simulation for RCS 1, fs = 57.5°, input emittance 0.1 eVs:
This study will be repeated with updated values after optimization of the RF voltage and ramping
Synchronous phase for nonlinear ramping
F. Batsch
 54% of the bunch lost

## Slide 22: Outline
Longitudinal emittance definitions
Bunch length during acceleration
Synchronous phase optimization
Beam-induced voltages and HOM power estimates
Outlook
  emittance growth and budget
  multi-turn effects and induced voltages calculations
Summary
F. Batsch

## Slide 23: Beam-induced power losses
Question of possibly high HOM power for the TESLA cavity raised during collaboration meeting
HOM power in TESLA / ILC 1.3 GHz cavity calculated in two ways:
From power loss through loss factor k|| from approximated wake potentials in macro-particle tracking simulations (BLonD), containing the information about all HOM:
, with bunch charge density
with bunch charge Q and bunch spacing TB = Trev
F. Batsch
t/4st
short-range wakefield [ref, see appendix for details]

## Slide 24: Beam-induced power from mode analysis
Using the output of ABCI code for detailed RF structure and an approximation for short Gaussian bunches to compute loss factor
( for Linac norm)
This gives the loss factor per mode, for longitudinal modes, see here (TESLA) & paper (ILC LL)
Total HOM loss factor is sum over all HOMs:
,
F. Batsch
From
“Higher order mode coupler for TESLA”, J. Sekutowisz

## Slide 25: Beam-induced power losses: results
Parameters in BLonD: nRF = 32 RF stations, 696 cavities, 90% survival, initial bunch length sz = 13 mm, 1 bunch, single-turn effects
E.g. = -2.11 V/pC
The HOM power loss per cavity reaches 10.4 kW
F. Batsch
(Bunch population 2.54x1012, Trev = 20 µs  I = 20.4 mA as upper estimate)
RCS1 RCS2 RCS3

## Slide 26: Beam-induced power losses: results
From HOMs from ABCI: (ABCI file from S.-A. Udongwo): For RCS1:
F. Batsch
First two “strong” monopole HOM’s already contribute with 4.7 kW
fundamental mode, 2 V/pC
HOMs 1.5 V/pC
1.5 V/pC results in 7.9 kW
 Consistent with BLonD
TM012
See talk by Sosoho U. [link], detailed studies of 1.3 GHz cavity types, structures, HOMs, other frequencies

## Slide 27: Beam-induced power losses
The induced power is very large, up to 10 kW for RCS1&2 per bunch and cavity
Bunch crossings inside the cavity increases power up to 4 times, to be avoided
Central question: What is the CW value? 10kW over 0.3 to 2.4 ms correspond to which CW power in 5Hz operation?
Example: HOM power absorber capacity limit is 1 kW, 3-4 kW under development  up to 20 kW per cavity estimate
Detailed studies on HOM and high-capacity power absorbers (or larger iris, wakefields scale with 1/a², a the iris radius)
F. Batsch
from [R.Rimmer]
See e.g. also PhD thesis by S. Zadeh

## Slide 28: Outline
Longitudinal emittance definitions
Bunch length during acceleration
Synchronous phase optimization
Beam-induced voltages and HOM power estimates
Outlook
  emittance growth and budget
  multi-turn effects and induced voltages calculations
Summary
F. Batsch

## Slide 29: Emittance budget
The emittance budget was discussed in the Accelerator design meeting, see talk by D. Schulte:
Challenge assuming 4% per RCS and beam transfers
Beam transfer possible source of emittance growth
Beam transfer optimized with ramping functions after the HOM and multi-turn/bunch effects are determined
F. Batsch
Rel. emittance blow-up | Relative tolerance | Relative luminosity
0.1% | 0.03 | 0.999
1% | 0.1 | 0.99
10% | 0.3 | 0.9
100% | 1 | 0.5
“Would assume a total budget of 10% (most relaxed acceptable tolerance)”
See last annual meeting: [link]
For the entire 5-GeV-to-1.5-TV acceleration chain!

## Slide 30: Multiturn effects and mode analysis
Multi-turn effects computational challenge
We compute the induced voltages only for the bucket one turn later
Currently implementing this in our code, together with an improved calculation of the induced voltages
F. Batsch

## Slide 31: Multiturn effects and mode analysis
Improved calculation of the induced voltages needed:
K. Bane formulism only valid for short bunches with respect to the cavity cell
We will not differentiate between short-range (K. Bane) and long-range effects, but use the mode analysis of ABCI and resonator models of the first 10 main HOMs:
Add contributions from each mode, and later from the counterrotating bunches
F. Batsch

## Slide 32: Summary
Challenging target for longitudinal emittance, its budget and its growth
Bunch length after acceleration below 7 mm to be expected
Emittance after cooling and linac systems is essential input
Synchronous phase baseline is
HOM power losses are on the 10 kW range during acceleration  CW level estimates and HOM coupler development important
Working on a new calculation of the induced voltages and multiturn effects
F. Batsch

## Slide 34: The BLonD code (Beam Longitudinal Dynamics code)
BLonD: macro-particle tracking code, developed at CERN since 2014
Links: documentation and github
MuC-specific to multiple RF stations & muon decay
Studies of today with only one bunch, 2nd to follow
From BLonD documentation
F. Batsch

## Slide 35
The beam losses increase gradually with the shrinking bucket
 Used single bunch for fs = 45° and “injected” it in all cases to avoid that the matching routine shrinks the bunch,
Extra

## Slide 36
Based on K. Bane et al., ‘Calculation of the short-range longitudinal wakefields in the NLC linac’, ICAP98, 1998
The longitudinal wake function is given by:
One can approximate this by a semi-analytically expression, valid for small bunch length s and s/L < 0.15:
The parameters for the Tesla cavity1 gives long. wake functions on the order of 30 V/pC/m:
21 June 2023
36
L= 115.4 mm
g= 82 mm
a= 35 mm
b= 103.3 mm
The BLonD code convolutes this wake function with the beam profile to obtain the induced voltage
1Wakefield studies for the Tesla cavity shown in TESLA Report 2003-19
Adjusting inner diameter can be a powerful tool to mitigate wakefields!
36
F. Batsch
Induced voltages: Short-range wakefields

## Slide 37: Induced voltages: Short-range wakefields
The induced voltage from the short-range wakefield is as large as 1.5 MV per cavity, i.e., also 1.5 MV/m
The total induced voltage per turn is around 400 MV, thus 3-4% of the accelerating voltage
From design report
Simulation for RCS1, 0.1 eVs

## Slide 38: Induced voltages: Long-range wakefields
The induced voltage from fundamental beam loading for a single turn is 1.5 MV per cavity
So far for a single turn
Important cavity parameters :
Gradient in cavity: 30MV/m
L=1.04m
R/Q = 518 Ω
f = 320 Hz
QL=2.2e6
for beam loading compensation
Simulation for RCS1, 0.1 eVs

## Slide 39: Induced voltages: Combined wakefields
Both effects combined: total induced voltage in a cavity is around 2.2 MV per cavity / per meter, i.e. 10-11% of the RF voltage
Total induced voltage = short-range wakefield + long-range wakefield
RF voltage
Induced voltage
Total voltage
nRF = 48
nRF = 48
Vind (V)
Vind (V)
Vind (V)

## Slide 40: Beam-induced power with BLonD
The geometry of the cavity defines all HOM, i.e. for single-bunch cases, the short-range wakefield from K. Bane [ref, see appendix for details] includes these, but not the long-range fundamental mode
 Use short-range wake potential to compute power
F. Batsch
Plot shows:
bunch charge density, s = 6.6mm
Uind, short-range
Uind, fundamental mode
Total Uind
Wake potential from ABCI
(for RCS1, nRF = 32, parameter in appendix)

## Slide 41: Studies for 801.58 MHz cavities
Some RCS parameter that change with the FCC-ee 5-cell cavity:
F. Batsch
 | TESLA/ILC | FCC-ee
Frequency fRF [MHz] | 1300 | 801.58
Cells | 9 | 5
Active length Lactive [mm] | 1038 | 935
Cavity length Lcav [mm] | 1276 | 1291
Gradient [MV/m] | 30 (conservative) | 25
Number of cavities RCS1 | 696 | 835
Straight length RCS1 | 2334 | 2334
Straight length with RF | 38 % | 46 %
46% instead of 38% use of straight section, feasible!