## Slide 1: Medicine. Research. Hope.
Particle Therapy at MedAustron
Sandor VÖRÖS, MSc
Controls Engineer

## Slide 2: About medaustron
  Center for particle therapy for cancer treatment and for research.
Is one of only six comparable centers worldwide.
  Helps cancer patients with an advanced and rare treatment method.
  Improves particle therapy and creates more evidence through research.
  Has expertise in designing, building, commissioning, certifying & operating an accelerator.

## Slide 3: Company History
AUSTRON feasibility study (research facility neutron spallation)
Reorientation: MedAustron – therapy and research
MedAustron feasibility and design studies
Proton-Ion Medical Machine Study
  Signing basic agreement on realisation Rep. of Austria - Federal State of Lower Austria – city of Wiener Neustadt
Company foundation EBG
EIA process
Ground breaking
  Cooperations CERN & CNAO: design, tendering, manufacturing of accelerator components
Building finished
Start accelerator installation
Commissioning, preparation certification
Start research program
CE certification & 1st patient
1989 - 1994
1995
1996 - 2000
1998 - 2004
2005
2007
2009 - 2010
2011
2012
2007 - 2012
2013
2014 - 2016
2016

## Slide 4: Particles in particle therapy
PROTONS
Up to 250 MeV
CARBON IONS
Up to 430 MeV/u
H
Hydrogen
1,008
1
C
Carbon
12,011
6
Sparing of organs at risk and healthy tissue
Higher dose in the tumor / application in radioresistant tumors
Possible future canditate – currently subject of research
HELIUM IONS
He
Helium
4,003
2
Notes: Protons up to 800 MeV for NCR, 250 MeV for clinical treatment
Carbon Ion up to 430 MeV

## Slide 5: Indications treated at medaustron
Total planned 2023:
550
Patients
11,000
Single Fractions
Values (rounded) as of May 2023
Central Nervous System
Head & Neck
Re-Irradiation
Pediatrics
Sarcoma
Skull Base
Prostate
Gastrointestinal (upper)
Gastrointestinal (lower)
Gynecological Tumors
Urogenital Tumors
Breast/Mamma-Ca<
26%
20%
16%
16%
11%
6%
3%
2%
<1%
<1%
<1%
<1%
Notes: CNS…Central Nervous System

## Slide 6: Facility overview
  Irradiation Rooms Three rooms for patient treatments
  Research Irradiation room for non-clinical use
  Synchrotron = circular accelerator
  Ion Sources and linear accelerator
  140 m

## Slide 7: PLCs in the Medaustron control System

## Slide 8: Architecture

## Slide 9: Ongoing challenges

## Slide 10: Operational Safety system
Purpose
  Protection of personal against unintended irradiation
  Device protection
Key features
  Separated into 2 main PLCs
    Beam Interlock System
    Patrol Control System
  2x SIMATIC S7 CPU 417-5H
  Protection of personal up to SIL 2 according to IEC 62061 (TÜV certified)
  Distributed communication via Profibus over 23 racks
  Connected to 900 different devices via 1600 inputs and 1000 outputs
  Protection of personal programmed in Continuous Function Chart
  Device protection programmed in Instruction List (script generated)

## Slide 11: MAJOR challenges
Single CPU for the entire accelerator
  Service activities and changes are exclusive of machine time in case of a CPU stop
Difficult to ensure that only indented source code is changed
  Lack of regression testing makes code refactoring almost impossible
Site Acceptance Test is a lengthy task occupying the entire accelerator
  Lack of factory acceptance tests

## Slide 12: MAJOR challenges – Single CPU
Option 1 – Separation of concerns
Advantages
  Parallel commissioning
  Reduced downtime in case of a failure
  Better traceability of code changes
Disadvantages
  Increased cost – 14 CPUs instead of 2

## Slide 13: MAJOR challenges – Single CPU
Option 2 – Redundancy
Advantages
  Switchover during program changes
  Increased availability
Disadvantages
  Increased cost – 4 CPUs instead of 2
1

## Slide 14: MAJOR challenges – Regression tests & FAT
TCP/IP
OPC UA
OPC UA
TCP/IP
FAT
2
1
3
4
CAUSE & EFFECT TABLE
5

## Slide 15: Thank you for your attention!

## Slide 16: References and sources
https://www.siemens.com/global/en/products/automation/systems/industrial/plc/simatic-s7-400.html
https://atvise.vesterbusiness.com/
https://www.winmod.de/english/utilizations/plant-simulation/
https://www.iconbunny.com/icons/banking-record-clearance-line-green-black-icon
https://www.360logica.com/blog/wp-content/uploads/2014/05/Importance-of-Regression-Testing-in-Software-Development.png