## Slide 1: Microbunching Instability in FELs: Present and Future Perspectives
Brynes, S. Di Mitri Elettra-Sincrotrone Trieste
CompactLight Final Meeting
03/04/2023
Notes: Slide 2: Title of the Presentation
Before you start editing the slides of your talk change to the Master Slide view:
Microsoft Office :Menu: View > Slide Master;
Macintosh – View > Master > Slide Master
Edit the following items:
On the Slide Master (first master slide) – lower area
a) On the left Delete the text and write the title of the event/Conference, Location
b) On the right delete the text and write the name and surname of the speaker and the date (day, month , year)
Close Master View
To start adding slides insert a new slide and select a Layout:
For Title & Subtitle
For text with bullet points
For Text
For Picture, graphs, visuals
Two columns
Blank

## Slide 2: Contents
Introduction – Causes and Consequences of Microbunching
Modelling Microbunching
Measuring Microbunching
Mitigating Microbunching
Conclusions and Future Perspectives

## Slide 3: Causes and Consequences of Microbunching
Microbunching instability (MBI) is a broad-band modulation of a particle bunch arising from collective effects.
What is it?
Microscopic energy-time correlations in the particle bunch.
What causes it?
Imperfections in the injector bunch.
Modulations are amplified due to longitudinal space charge, coherent synchrotron radiation and wakefields.
What are its effects?
Reduced FEL intensity.
Degradation of FEL spectrum.
Ratner et al., PRSTAB 18, 030704 (2015)
Di Mitri et al., New J. Phys. 22, 083053 (2020)
Di Mitri, CAS Lectures (2016)
Zhang et al, PRAB 23, 010704 (2020)

## Slide 4: Modelling Microbunching
Multi-particle Simulations
Some codes are able to simulate large numbers of particles with (simplified models of) collective effects – ELEGANT, IMPACT, etc.
(Semi-)Analytic Methods
Much faster methods can approximate the amplification of modulations, given some realistic initial conditions.
Qiang et al., PRSTAB 17, 030701 (2014)
Borland, PRSTAB 11, 030701 (2008)
Di Mitri & Perosa, Sci. Rep. 11, 7895 (2021)
Tsai et al, PRAB 23, 124401 (2020)
Requirements
Knowledge of the injector bunch properties:
  Slice energy spread
  Current profile
  Accurate simulation of gun / low energy dynamics.
Accurate physical models of collective effects:
  Coherent synchrotron radiation (CSR)
  Longitudinal space charge (LSC)
  Intrabeam scattering (IBS)
  Wakefields

## Slide 5: Measuring Microbunching - Direct
2D Fourier analysis
IR spectrometer
For typical FEL parameters, MBI gain is peaked at ~1 – 10 μm.
It is hard to measure MBI directly:
Longitudinal phase space measurement
IR spectrometer
Direct measurement can yield more detail than indirect methods:
Bunching factor
Plasma oscillation phase
Brynes et al., Sci. Rep. 10, 5059 (2020)
Perosa et al., in preparation

## Slide 6: Measuring Microbunching - Indirect
Longitudinal phase space fragmentation
FEL Performance
Coherent OTR
Sidebands in FEL spectrum
For FELs, the figure of merit is the FEL itself! We can also measure MBI via COTR.
Marcus et al., PRAB 22, 080702 (2019)
Perosa et al., PRAB 23, 110703 (2020)
Lumpkin et al., FEL09, TUPC47 (2009)
Hüning et al., NIM A 475, 348 (2001)
Huang et al., PRSTAB 13, 020703 (2010)

## Slide 7: Comparing Models to Experiments
Semi-Analytic Model When we include the effect of intrabeam scattering the predicted slice energy spread matches experimental values.
Particle Tracking
By imposing modulations on the bunch at a known frequency we can benchmark simulation models.
How well does our theory (inc. approximations) of MBI gain match measurements?
Pretty well!
Prat et al., PRAB 25, 104401 (2022)
Brynes et al., PRAB 23, 104401 (2020)
Di Mitri et al., New J. Phys. 22, 083053 (2020)
Measurement
Simulation

## Slide 8: Mitigating Microbunching – Laser Heater
The standard method: Laser Heater
If we increase the energy spread at low energy, MBI is suppressed.
Ferrari et al., PRL 112, 114802 (2014)
Tang et al., PRL 124, 134801 (2020)
Brynes et al., Sci. Rep. 10, 5059 (2020)
XLS Laser heater
However: Increasing the energy spread is bad for the FEL!
Are there other methods?
Saldin et al., NIM A 528, 355 (2004)
Spampinati et al., PRSTAB 17, 12705 (2014)

## Slide 9: Mitigating Microbunching - Alternatives
Exploiting IBS through strong focusing
Longitudinal mixing using bending magnets
Reversible energy spread increase by leaking dispersion
Using a transverse gradient undulator before compression
Proposed
There are many ideas yet to be implemented that could
remove MBI without the use of a laser heater
Feng et al., New J. Phys. 17, 073028 (2015)
Qiang et al., PRL 111, 054801 (2013)
Li et al., PRAB 23, 014403 (2020)
Qiang, NIM A 1048, 167968 (2023)

## Slide 10: Mitigating Microbunching - Alternatives
Copper (above) vs. Cs2Te (below) cathode
Longitudinal phase-mixing in a bunch compressor
Adjusting bunch compression ratio
Control of linear optics in the
spreader line
Realised
Numerous experimental demonstrations of MBI suppression – is the LH required for a new FEL?
Bettoni et al., PRAB 23, 024401 (2020)
Di Mitri et al, PRL 112, 134802 (2014)
Di Mitri et al, PRAB 20, 120701 (2017)
Cheng et al, NIM A 1050, 168145 (2023)

## Slide 11: Summary and Future Outlook
Tenative results: Transverse optics
control in the spreader
reduces microbunching
signal
The microbunching instability has long been studied as a source of problems for FELs.
A good agreement has been found between models and experiments in recent years.
New developments have shown numerous methods for mitigating – and even exploiting – microbunching.
Planned facilities should take this recent work into account when considering this phenomenon, although the laser heater is a tried-and-tested method.

## Slide 12
Notes: Last Slide 1: Thanks to the audience