## Slide 1: Jacks for HL-LHC Batch#1 Tests Results
Simon Barrière, Michel Noir, Mateusz Sosin, Patrick Bouvier, Jaime Perez Espinos
31/01/2022

## Slide 2: Last discussions (16-12-2022)
Following non-conformities on CERN test results, we proposed to disassemble, check and re-assemble one of the longitudinal jacks (UN00001)
Assembly took place the last week of December, and then new testing campaign started
  Ram backlash “radial free play”
  Gear backlash
  Actuation torque

## Slide 3: Visual Inspection – All Jacks
Paint quality to be improved (already damaged at reception)
General feedback OK, 2 points to be improved

## Slide 4: Visual Inspection – All Jacks
Burrs on the ram must be removed (picture after machining and treatment?)
General feedback OK, 2 points to be improved

## Slide 5: Visual Inspection – Jack #1
Worm damaged: deep scratches, traces of grinding
surface flatness/finishing not conform to specification
For Batch #2 we will require pictures of all bearing interfaces before assembly
Worms of Jack #2 and Jack #3 are visually OK

## Slide 6: Visual Inspection – Jack #1
Lubrication not sufficient – likely to be the cause of high torques in the mechanism
CERN is working on a more detailed procedure for lubrication (Annex 5)

## Slide 7: RAM Backlash  “Radial Free play”
Chart: RING backlash - range under +/-500N
| -7.3 | -4 | 0 | 4.3 | 7.3
SN01 | 29 | 26 | 34 | 31 | 28
SN02 | 11 | 11 | 11 | 16 | 14
SN03 | 22 | 23 | 22 | 21 | 23
SN01-B | 16 | 18 | 18 | 7 | 22
Chart: RAM backlash - range under +/-500N
| -7.3 | -4 | 0 | 4.3 | 7.3
SN01 | 53 | 43 | 58 | 54 | 56
SN02 | 24 | 14 | 19 | 14 | 14
SN03 | 27 | 32 | 21 | 26 | 28
SN01-B | 12 | 27 | 35 | 21 | 37
Limit | 50 | 50 | 50 | 50 | 50

## Slide 8: Gear Backlash - Nominal
Some values are still above the 30 defined limit – but improved significantly after the new assembly

## Slide 9: Actuation torque under 110% load

## Slide 10: Conclusion
Assembly procedure is a key parameter of jacks functionality – Dimensional cross-checks shall be done at CERN.
Lubrication was not sufficient in the UNIOR jacks – To be improved for next batch following revised CERN procedure
CERN gives greenlight for machining of Batch #2 components, not for assembly yet
Specification attention shall be paid by UNIOR on surface quality, pictures will be required
As discussed, minor design modifications are needed for Batch #2 - updated drawings will be provided this week (Frame, Push-pull ring, Ram)