## Slide 1: Radionuclide production and translational research
Edgars Mamis
University of Latvia, CERN
25/05/2023

## Slide 2: Radiopharmaceuticals and theranostics
Radiopharmaceuticals - group of pharmaceutical drugs containing radioactive isotopes used for:
  SPECT – Single Photon Emission Computed Tomography;
  PET/CT – Positron Emission Tomography/Computed Tomography;
  Radionuclide therapy.
Biological molecules or sometimes artificial building blocks for specific targets, labelled with radioactive positron (β+)/gamma or alpha and β- emitters;
Theranostics – Therapy and Diagnostics
  Radiolabelled drugs for both purposes
  “Matched pair” theranostic agents
Fig. 2 Illustrative structure of a ligand radiopharmaceuticalradiopharmaceutical and its cell binding
Fig. 3. Illustrative structure of drug develoment
Fig. 1. Theragnostic principle: matched pairs of radionuclides for PET and SPECT imaging and for therapeutic application in nuclear medicine.
Sc 43 ??

## Slide 3: Theragnostics = Diagnostics + Therapy
25/05/2023
Radiopharmaceuticals – radioactive drugs
PET/CT – a standard in cancer diagnostics.
  First PET/CT scan in 2016 in Latvia
“Treat what You see” method
  First Lu-177 treatment in 2019 in Latvia

## Slide 4: Targeted (α and β-) therapy

## Slide 5: Linear energy transfer
Ac-225
T1/2 = 9.92 d
Alpha decay RN labelled with PSMA are very aggressive to salivary glands

## Slide 6: Pure radionuclides for medical applications
CERN-MEDICIS mass-separator to obtain isotopically pure medical radionuclides.
Chemically pure radionuclides are obtained through radiochemical separation
Mass-separator
Radiochemistry (…or lasers)
25/05/2023
Isotopically pure target material (e.g. Ca-44 20k Eur/g, Ni-64 80k Eur/g) or …
Fig. 4. MEDICIS mass-separator
Fig. 5. Column for chemical separation

## Slide 7: Nat-Ti and nat-V as target material for xxSc production
Relatively cheap metals titanium and vanadium are light, corrosion resistant, refractory and non-toxic;
Natural titanium has five stable isotopes with different percentages, i.e. 46Ti (8.25%), 47Ti (7.44%), 48Ti (73.72%), 49Ti (5.41%), and 50Ti (5.18%);
natV consists of 2 stable isotopes (51V: 99.750%, 50V: 0.250%)
Melting point:
  Vanadium - 1910 oC
  Titanium – 1668 oC
Fig. 3. Excitation function of natTi(p,x)xxSc reaction by the TALYS-1.9 code
A. Jafari, et. All. Cyclotron-based production of the theranostic radionuclide scandium-47 from titanium target, Nuclear Inst. and Methods in Physics Research, vol. 961, no. Elsevier B.V., 2020
Table 1. Data of the natV(p,x)47Sc,46Sc nuclear cross sections and the values of the IAEA reference cross sections used.
Gaia Pupillo, et.all. Production of 47Sc with natural vanadium targets: results of the PASTA project, Journal of Radioanalytical and Nuclear Chemistry, 2019, https://doi.org/10.1007/s10967-019-06844-8
During medical Sc radionuclide production contaminants such as 46Sc (t1/2=83d; E𝛾= 889 keV; 1120 keV) or 44Sc (t1/2=4.04h; E𝛾= 1157 keV) in 43Sc production mostly cannot be avoided, even with highly enriched target materials;
  Such high contaminant energy is bad for shielding and patient dosimetry;
  Mass-separation step therefore is mandatory

## Slide 8: SIA NUCLEO (Riga, Latvia)

## Slide 9: Equipment
6 hot-cells located in Class C clean rooms of whom:
  4 dedicated for active ingredient synthesis
  2 for sterile dispensing
  1 additional dedicated for radiometal labelling - underway
2x semi-automatic sterile open-vial dispensers
25/05/2023

## Slide 10
Expertise and infrastructure in radiopharmaceutical production and quality control:
[¹⁸F]-FDG
[¹⁸F]-NaF
[¹⁸F]-FLT
[¹⁸F]-F-Choline
[¹⁸F]-FPSMA-1007
[⁶⁸Ga]-PSMA-11
[177Lu]-PSMA-I&T
[⁶⁸Ga]-DOTA-TOC;NOC;TATE
Other possibilities:
[¹1C]-Met and PiB
[¹⁸F]-FDOPA
[¹⁸F]-FMISO
[64;67Cu] labelled compounds
…

## Slide 11: CERN-MEDICIS
Located after the PS Booster, it receives protons with an energy of 1.4 (possibly 1.7 or 2 GeV in upgrade scenarios).
MEDICIS - MEDical Isotopes Collected from Isolde;
ISOLDE - Isotope mass Separator On-Line facility;
Production of non-conventional radionuclides for R&D in cancer imaging, diagnostics and radiation therapy done at partner institutes;
Fig. 7. 3D model of the ISOLDE-MEDICIS facility in 2017.
Fig. 6. CERN-MEDICIS in CERN accelerator complex
Beam dump
ISOLDE Target
MEDICIS Target
Protons 1.4 GeV
Isotopes for ISOLDE
Fig. 8. ISOLDE and MEDICIS irradiation point
1.4 GeV
1 uA

## Slide 12: CERN-MEDICIS principle – view inside the bunker
Ions
Radioisotopes
Vacuum
Air
Courtesy of C. Duchemin
Fig. 9. Animated MEDICIS mass-separator radionuclide extraction principle

## Slide 13: MEDICIS mass separator collection chamber
Double collection slit system and sample holder to collect 2 close mass beams at the same time;
Sample holder with tilted foils suport to reduce sputtering and foil cross-contamination;
Kromek on-line gamma spectrum measurement to monitor implanted radionuclide activity and implantation rate.
Fig. 12. MEDICIS separated isotope collection foils
Fig. 13. Implanted foil retrieval
Fig. 10 Kromek gamma spectrometer software
Fig. 11 MEDICIS mass-separator double collection slit system, separated beam and double collection, tilted foil sample holder
13
Courtesy of S. Marzari and R.E.Rossel

## Slide 14: MEDICIS (and PRISMAP) radionuclides produced/separated
Year of operation | Mode of operation | Radionuclides of interest | Weeks of operation/ collection | Total activity collected (MBq) | Institutes received the radionuclides
2019 | External sources (LS2) | Tb-155, Er-169, Yb-175, Pt-195m | 15 | 870 | KU Leuven (BE), PSI (CH), HUG (CH), NPL (UK)
2020 | External sources (LS2) | Sm-153, Tb-155, Tm-167, Ac-225 | 17 | 540 | KU Leuven (BE), SCK CEN (BE), PSI (CH), NPL (UK)
2021 | CERN PSB Beam External sources | Sc-44,47, Ba-128/Cs-128, Sm-153, Tb-155, Tm-167, Pt-191, Yb-175, Ac-225 | 25 | 1300 | KU Leuven (BE), SCK CEN (BE), PSI (CH), CHUV (CH), NPL (UK), PAEC (PK)
2022 | CERN PSB Beam External sources | Sc-44,47, Ba-128/Cs-128, Sm-153, Tb-155, Tm-165, Tm-167, Pt-195m, Ac-225,227 | 26 | 840 | KU Leuven (BE), SCK CEN (BE), PSI (CH), CHUV (CH), NPL (UK)

## Slide 15: Radionuclides and their respective characteristics considered by NIMMS project for production with linear accelerator
Radionuclide | Usage of radionuclide | Particle beam used for production | Necessary target material | Decay half-life
Sc-43 | Diagnostic – PET | α | Calcium-40 | 3.9 h
Sc-44 | Diagnostic – PET | Deuteron | Calcium-44 | 4 h
Co-57 | Diagnostic – SPECT | α | Manganese-55 | 272 days
Cu-64 | Theranostic (β-) | Deuteron | Nickel-64 | 12.7 h
Cu-67 | Theranostic (β-) | α | Nickel-64 | 61.9 h
In-111 | Diagnostic – SPECT | α | Silver-109 | 67.2 h
Sn-117m | Theranostic (β-) | α | Cadmium-114 to Cadmium-116 | 14 days
Sm-153 (c.a.) | Theranostic (β-) | α | Neodymium-150 | 2 days
Re-186 | Theranostic (β-) | Deuteron | Tungsten-182 to Tungsten-183 | 90.6 h
At-211 | Therapeutic (α) | α | Bismuth-209 | 7.2 h
Courtesy of K. Paļskis and T. Torims

## Slide 16: Cyclotron production
Need of specialized vaults and infrastructure built

## Slide 17: Alpha particles for radionuclide production
Ca-40 for Sc-47 production
Ca-40 abundancy = 97%
Ca-46 abundancy = 0.004 % and thermal neutrons needed

## Slide 18: What else ?
Radionuclides of interest | 
Scandium - 43 | Gallium - 68
Scandium - 44 | Terbium – 149
Calcium - 47 | Terbium – 152
Scandium - 47 | Terbium – 155
Titanium - 44 | Terbium – 161
Copper - 64 | Lutetium - 177
Copper - 67 | Actinium - 225
25/05/2023

## Slide 19: Radiochemistry
Radiochemistry lab setup at UoL
Radionuclide chemical puridfication
Labelling studies with chelators for drug development
Optimization of methods and synthesis
Analythical methods
Courtesy of P. Kalniņa
Fig. 38. Setup for radiochemical Sc-47 separation from collection foil
Table 10. Gamma spectroscopy results of radiochemically separated Sc-47 sample from mass separation

## Slide 20: Cross-section measurements
Refined or new nuclear reaction cross-section data for target materials
  E.g. stacked foil technique (deuterons on V material)
Unique opportunity to use He ions
Nuclear physicist involvement
  Chemical and nuclear engineers for targets

## Slide 21: Activity and radiochemical purity
𝛾 and β spectroscopy studies on produced radionuclides
Half-life measurements and result refinement
  E.g. Sc-43 could not be produced without Sc-44 contaminants

## Slide 22: Looking beyond – some GMP principles undertaken
Type of manufacture | Non - GMP * | GMP part II & I (Increasing) including relevant annexes |  |  | 
Radiopharmaceuticals PET Radiopharmaceuticals Radioactive Precursors | Reactor/ Cyclotron Production | Chemical synthesis | Purification steps | Processing, formulation and dispensing | Aseptic or final sterilization
Radionuclide Generators | Reactor/ Cyclotron Production | Processing |  |  | 
* Target and transfer system from cyclotron to synthesis rig may be considered as the first step of active substance manufacture.
Radiopharmaceuticals intended for use in clinical trials as investigational medicinal products should in addition be produced in accordance with the principles in Eudralex Volume 4, annex 13.
QC: A written procedure detailing the assessment of production and analytical data, which should be considered before the batch is dispatched, should be established.
  Traceability of radionuclide production and separation

## Slide 23: Baltics, MEDICIS and PRISMAP
Pre-clinical and biomedical facilities available for project implementation.
MEDICIS Website: https://medicis.cern/
Courtesy of C. Duchemin and T. Stora
PRISMAP Website: https://www.prismap.eu
PRISMAP will create a single-entry point for a fragmented user community distributed amongst universities, research centres, industry and hospitals.
No projects submitted from Baltics!

## Slide 24: Step forward
Proof-of-concept: High molar activity has been achieved with mass-separation: 7.0 GBq/mg to 1.5 TBq/mg
Up to 280 MBq in a single collection