## Slide 1: HL-LHC Integration meeting Ancillaries around CRAB-DQW cryomodule 2.0
G. Aparicio
J. Dequaire
10/06/2022
Status Update!
10/02/2023

## Slide 2: CRAB DQW – IP5 right area
Proposed configuration for IP5R ; View from transport area ST1516873_01
CRAB DQW in IP5 left
Should be a translation or symmetry of IP5 right configuration
CRAB RFD in IP1 area
Integration study after IP5
Should be a copy of IP5 configuration
Small adaptations to match RFD dimensions
Integration
June 2022

## Slide 3: CRAB DQW – IP5 right area
Proposed configuration for IP5R ; View from transport area ST1516873_01
CRAB DQW in IP5 left
Should be a translation or symmetry of IP5 right configuration  still to be done
CRAB RFD in IP1 area
Integration study after IP5
Should be a copy of IP5 configuration
Small adaptations to match RFD dimensions
Present Integration

## Slide 4: Equipment below CRAB-DQW
Jacks positions
2 jacks located on the jumper side and 1 on the opposite
Ease the FSI integration
More available space between the cryomodules
Less interfaces needed on the cryomodules
FSI lower ports
All FSI lower ports should be located below the cryomodule
Feasibility to be checked on the jumper side
Jacks and FSI patch panels
2 Relocated below D2 and 1 between CRAB and the Q4, under the passerelle
NEED VALIDATION
LEVEL 1
Integration
June 2022

## Slide 5: Equipment below CRAB-DQW
Jacks positions
2 jacks located on the jumper side and 1 on the opposite
Ease the FSI integration
More available space between the cryomodules
Less interfaces needed on the cryomodules
FSI lower ports
All FSI lower ports should be located below the cryomodule
Feasibility to be checked on the jumper side
Jacks and FSI patch panels
2 Relocated below D2 and 1 between CRAB and the Q4, under the passerelle
NEED VALIDATION
LEVEL 1
Present Integration
Released EDMS 2511764
Already relocated by WP4
and validated by BE/GM
Already relocated by WP15
BUT some interferences between the equipment and the jacks were found

## Slide 6: Equipment below CRAB-DQW
Primary pump
Located on the jumper side close to the insulation pump
Mini-racks for vacuum
Located on the jumper side close to the primary pump
Insulation pumps
Located on the jumper sides
Possibility to relocate the insulation pumps in the inter-cryomodule area
Small clashes between insulation pump and Beam vacuum extension roughing
Possibility to add more length on the cryomodule dedicated ports and / or rotate the pump’s upper equipment ?
Rotation possible ?
NEED VALIDATION
LEVEL 2
Integration
June 2022

## Slide 7: Equipment below CRAB-DQW
Primary pump
Located on the jumper side close to the insulation pump
Mini-racks for vacuum
Located on the jumper side close to the primary pump
Insulation pumps
Located on the jumper sides
Possibility to relocate the insulation pumps in the inter-cryomodule area
Small clashes between insulation pump and Beam vacuum extension roughing
Possibility to add more length on the cryomodule dedicated ports and / or rotate the pump’s upper equipment ?
Rotation possible ?
NEED VALIDATION
LEVEL 2
Present Integration
Not considered for the moment
No news since June 2022
SOLVED by WP4 with the integration of an elbow connection interface
STILL to validate by WP12
ONGOING DISCUSSION (BE/GM, WP12) about the possibility of rotating the primary pump looking down depending on the new radial motor dimensions

## Slide 8: Equipment below CRAB-DQW
Compressed air tank for beam gate valves
3 tanks located 1 in each jumper side + 1 between the cryomodule
Possibility to have less tank ?
Cryo-instrumentation feedboxes
Located between the cavities
Double beam chambers supports
Fixed on the cryomodules
Big clash between the feedboxes and the inter cryomodule beam chambers
Relocation above the beam chambers
Relocation on the cryomodules has the advantage of pre-cabling on surface but limits the access on the QXL side in tunnel
Mismatch between double beam support and cryomodule interfaces of Z100 mm
Possible clash between FSI and double beam support
Possibility to modify the double beam support to match the cryomodule interfaces ?
NEED VALIDATION
LOWER PRIORITY
Integration
June 2022

## Slide 9: Equipment below CRAB-DQW
Compressed air tank for beam gate valves
3 tanks located 1 in each jumper side + 1 between the cryomodule
Possibility to have less tank ?
Cryo-instrumentation feedboxes
Located between the cavities
Double beam chambers supports
Fixed on the cryomodules
Big clash between the feedboxes and the inter cryomodule beam chambers
Relocation above the beam chambers
Relocation on the cryomodules has the advantage of pre-cabling on surface but limits the access on the QXL side in tunnel
Mismatch between double beam support and cryomodule interfaces of Z100 mm
Possible clash between FSI and double beam support
Possibility to modify the double beam support to match the cryomodule interfaces ?
NEED VALIDATION
LOWER PRIORITY
Present Integration
No need for them anymore,
confirmed by WP12
Relocated by WP4 to the transport side
SOLVED by WP4 with the relocation of the FSI below the crabs
SOLVED by WP4 with the relocation of the cryo instrumentation

## Slide 10: Equipment around CRAB-DQW
Electrical junction boxes VPI
3 boxes per cryomodule located on the sides, fixed on the cryomodule
Add interfaces on the cryomodule
Electrical coffrets
Located between the cryomodule
Possibility to move it elsewhere ?
DQW cryogenic safety line
Located on the top of the cryomodule
Clash between the safety line and the RF waveguides
The safety line will be relocated between the waveguides
NEED VALIDATION
LOWER PRIORITY
Integration
June 2022

## Slide 11: Equipment around CRAB-DQW
Electrical junction boxes VPI
3 boxes per cryomodule located on the sides, fixed on the cryomodule
Add interfaces on the cryomodule
Electrical coffrets
Located between the cryomodule
Possibility to move it elsewhere ?
DQW cryogenic safety line
Located on the top of the cryomodule
Clash between the safety line and the RF waveguides
The safety line will be relocated between the waveguides
NEED VALIDATION
LOWER PRIORITY
Present Integration
2 VRJA boxes per cryomodule (instead of 3)
Orientation rotated by 90º looking to the transport side
SOLVED by WP4 with the displacement of the safety line
Cable trays already protected

## Slide 12: Equipment above CRAB-DQW
WPS supports
3 supports per cryomodule located on the transport sides of the cryomodule
Inclinometers
2 items per cryomodule located on the sides
Clash between the WPS supports and cryomodule
Possibility to adapt the supports ?
NEED VALIDATION
LOWER PRIORITY
Clash between the inclinometers supports and cryomodule
Possibility to move the inclinometers ?
Integration
June 2022

## Slide 13: Equipment above CRAB-DQW
WPS supports
3 supports per cryomodule located on the transport sides of the cryomodule
Inclinometers
2 items per cryomodule located on the sides
Clash between the WPS supports and cryomodule
Possibility to adapt the supports ?
NEED VALIDATION
LOWER PRIORITY
Present Integration
Ongoing
(together with BE/GM)
relocated by WP4 BUT interferences found between the jumper-side inclinometer and the jumper connection

## Slide 14: Equipment above CRAB-DQW
NEW FINDINGS
Interference between the electrical feedthrough and the RF wave guide connections on the non-IP crab.
Interference between the WPS space reservation and FSIs on top of the IP crab.

## Slide 15: Thank you for your attention