## Slide 1
The DAQ system of the Mu3e SciFi detector
Joint Annual Meeting of the Swiss Physical Society and Austrian Physical Society
Yifeng Wang
on behalf of the Mu3e Collaboration
6.9.2023
Notes: 20′ long (+ 3′ for discussion)
0

## Slide 2: Physics goal: Lepton flavor violation (LFV)
Motivation: Lepton flavor violation has been observed in neutrino sector
  SM extension for nLFV, i.e. PMNS-matrix
  Lepton flavor violation (cLFV) has never been observed in charge lepton sector
Benefit: Free of SM background
Status: current limit in cLFV searches (mu->eee)
1
SM suggested decay
Current: SINDRUM ()
Future: Mu3e ()
Worldwide status of muon decay search for charged LFV
Notes: Limits and data from other

## Slide 3: Introduction of Mu3e Collaboration
Constructing a future experiment in search for the cLFV decay µ+ -> e+e-e+
Goal:
  - Observe µ+ -> e+e-e+ if
  Exclude at 90% CL
Two-staged approach:
  a few in Phase I (2025-26)
  in Phase II (2029+)
Under construction at Paul Scherrer Institute (PSI) in Switzerland
~70 collaborators from institutes in Switzerland, Germany and UK.
Ref:adapted from New Frontiers in Lepton Flavor
by Cristina Martin Perez
2

## Slide 4: Searching for cLFV at Mu3e
Background:
() signature
Accidental background
(
Rejected with excellent timing and vertex resolution
Internal conversion background
Rejected with excellent energy and momentum resolution
Signal:
Same vertex and time coincidence
.
Different vertex and time coincidence
.
Same vertex and time coincidence
.
Phase I: >1015 muons = time x rate = 2.5*107s (290days) x 108µ+/s
3
Yifeng Wang – ETH Zürich

## Slide 5: Mu3e design challenges
Unknown cLFV kinematics
High and continuous muon rate
Internal conversion
Accidental background
Multiple scattering
Large solid angle and kinematics acceptance
Fast and small dead-time readout electronics
Excellent momentum resolution (<1 MeV)
Excellent timing and vertex resolution (<100 ps and <0.5 mm)
Ultra-low material budget (<0.2% X0 SciFi layer, ~0.1% X0 per Pixel layer)
4

## Slide 6: Timing layers in Mu3e
Goals of timing layers: time coincidence of tracks, charge identification and global event recons.
timing resolution: SciFi<200ps, SciTile<50ps, Pixel<26ns
SciFi
SciTile
5

## Slide 7: SciFi detector - construction
Fiber and SiPM array attached
SiPM
SMB (SciFi Module Board)
MuTRiG x4
on one end of the fiber ribbon
interposer
To FPGA
Ref: Y. Demets, BVR 2023
Ref: 2208.09906
Fill factor >60%
one SciFi super-module (6 in total)
SiPM arrays (24 in total)
SiPM readout waveform
6

## Slide 8: Specialized timing chip - MuTRiG
Analog
to SiPM
Digital
to DAQ
MuTRiG floorplan
MuTRiG bonded
MuTRiG (Muon Timing Resolver including Gigabit-link)
bare die version in picture for SciFi
BGA packaging used for SciTile
Data link | 1.25 Gbps LVDS
IO ports | Fully differential
Analog channels count | 32
Wafer | UMC 180 nm
Size | 5 mm x 5 mm
Clock speed (nominal) | 625MHz
Analog FE digitization
Functional block diagram of MuTRiG
Event rate > 25 MHz
50 ps time resolution
On-die hit validation hardware algorithm
  Rejecting 50%+ of DCR
7

## Slide 9: Triggerless Data acquisition (DAQ) system
Front-end Board - Customized Arria V board - 8 XCVR
Mu3e DAQ architecture
Intel(Altera) FPGAs and GPU farm
Farm Board – Dev kit Arria 10 – Customized PCIe DMA controller
120 Gbps
144 Gbps
38 Gbps
a few Gbps (whole mu3e)
Link bottleneck bandwidth
(maximum allowed data rate) of SciFi
8

## Slide 10: System Design (FPGA DAQ)
Front-end Board
Arria V
MAX 10
Optical Firefly® Transceiver
MuTRiG
LVDS Receiver
Slow Control Master
Timestamp
Decoder and Aligner
MuTRiG Configure SPI Master
Dummy
MuTRiG Frame Generator
Frame Parser
TS Sorter
ch 0-3
ch 0-3
ch 0-3
Bypass select
To SWB
(fiber)
Data Packer
ch 4-7 omitted
Streaming Data
Slow Control
Protocols:
Rate statistics
CFG
CFG: configure
CFG
Data/SC select
Error flags
CFG
: Arria V firmware (2 copies)
: Arbiter
: entity (functional block)
Yifeng Wang – ETH Zürich
: ASIC data frame
MM
MM
MM
MM
MM
MM
MM
MM
MM
:
Memory-Mapped
Interface
System Design
Data/control plane
Integrated design vs traditional HDL
IP-core lib for Mu3e
9

## Slide 11: System Design (FPGA DAQ)
Front-end Board
Arria V
MAX 10
Optical Firefly® Transceiver
MuTRiG
LVDS Receiver
Slow Control Master
Timestamp
Decoder and Aligner
MuTRiG Configure SPI Master
Dummy
MuTRiG Frame Generator
Frame Parser
TS Sorter
ch 0-3
ch 0-3
ch 0-3
Bypass select
To SWB
(fiber)
Data Packer
ch 4-7 omitted
Streaming Data
Slow Control
Protocols:
Rate statistics
CFG
CFG: configure
CFG
Data/SC select
Error flags
CFG
: Arria V firmware (2 copies)
: Arbiter
: entity (functional block)
Yifeng Wang – ETH Zürich
: ASIC data frame
MM
MM
MM
MM
MM
MM
MM
MM
MM
:
Memory-Mapped
Interface
Stream data
Low latency
High throughput
Fixed topology
10

## Slide 12: System Design (FPGA DAQ)
Front-end Board
Arria V
MAX 10
Optical Firefly® Transceiver
MuTRiG
LVDS Receiver
Slow Control Master
Timestamp
Decoder and Aligner
MuTRiG Configure SPI Master
Dummy
MuTRiG Frame Generator
Frame Parser
TS Sorter
ch 0-3
ch 0-3
ch 0-3
Bypass select
To SWB
(fiber)
Data Packer
ch 4-7 omitted
Streaming Data
Slow Control
Protocols:
Rate statistics
CFG
CFG: configure
CFG
Data/SC select
Error flags
CFG
: Arria V firmware (2 copies)
: Arbiter
: entity (functional block)
Yifeng Wang – ETH Zürich
: ASIC data frame
MM
MM
MM
MM
MM
MM
MM
MM
MM
:
Memory-Mapped
Interface
Slow Control
Versatile topology
Large addressable space
Crossing clock domains
11

## Slide 13: Conclusion
Two-phase physics plan
  a few in Phase I (2025-26)
  in Phase II (2029+)
Mu3e searching for cLFV violation decay mu->eee
Technical challenges in SciFi (timing, high data-rate, …)
FPGA-based DAQ system (low latency, high throughput, IP-packaging, …)
Integration runs
12

## Slide 14: Backup slides

## Slide 15: SciFi detector – light detection
SiPM Array
(Hamamatsu S13552-HRQ)
Side view 32.5 mm
Top view 300 mm
e- or e+
Induced light
Induced light
1.625 mm
~32 mm
Attaching
SiPM pulse time resolution
measured with DRS4 (ADC, timing resolution 200 ps)
To be measured with MuTRiG (TDC, timing resolution 50 ps)
Fiber and SiPM array attached
SiPM readout waveform
fiber ribbon (3 layer 250 µm round black epoxy coated rods)
(Kuraray SCSF-78MJ)

## Slide 16: Worldwide status of muon decay search for charged LFV
Current: MEG ()
Future: MEG II (S.E.S. )
Current: SINDRUM II ()
Future: Mu2e and COMET (S.E.S. )
Current: SINDRUM ()
Future: Mu3e ()
(within nuclei)

## Slide 17: Why is a golden channel?
1. Strongly suppressed by SM very clean channel
SM suggested decay
BSM suggested decay
consider acceptance of detector
Phase space decay (Dalitz plot)
2. Full 3-body decay kinematics large kinematic space coverage

## Slide 18: Beam and target
Delivered by HIPA proton accelerator at PSI
Proton -> pions -> “surface” muon
~28 MeV DC muon beam
πE5 / CMBL shared by MEG II and Mu3e
7.5 x 107 muons/s on target
Double-cone hollow target
Distribute muon stops over large surface
Made in Mylar
Muon stopping ratio: 95.5%
100 mm long, 38 mm diameter,
Notes: surface muon has 28MeV. move it up

## Slide 19: Magnet and track recurl
Solenoid magnet with 1.0 T nominal field
Delivered at PSI, operational
Recurl helps on reducing multiple scattering uncertainties
Momentum resolution increases as material budget decreases
1T Magnet: Maximize the acceptance of recurler
Notes: explain the recurl more
maximumize the acceptance of recurler

## Slide 20: Pixel tracker in Mu3e
Goal of tracker: vertex and tracking
Granularity: Pixel=80µm*80µm, ScFi fiber=250µm*300mm, Tile 5mm*5mm
Outer pixel (recurl)
Inner pixel (vertex)
Notes: Explain first the event
bit cut
ref is in pic
rotate the CAD
why tracking vertex

## Slide 21: MuPix (HV-MAPS tech.)
General Operating Scheme of
High-Voltage Monolithic Active Pixel Sensors
Block diagram of signal flow
Integration of diode sensor and detector circuit into one-die
World-most thin HV-MAPS, 50 µm (~0.1% X0) version taped-out
Pixel size: 80 x 80 µm2
Pixel matrix: 256 x 250 pixels
Active region: 85.5% of the whole chip
Link type: 1.25 Gbps LVDS
Floorplan of MuPix
Digital/Analog Chip bottom
Active region
- high voltage, monolithic, fast charge collection, smart diode
Notes: just highlight bullet points
world-most thin

## Slide 22: MuPix performance
Raw timing resolution
(w/o time-walk and delay correction)
Innovative gaseous helium cooling solution with 2g/s, sensor < 70˚C
Measured temperature difference of dummy load
(at ~ 215 mW/cm2)
Max. temperature difference < 35 K (215 mW/cm2)
Max. temperature difference < 54 K (350 mW/cm2)
spTAB bonding for High-Density Interconnects
MIP detection efficiency
MuPix11 (100µm)
Timing resolution
Notes: backup
just mention helium cooling

## Slide 23: Scintillating Tiles detector
Tile Subdetector
Tile Matrix
(top) w/ scintillator
(bottom) w/o scintillator
Tile-shape scintillator
Consists of size of 6 x 6 x 5 mm3 scintillating tiles
Readout with 3 x 3 mm2 SiPM (MPPC S13360-3050VE)
Digitized by MuTRiG (TDC)
Efficiency > 99%, time resolution ~40ps
Notes: why thick more material not in center
TODO: What is this figure?

## Slide 24
Frame Parser
MM
LVDS Receiver
MM
MuTRiG
Raw waveform
8b/10b symbols
MuTRiG Event Table

## Slide 25: Filter farm
Triggerless, continuous reconstruction
Track reconstruction in central pixel detector and vertex finding on GPUs
Events with μ → eee candidates are send off to mass storage
Data reduction by a factor of 80
Notes: GPU highlight
Own scheme

## Slide 26: Past integration runs
Integrated runs and testbeam of DAQ, helium/water cooling, magnet
Reconstructed cosmic muons and recurl electrons
Track reconstruction and coincidence found to validate the prototype
Pixel-SciFi and Pixel SciTile combined coincidence search
Notes: re-do this plot quality

## Slide 27: Simulation for Phase I physics
Sensitivity
Vertex resolution ~0.3 mm (<0.5 mm)
Momentum resolution ~0.9 MeV (<1 MeV)
Phase space
Notes: more time on this slides

## Slide 28: MuPix assemble to pixel ladder
Mock-ups of cabling and assembly performed for innermost pixel layers
Extreme space constrains for cabling, flex and uTP cable used
Assembling steps
1:4
Notes: show only some pictures

## Slide 29: Lepton flavor violation (LFV)
Lepton flavor violation has been observed in neutrino sector (nLFV)
=> SM extension for nLFV, i.e. PMNS-matrix
Lepton flavor violation has never been observed in charge lepton sector (cLFV)
Standard Model particles
Notes: u->e not e->u
Highlight information: cLFV

## Slide 30: Mu3e physics with kinematics
All decayed tracks have momemtum <53MeV

## Slide 31: physics sensitivity, simulations

## Slide 32: More about beam

## Slide 33: construction and commissioning status, staging-setup, etc

## Slide 34: IP-core library of Mu3e experiment
Created Mu3e-specific IP category
Avalon-MM
Slave
Exportable across system (FEB or SWB)
Integration with NIOS or System Console
One-click instantiation
Zero-debugging effort from user side
User Friendly GUI
Auto-interconnection with Avalon-Memory Mapped interface
Display floating-point 32 reading
Support parasitic powering (with 500 Ohm pull-up resistor)
Support rolling or one-time readout
Instantiation tab
Yifeng Wang – ETH Zürich

## Slide 35
Slides from Frederik Wauters in CLFV2023
Yifeng Wang – ETH Zürich

## Slide 36
Slides from Frederik Wauters in CLFV2023
Yifeng Wang – ETH Zürich

## Slide 37: Conceptual design for gamma conversion at Mu3e
Slides from Frederik Wauters in CLFV2023
Yifeng Wang – ETH Zürich

## Slide 38: Connector boards
uTP cable
Yifeng Wang – ETH Zürich

## Slide 39
FEB
Backplane
DAB 2.1
SMB
Charge Injection Evaluation Board
CMOS 2.5V
CMOS 2.5V
Charge injection port
+ -
Normal data reading
Analog pulse
How do we test charge injection without final DAB

## Slide 40
Yifeng Wang
D-​PHYS
yifenwan@phys.ethz.ch
ETH Zürich
Inst. f. Teilchen-​ und Astrophysik
HPK E 25
Otto-​Stern-Weg 5
8093 Zürich Switzerland