## Slide 1: Layout Half Layer 0 Sensor
~27 cm
R0*π = 56.5 mm
1.28 – 1.8 mm
1.28 – 1.8 mm
0.6 – 0.86 mm
0.6 – 0.86 mm
3.76 – 5.32 mm
6.7% – 9.5%
z
rϕ
Non sensitive peripheral regions:
Sub-Module

## Slide 2: Dimensions and layout of one sub-module
PIXEL MATRIX TOP
PIXEL MATRIX BOTTOM
18 mm
~26 cm
18 mm
25.5 mm
0.6 – 0.86 mm
0.6 – 0.86 mm
2.5 – 3.5 mm (tbc)
Layer 0: 3 sub-modules. Layer 1: 4 sub-modules. Layer 2: 5 sub-modules

## Slide 3: Power Densities Estimates
18 mm
25.5 mm
0.6 mm
0.6 mm
2.5 – 4 mm
(can be tuned, probably >=3)
Pendcap : 750 - 1000 mW
(PΣ : 1000 – 2200 mW/cm2 )
Pmatrix : ~51 mW
PΣ : 12 mW/cm2
Pperiphery : (24+21) = 46 mW
PΣ (*) : (160+140) = 300 mW/cm2
Pstitch_unit : ~143 mW
PΣ : ~30 mW/cm2
x10
(*) The power dissipation density on the long peripheries will also have a dependence on the z-coordinate. Not included here

## Slide 4: Notes
Estimates based on analysis, projections, estimates: best educated guesses.
Included additional dissipation due to on-chip linear regulators
  The regulators are assigned on the long edge peripheries. The two values of power are the circuit dissipation and the loss in the pass transistors of the regulators
Did not include margin, in particular over the sensing area (matrix)
The power dissipation density will also have a dependence on the z-coordinate.
  This is due to the IR drops on the rarils and the addition of the on-chip linear regulation. A parabolic dependency with a minimum at z=0 is expected at first approximation. This spatial dependency is not shown, the resulting average value was added to the values shown.
The z-dimension of the endcap (short edge periphery) can be fine tuned
  The determining value is the power for the endcap. Minimum width is 2.5 mm. Probably will require more width (3 mm or more), bringing possible reduction of power density.