## Slide 1: HL-LHC - status of preparation
Mike Lamont LHCP 7th June 2024

## Slide 2: HL-LHC - goals
Prepare machine for operation beyond 2025 and up to ~2040
Operation scenarios for:
  Total integrated luminosity of 3000 fb-1 in around 10-12 years
  An integrated luminosity of ~250 fb-1 per year
  Nominal: levelled luminosity of 5 x 1034 cm-2s-1 (events/crossing ~130)
  Ultimate: levelled luminosity of 7.5 x 1034 cm-2s-1 (events/crossing ~200)

## Slide 3
Increase bunch population
Higher Intensity
Smaller
Reduced emittance
Smaller beam size at IP
Crossing angle reduction factor
Shorter bunches, smaller crossing angle, crab cavities
Increase F

## Slide 4
Injector upgrade (bunch population, emittance)
Interaction region upgrade (beta*)
Crossing angle compensation (crabs)
Operate in a high luminosity regime

## Slide 5: The realization of HL-LHC as a truly international collaboration
Q1
Q2a
Q2b
Q3
D1
DFX
DFM
Connection to LHC (UL)
Service gallery (UR)
TAXS
Crab cavities
UA Gallery
Q4
TAXN
Service cavern
SC Links
D2
Collimators
CP
DFHX
DFHM
DQHDS

## Slide 7: High Luminosity LHC (HL-LHC)

## Slide 8: HL-LHC era - indicative timeline
LS3: HL-LHC installation
LHCb-II, ALICE3 upgrades (tbc)

## Slide 9: And then another miracle occurs…

## Slide 10: A diverse physics programme
ALICE 3 proposed for LS4
LHCb Upgrade II proposed for LS4
Forward physics
  Precision Proton Spectrometer II (PPS II)
Neutrinos
  SND, FASERnu, AdvSND, Forward Physics Facility (FPF)
Long Lived Particles/FIPS
  GPDs, FASER, SND, MoEDAL, milliQan, FPF, CODEX-b, MATHUSLA, (pro)ANUBIS
Fixed target
  SMOG-2@LHCb, LHCspin, TWOCRYST (Λc+ MDM/EDM)

## Slide 11: HL-LHC Work Packages

## Slide 12: HL-LHC technology landmarks
HL-LHC has many challenging novelties covering a broad technology spectrum
Technology intensive project!
Finished in 2023
Successfully deployed in 2023 Pb-Pb run
Finished in 2023
½ system already installed for Run 3
Series production in Industry well underway
Complete Prototype System installed in SM18 and tested
Fully validated in 2023 and first magnets ready for installation

## Slide 13: Magnets

## Slide 14: Magnets
This year will be a crucial year for qualifying
HL-LHC magnets and the cold powering system
repeatability of CERN Nb3Sn quadrupole performance – confirmed (April)
test of first complete cold powering system
electrical robustness of cryomagnets and cold powering system
horizontal test bench upgrade to be completed

## Slide 15: SM18 – this week
MQXFB04 successfully completed test program
LQXFA01 (Q3 in IT String) placed on bench for cold tests

## Slide 16: Latest series CERN inner triplet quarupole (QXFB)
Increased magnetic field at coil → shift from niobium-titanium to niobium-tin (Nb3Sn)
However, Nb3Sn is brittle – some issues with degradation at prototype phase

## Slide 17
LQXFA01 AKA Q1/Q3 – FIRST QUADRUPOLE CRYO-ASSEMBLY PRODUCED IN THE US BEING TESTED IN SM18

## Slide 18: Inner Triplet (IT) String components in preparation
  Q1: magnet cold mass being welded  Available in September 2024
  Q2a: MQXFBP2b completed  On SM18 Testbench  Available April 2024
  Q2b: MQXFBP3b completed  Available for Testbench Jan.  April 2024
  Q3: magnet being prepared for shipment to CERN  Available July 2024
  CP: cryostating Phase II ongoing  Available August 2024
  D1: cryostating completed  Available for Testbench  Available March 2024
CP
Q2a
(in SMI2)
CP
(SMI2)
Q3
(in FNAL)
D1
(in SMI2)
Q2b
(in SM18)
Q2b
In SM18
Notes: To be updated by Ezio’s PSM presentation

## Slide 19: Cold Powering System
D2
DSHM
DFHM
Q1
Q2A
Q2B
Q3
CP
D1
DCM
DFM
DFX
DSHX
DFHX
140 m
89.5 m
Power converters: (18, 7, 2) kA
Power converters: (18, 0.6) kA
Power converters: (60, 120, 200) A

## Slide 20: Superconducting link
The flexible, double-wall, corrugated cryostat comprises 19 MgB2 superconducting cables in a single assembly, twisted together to form a compact bundle. These 19 superconducting cables can transfer altogether a DC current of about 120 kA at ~20 K.

## Slide 21
SC-Link-DFHX assembly in pictures
Complete system test of full SC link now complete

## Slide 23: Crab Cavity series production well underway
  DQW Dressed Cavity
First two series DQW cavities (CERN + RI) reached performance beyond specification!
  RFD cryomodule assembled in UK at CERN
  RFD pre-series 1 and 2
  RFD series fabrication launched at Zanon since May 2023

## Slide 24: UK Crab Cavity Cryomodules

## Slide 25
RFD cryomodule assembled in UK and being tested in M7 bunker (SM18-CERN) before installation in SPS

## Slide 26: HL-LHC LS3 Schedule
Warm-up and related tests
LSS dismantling after cryo lockout
Cabling dismantling
Core excavation (LHC side)
Cabling installation
LSS installation
LS3 Schedule – TCC October 2023
Cool-down, related test and HWC
Plus
Injector Complex
North Area Consolidation
ECN3
Experiments (+CO2 cooling)
…
Long Shutdown 3 (LS3) is going to be very busy!
Q4 2025
Q3 2029

## Slide 27: Conclusions
MQXFB02
D1
proto
Repaired
MB Dipole
CP
MQXFBP3
Nb3Sn Technology validated
Superconducting Link demonstrated
Crab Cavity Operation and Production demonstrated
Civil Engineering Work Completed
1st Part of Collimation Upgrade completed
”The project is on track for installation during LS3 starting in 2026”
Stay tuned for completion of the IT-String installation in 24 and operation @ cold as of 2025
All magnet production on a good track
STILL A LONG WAY TO GO…