## Slide 1: The HL-LHC Plan
Oliver Brüning – CERN – Project Leader
On behalf of the HL-LHC project
Ceremony for the delivery of the last High Order Corrector Magnet by INFN to CERN for the HL‐LHC project,
LASA February 17th 2023

## Slide 2: Reminder of the HL-LHC Goals
The main objective of HiLumi LHC Design Study is to extend the LHC lifetime by another decade and to determine a hardware configuration and a set of beam parameters that will allow the LHC to reach the following targets:
A peak luminosity of Lpeak = 5×1034 cm-2s-1 with levelling, allowing:
An integrated luminosity of 250 fb-1 per year, enabling the goal of Lint = 3000 fb-1 twelve years after the upgrade. This luminosity is more than ten times the luminosity reach of the first 10 years of the LHC lifetime.
From FP7 HiLumi LHC Design Study application in 2010
Ultimate performance established 2015-2016. With same hardware and same beam parameters, by using engineering margins:
Lpeak ult  7.5 1034 cm-2s-1 and Ultimate Integrated Lint ult  4000 fb-1
LHC should not be the limit, would Physics require more than nominal
Goals in a nutshell:
Extend the LHC lifetime by 15+ years
Prepare the machine for producing in that period 10 times more data as compared to the nominal LHC operation period
Transition from Prototype tests to Series production!!!
And preparing for installation work

## Slide 3
Technology
Landmarks
Separation / Recombination
dipole magnets: D1 & D2

## Slide 4
Run3 operation
Approval of
HL-LHC Project
EU funded HiLumi
Design Study
Transition from Prototype development to
Series production is well underway!
Ca Half Way!
6 years since project approval
6 years until start Run4
HL-LHC Operation
We are here

## Slide 5: HL-LHC Scope in 1R and 5R
UA57
US57
UR55
UL57
UPR57
PC IT
PCs IT Trims
DFX
DSHX
DFHX
CDBs
PIC,BIS
QDS
CLIQ
Warm Diodes
DCM
Q1
Q2A
Q2B
Q3
CP
D1
OC PCs
D1 PC
Cold Diodes
OC EE
DSHM
D2 PC
D2 OC EE
Cold box
CDBs
DFM
DFHM
DQHDS
D2
Q4
Q5
Q6
Valve box
D2 OC PCs
Crab
Cavities
RF Powering
UW57
TAXN
Underground Civil Engineering Excavation work was completed during LS2!
Cooling and Ventilation

## Slide 6: Completion of the civil engineering works
SF17
SHM17
SD17
SE17
SU17
Example Point 1

## Slide 7: Ceremony for completion of CE on January 20th 2023
Notes: To be updated with latest plans for Ceremony

## Slide 8: New HL-LHC Triplet Layout:

## Slide 9: The Insertion Region (up to Q4)
Q1
Q2a
Q2b
Q3
CP
D1
DFX
DFM
Connection to LHC (UL)
Service gallery (UR)
TAXS
Crab cavities
UA Gallery
Q4
Collimators
TAXN
Service cavern
SC Links
D2

## Slide 10
Cryostated Assembly LMQXFA-01
Magnet Pair Alignment
Heat Exchanger Installation
Shell Longitudinal Seam Welding
Cryostated Assembly @ FNAL
  First AUP horizontal test  spring 2023
Update on MQXFA – Q1 & Q3: Cryo-Module Assembly in the USA
May 2022: Endurance Test on MQXFA05: 50 quenches, 5 TC  magnet remains @ nominal! ✓
6 magnets constructed and validated  ready for Coldmass construction [2 / Coldmass]! ✓

## Slide 11
Update on MQXFB – Q2: Cryo-Module Assembly at CERN
  MQXFBP3 test at CERN  nominal + 300 and TC ✓
  MQXFB02 test @ CERN  nominal +300A and TC – still ongoing ✓
P3 and MQXFB02 satisfy the CERN acceptance criteria ✓
Limitation @ 4.5K, but Temperature margins compatible with nominal operation:
P3 & 02 reached nominal +300A,
P3 went through
3 TC without degradation;
MQXFB02 through 2 TC -
tests ongoing
Notes: To be updated in time

## Slide 12: Corrector Package Production
November 2021: HO corrector manufacturing and assembly completed ✓
The last High Order Corrector Magnet by INFN has been delivered to CERN for the HL‐LHC project
Excellent performance of the delivered magnets!!!

## Slide 13: D1 Prototype at KEK
Insertion into vertical cryostat
Lifting up the D1 magnet
Prototype passed acceptance criteria and is now on its way to CERN

## Slide 14
D2 Cold-Mass Assembly
Cryogenics by-pass
D2 Prototype Cold-Mass @ CERN in Hall 180
D2 Prototype on the test bench in SM18: reached ultimate current after TC without quench

## Slide 15: Flexible MgB2 superconducting links
MgB2 cable:
  90 mm
Itot > 100 kA @ 25 K
L= 60 m
MgB2
Demonstration of 2 x 20kA +
2 x 7kA in June’20
in MgB2 @ 30K
in flexible cryostat
over 60m [54kA total]
 90 mm

## Slide 16
Next Milestone: HL-LHC IT STRING: P5L
P5
P5L
P5R
SPS
HL-LHC
P1
P2
P3
P4
P5
P6
P7
P8

## Slide 17
The IT STRING will deliver the first complete experience of installing and operating the IT zone
The scope of the IT STRING is to represent, as best as reasonably achievable in a surface building, the various operation modes to STUDY and VALIDATE the COLLECTIVE BEHAVIOUR of the different systems of the HL-LHC’s IT zone (magnets, magnet protection, cryogenics of the magnets andof the superconducting link, magnet powering, vacuum, alignment, interconnections between magnets, and the superconducting link itself).
The IT STRING Scope
Installation of IT-String started and will proceed throughout 2023
and will continue in 2024. Hardware Commissioning to start in 2024

## Slide 18
Under the metallic structure
On top of the metallic structure
Status in pictures

## Slide 19: HL-LHC is ready for Series production of most components We are getting ready for installation:  IT-String
LASA the first to finish magnet production!!!

## Slide 21
  MQXFBP3 test at CERN  nominal + 300 and TC ✓
  MQXFB02 test @ CERN  nominal +300A and TC – still ongoing ✓
P3 and MQXFB02 satisfy the CERN acceptance criteria
Limitation @ 4.5K But Temperature margins compatible with nominal operation:
P3 & 02 reached nominal +300A,
P3 went through
3 TC without degradation;
B02 through 2 TC -
B02 tests ongoing
Update on MQXFB – Q2: Cryo-Module Assembly at CERN
Notes: Pictures and updates to be implemented

## Slide 22
Update on MQXFA – Q1 & Q3: Cryo-Module Assembly in the USA
Cryogenics by-pass
Fitting of bottom SS shell and longitudinal welding
May 2022: Endurance Test on MQXFA05: 50 quenches, 5 TC  magnet remains @ nominal! ✓
Coldmass assembly of long magnet [2 of the 4.2 meter long magnets] ongoing @ FNAL
6 magnets constructed and validated  ready for Coldmass construction [2 / Coldmass]! ✓

## Slide 23
Cryogenics by-pass
Integration of the Cold-Mass components and installation of end plates and pipes
23
Update on MQXFA – Q1 & Q3: Cryo-Module Assembly in the USA

## Slide 24
Main civil engineering work at Point 1 (ATLAS)
US17
UR15

## Slide 25
Main civil engineering work at Point 1 (ATLAS)
SF17
SHM17
SU17
SE17
SD17

## Slide 26
Main civil engineering work at Point 5 (CMS)
US57
PM57
UR55

## Slide 27
Underground
(Fully completed on 25 Oct’21)
Surface
Main civil engineering work at Point 1 (ATLAS)
SF17
SHM17
SU17
SE17
SD17
Fully completed and delivered by Sep’22
(+ ~1 months w/r to the initial contractual date)

## Slide 28
Surface
Main civil engineering work at Point 5 (CMS)
SF57
SHM57
SU57
SE57
SD57
Underground
(fully completed on 25 Feb’22)
Fully completed and delivered by Jan’23
(+ ~2 months w/r to the initial contractual date)

## Slide 29
Main civil engineering work at Point 5 (CMS)
SE57
SU57
SD57
SF57
SHM57

## Slide 30: Technical infrastructures in the delivered buildings
SL172
SHM57
SF57
Sectional doors
Cranes
Cable trays
Lighting
Ventilation system
Primary water system

## Slide 31: Cryostat Preparation @ CERN

## Slide 32: International Collaboration
SC Links
D1
DFX
CP
Q3
Q2b
Q2a
Q1
Service gallery (UR)
Connection to LHC (UL)
TAXS
DFM
DFHM
DFHX

## Slide 33
FP7
EuCARD
HiField Dip
LARP
generic
FP6
CARE
Nb3Sn
DOE Nb3Sn R&D
LARP
HiField quads
LARP
Demo
FP7 sLHC PP
(INJ)
sLHC INJ implem.
FP7 DS Hi-Lumi LHC
HL-LHC Construction
M
Injector
upgrade
HL-LHC install.& comm.
2000
2005
2010
2015
2024
CERN-KEK R&D
KEK D1 design and construction
IHEP
CCT corrector
TRIUMF CC cryostat
Crystals, …?
today
Personnel!
Project DS started