## Slide 1: Some considerations on ID cards of HL-LHC magnets
Massimo Giovannozzi
Acknowledgements: L. Bottura, R. De Maria, E. Maclean, S. Le Naour, E. Todesco, R. Tomás
27 February 2023

## Slide 2: General comments
ID cards are essential for magnet assessment and slot allocation activities.
To this goal they should collect all relevant information for magnet activities.
The layout has been one of the first objective of the MEB, which took particular care of the ID cards of main dipoles and quadrupoles (given the relevance and number of these magnets).
The data are taken from relevant databases and the ID cards filled in either in automatic (dipoles and quadrupoles), or manual way (all other magnets).
After magnet acceptance and slot definition, this additional information is added to the ID cards and stored in MTF.

## Slide 3: General comments
With the appointment of the Magnet Assessment Board (MAB), ID cards have regained interest, in particular in the context of HL-LHC activities.
The new HL-LHC magnets require changes to the information reported in the ID cards. These changes have been discussed with WP2 and WP3 Leaders (and few experts) and the final proposal is being presented to MAB for endorsement.
Another big topic to be discussed is the storage of measured data (magnetic and geometry).

## Slide 4: Examples of ID cards: triplet quadrupoles – Q2.R5
All data relevant for magnet assessment included
  Quench performance
  Geometry of magnet
  Field quality (note the colour coding of cells)
  Main milestones
  Important specificities
Proposal for HL-LHC magnet
  Keep same format (without missing data, of course)
  Colour coding: two colours (inside or outside acceptance range)
  Include information from BPM and orbit corrector
  Include maximum b3 and b5 of orbit corrector (with colouring)
  Include maximum gradient reached

## Slide 5: Examples of ID cards: triplet quadrupoles – Q1.L8
All data relevant for magnet assessment included
  Quench performance
  Geometry of magnet
  Field quality (note the colour coding of cells)
  Main milestones
  Important specificities
Proposal for HL-LHC magnet Q1 and Q3
  Use same format as for LHC Q2, i.e. report data for both cold masses
  Colour coding: two colours (inside or outside acceptance range)
  Include information from BPM
  Include maximum gradient reached

## Slide 6: Examples of ID cards: separation dipoles – D2.L5
All data relevant for magnet assessment included
  Quench performance
  Geometry of magnet
  Field quality (note the missing colour coding of cells)
  Main milestones
  Important specificities
Proposal for HL-LHC magnet
  Use same format
  Colour coding: two colours (inside or outside acceptance range)
  Include information from BPM and orbit correctors
  Include maximum b3 and b5 of orbit corrector (with colouring)
  Include maximum field reached

## Slide 7: Examples of ID cards: separation dipoles – D1
I could not find any trace of LHC cold D1 magnets in MTF (certainly my fault)
Proposal for HL-LHC magnet
  Use same format as D2, but a single aperture
  Colour coding: two colours (inside or outside acceptance range)
  Include information from BPM
  Include maximum field reached

## Slide 8: Corrector package
New element in HL-LHC, with no corresponding case in LHC. We need to build an ID card. Proposal
  Quench performance and general information (like for other magnet classes) for each corrector magnet in the package
  Geometry of each corrector magnet
  Transfer function of each corrector magnet
  Main milestones
  Important specificities

## Slide 9: Thanks a lot for your attention